## Slide 1: Pixel Readout for Large Cryogenic Detectors
Dan Dwyer (LBNL)
Pixel 2022 (Santa Fe, NM)
12 Dec 2022

## Slide 2: Neutrino Instrumentation Challenge
Deliver mm-scale spatial granularity for stadium-sized detectors.
Example: DUNE
- DUNE consists of four Far Detector modules, with a total volume on the order of 50,000 cubic meters.
- To achieve the required precision, a spatial granularity of ~4mm is required over this volume.
- Corresponds to a detector with a total of ~1 trillion spatial voxels.
DUNE prototype cyrostat (~1/200th of a DUNE Module)

## Slide 3: 2D vs. 3D LArTPCs
2D Projective TPC
3D TPC
DUNE prototype anode plane
on winding machine
6.4k-channel LArPix
prototype pixel anode tile
2D Projections in MicroBooNE
Raw 3D Cosmic Ray images in
LArPix prototype LArTPC
2D Wire Plane TPC:
- Established technology,
demonstrated in ProtoDUNE-HD
- Multiple 2D views used to
estimate 3D signal
- Baseline technology for
Far Detector #1 (& Strip variant
planned for FD #2)
3D Pixel TPC:
- True 3D imaging
- Continuous readout,
~100% uptime
- Intrinsically sparse data,
low data volume
Science Gains:
- Improved signal fidelity, S/B
- Enhanced low-energy program
JINST 15 P04009
arXiv:2203.12109

## Slide 4: True 3D Readout Technical Targets
For the upcoming large cryogenic detectors (e.g. DUNE)
Resolution and noise
- A granularity of O(mm) in space and O(μs) in time
- Triggering and charge resolution of signals of O(1000 electrons)
Cryogenic compatibility
- Long-term reliable operation at 87 K (in liquid argon)
- Total power dissipation of O(100 μW) per pixel, O(10 W/m2) of sensitive anode
Scalability
- Low-power reliable digital multiplexing of O(10,000 pixels)
- Viable production path for anodes of O(1000 m2)
- Full system production cost of O($10k / m2) at detector scale
Simulation of one neutrino beam spill
in the DUNE LArTPC Near Detector
Prototype LArPix
50k-pixel (0.8 m2)
anode

## Slide 5: LArPix

## Slide 6: R&D on Feasibility: LArPix-v1 System
JINST 13 (2018) P10007
v1 Pixel Anode, Front
LArPix-v1 ASIC
v1 Pixel Anode, Back
3D image of cosmic
shower in a LArTPC
Multi-layer anode cross-section
LArPix-v1 Tile Controller
LArPix-v1: 2016-2018
Complete 3D Pixel System for LArTPCs:
- Custom ASIC with amplifier, digitizer, multiplexer
- Integrated Pixelated Anode w/ASICs
- Control electronics and software (outside cryo)
Key R&D Achievement:
Demonstrated technical feasibility
-> Successfully imaged cosmic rays in LArTPC
ASIC:
- Cryogenic-compatible
- Low-power: 62 uW/channel
- Low-noise: 275 e- ENC @ 87K
Pixel Anode:
- Cryogenic-compatible
- Low Digital-Analog cross-talk
- O(1k) channel readout via 2 wires
Control electronics:
- Fieldable system: noise-isolated and wifi accessible
Main drawback:
Difficult to scale above O(1k) pixels
- Anode requires manual assembly, bare chip wirebonding

## Slide 7: R&D on Scalability: LArPix-v2 System
LArPix-v2: 2019-2021
Substantial Design Evolution:
ASIC Improvements:
- 64 channels/ASIC (twice channel density of v1)
- Hydra-I/O: Dynamic routing, robust to chip failure
- Cryogenic-compatible custom SRAM memory
- Improved tunability, testability
- Packaged to facilitate commercial mass production
Pixel Anode Design Overhaul:
- ‘Tileable’ design to cover anodes of arbitrary scale
- 32cm by 32cm pixel anode PCB tile
- Frontside: 4900 square pixels, 4.4 mm spacing
- Backside: 10x10 grid of ASICs
- Enable fully-commercial mass production and assembly
Warm Controller (PACMAN) Redesign:
- Noise-isolated, compact, flange-mounted
Key R&D Achievement:
Demonstrated robust and scalable pixel anode
- Fast (~few weeks) fully-commercial production/assembly
- Robust to repeated cryogenic cycling
- Successfully imaged cosmic rays in LArTPC
on first try
Production-scale LArPix-v2 Pixel Anode
LArPix-v2 ASIC
Raw 3D images of cosmic rays from initial single-tile test
PACMAN Tile Controller
8-Tile Feedthrough
“LArPix-v2: a commercially scalable large-format 3D charge-readout scheme for LArTPCs”
publication in preparation

## Slide 8: R&D on Robustness: Hydra-I/O
New design for robust I/O and control architecture
Repurpose existing LArPix-v1 low-power data I/O circuit
Very slight change enables richer, dynamic I/O architecture
- I/O can occur between any neighboring chips on pixel tile
- Network is built by explicitly connecting neighboring ASICs in a determined fashion
Successfully exercised with LArPix-v2 chip
Upstream configuration commands
Downstream data flow
Example: 5 x 5 Pixel Tile
Four chips have direct off-tile I/O channels
(10 MHz, < 4 m)
Network reconfigured to avoid failed ASIC
Example failed chip.
AD-HOC NETWORK OF READOUT APPLICATION-SPECIFIC INTEGRATED CIRCUITS FOR RELIABLE DETECTOR INSTRUMENTATION
U.S. Patent Application Ser. No: 63/140,434
2022 R&D 100 Award

## Slide 9: LArPix-v2b: Very low-voltage low-power digital I/O
Custom tunable low-voltage digital transmitter and receiver
- Similar to LVDS in concept, but much lower power: O(10 uW) per transmitter & receiver
- Highly-tunable loop current and termination resistance supports multiple modes of operation (chip-to-chip, multi-drop, etc.)
- Optional mode for automatic transmitter power-down when no data
- LArPix-v2b ASICs received Aug. 2021
- Low-voltage I/O working as designed
- Prototype v2b-based pixel tiles now in production

## Slide 10: LArPix-v2: Scalable Production and Testing Process
ASICs produced and packaged
(@ vendors)
ASIC room-temp QC testing
(@ Lab/Univ. partners)
Anode tiles produced and checked
(@ vendor)
Anode tiles loaded
and inspected
(@ vendor)
LArPix System
room-temp QC testing
(@ Lab/Univ. partners)
LArPix-v2 testing:
~8,000 ASICs tested (so far)
~600 chips/day (1 robot)
Results:
~1% DOA
~10% sub-spec performance
LArPix-v2 testing:
~60 tiles tested (so far)
~8 tile batches, ~1hr
Results:
~0.5% chips failed post-assembly
Chip replacement: ~30 min
LArPix System
QC Cryo-testing
(@ Lab/Univ. partners)
LArPix-v2 testing:
~60 tiles tested (so far)
~8 tile batches (time limited by LN fill/empty)
Results:
No cryo-failures yet
All production/assembly done via commercial vendors; QC testing performed by scientific staff
Controllers, cables, feedthroughs produced and checked
(@ vendor)
ASIC Testing Robot
Cryo-test of Pixel Tiles
Room-temp System Test

## Slide 11: Prototyping: ArgonCube 2x2 LArTPCs
Single pixel tile &
light module assembly
One anode, fully-assembled
Two anodes, installed
inside field cage
LArTPC module
attached to
cryostat lid
LArTPC inside cryostat
Single Module
Cryostat
Four ton-scale Prototype TPC Modules
to validate DUNE Near Detector Design
Each TPC Module:
- Active Size: 0.7m x 0.7m x 1.25m
- 16 pixel tiles, with ~80k pixel channels total
- 16 light collection modules, with 96 light sensors (SiPMs)
- Resistive-film-on-fiberglass field cage
Progress @ Univ. of Bern:
- TPC Module 0:
Run 1 (Demonstration): Apr. 1-10, 2021
Run 2 (Extra Cryo-test): Jun. 21-26, 2021
- TPC Module 1 Operation:
Feb. 5-13, 2022
Achievements:
Demonstrated fully-integrated prototype
detector module at a scale relevant to
the DUNE Near Detector

## Slide 12: Prototyping: ArgonCube 2x2 LArTPCs
Verified design meets technical requirements:
- Collected >107 cosmic ray events
- Stable HV at ~30kV (~1 kV/cm drift, 2x target)
- Stable Purity at >2ms (>4x target)
- MIP Charge Signal-to-Noise >20:1 (at target)
Typical raw data from cosmic ray interactions imaged in 3D prototype detectors
Arguably the most performant
ton-scale LArTPC to date.
Module 0 LArTPC
Module 1 LArTPC
Continuous readout:
~100% live, independent of light system
Low data rate due to self-triggered design
Feb 2023: Four ton-scale TPC modules ready
Mid 2023: Operation in NuMI Neutrino Beam
Prototype for the DUNE Near Detector

## Slide 13: LightPix: Scalable Cryogenic SiPM Readout Electronics
Readout Electronics Needs:
  Low-power cryogenic-compatible scalable SiPM readout electronics at very low system cost
R&D Plan:
  LightPix:
    Adapt existing LArPix ASIC to provide scalable readout for many (e.g. >106) Silicon Photomultipliers
    Reuse all of LArPix system architecture (low-power, cryo-compatible, scalable, O($0.10)/channel system cost)
    Provide a path for highly-granular photodetection systems for very large detectors
Rough concept: Replace LArPix charge-collection pixels with SiPMs
Why LightPix:
Existing readout electronics are either too high power or too high cost for our cryogenic detector needs.
Looking ahead:
Personally, I think LightPix fits
some specific near-term HEP needs (next 5yrs). In the long-term (5-10yrs), my guess is that digitally-integrated SiPMs may eventually provide better performance at lower cost.
e.g. Prototype 6.4k-channel LArPix-v2 tile
e.g. Darkside-20k prototype light sensor

## Slide 14: LightPix ASIC
LightPix-v1:
- Develop and test dedicated time-to-digital converter (TDC)
to provide < 10ns time resolution
- Add multi-channel coincidence triggering mode to suppress
excess data from dark noise at room temp
Progress:
- Received Aug. 2021
- Power-up, configuration successful
- TDC meets design targets
Next Steps:
- LightPix-v2:
Provide both TDC and ADC functionality
- Deployment and testing of light detector system
in prototype LArTPC
- Exploration/optimization of light detector formats
LightPix-v1b ASIC
Very-low-power TDC achieves ~ns-scale
precision in response to external pulse
Offset between
external pulse
and TDC stop
signal
TDC
Triggers (normalized)
Tunable TDC (here ~0.5ns/tick)
Photoelectron signal spectrum vs. SiPM bias

## Slide 15: QPix

## Slide 16: QPix: Concept and Progress
Concept: arXiv:1809.10213
Report ‘time between resets’ instead of digitizing charge
Distribution of reset times proxy for signal current on pixel
Front-end Prototype ASIC
(180nm, UPenn)
Front-end Prototype ASIC
(130nm, UTA)
Front-end Design
(65nm, FNAL)
Digital Back-end Prototype
(FPGA-based, U-Hawaii)

## Slide 17: QPix: Light-sensitive Pixels
Concept:
Add photoconductive (ASe) film to pixel anode to make
pixels sensitive to both TPC charge and scintillation light
Prototype PCBs with biased traces coated in ASe
127 um trace spacing
5V/um max field
UTA/ORNL
127 um trace spacing
5V/um max field
UTA/ORNL
25 um trace spacing
40V/um max field
UCSC/UTA/FNAL
Example signal traces in response to light pulses

## Slide 18: ARIADNE+
Concept:
Achieve Dual-phase TPC 3D readout by
imaging electroluminescence in THGEM
with fast optical cameras
TimePix 3 Camera
Camera System
Relay Optics
Image Intensifier
Objective Lens
Advantages:
Low noise via optical-only readout
Low threshold due to gas amplification
Accessible/upgradeable: Cameras outside cryostat
Disadvantages:
Only viable in a dual-phase TPC
- High cathode voltage
- High-field e- extraction region
- THGEM amplification
Scattered/indirect light
Example 3D
cosmic ray
imaged in
prototype
Camera
Systems
THGEM

## Slide 19: Summary: Neutrino Pixels
LArPix:
- True 3D pixelated charge readout for LArTPCs
- Low-noise, low-power, cryogenic-compatible
- Self-triggering, 100% live
- Scalable anode design leverages commercial production
- Two recent 80k-pixel ton-scale prototype exceeded expectations
- Baseline technology for the DUNE Near Detector
LightPix:
- Highly-scalable readout for cryogenic SiPMs
- Reuses much of LArPix system design
QPix:
- Record trigger time distribution instead of digitizing charge
- R&D on ASe coating to make pixels light-sensitive
ARIADNE+:
- Optical 3D readout for dual-phase TPCs
- Successful mid-scale prototyping at CERN
Potential technologies for future highly-granular detectors
LArPix-v2 ASIC
LArPix-v2 Tile
DUNE Near Detector
Prototype LArTPC
QPix ASe prototype
ARIADNE+ Camera System and 3D imaging
LIghtPix-v1 ASIC
Cosmic ray 3D images
from prototype

## Slide 20: Backup

## Slide 21: 2x2 Module 0 Physics Performance
Energy loss for minimum ionizing muons (dQ/dx)
Observation of positron decay
Energy loss for stopping muons
Data/MC comparison of low-level
self-trigger charge distribution
versus pixel threshold.

## Slide 22: ArgonCube 2x2 @ NuMI
2x2 Operation in NuMI Neutrino Beam 2022-2023
- Install four TPC modules in former location of MINOS-ND
- Includes upstream/downstream trackers, repurposed from Minerva
Goals:
- Develop neutrino signal analysis and reconstruction techniques
- 3D reconstruction of neutrino signals
- Charge-light signal correlations, tolerance to beam pileup
- Track matching with external trackers
Status:
- Cryostat & controls commissioned at Bern
Delivered to FNAL: July 2021
- TPC Module 0, 1 commissioned at Bern
Delivered to FNAL: Oct. 2021, June 2022
- TPC Modules 2, 3 currently in production
To be delivered to FNAL: Winter 2022/2023
- Remaining cryogenics system procurements/production
To be delivered to FNAL: Winter 2022/2023
- Installation and commissioning in NuMI hall
Targeting Spring 2023
Demonstration of ½-million pixel detector
in a GeV neutrino beam!

## Slide 23: Far Detector Pixel Readout: Key Requirements
Requirement Approx. Value LArPix Comment
Granularity < 4.7 mm 3.8 mm Latest LArPix-v2b design has 3.8mm pixel pitch
Noise < 1000 e- ENC 900 e- ENC Noise as measured in ~100k-pixel TPC with LArPix-v2a
Threshold < 200 keV 200 keV 1/4-MIP signal efficiency currently marginal for both ND and FD
Power < 20 W/m2 14 W/m2 Anode heat flux less than heat from cryostat walls. Mitigate boiling at anode.
Digital Multiplexing > 106 pixels/channel 105 pixels/channel Ok for ND. O(10x) digital aggregator needed to reduce FD cabling/feedthroughs
Reliability/Longevity < 5% failure/10yrs (Unknown) Cryo-longevity to be assessed as part of ND prototyping program
Total system cost < $20k/m2 $10k/m2 Total production cost includes full system assembly, cold/warm electronics, etc.
Production throughput > 1000 m2/yr O(200) m2/yr OK for ND. 5x needed for FD. May be possible with current or additional vendors.
Testing throughput > 1000 m2/yr O(50) m2/yr 4x needed for ND; 20x needed for FD. More QC testing partners needed.
My summary of the requirements that would drive system design and production for a future Far Detector
Science
Engineering
Production
Most important steps toward Pixelization of a Far Detector:
- Design and prototype a cryo-robust digital aggregator
- Develop plan and partners to achieve FD-scale QC testing throughput