## Slide 1: Pixel detectors with built-in signal processing and bandwidth-efficient data transmission
PIXEL 2022: 12/14/2022
G.W. Deptuch, G.A. Carini, D. Gorni, S. Mandal, S. Miryala, G. Pinaroli,

## Slide 3: Pixel diagram
detect X-rays < 2 keV Þ ENC=O(10 e-) + ~10b DR in ~100 ×100 mm2

## Slide 4: CSA: Charge Sensitive Amplifier

## Slide 5: Commonly used CSA concepts with ILEAK compensation and with p-z cancellation
Krummenacher’s / Manfredi’s [1]
Common Source Feedback (CSF) [4]
Common Gate
Feedback (CGF) [3]
Ð
Í
Í
feedback resistance µ current source,
IKRUM must exceed ILEAK, Þ parallel noise,
too large ILEAK Þ loss of stability [2],
requires large (~pF) Cint,
not connectable in p-z cancellation.
operates in p-z cancellation,
one-fit-all VRFB is needed,
Reset Quiescent Current (RQI) is optional; if used, multiplied RQI to next stages Þ shift of baseline.
operates in p-z cancellation,
RQI (typ. at some pAs) is required, but difficult to control and match,
larger ILEAK+RQIs Þ loss of stability,
multiplied both RQI and sensor ILEAK to next stages Þ shift of baseline.
input charge signal multiplication
L
L
L
[1] F. Krummenacher, "Pixel detectors with local intelligence: An IC designer point of view", Nucl. Instrum. Methods Phys. Res., vol. A305, pp. 527-532, 1991, P.F. Manfredi, et al, “The analog front-end section of the BaBar silicon vertex tracker readout IC”, Nuclear Physics B - Proceedings Supplements, Vol. 61, Is. 3, February 1998, 532-538
[2] Y. Hu, et al, "A low-noise, low-power CMOS SOI readout front-end for silicon detector leakage current compensation with capability," in IEEE TCAS I, vol. 48, no. 8, pp. 1022-1030, Aug. 2001
[3] G. De Geronimo et al., “A CMOS detector leakage current self-adaptable continuous reset system: theoretical analysis”, Nucl. Instr. Meth. A 421 (1999) 322-333
[4] G. De Geronimo et al., “Front-End ASIC for a GEM Based Time Projection Chamber”, IEEE Trans. Nucl. Sci Vol. 51, No. 4, August 2004 1313-1317
all shown for holes

## Slide 6: New CSA concept with ILEAK compensation and with p-z cancellation
[5] G. W. Deptuch, P. Otfinowski, “Charge Sensitive Amplifier with Pole-Zero Cancellation”, provisional patent application USPTO Serial No. 63/379,887
CSA with Self-Cascoded Field-Effect Transistor (SCFET) feedback network in configuration for integration of input charge signals [5];
Í
CSA with (SCFET) configured in pole-zero cancellation scheme [5], realizing multiplication (gain) of input charge signal ´ n;
Ë
assuming:
no body effect in transistors,
negligible sensor leakage current,
very high open-loop gain of amplifier (OpAmp or OTA)
… in real conditions, VDS1 is only close to “0”, nevertheless transistor M1 act as diode-connected, providing minimal voltage drop across and external voltage bias on its gate is not required
all shown for holes
J
J
L

## Slide 7: Configuration for both polarities
Inverter-type OTA with bias current reuse + active cascode gain boosting
single stage amplifier and 90 dB open loop DC gain,
single stage amplifier Þ intrinsically stable
M1 and M2 = thick gate oxide Þ low gate leakage currents,
other transistors to optimize swing and open loop gain,
inverter-type OTA current defined by power supply
local bias generated for cascode Þ reduced interferences
either electrons or holes programmed or switched

## Slide 8: Stage cascading
1st charge gain stage ‘×n’
2nd charge gain stage ‘×m’

## Slide 9: CSA in simulation
bpad
aout
cout
Qout [e]
Two-stage CSA Þ charge multiplication IOUT=12×12×IIN, with Cf1=4 fF, Cc1=12×4 fF, Cf2=40 fF and Cc2=12×40 fF and for Qinj= 1 fC h+ (2.25 keV X-ray in Si) and ½ of this value every 2.5 ms interchangeably
left axis: magenta ½ fC injections, cyan 1 fC injections, green summed injections.
right axis: yellow Qout

## Slide 10: Shaping Filter with Baseline Adjustment

## Slide 11: Shaping filter with baseline adjustment
Cc is coupling capacitance for the last stage of the CSA
3rd order, 1-real + 2-complex conjugate poles [6], shaping filter (tp=300 ns) with baseline adjustment using current-mode DAC (7.5 bit equiv. +1 bit for polarity setting DAC – k=8)
Rpr = 571.6 kW, Cpr = 304.0 fF
Rpc11 = 183.2 kW /7 = 26.17 kW, Cpc11 = 4.52 pF
Rpc12 = 183.2 kW, Cpc12 = 304.0 fF / 2 =152.0 fF, Rpc13 = 183.2 kW
I current DAC = ±250 nA (baseline) + 1 mA (polarity)
DAC current is injected into node ‘d’ for noise performance
IR drop across Rpc12 Þ shifts of baseline.
[6] G. De Geronimo and S. Li, "Shaper Design in CMOS for High Dynamic Range," in IEEE Transactions on Nuclear Science, vol. 58, no. 5, pp. 2382-2390, Oct. 2011

## Slide 12: CSA + shaping filter in simulations
AC noise simulation for positive polarity for 0 pA, 2 pA, 12.5 pA, 25 pA and 50 pA current biasing SCFET feedback in CSA
two-stage CSA Þ charge multiplication IOUT=12×12×IIN, with Cf1=4 fF, Cc1=12×4 fF, Cf2=40 fF and Cc2=12×40 fF and semi-gaussian shaping filter (1RP2CCP) tp=300 ns; CDET = 50 fF, VDDA=1.5 V, Ibias=~50 mA/OTA stage.
2.95 mVrms ð ENC=16.5 e-
2.32 mVrms ð ENC=12.9 e-
1.93 mVrms ð ENC=10.7 e-
1.53 mVrms ð ENC=9.5 e-
1.32 mVrms ð ENC=7.3 e- (limit)
positive baseline
negative baseline
injection of holes
VVG=752.8 mV
0 h+ ¸ 5,580 h+
0 e- ¸ 5,580 e-
injection of electrons
22 steps
22 steps
linearity for positive and negative signals
obtained separately

## Slide 13: Correct ENC reporting
CSA uses passive, i.e., capacitors, and active, i.e., transistors, components in feedback path of high open-loop gain amplifier.
FE circuit transfer function is non-nonstationary Þ the noise (variance at specific points of time series data) needs to be calculated using transient noise simulation,
Simulation test setup for estimation of noise (SNR and DE/E)
DE/E=~1.6%
DE/E=~0.9%
DE/E=~0.8%
DE/E=~0.85%
1.5 ms long simulations - injections every 5 ms
(max noise frequency 250 MHz)
presented in ‘eyeDiagram’ mode with period of 5 ms
Often SNR is incorrectly reported as
As ratio of pulse amplitude (transient sim.) to rms at not signal (AC noise sim.)

## Slide 14: CRT: Configuration, Readout, Testability

## Slide 15: Static arbitration (priority encoder)
[7] G.W. Deptuch et al., "Design and Tests of the Vertically Integrated Photon Imaging Chip," in IEEE Transactions on Nuclear Science, vol. 61, no. 1, pp. 663-674, Feb. 2014
[8] G.W. Deptuch, “VIPIC-Large, Analysis of RStrobe and RStrobe-less solution”, FERMILAB-TM-2709-PPD, https://lss.fnal.gov/archive/test-tm/2000/fermilab-tm-2709-ppd.pdf
L
Peter Fischer’s
Mephisto-like
fasten “ACK” apply “ReadStrobe”
L
How to switch from one pixel to another?
ACK
L
act on “ACK”
[7]
change way of thinking …
J
common signal to all pixels
effectively serializer’s clock (high speed) sent as ack
[8]

## Slide 16: Dynamic Arbitration: GALS
[9] C.L. Seitz, “Ideas About Arbiters”, Lambda 1st Quarter 1980: Vol. 1 Iss. 1, pp. 10-14
[9]
[10] Shih-Chii Liu, et al, “Event-Based Neuromorphic Systems”, Wiley 2015
In inter-processor networks (CALTECH) it was assumed that sources are synchronous and acquisition is asynchronous (Global Asynchronous – Local Synchronous) Þ source has ¸ for duration of access to medium
but pixel systems are LAGS!
Þ arbiters with Mueller-C gates, where access granted can only be canceled by source by removing request, an it is impossible to communicate with source after Mueller-C gate is set
L
[10]
[10]

## Slide 17: LAGS
digital data, e.g., addresses
analog data, e.g., amplitudes
[11] D.S. Gorni, G.W. Deptuch, S. Miryala, WO2022221068 - EVENT-DRIVEN READOUT SYSTEM WITH NON-PRIORITY ARBITRATION FOR MULTICHANNEL DATA SOURCES
1st event
J
2 requests are arbitrated by “S1”
1 selected request can make up to “rqo” through “S2” and “S3” only when acknowledge is inactive
when “gnt0” or “gnt1” are active, AND gates, unlike C-gates, allow passing activity on “acki” to channel on established connection!
ain – analog sample
din – digital data
rdy – ready to read
cfg – config
sets ‘default’
when no
events
fair (unfair) arbitration
= no close neighbor order
2nd event
programmed to output two values / pixel
no dead time
S1
S2
S3
channel
instructed: terminate or send more data
1 arbiter
needs
3 Seitzes

## Slide 18: CRT: Configuration, Readout, Testability
PLATFORM:
RTL code of complete Configuration-Testability-Readout features,
parametrized and scalable for “virtual painting” of back-bones of pixel detectors,
code may be shared with interested parties
Testability structures
  Integrated into system
  Enable by configuration
  Using readout path to avoid duplication
Configuration path
  Externally - I2C interface
  Internally - Custom Serial-Parallel Bus (SPB)
  Banks of latches
Readout path
  EDWARD architecture
  Event-driven synchronized with acquisition clock
C
R
T

## Slide 19: Layout: pixel and CRT skeleton
Pixel AFE: CSA, SH w DAC, DISC, TeOD, SH/RI + BIAS Þ 90×91 mm2
Pixel Group: 8×8 Pixel AFE + Group CRT
Þ 790×791 mm2
Pixel Matrix: 4×4 Pixel Group + Group CRT
3,205×3,200 mm2
(32×32 100×100 mm2 pixels)
32 × 32 pixels matrix obtained by tiling 4 × 4 basic 8 × 8 pixels groups Þ suitable for tiling into still larger matrix sizes.

## Slide 20: S/H and Readout Interface
BSA prioprietary

## Slide 21: Common Source S/H and Readout Interface
source follower = variable, typically <1, unless complicated architectures [US Patent No 11,108,981 B2]
CS with the S/H capacitor in feedback path is used.
C, N, W, S, E, NW, SW, SE, NE
C, N, W, S, E, NW, SW, SE, NE
read0
read1
read2
read3
read4
read5
read6
read7
read8
shaper(t)
Vthreshold
disc(t)
extr._det(t)

## Slide 22: Summary
Presented design flow for pixel RO ASIC:
  suitable for amplitude spectroscopy with handling of charge shared events
  providing continuous time of operation to handle asynchronous signals
  equipped with true event driven readout
        with analog output, but per/pixel ADC is the next step