## Slide 1
Hamza Javed
Supervisors : Maurizio Perini, Jennifer Ngadiuba, Vladimir Loncar

## Slide 2: Problem
1 collision every 25 nanoseconds
99.99975% of data has to be rejected
Notes: 1 collision every 25 nanoseconds
Immense Data
Data needs to filtered to an acceptable rate
These filters are also called as Trigger systems.
Practically, these filters are not ideal and lose valuable data.
Through machine learning we can optimize this

## Slide 3: Why FPGAs?
During First Trigger
  99.75% rejected
  Decision in ~10 μs
FPGA’s are fast and massively parallelizable

## Slide 4: What are FPGAs?
It’s a whiteboard for hardware
Programmable Circuits
Can emulate any logic

## Slide 5: Why Machine Learning?
Classical HEP algorithms for triggers are accurate.
But, Machine Learning algorithms are faster and can be parallelized
Is there a way to combine the two?
Notes: J

## Slide 6: Fast inference of DNN on FPGAs for L1 Systems

## Slide 7: Approach
Model can be trained in any library
Converted and Optimzied by hls4ml
Deployed on an FPGA
JSON
HLS + Quartus
[1] Javier Duarte, Song Han, Philip Harris, Fast inference of deep neural networks in FPGAs for particle physics, 2018.

## Slide 8: Architecture
Old
New
300x Faster

## Slide 9: Architecture
Old
New
600x Faster

## Slide 10: Test Case
A Deep Neural Network trained for jet classification
Five outputs corresponding to each of the g, q, w, z & t jet.
[1] Javier Duarte, Song Han, Philip Harris, Fast inference of deep neural networks in FPGAs for particle physics, 2018.

## Slide 11: Results
Throughput of 250M events/sec
54 x 4ns = 220ns latency (50 times lower)

## Slide 12: Accelerated ML for HLT Triggers using Openvino

## Slide 13: What is Openvino?
It’s a toolkit for deploying neural networks across multiple intel platforms.
Highly scalable and cross platform compatible.

## Slide 14: Accelerated ML for HLT Trigger
Custom Resnet-50 model used for identifying top quark jets
Optimized using Openvino.
Tested on FPGA, GPU and CPU
[1] Javier Duarte, Philip Harris, Scott Hauck, FPGA-accelerated mache learning inference as a service for particle physics computing, 2019.

## Slide 15: Accelerated ML for HLT Trigger
Chart: Performance comparison between Tensorflow and Openvino
| CPU | GPU
Tensorflow | 5 | 111
Openvino | 12 | 180
2x Faster

## Slide 16: Accelerated ML for HLT Trigger
Type | Hardware | Accuracy | Inference Time | Max Throughput | Power | Throughput/W
CPU | 2 x Xeon 2.1Ghz, 8 core | 0.91 | 88 ms | 11.36 img/s | ~30W | 0.38
FPGA | Arria 10 PAC - FP16 | 0.91 | 14 ms | 84.44 img/s | ~31W | 2.72
 | Arria 10 PAC - FP11 | 0.88 | 7.5 ms | 187.21 img/s | ~31W | 6.03
GPU | GTX 1080 | 0.90 | 7.5 ms | 192 img/s | ~180W | 1.06
FPGA is 3-6x more efficient than a GPU
v
v
v
v

## Slide 17: Acknowledgements
Maurizio Perini, Jennifer Ngadiuba, Vladimir Loncar
Thank You!
hjaved@cern.ch

## Slide 18: Questions?

## Slide 19: Backup

## Slide 20: My Contribution
Wrote and Optimized HLS4ML for Intel FPGA’s
JSON
HLS + Quartus

## Slide 21: Initial Tests
Latency on the order of 80µs
No pipelining
Unusable for L1 systems

## Slide 22: Challenges
Parallelizing operations within a layer.
Achieving sub µs latencies
Speed limitations of Intel’s DSPs.
15973 x 4ns = 64µs latency

## Slide 23: Architecture