## Slide 1: The critical zones around IP1 and IP5
More than 1.2 km of LHC !!
Plus technical infrastructure (e.g. Cryo & Powering)
Alignment and aperture are critical for HL-LHC performance reach!!!
ATLAS
New triplet Nb3Sn
required due to:
-Radiation damage
-Need for more aperture
Changing the triplet region is not enough for reaching the HL-LHC goal!
3. Need also o modify a large part of the matching section
e.g. Crab Cavities &
D1, D2 & corrector
4. For collimation we also need to change the DS in the continuous cryostat: 11T Nb3Sn dipole
CMS
2. Need also to change TAS and TAN passive absorbers and collimators
 TAXS and TAXN

## Slide 2
DFHM
DFHX_1
DFX
VALVES
BOX
SCLINK
UA57
US57
UR55
UL57
R571
UPR
UJ57
COLD BOX
DFHX_2
Q1
Q2A
Q2B
Q3
P5
QDS
Power Converters
Cooling and Ventilation
CP
D1
TAXN
CRAB CAVIITIES
Q4
Q5
D2
HL-LHC WP15
New underground structures for the HL_LHC!
2

## Slide 3: HL-LHC Insertion Regions around Experiments
Parallel to point focusing of triplet:
 Operation requires regular orbit correction along the Matching Section
Requires sufficient aperture margins in the elements of the Matching Section
or regular re-alignment campaigns
HL-LHC proposes a fully remote alignment system to cope with the radiation environment
and to allow regular alignment campaigns
Insertion Layout:
ca. 150m
ca.50m
Offset of the triplet magnets generates transverse shift of the bunches at the IP equal to the triplet offset
 s = 7.5mm  4mm triplet alignment error separates the beams at the IP

## Slide 4: Alignment of Active components Inside a Cryostat
Requires innovative solutions for high precision Internal Metrology!
Crab Cavities
Superconducting magnets

## Slide 5: Review of the HL-LHC Alignment and internal Metrology
Mandate of the review:
The main objective is to review the alignment solutions foreseen for HL-LHC, with a focus on the
internal metrology, the monitoring of inner triplet cold masses and crab cavities inside their cryostat and
full remote alignment systems.
Scope of the review:
The scope of this review is:
To examine the soundness of the proposed solutions individually and as a global system;
To verify that all requirements from equipment owners and machine operation are duly covered;
To check that the interfaces between WP15.4 and the other WPs are clear;
To check the readiness of the solutions proposed and evaluate the associated risk if any;
To evaluate the related test plan, acceptance criteria and the overall schedule;
To examine the procurement strategy, identifying possible risks;
To put in evidence possible integration issues and safety aspects.

## Slide 6: Review of the HL-LHC Alignment and internal Metrology
Review Panel members:
Georg Gassner (SLAC, Chairman),
Johannes Prenting (DESY),
Jean-Philippe Tock (CERN) and
Jörg Wenninger (CERN)
Horst Friedsam (FNAL) via remote connection.
Secretarial support: Elodie Kurzen
Scientific secretary: Mark Jones
Review link persons: Hélène Mainaud Durand and Paolo Fessia.

## Slide 8: TAXNB – absorber of neutrals - necessary for the LHCb upgrade First harware for HiLumi (installation Sept’19)
The new precise alignement tables for TANB.
The 2 TANB ready for installation
HiLumi WP8 – Collider-Experiment interface (EN-EA)
8