## Slide 1: Automation of magnet model generation with SIGMA Short-term internship programme February 1st – July 25st Barakat Bokharaie Supervisor: Matthias Mentink

## Slide 2: Overview
Objective & motivation
What is SIGMA?
Restructuring
Automatic definition of:
  Quench heaters
  Solver settings
  Mesh settings
  Output plots
Validation
Documentation
Summary

## Slide 3: Objective
Restructure SIGMA for reduction of computation time and model complexity
Automate the creation of Quench Heaters in models generated from SIGMA
Automate the definition of standard simulation settings in COMSOL:
  Automatic creation of solver settings
  Automatic creation of mesh
  Automatic creation of frequently used plots

## Slide 4: Motivation
Why is a restructuring required?
  ↑ Complexity  ↑ Variables  ↑ Time
    Complexity reduction becomes vital!
Take the user of SIGMA in account:
  Completely automated with minimum set of features
    QHs, solver settings, mesh, output plots
    Reduced risk of input errors
    Less setup time – more simulations
    Consistency across different models and simulations

## Slide 5: What is SIGMA?
Part of the STEAM framework
Simulation of Transient Effects in Accelerator Magnets
Java-based tool using the COMSOL API for generating magnet models
How SIGMA works:
Magnet geometry in SIGMA:
Courtesy of M. Maciejewski, SIGMA, STEAM Workshop
T0 magnet model
MQXF magnet model
STEAM SIGMA Documentation v1.2,
EDMS nr. 2141579

## Slide 6: Before restructuring SIGMA
Variables before restructuring:
For every half-turn:
  3 averaging operators
  1 minimum operator
  1 variable group (with 12 variables)
For every winding:
  1 integration operator
Voltage and current described
  on half-turn level
Example: Magnet_T0
Magnet_T0 definitions, before restructuring
Variable group generated pr. half-turn
6

## Slide 7: After restructuring SIGMA
Current polarity assigned globally
Coil currents and voltages assigned globally
Significantly reduced
complexity of definitions
Changes:
  Globally assigned polarity and coil currents
  Coil voltage calculation with a single integration operator per coil section depending on CLIQ
  Easy enabling / disabling of CLIQ
Gains:
  Significantly reduced complexity
  Significantly reduced computational time
Costs:
  ISCC physics disabled
  Extra post-processing required to find local voltage-to-ground
Unchanged
Current: I
Current: I+I_cliq
Deleting iscc physics
I_cliq depends on value of withCLIQ
V_Coils_no_cliq
V_Coils_cliq

## Slide 8: Before and after restructuring - comparison
From this….
…to this!
Reduced complexity!

## Slide 9: Automatic creation of Quench Heaters
Automatic generation of additional COMSOL component with:
Multiple quench heaters, implemented in HT module
Automatic coupling to the 2D magnet component
Correct geometry
Automatic generation of relevant material properties
[1] STEAM SIGMA Documentation v1.2, EDMS nr. 2141579
Quench heater geometry [1]
Added materials in quench heater component
Added global definitions

## Slide 10: Automatic creation of Quench Heaters

## Slide 11: Automatic definition of standard COMSOL settings
Creation of two studies:
Stationary
Time dependent
Solver configuration
Stationary solver settings
Transient solver settings

## Slide 12: Automatic definition of standard COMSOL settings
Creation of different meshes:
Mapped
Free Triangular
Mesh settings: Mapped (coils) + triangular (rest)
Mesh after automatic generation

## Slide 13: Automatic definition of standard COMSOL settings
Creation of plots:
Magnetic flux density
Currents
QH temperatures
Quench heater temperatures
Stationary magnetic field
Magnet circuit discharge (EE + QHs)

## Slide 14: Validation (1/2): Comparison of non-restructured and restructured models
Magnetic flux density in non-restructured model
Magnetic flux density in manually restructured model
No difference in magnetic flux density
No difference in current during discharge
 Consistent!

## Slide 15: Validation (2/2): Comparison of manual and automatically generated Comsol models
Identical current discharge
 Consistent!

## Slide 16: Attained speedup due to restructuring
Non-restructured | Restructured
Time-range: range(0,0.001,0.05),range(0.05,0.01,0.25) | 
67s | 64s
Time-range: range(0,0.0002,0.005) range(0.005,0.0005,0.05),range(0.05,0.01,0.25) | 
169s | 79s
Results:
Modest improvement for T0
More improvement for higher complexity models previously demonstrated (11 T double aperture: 15x reduction in computational cost)
So, does the restructured model run faster??

## Slide 17: Documentation (work in progress)
STEAM SIGMA documentation
Documentation of revisions made to SIGMA
Training report for Matthias, Aarhus University (AU) and future students from AU at CERN

## Slide 18: Summary
Completed:
SIGMA restructured for reduction in complexity and computation times
Automatic QHs added with correct geometry, properties and coupling to 2D magnet model
Automatic solver settings, mesh and output plots added
Documentations (in progress)
To do:
Make number of QHs a magnet property
Code convention
Test classes

## Slide 19: Thank you for your attention! Questions?