## Slide 1
Transverse-to-Longitudinal Emittance Exchange Using an RF Deflecting Cavity
V. Dolgashev for P. Emma
3 September, 2010
ICFA Beam Dynamics Mini-Workshop on Deflecting/ Crabbing Cavity Applications in Accelerators
Cockcroft Institute, 1-3 September 2010

## Slide 2
Transverse emittance must be < radiation wavelength (e.g., eN < 1 mm at lr ~ 1 Å)
Energy spread must be < r , the FEL parameter
(e.g., sd < 0.04%)
So we need x < 1 m, and also z  z < 100 mm
Can we reduce x at the expense of z ?
While RF guns produce x ~ z ~ 1-3 mm
Motivation-1 (for X-Ray FEL)

## Slide 3
Final LCLS long. phase space at 14 GeV for initial modulation of 1% at l0 = 15 mm
heated beam stays cool
beam blows up with no heater
Very bright beam from RF guns are susceptible to a m-bunching instability (M. Borland, et al.).
This can be controlled by increasing the intrinsic (slice) energy spread (Landau damped in bunch compressors) → requires a laser heater, but degrades 6D brightness!
Motivation-2 (for X-Ray FEL)

## Slide 4
Strategy for FEL
Use ‘flat-beam injector’ to generate a beam such as: gex ~ 10 mm, gey ~ 0.1 mm, and gez ~ 0.1 mm
Exchange emittances (bends + RF deflector): gex  gez
Saturate FEL at 0.4 Å with no m-bunching instability
gex,y  1 mm, Ipk  3.5 kA, sd  0.01%
gex,y  0.1 mm, Ipk  1 kA, sd  0.01%

## Slide 5
(Y. Derbenev), (R. Brinkmann, Y. Derbenev, K. Flöttmann), (D. Edwards …), (Y.-E Sun)
UV light
rf gun
skew quads
experiment
simulation
X3
X4
X5
X6
X7
X8
gex  0.4 mm
gey  40 mm*
* Ph. Piot, Y.-E Sun, and K.-J. Kim, Phys. Rev. ST Accel. Beams 9, 031001 (2006)
booster cavity
Flat Beam Injector (FNAL)

## Slide 6
Introduce Transverse RF Deflecting Cavity

## Slide 7
Particle at position x in cavity gets acceleration: DE/E  d  kx
This energy deviation d in cavity causes position change: Dx = hd
Choose k to cancel initial position: Dx  hkx = -x  hk = -1
h
k
ex0
ez0
Transverse RF cavity (TM110) in a double dog-leg…
e-
Cornacchia, Emma, PRST AB 5, 084001 (2002), & Emma, et al., PRST AB 9, 100702 (2006).
Exchanger perfected by K.-J. Kim (2005)
Emittance Exchange Beamline

## Slide 8
h
k
R1
Rk
R1
h
2L
x  R56 of dog-leg
rectangular RF deflecting cavity
x, z mapping (ignore y coordinate here)
Emittance Exchanger Transfer Matrix

## Slide 9
If RF deflector voltage is set to: k = -1/h
…then transverse (bend-plane) and longitudinal emittances are completely exchanged.
Full Emittance Exchanger

## Slide 10
Emittance Exchange Limitations
4x4 transfer matrix is four 2x2 blocks1:
[2] Thanks to Bill Spence.
Equal emittances remain equal. (if ex0 = ez0 then ex = ez.)
Equal, uncoupled emittances cannot be generated from unequal, uncoupled emittances3. (Setting |A| = ½ produces equal emittances, but then they are highly coupled with 2  0.)
[3] E. Courant, in “Perspectives in Modern Physics...,” R.E. Marshak, ed., Interscience Publishers, 1966.
[1] K.L. Brown, SLAC-PUB-2370, August 1980.
2
2
symplectic conditions

## Slide 11
Parameters (20 pC bunch charge) | symbol | value | unit
Electron energy | E | 216 | MeV
Dipole magnet length | LB | 20 | cm
Drift length between dipole magnets | L | 1 | m
Bend angle per dipole magnet | q | 20 | deg
Length of rec. RF cavity | Lc | 30 | cm
Initial horizontal norm. emittance | gex | 9.92 | mm
Initial longitudinal norm. emittance | gez | 0.080 | mm
Initial rms bunch length | szG | 51 | mm
Initial rms slice energy spread | sEG | 0.9 | keV
Initial energy chirp (d-z slope) | h | 6.9 | m-1
Initial horizontal beta function | bx | 100 | m
Initial horizontal alpha function | ax | 0 | 
Emittance Exchange Simulation Parameters

## Slide 12
acc. cavities
rf gun
skew quads
intrinsic
gex,y  0.23 mm
9.9 mm
0.084 mm
0.0054 mm
coupled values
gex
gez
gey
Evolution of Transverse Emittance Along Simulated Photo-Injector Beamline (to 216 MeV)

## Slide 13
Transverse phase space (left two plots) and longitudinal phase space (right two plots) before (top) and after (bottom) emittance exchange.
BEFORE EXCHANGER
AFTER EXCHANGER

## Slide 14
Thick-lens: By kick, and then x-offset changes d
add ‘chirp’ to compensate: no mean x-offset
l
tail
head
tail
head
tail
head
Thin-lens gives no x-offset in cavity
Cavity Thick-Lens Effect Requires Some Attention

## Slide 15
Dx
energy error
starts b-osc.
k
k
DE/E
b-tron oscillations disappear
Need extremely stable energy (0.510-6 rms jitter  10% x-beam size jitter)
Unusual System Characteristics

## Slide 16
Yin-e Sun, Philippe Piot, Linac’08
ANOTHER IDEA: Femtosecond Bunch Trains from Phase Space Exchange Technique
Multi-slit mask is used to establish a transverse modulation
Exchanger maps this modulation into temporal

## Slide 17
R33
R43
R34
R44
R11
R21
R31
R41
R12
R22
R32
R42
R13
R23
R14
R24
k/k0 (%)
k/k0 (%)
k/k0 (%)
k/k0 (%)
k/k0 (%)
k/k0 (%)
k/k0 (%)
k/k0 (%)
k/k0 (%)
k/k0 (%)
k/k0 (%)
k/k0 (%)
k/k0 (%)
k/k0 (%)
k/k0 (%)
k/k0 (%)
Measurement of Exchange System (FNAL)
T. Koeth, Linac’08
4×4 matrix measurement vs. RF power
Both on-diagonal 2×2 sub-matrices = 0 at full RF power (k/k0 = 100%)

## Slide 18
Summary
Simulations of flat-beam gun with emittance exchanger suggest possible levels of: gez  10 mm, gey  0.005 mm, gex  0.16 mm
This beam allows shorter wavelength FELs and/or smaller, lower cost accelerators
The resulting large z-emittance should also Landau-damp the micro-bunching instability
Sensitivity to energy jitter may be Achilles heel
Transverse RF opens great new potential !