## Slide 1: Implementation of cross-species ionization in PyECLOUD
L. Mether, G. Iadarola
Acknowledgements: K. Poland, G. Rumolo

## Slide 2: Outline
Introduction
Cross-species ionization model and implementation
First simulation results

## Slide 3: Motivation
  Throughout 2017 operation, abnormal losses were observed in the LHC
  Located in the 16th half-cell left of Point 2 (‘16L2’)
68 premature dumps with the following signature occurred during 2017:
Sudden onset of high beam losses in 16L2
Coherent beam motion with extremely fast rise times
Beam dump either due to losses on the collimation system or directly in 16L2
To stay operational, the LHC was limited to fewer than the nominal number of bunches for most of the 2017 run. Several 16L2 events occurred also in 2018.
X. Buffat
L. Ponce et al.

## Slide 4: Sequence of events in 16L2
The problems in 16L2 are thought to have been caused by air frozen inside the beam chamber, through the following sequence of events:
The macro-particle undergoes a phase transition to a gas, leading to a a high local gas density
A macro-particle of frozen air (N2, O2) is detached,
triggered by e-cloud?
and enters the beam
The beam ionizes some of the gas in its path. Its interaction with the
The beam ionizes some of the gas in its path. Its interaction with the generated electrons/ions causes the fast instabilities
frozen air
beam
macro-particle
electron
gas
ion
A. Lechner

## Slide 5: Sequence of events in 16L2
The problems in 16L2 are thought to have been caused by air frozen inside the beam chamber, through the following sequence of events:
The macro-particle undergoes a phase transition to a gas, leading to a a high local gas density
A macro-particle of frozen air (N2, O2) is detached,
triggered by e-cloud?
and enters the beam
The beam ionizes some of the gas in its path. Its interaction with the
The beam ionizes some of the gas in its path. Its interaction with the generated electrons/ions causes the fast instabilities
Our aim is to model the last part of this sequence of events:
If we assume a high gas density in the beam chamber, can we reproduce the observations in a consistent manner?
Previous studies and development:
Implementation of multi-species simulations
Multi-species build-up and stability simulations with beam-induced ionization of N2 gas
See e.g. LBOC #82
New model ingredient:
Implementation of cross-species ionization

## Slide 6: Multi-species build-up
Multi-species simulations show that electron multipacting becomes less important than beam-induced ionization from gas densities around 1020 N2/m3 and the dynamics are qualitatively and quantitatively different compared to single-species simulations
450 GeV, SEY=1.75

## Slide 7: Beam stability
The gas density during the 16L2 events could be estimated based on the observed loss rates
For the 2017 events, N2 gas densities were estimated to 1019 – 1021 L-1m-2, with the gas covering the length L
A. Lechner et al IPAC 2018
First multi-species beam dynamics simulations show beam instabilities for gas densities ≥ 1021 L-1m-2
This covers only the upper range of the observed instabilities in the machine (1019 – 1021 L-1m-2)
Electron-induced ionization, which has been neglected here, may increase the electron and ion densities for a given neutral gas density, if it is important in the studied cases

## Slide 8: Gas ionization
The rate of gas ionization events is determined by the ionization cross-section and the gas density

## Slide 9: Gas ionization
The rate of gas ionization events is determined by the ionization cross-section and the gas density

## Slide 10: Beam-induced gas ionization
The rate of gas ionization events is determined by the ionization cross-section and the gas density
If the projectile is a beam particle, the path length
and with beam particles, we get

## Slide 11: Beam-induced gas ionization
The rate of gas ionization events is determined by the ionization cross-section and the gas density
If the projectile is a beam particle, the path length
and with beam particles, we get
In a 2D code, we deal with line densities instead of numbers

## Slide 12: Cross-species gas ionization
The rate of gas ionization events is determined by the ionization cross-section and the gas density
If the projectile is a cloud particle, the path length

## Slide 13: Cross-species gas ionization
The rate of gas ionization events is determined by the ionization cross-section and the gas density
If the projectile is a cloud particle, the path length

## Slide 14: Cross-species gas ionization
The rate of gas ionization events is determined by the ionization cross-section and the gas density
If the projectile is a cloud particle, the path length and with projectiles we get

## Slide 15: Cross-species gas ionization
The rate of gas ionization events is determined by the ionization cross-section and the gas density
If the projectile is a cloud particle, the path length and with projectiles we get
In a 2D code, we deal with line densities instead of numbers

## Slide 16: Electron-induced ionization
The beam-gas ionization cross-section at injection and top energy is estimated to be around 2 Mb = 2 × 10-18 cm2
Electrons in the energy range of 50 – 500 eV have a 50 – 100 times larger ionization cross section than the beam particles
The amount of ionization depends on the electron energy distribution during the simulations
BUG et al., Phys. Rev E.88

## Slide 17: Electron energies
Electron energies during the multi-species build-up were previously analysed
See e-cloud meeting #67
6.5 TeV, SEY=1.75

## Slide 18: Electron energies
Electron energies during the multi-species build-up were previously analysed
See e-cloud meeting #67
Energies are favourable for electron impact-ionization in particular for neutral gas densities of 1020 – 1022 N2/m-3

## Slide 19: Electron energy spectrum
Electron energies during the multi-species build-up were previously analysed
See e-cloud meeting #67
Energies are favourable for electron impact-ionization in particular for neutral gas densities of 1020 – 1022 N2/m-3
The amount of electrons in the favorable energy range increases with increasing neutral gas density

## Slide 20: Electron energy spectrum
Electron energies during the multi-species build-up were previously analysed
See e-cloud meeting #67
Energies are favourable for electron impact-ionization in particular for neutral gas densities of 1020 – 1022 N2/m-3
The amount of electrons in the favorable energy range increases with increasing neutral gas density
This gives reason to believe that electron impact-ionization is important for the gas densities that we think occurred in 16L2

## Slide 21: Cross-species ionization model
For the implementation of the cross-species ionization, we want to keep the same simplifying assumptions as are made for the beam-induced ionization
Assume a uniform gas density in the chamber (no neutral macroparticles – we don’t want to go to full-scale plasma simulations)
Consider single ionization only

## Slide 22: Cross-species ionization in PyECLOUD
A new cross-species ionization module has been implemented in PyECLOUD
Holds the necessary information on the user defined cross-species ionization processes
Handles the generation of particles through cross-species ionization
Can handle multiple projectiles and any number of ionization processes per projectile
Other generation processes (secondary emission, photoemission, beam-induced ionization) are performed separately for each cloud
Since the cross-species ionization includes interactions between clouds, all clouds must be handled together
The generating function is called once per time step during build-up simulations

## Slide 23: Generation of ionization products
Loop over projectiles
  Determine the energies of each macroparticle (MP) in the projectile cloud
  Loop over processes for current projectile
    Call process generation function
Ionization_Process. generate()
Cross_Ionization.generate()
Projectile MP info
Called from buildup simulation

## Slide 24: Generation of ionization products
Interpolate the user input cross-section to the projectile MP energies
Determine the number of product particles to be generated by each projectile MP, using their weight
Ionization_Process.generate()
Cross_Ionization. generate()
Projectile MP info

## Slide 25: Generation of ionization products
Interpolate the user input cross-section to the projectile MP energies
Determine the number of product particles to be generated by each projectile MP, using their weight
Loop over products of process
  For each product calculate the number of new MPs to produce, based on the current default weight of the product cloud
    Non-integer parts define probability to generate 1 MP
Ionization_Process.generate()
Cross_Ionization. generate()
Projectile MP info

## Slide 26: Generation of ionization products
Interpolate the user input cross-section to the projectile MP energies
Determine the number of product particles to be generated by each projectile MP, using their weight
Loop over products of process
  For each product calculate the number of new MPs to produce, based on the current default weight of the product cloud
    Non-integer parts define probability to generate 1 MP
  Define coordinates of new MPs:
    Initial position corresponding to position of projectile
    Initial velocities according to initial energy defined by user input
Return information on new MPs for product clouds
Ionization_Process.generate()
Cross_Ionization. generate()
Projectile MP info
Cross_Ionization. generate()
New product MP info

## Slide 27: Generation of ionization products
Loop over projectiles
  Determine the energies of each macroparticle (MP) in the projectile cloud
  Loop over processes for current projectile
    Call process generation function
    Add info on new MPs from process to list of new MPs for each cloud
After looping over all projectiles and processes, generate new MPs in each cloud
Keep record of number of particles and number of MPs generated per cloud every time step
  Saved to output by pyecloud_saver
Ionization_Process. generate()
Cross_Ionization.generate()
Projectile MP info
New product MP info

## Slide 28: Defining the ionization processes
Cross-species ionization is activated by adding in the simulation_parameters input file a dictionary that describes the desired ionization processes:
cross_ion_definitions = {projectile 1: {process 11: process_definitions, process 12: process_definitions}, projectile 2: {process 21: process_definitions, process 22: process_definitions}}
process definitions = {target_density, products, cross_section_file, initial_product_energy, flag_extract_sigma}
projectiles and products must of course correspond to existing clouds

## Slide 29: Test routine
The cross-species ionization module also contains a self-test routine, which runs by default at the beginning of a simulation, and saves a file for every process
The interpolation of the cross-section for an array of energies

## Slide 30: Test routine
The cross-species ionization module also contains a self-test routine, which runs by default at the beginning of a simulation, and saves a file for every process
The interpolation of the cross-section for an array of energies
The cross-section is explicitly set to zero outside the energy range given in the cross-section input file

## Slide 31: Test routine
Reconstructed cross-sections based on the generation algorithm
  For each energy in an array of energies, a mono-energetic projectile macroparticle distribution is passed to the generate() function
  The cross-section at the corresponding energy is estimated based on the ratio between the total number of new particles to be generated and the total number of projectile particles initially passed to the function

## Slide 32: First simulation study
Considered the same simulation set-up as previously studied with multi-species build-up without cross-species ionization
Added electron-induced ionization
cross_ion_definitions = {'electron': {'electron-n2': {'target_density': 1.00e+20, 'products': ['n2', 'electron'], 'cross_section':'cross_section_n2_15.59_20000.00_N1000_log.mat’, 'E_eV_init': 0., 'extract_sigma': True}}}
Scan over gas densities

## Slide 33: 1018 N2/m3
Comparing the densities against the equivalent simulation without cross-species ionization
There is no impact of the electron-induced ionization
SEY=1.25

## Slide 34: 1019 N2/m3
Comparing the densities against the equivalent simulation without cross-species ionization
There is hardly any impact of the electron-induced ionization
SEY=1.25

## Slide 35: 1020 N2/m3
Comparing the densities against the equivalent simulation without cross-species ionization
The densities grow significantly over the bunch train – in agreement with predictions
Densities continue growing after the end of the bunch train (?)
SEY=1.25

## Slide 36: 1021 N2/m3
Comparing the densities against the equivalent simulation without cross-species ionization
The densities grow significantly within a few bunch passages
Electrons very noisy
SEY=1.25

## Slide 37: 1022 N2/m3
Comparing the densities against the equivalent simulation without cross-species ionization
The densities reach a saturation value within a single bunch passage
Electrons very noisy
SEY=1.25

## Slide 38: 1023 N2/m3
Comparing the densities against the equivalent simulation without cross-species ionization
The densities reach a saturation value within a single bunch passage
Electrons very noisy, ions also somewhat noisy
SEY=1.25

## Slide 39: Density dependence
For gas densities from 1020 N2/m3, electron and ion densities in the range 1016 – 1017 m-3 are reached. For higher gas densities, electron and ion densities are similar, but reached faster
6.5 TeV, SEY=1.25

## Slide 40: 450 GeV, SEY 1.25
For gas densities from 1020 N2/m3, electron and ion densities in the range 1016 – 1017 m-3 are reached. For higher gas densities, electron and ion densities are similar, but reached faster
450 GeV, SEY=1.25

## Slide 41: 450 GeV, SEY 1.0
With SEY = 1.0, the results are very similar to the previous case, mainly the behaviour of the 1020 N2/m3 gas density is modified
450 GeV, SEY=1.0

## Slide 42: 450 GeV, perfect absorber
Wit perfect absorber boundary conditions, the results are very similar to the case with SEY = 1.0
450 GeV, SEY=0

## Slide 43: Observations
An unexpected self-sustaining behaviour is observed for a gas density of 1020 N2/m3 – is it physical?
Appears to be a combined effect of secondary emission and cross-species ionization – it is suppressed for low or no SEY
From a first look at the available output no clear physical inconsistency could be identified
Further checks, e.g. the evolution of the total energy in the system, will be performed

## Slide 44: More observations
With the cross-species ionization, the cloud densities can increase by several orders of magnitude over a single or just a few bunch passages
Although PyECLOUD has good macroparticle size management for electron multipacting, the routines are not perfectly adapted to this case
  Normally the macroparticle number is checked for, and adjusted if needed, at the end of each bunch passage
  Asynchronous macroparticle regeneration has already been implemented, where their number is checked and adjusted if needed, at every time step
  Plan to implement more suitable handling of decreasing macroparticle numbers – hope to reduce the noisiness of electron numbers
Currently cross-species ionization is performed at every simulation time step
If generation over this time step is small  poor sampling of the cross-section
  To be investigated if there is a need for a separate ionization time step

## Slide 45: Conclusion & Outlook
Electron-induced ionization was estimated to be important in the 16L2 events
A module for cross-species ionization has been implemented in PyECLOUD to allow for simulations including electron-induced ionization
First simulation studies have been performed and show that the ionization has a significant effect for gas densities from 1020 N2/m-3, as was predicted
In some cases, a self-sustaining behaviour is seen, where generation occurs in the absence of beam – still unclear if the behaviour is physical and real
Further checks and small code improvements e.g. on macroparticle management are required to confirm validity and improve results
Convergence scans to be performed before full-blown simulation studies