## Slide 2
YZ Area ~ 1900 x 600 mm = 1,140,000 mm2
# CITIROC chips need max 888 per side
1284 mm2 / CITIROC
~ 36 x 36 mm available per CITIROC
CITIROC BGA package is ~ 12x12 mm2
About 90% of YZ area free for ADCs, connectors, etc.
Connections from CITIROC to FPGA:
  Trigger outputs – 32 + 1??
  Control I/O – 12+/-
Connections from FPGA to ADC – SPI (?) 4
Total connections layer 1-2 = ~ 150 – 180?? Per 4 CR
Instead of crates with boards || to XY axis
  Layers of boards || to YZ plane
  CITIROC and ADCs on boards closest to detector
  FPGAs, power and optics on backplane board
  Cool with Cu/Al frame in 4x3 or 4x4 shape
    e.g. Cu 50 mm x 12 mm bolted together
    6 mm dia. Cu tube soldered to outer face
    Boards bolted to thermal tabs on frame
If 888 CITIROC in 3x4 grid then 74 per frame
Make CR/ADC boards with 16 CR chips each (~80 x 135) mm
Backplane ~ 350 x 100 mm with 20 (?) ARIA 10s + power + optics
Probably can use much shorter cables if can install CR/ADC boards
Individually in pit(???)

## Slide 3: Basic Numerology
CITIROC –
YZ Area ~ 1900 x 600 mm = 1,140,000 mm2
# CITIROC chips need max 888 per side
1284 mm2 / CITIROC
~ 36 x 36 mm available per CITIROC
CITIROC BGA package is ~ 12x12 mm2 (datasheet)
Connections from CITIROC to FPGA:
  Trigger outputs – 32 + 1??
  Control I/O – 12+/-
Connections from FPGA to ADC – SPI (?) 4
Total connections layer 1-2 = ~ 50?? Per CR
If 888 CITIROC in 3x4 grid then 74 per grid frame
Possible CR/ADC boards with 16 CR chips each (~80 x 135) mm – five per frame  80 CR / grid frame
Needs ~800 pin connector – e.g. two Samtec SEAM / SEAF 40x10 connectors
For 16 chip board (~80 x 135 mm) have 10,400 mm2, need 3600 mm2 for CR, ~ 1600 mm2 for ADCs and ~ 2000 mm2 for connectors – about 70% fill so should be routable but might need blind vias
Backplane ~ 350 x 100 mm with 20 (?) ARIA 10s + power + optics – clearly routable
Perhaps can use much shorter cables if can install CR/ADC boards Individually in pit(???)

## Slide 4
YZ Area ~ 1900 x 600 mm = 1,140,000 mm2
# CITIROC chips need max 888 per side
1284 mm2 / CITIROC
~ 36 x 36 mm available per CITIROC
CITIROC BGA package is ~ 12x12 mm2
About 90% of YZ area free for ADCs, connectors, etc.
Connections from CITIROC to FPGA:
  Trigger outputs – 32 + 1??
  Control I/O – 12+/-
Connections from FPGA to ADC – SPI (?) 4
Total connections layer 1-2 = ~ 150 – 180?? Per 4 CR
Instead of crates with boards || to XY axis
  Layers of boards || to YZ plane
  CITIROC and ADCs on boards closest to detector
  FPGAs, power and optics on backplane board
  Cool with Cu/Al frame in 4x3 or 4x4 shape
    e.g. Cu 50 mm x 12 mm bolted together
    6 mm dia. Cu tube soldered to outer face
    Boards bolted to thermal tabs on frame
If 888 CITIROC in 3x4 grid then 74 per frame
Make CR/ADC boards with 16 CR chips each (~80 x 135) mm
Backplane ~ 350 x 100 mm with 20 (?) ARIA 10s + power + optics
Probably can use much shorter cables if can install CR/ADC boards
Individually in pit(???)

## Slide 5
CR/ADC Board
~ 135 x 80 mm
16 CITIROC
16 ADCs each
5 per frame
FPGA/Power Board
(Backplane)
~ 100 x 350 mm
20 ARIA 10
Power etc.
Frame of Cu (or Al) bars ~ 50 x 10 x 1900 (or 625) mm to make 12 regions
Bolt CR/ADC Board
to frame for good thermal
contact
Solder or braze or press fit
Cu tube to
frame for coolant
Strap from frame to FPGA “tophat”
for FPGA cooling

## Slide 6: Area available
Crate Scheme (4x3)
  222 boards @ 144x170 mm
  5.4 E6 mm2
Parallel board scheme
  Five 135 x 80 / crate = 648 k mm2

## Slide 8: CITIROC Architecture (from CITIROC datasheet v. 2.5)
SIPM voltage control
Preamps – two gain paths
(High Gain, Low Gain)
Shaping – multiple ST
(12.5—87.5 ns) LG & HG
Voltage Sampler – OR
Peak Detector
Analog output – muxed
Trigger outputs from fast
shaping of preamp

## Slide 9: Readout - charge
Either sample and hold or peak detector per channel
Serially muxed to single output pin into external ADC
Settling time for 10 bit resolution is 200 ns – Baby Mind board uses 12 bit ADC
Deadtime (for reading all samples) ~ 6 – 10+ us
Baby Mind board used ONE ADC for 3 CITIROC chips – so 30 – 50 us deadtime

## Slide 10: Trigger? What can CITIROC do?
“Fast” discriminator - per channel (32 per chip)
  Discriminator per channel
  Wide dynamic range setting
  One digital output per channel
  Use FPGA resources to find “patterns” and do timing
“OR” discriminator – per chip
  Same per channel settability