## Slide 1: Quench detection firmware security
R. Denz for WP7
HL-LHC Circuits Review, September 9-10, 2019

## Slide 2: Firmware security - development
Firmware development
  Generic FPGA code only, no vendor specific libraries
  Dedicated tools supporting code development including automatic error correction e.g. SIGASI™ plug-in for Eclipse™ IDE
  Strict version control (also for all hardware designs)  SVN/GIT
  Exhaustive documentation  Confluence™ collaboration software during development  technical specification / user manual after completion stored in EDMS
  Partially automatic firmware generation using standard, already verified building blocks e.g. for ADC readout
  Core of the FPGA code is the finite state machine (FSM) ensuring the proper execution of the code
    FSM is protected by watchdogs (hardware and/or software)
  Device configuration data are transmitted continuously and stored in the LHC logging database (defined as a QPS signal)

## Slide 3: Firmware security - verification
Functional and type testing
  System is regarded as a black box and response to external stimuli i.e. analog input signals verified with respect to the functional specification
  Testing and development of test systems typically done by team members not involved in the firmware development process
Code verification
  Performed by external specialist(s); in the QDS case within a long term collaboration with AGH Krakow
  Verification of code integrity, identification of potentially dangerous constructs, analysis of the synthesis process (not always perfect, results may depend on the version of the tool chain)
During operation
  Verification of device configuration, signal integrity checkers (already successfully in use during RUN2), automatic self checks ( part of QPS_OK signal  affects power and beam permit)