## Slide 1
The CNAO Experience
Notes: 1

## Slide 2
ATER-INFN
Year 1991…

## Slide 3: From 1996 to 1999 at CERN
PIMMS (Proton-Ions Medical Machine Study)
Objective: define the optimal hadrontherapy centre without constraints
CERN-GSI-MedAUSTRON-Oncology2000-TERA
PL: P. Bryant (CERN+experts)
PAC: G. Brianti chairman
TERA: 25 manyrs
MedA.: 10 manyrs
O2000: 3 manyrs
GSI: experts advices

## Slide 4: Created by ministry of health Art. 92 Law 23 December 2000, n. 388 Established 21 Novembre 2001:
To build and run CNAO
To carry on care activities and research

## Slide 5: The CNAO board
Founders:
Fondazione Policlinico Ospedale Maggiore - Milano
Fondazione Istituto Neurologico C. Besta - Milano
Fondazione Istituto Nazionale dei Tumori - Milano
Istituto Europeo di Oncologia - Milano
Fondazione Policlinico San Matteo - Pavia
Fondazione TERA - Novara
Institutional participants:
Istituto Nazionale di Fisica Nucleare
Università di Milano
Politecnico di Milano
Università di Pavia
Comune di Pavia
Participants:
Fondazione Cariplo
Health ministry

## Slide 6
NATIONAL
TERA Foundation: final design and high tech specifications
INFN: co-direction HT, technical issues, radiobiology, research, formation
University of Milan: medical coordination and formation
University of Pavia: technical issues, radiobiology, formation
University of Catania: medical physics
University of Florence: medical physics
Università del Piemonte Orientale: clinical activities
University of Turin: interface beam-patient, TPS
Polytechnic of Milan: patient positioning, radioprotection, authorisations
European Institute of Oncology: medical activities, authorisations
San Matteo Foundation: medical activities, logistics
Town of Pavia: land and authorisations
Province of Pavia: logistics and authorisation
Collaborating Institutes: a network for construction and research

## Slide 7
INTERNATIONAL
CERN (Geneva): technical issues, PIMMS heritage
GSI (Darmstadt): linac and special components
LPSC (Grenoble): optics, betatron, low-level RF, control system
Med-Austron (Vienna): technical collaboration for MA centre
Roffo Institute (Buenos Aires): medical and research activities
NIRS (Chiba): medical activities, radiobiology, formation
HIT (Heidelberg): research activities
KIRAMS (Corea del Sud): clinical and accelerator activities
CLH - Plc (Croazia): hadrontherapy center development
IFJ PAN (Cracovia - Polonia): medical activities
Uni Essen (Germania): medical activities
Sykehuspartner (Norvegia): medical activities
Collaborating Institutes: a network for construction and research

## Slide 8: The CNAO Phases
Phase 1: construction
Years: 2005 - 2009
Phase 2: experimentation
Years: 2010 - 2013
Phase 3: running
Years : 2014 …
Phase 0: organisation
Years: 2002 - 2004

## Slide 9
The high-tech for protons and carbon ions

## Slide 10
AIM OF THE PROJECT
To treat deep tumours :
With ion beams in the range 1 ≤ Z ≤ 6
With active scanning
In approximately 3 min/field
Synchrotron with slow extraction!
Everything safe, proven and/or redundant

## Slide 11: Basic specs
Starting from the patient

## Slide 12: Compact design
4 treatment lines
3 treatment rooms
2 ECR sources
Synchrotron
25m diameter
7 MeV/u LINAC
Designed and built for: safety, efficiency, reliability, maintainability

## Slide 13
LEBT
0.008 MeV/u H3+
0.008 MeV/u C4+
I ~ 0.7 mA (H3+)
I ~ 0.2 mA (C4+)
Continuous beam
LEBT Chopper
Two sources

## Slide 14
RFQ-LINAC
LINAC
0.4-7 MeV/u H3+
0.4-7 MeV/u C4+
RFQ
0.008-0.4 MeV/u H3+
0.008-0.4 MeV/u C4+
217 MHz

## Slide 15
MEBT
7 MeV p
7 MeV/u C6+
I ~ 0.7 mA (p)
I ~ 0.15 mA (C6+)
Stripping foil

## Slide 16: Multiturn injection
Bumper
Bumper
Septum
Closed orbit
Incoming beam
The bumpers create an orbit bump collapsing in tens of turns

## Slide 17
7-250 MeV p
7-400 MeV/u C
Slow extraction
I ~ 0.1-6 mA (p)
I ~ 0.03-1.5 mA (C)
Synchrotron

## Slide 18
Smooth spill to allow tumour painting
0 V
50 ms
Intensity ripple (DI/I) ≤ ± 20% at 2 kHz
(extraction with a betatron core - PIMMS)

## Slide 19: Treatment execution
Synchrotron magnets
Extraction magnets
Injection magnets
1 s
Extracted beam

## Slide 20
HEBT
60-250 MeV p
120-400 MeV/u C
1010 p/spill (~2nA)
4 108 C/spill (~0.4nA)
different settings for
Treatment Line
Horizontal beam size
Vertical beam size
Extraction energy

## Slide 21: Chopper
Fast turn on/off for the beam
Intrinsically safe
Allows beam qualification
The chopper stops (and starts)
the beam within 200 ms.
Used for irradiation of separated parts
of slices and for synchronization with
breathing.

## Slide 22: Irradiation technique active scanning
(Courtesy of Siemens Medical)

## Slide 23: Dose Delivery System
        Real time measurement and control of beam position and delivered number of particles
        Set the current of the scanning magnets spot by spot
        Real time correction of the beam position (feedback)
        Stop beam delivery at the end of each slice or in case of interlock
BOX 1
BOX 2
PS
PS
DD control system
Intensity and position monitors
Scanning magnets
IDD
IDD
IPS
IPS
FPGAs
En-1
En

## Slide 24
Collaboration CNAO-PoliMi
High precision devices for patient positioning

## Slide 25
Patients per year
CLINICAL ACTIVITY
CE Marking

## Slide 26: CNAO is Manufacturer of Medical Device (directive 93/42/EEC)
CNAO obtained the CE label after clinical experimentation

## Slide 27
CNAO: > 1800 patients
66% carbon ions – 34% protons

## Slide 28
Outcome
Treatment results: outcome + toxicity
Chart: Tox at the end of treatment
| G0 | G1 | G2 | G3 | G4
 | 30.0372 | 34.052 | 30.4089 | 5.5019 | 0

## Slide 29: 56 anni maschio Osteosarcoma di basso grado vertebra C1-C2
eritema G1 al termine della CIRT
Effetto stabile dopo 1 anno
Caso simile al NIRS in CR dopo 7 anni
Imai et al. Lancet Oncology 2006
CIRT 73.6 GyE
16 frazioni IMPT

## Slide 30: Clinical experience
SKULL BASE TUMORS | TOT (PT/CIRT) | Median FU (months) | LC (%) | Local Failures
CHORDOMAS | 108 | 27,8 | 85 % | 16
CHONDROSARCOMAS (G1-G2) | 28 | 26,9 | 97 % | 1
Gross tumor volume (GTV)
Chordomas > median (GTV) : 33.4 mL (range, 0-127 mL)
Chondrosarcomas > median (GTV) : 16.9 mL (range, 7,9-53,3 mL)

## Slide 31
10 months F-UP
Skull base chordoma: carbon ions

## Slide 32: Sacral Chordoma
52 patients treated from january 2013
35 patients Fup mean: 21.8 m (range 7- 43)
CR  0 (0%)
PR  10 ( 28%)
SD  18 ( 51%)
PD  7 (20%)
79% LC
CIRT 74 GyE/16 fractions
Notes: 70 Gy(RBE) for chondrosarcoma

## Slide 33
CNAO experience after 1 year
CIRT 74 GyE
16 fractions IMPT
Notes: This is Cnao experience
Among the patients with partial response we had some encouragin results after 1 year.
About PR we started to observe very good response on some pts in terms of mass reduction as you cans see on this images
Analazing data based on RECIST criteria we don’t have any partial response even if we can see the reduction of mass, so…

## Slide 34
Mucosal Melanoma: carbon ions could change the paradigm
1Y OS 74.5 %
CIRT
VS
Surgery
Notes: Quality of life

## Slide 35
Big killers: pancreatic cancer – Clinical Trials
43.2 Gy RBE in 9 fx
14.4 Gy RBE in 3 fx
CTV1: Tumor＋N2 nodes and plexus
9 fractions, prone position, 2 fields
CTV2 ( Main tumor)
3 fractions, 1 field, rolled position
11 patients: 1 Year actuarial LC 82%
Randomized Clinical Trial
CIPHER
CNAO – USA – Germany - Japan

## Slide 36: CNAO is treating tumours in moving organs
Accelerator cycle synchronized with patient breathing (gating)
Goal: tumour tracking in real time

## Slide 37: Re-treatments: 160 patients
NO OTHER THERAPEUTIC OPTION
Notes: Network for patient collection needed

## Slide 38: Ocular treatments with active scanning: FIRST TIME EVER !
Non invasive eye tracking system for intraocular tumour localization in proton therapy treatments
(Collaboration with PoliMi, Galliera, INT, Sacco, UniPv and INFN)
250 patients/year in Italy

## Slide 39
Protons
Protons
X-rays
Pediatric patients elective for protons Less dose to healthy tissues to reduce long term risks of secondary tumours
Notes: In the real world, with a real patient on a real tumor now with modern radiotherapy we have a lot of choise:
Do you want to irradiate a lesion with an irregular shape? You can use Intensity Modulated. But the low dose will spread around.
OF course hadrontherapy is better.
Do you want to irradiate a lesion with high doses, with ablative intent and sparing the most of normal tissue around? You can use radiosurgery.
Hadrontherapy can be a choice in both cases!
in pediatrics cases like this the sparing of the dose at healty tissues is mandatory, for the late toxicity and the high risk of second tumor

## Slide 40: Essential Levels of Assistance (LEA)
Chordoma & chondrosarcoma base/spine
Meningiomas
Brain tumors (trunk)
ACC Salivary Glands
Orbit tumors including eye melanoma
Sinonasal carcinoma
Soft Tissue & bone Sarcoma (every sites)
Recurrent tumors (retreatment)
Patients with immulogical desorders
Pediatric solid tumors
Tumors for which hadrontherapy guarantees a better dose distribution wrt the best alternative providing a 10% better result in terms of NTCP or TCP

## Slide 41
Access to CNAO

## Slide 42
Weekly internal
Board
Waiting list
Treatment begins
REGIONS
Weeks or monts
First visit
Il percorso del paziente

## Slide 43
TAC
RNM
TC/Pet
ANZAI and OTS
Moving organs:
4-D treatment
Gating and rescanning
Pretreatment imaging procedures
Images Fusion

## Slide 44
Individual Treatment Plan Optimization
Target Dmin
OAR DVH
OAR Dmax

## Slide 45: 10% difference is clinically relevant
High dose
(70.4 Gy (RBE)jp )
5yrs. 76.4%
Low dose
(64.0 or 57.6 Gy (RBE)jp)
5yrs. 21.4%
LogRank
p<0.0001
H&N Sarcoma at NIRS
Courtesy of Dr. Hasegawa, NIRS

## Slide 46
Plan verification:
simple cases
Excellent agreement <±2%

## Slide 47
“LEGO Model”: integrated technical and medical solutions
The real challenge: make ALL systems running together
safely, efficiently, reliably and easily maintainable.

## Slide 48: Performance CNAO from Nov. 2011 to Dec. 2017
2095 running days
1523 treatment days
129 days preventive maintenance
36 days of downtime
System availability: 94.2%
System reliability (days): 98.3%
System reliability (sessions)
327 gg
238 gg
25 gg
0 gg
92.8%
100%
96.8% (314 vs 9937)
Year 2017

## Slide 49
Research: the second pillar of CNAO

## Slide 50: Research beamtime with external groups
224 h

## Slide 51: New beamline for Research
Linac
Treatment Rooms
Synchrotron
Ion Sources
High Energy Transfer Lines
Coming up in 2018
New experimental room
(in collaboration with INFN)

## Slide 52
(Courtesy C. Bisogni)

## Slide 53
10 x 25 x 5 cm3
Distance from the
isocenter=30 cm
256 LFS pixel crystals (3x3x20mm3) coupled one to one to MPPCs (Multi Pixel Photon Counters, SiPMs).
2 planes, each one composed of 2 segmented thicker plastic scintillators (6 mm), to perform the energy measurement with a better resolution
6 planes, each one composed of 2 orthogonally oriented scintillating fibres layers
Dose Profiler
In beam PET - panels
Notes: The INSIDE system is mounted on a cart to be fully compatible with clinics

## Slide 54
GEMPix, reference PTW ion chamber and 3D movement in water phantom, HW/SW integrated in one system
IC
Beam
Measurements at CNAO – Italian National Centre for Oncological Hadron therapy
Measurement of 3D energy deposition in water phantom
GEMPix
Beam
Bragg Peak
Fragmentation Tail

## Slide 55: Cancer stem cells
Since cancer stem cells appear to be responsible for driving and maintaining tumor growth in many tumors, it is critical to understand the mechanisms by which these cells resist commonly used therapies such as chemotherapy and radiotherapy
“A small subset of cancer cells within the tumor mass, which constitutes a reservoir of self-sustaining cells with exclusive ability of self-renewal and tumor maintenance” (from the Cancer Stem Cell Workshop of the American Association for Cancer Research in 2006)
bio-markers
Notes: There is increasing evidence that CSCs have a higher intrinsic radioresistance than non-CSC tumor cells
While standard therapies, including chemotherapy and radiation, may initially shrink tumors by killing tumor bulk, the failure of these therapies to eradicate CSCs may be a major contributor to treatment failure, tumor relapse and poor survival.
It has also been suggested that cancer stem cells are more resistant to chemo- and radiotherapy than other cells in a tumour. This could be one cause of tumour relapse after therapy. Understanding how cancer stem cells resist medical therapy could lead to the development of new, more efficient cancer treatments.

## Slide 56: Combined treatments
Particles + radiosensitizers = ???
Particles + chemotherapics = ???
Particles + photons = ???
Particles + …..= ???
Although heavy-ion therapy has provided favorable clinical outcome with irradiation alone, the suitability of particle beam irradiation for combination with other therapeutic modalities such as chemotherapy, endocrine therapy, low LET radiation (“boost protocols”) and biological therapies warrants extensive studies, in the context of both enhancing tumor control and reducing normal tissue complications.

## Slide 57: View of the site
Expansion Area 1
Expansion Area 2

## Slide 58
Expansion Area 1
Work in progress in collaboration with TERA Foundation

## Slide 59
Expansion Area 2
Work in progress in collaboration with TERA Foundation