## Slide 1
Michele Martino
based on Quentin King lecture “Controls and Interfaces” at:
“Power Convertors” CAS, Baden, May 2014
Control of the HO Super-ferric correctors with magnetic saturation
First test results on the MCTXF

## Slide 2: Preamble
In February 2019, WP3 informed WP6B that, for some magnets, differential inductance at 0 A and at nominal can differ by a factor of 3 …
At 69th TCC (28th February 2019) I raised this potential issue and stated that EPC had a working solution which would have however needed experimental validation

## Slide 3: Some definitions
Apparent (or secant) Inductance
Differential (or incremental) Inductance
Energy-equivalent Inductance
In terms of voltages and currents only matters:
EDMS 1148084, Buzio et al., Measurement of the inductance of resistive magnets: two case studies

## Slide 4: HO Correctors Differential Inductance
EDMS 2156334, Mariotto et al., HL-LHC High Order Correctors Differential Inductance
it drops by a factor !

## Slide 5: Some basics concepts of current control
Regulation
Reference Generation
Limitation
Actuation
Acquisition
Load

## Slide 6: Some basics concepts of current control
Regulation
Reference Generation
Limitation
Actuation
Acquisition
Load

## Slide 7: Regulation Variables
Regulation concerns three variables:
  The reference – what you want
  The measurement – what you have
  The actuation – what you can control to make the measurement follow the reference

## Slide 8: Regulation Variables
This presentation will refer to the CERN control model in which the reference and measurement concern the circuit current and the actuation is a voltage reference.
VS
Load
I_MEAS
Controller
V_REF
I_REF

## Slide 9: Regulation Requirements
In general, the objective of the regulator is to ensure that the current is within the acceptable limits from the reference value, when required
  DC operation
  Cycling operation
  Pulsed operation
Reject perturbations with the appropriate bandwidth
Track the reference with the appropriate bandwidth

## Slide 10: Regulation Error
The regulation error is not the difference between the reference and measurement !
Ideally indeed
The regulation error is the difference between the reference shifted by the delay and the measured current
1.7Treg
Time now

Regulation error

## Slide 11: RST algorithm
2-degree-of-freedom control algorithm
  Regulation and tracking performance can be set independently (under non restrictive hypotheses)
  Tracking performance is such that
Based on a rather simplified load model
Rs
Rm
Rp
L
V
I
Gain
Log(frequency)
g0
g1
f0
f1

## Slide 12: (Very) Simplified Scheme of Current Regulation
Function Generator
Real-time
reference
+ +
I_REF
Sat Comp
V_REF_SAT
RST: RefAct
V_REF
V divider
ADC
LPF
LPF
V_MEAS
I_REF_RST
Ref, Meas & Act histories
I_REF_LIMITED
Iref Lim
V_REF_LIMITED
Vref Lim
RST: RefAct
Sat Comp-1
Load
I_LOAD
VS model
Delay
- +
V_ERR
Verr Lim
DCCT
LPF
ADC
I_MEAS
LPF
I_ERR
Delay
Ierr Lim
+ -
V_LOAD
Link
VS
Imeas Lim
REG_MEAS
I_MEAS
I_MEAS_FLTR
FIR
Tmeas
Treg
Tmeas
I_MEAS
I_MEAS

## Slide 13: Magnet Saturation
Our governing equation is:
where is the differential inductance.
What to do when the inductor’s iron starts to saturate?
The differential inductance will fall which can lead to instability
Solution 1: reduce the bandwidth and accept poor performance
Solution 2: change the controller parameters as a function of current
Solution 3: hide the change in from the controller

## Slide 14: Magnet Saturation : CERN PS Main Magnets
O. Bayard, "La nouvelle alimentation de l'aimant du synchroton à protons du CERN, Fascicule 2: description des composants", CERN 71-20, September 1971.
Differential Inductance
Magnet Energy
0.95 H →
0.4 H →
Differential Inductance drops by 60%

## Slide 15: Magnet Saturation
Simple 3-segment linear model:
Defined by four parameters:
Differential Inductance
Current
Lnom
Lsat
Isat_start
Isat_end

## Slide 16: Magnet Saturation
Controller actuation pathway:
To calculate V_REF_SAT:
Differential Inductance
Current
Lnom
Lsat
Isat_start
Isat_end
Ld(I)=f(I).Lnom
f(I)
Current
1
Isat_start
Isat_end
Sat Comp
V_REF_SAT
RST: RefAct
V_REF
V_REF_LIMITED
Vref Lim

## Slide 17: Example of Saturation Compensation
Vref_sat
Vref
Imeas
V
4000
Isat_start
SPS Main Dipole Circuit

## Slide 18: First Test Results on MCTXF
Tests performed on July 16th 2019
Temperature 4.2 K (no implications on diff. inductance)
RPMBA.SM18.RC2.G (LHC600A10V with FGC2)
Ramp Rate: 1.4 A/s
  RST designed by setting only L = 5.35 H and R = 5.7 mΩ
  with Aux Poles @ 1 Hz ()
Slow application → large Gain Margin >18 dB achieved
  GM > 6 dB is usually imposed, but 18 dB is quite a luxury

## Slide 19: Solution 1 – setting only and
>16 dB
other possible dissipative effects not investigated here

## Slide 20: Solution 1 – setting only and

## Slide 21: Solution 1 – setting only and

## Slide 22: 3-segment Linear Model (from EDMS 2156334)

## Slide 23: Solution 3 – settings from EDMS 2156334

## Slide 24: Solution 3 – settings from EDMS 2156334

## Slide 25: Solution 3 – settings from EDMS 2156334

## Slide 26: Conclusions
Currently available magnet saturation compensation works satisfactorily for the MCTXF which has the largest expected change in differential inductance of all HO Super-ferric Correctors
No problems expected due to saturation 

## Slide 27: Thank you for your attention

## Slide 28: Solution 3 – settings from EDMS 2156334 - zoom

## Slide 29: Additional Graphs on Regulation

## Slide 30: Additional Graphs on Regulation

## Slide 31: Additional Graphs on Regulation

## Slide 32: Ramp Down

## Slide 33: Solution 3 – settings from EDMS 2156334

## Slide 34: Solution 3 – settings from EDMS 2156334

## Slide 35: Solution 3 – settings from EPC commissioning

## Slide 36: Solution 3 – settings from EPC commissioning