## Slide 2: FCT and CERN Portuguese Trainee Programme Report
Christopher Viana Lima
(June 2017 – June 2019)
Supervisor: Andre Rocha
CERN, Technology Department
Vacuum, Surfaces and Coatings Group
Interlocks, Controls and Monitoring Section
FCT and CERN Portuguese Trainee Programme Report
Notes: I’m SW dev in ICM

## Slide 3: Outline
Overview of Vacuum at CERN
Vacuum Control Architecture
My Main Project
  VacCC- Vacuum Control Configurator Tool
Challenges
Acquired Skills

## Slide 4: Overview of Vacuum at CERN
Beam and insulation vacuum
> 130 km of vacuum chambers across all accelerators
Pressure range from 10-4 to 10-12 mbar controlled by:
  ~3000 vacuum pumps
  ~3000 vacuum gauges
  ~500 sector valves
How to supervise and control such a large system?
  7 SCADA servers
  ~300 PLCs
  Backboned by vacuum-specific software
TE-VSC-ICM

## Slide 5: Vacuum Controls Architecture
SCADA (Supervisory Control And Data Acquisition)
  Communicates in real-time with controllers running the vacuum process
  Presents data to operators by an user interface (UI) in order to:
    Check the process / react to alarms / interact with devices
  Archives historical data
    Operators can check what happened in the past
PLC (Programmable Logic Controller)
  Connected to vacuum controllers and field equipment
  Communicates with vacuum SCADA
PLC Siemens S7-300
How to configure a large control system ?
LHC main view
Notes: Consist in SCADA and PLCS
SCADA (Human Machine Interface)
-Provides a UI to manage remotely
PLC (big industrial computer)
-interact with the controllers
-send and receive information for SCADA

## Slide 6: Configuring a Vacuum Control System
  Equipment specific parameters (type, control type)
  Equipment location (main part, position within sector)
  Equipment hierarchy (who controls who)
  Alarms
  Short and Long term archiving
  Publish data to other CERN services (CMW, DIP)
Synoptic from LHC
Historical data
History window
Notes: -Set the parameters between SCADA and PLC

## Slide 7: VacCC – Vacuum Control Configurator
Vacuum Control Configurator (legacy)
SCADA configuration files
PLC Configuration files
Export
Memory Mapping
  Reduces human mistakes by performing data validation
  Simplifies the management of the vacuum devices
  Generates SCADA and PLC configuration files
User
Notes: Benefits
-By avoiding conflicts

## Slide 8: VacCC – Problems with legacy application
Oracle ADF* Framework lacks support
Written in Java 6 (released Dec 2006)
Running ADF on new Java versions causes unpredictable behavior
Progressively harder to develop and maintain
User base is declining, only used in legacy projects
*ADF: Oracle Application Development Framework

## Slide 9: New VacCC – Motivations
Rewriting the VacCC Editor with:
Modern technologies with large support
Big set of components available to re-use
Modern test-driven development approach
Easy to maintain & expand current functionalities
=

## Slide 10: New VacCC - Objectives
    Migrate from obsolete technologies
    Porting from a standalone application to a web application
    Take advantage of a microservice architecture
    Improve usability
Notes: -SW modernization
-

## Slide 11: New VacCC Editor - Project Organization
Backend
Database
Frontend
Exporter
Application Logic
Handle requests from user interface
Authentication and authorization
Data validation
Interact with the database
Generates SCADA and PLCs configuration files
Under development
Stores configuration data
Extra data validation
User interface
My main contributions
Notes: -SW modernization
-

## Slide 12: New VacCC – Architecture
VacCC - Before
VacCC After
Monolithic architecture:
One big application
One component failure will cause the whole system to fail
Front End
(UI)
Backend
Exporter
Microservices architecture:
Different functionalities = different components
Allows incremental implementation
Mix different programming languages and frameworks
UI
DB
Exporter
DB
Backend
Notes: Gradually build a new application consisting of microservices, and run it in conjunction with your monolithic application

## Slide 13: New VacCC Editor – Workflow
Back End Server
Front End
Server
Vacuum Control
User
Client
Web Browser
vacdbeditor.cern.ch
Types http://vacdbeditor.cern.ch
Requests React code
Sends React code
API calls
Queries to DB
Returns query results
Returns data to the front end
Databases
Databases
Databases
Notes: The user makes an authentication with CERN credentilals, checking his role

## Slide 14
FCT and CERN Portuguese Trainee Programme Report
Notes: Example from LHC

## Slide 15: Challenges
New VacCC
Several use cases to cover for the DB
Databases logic very challenging and interconnected with external databases
Replicate all databases for test purposes
Critical nature of the application: failure can lead to vacuum downtime
In general
Takes time to be productive in all vacuum applications (SCADA, DB editors, vacuum monitoring)
Notes: The app works with more than accelerator

## Slide 16: Competences
Skills acquired/improved:
  Web technologies (JavaScript, React, REST)
  Programming (Spring Boot)
  Databases (Oracle, PL/SQL)
  Continuous Integration/Deployment (GitLab Runner, Docker)
  Siemens WinCC-OA (SCADA)
  Agile Methodology (Scrum)

## Slide 17: Currently (FELL)
Backend
Database
Frontend
Exporter
My main contributions
Notes: -SW modernization
-

## Slide 18: Currently (FELL)
Backend
Database
Frontend
Exporter
Layout DB Synchronization
My main contributions
Notes: -SW modernization
-

## Slide 19: Questions?
FCT and CERN Portuguese Trainee Programme Report