## Slide 1: HL-LHC Dynamic Aperture at Injection Additional Material
N. Karastathis and Y. Papaphilippou
with many thanks to
F. Asvesta, X. Buffat, R. De Maria, S. Kostoglou
K. Skoufaris, F.v.d.Veken
WP2 Meeting
20.08.2019

## Slide 2: Introduction
From our last presentation, we had two open actions on the DA scans.
Action #1: In the chroma/octupoles scan, extend the chromaticity axis to see if higher values of chromaticity can be used.

## Slide 3: Extending Chromaticity Axis
The overall result does not change significantly: i.e. close to IMO=0 we have plenty of DA.
Above 25 units of chromaticity there is only a narrow band of 6σ DA.

## Slide 4: Introduction
From our last presentation, we had two open actions on the DA scans.
Action #1: In the chroma/octupoles scan, extend the chromaticity axis to see if higher values of chromaticity can be used.
Action #2: In the tune/octupoles scan a tunesplit of 1.5e-2 was selected. Assume that we can correct coupling very well, repeat the study with a tunesplit of 5e-3.

## Slide 5: Reducing the tune split
As we had predicted during the previous presentation, given that the coupling is well corrected, approaching the diagonal increases the peak DA. The shape of the contours do not change dramatically.
Keep in mind that the selected tune must be below 0.29, due to the extra shift generated by e-cloud.
Thank you for your attention!