## Slide 1
CompactLight WP4 meeting
(29/8/2019)
David Alesini
On behalf of the XLS WP4 Study group @ LNF
(M. Diomede, A. Gallo, D. Alesini)

## Slide 2
Parameter | Value
Frequency [GHz] | 11.9942
Phase advance per cell [rad] | 2/3
Shunt impedance R [MΩ/m] | 90-131
Effective shunt Imp. Rs [M/m] | 387
Group velocity vg [%] | 4.7-1.0
Pout/Pin | 0.215
Filling time [ns] | 144
Number of cells per structure | 108
Unloaded SLED Q-factor Q0 | 180000
External SLED Q-factor QE | 23000
# structures per module Nm | 4
Module active length Lmod [m] | 3.6
Average iris radius <a> | 3.5
Iris radius input-output [mm] | 4.3-2.7
Structure length Ls [m] | 0.9
Accelerating cell length [mm] | 8.332
ACCELERATING STRUCTURE AND MODULE: PARAMETERS
 | Rep. rate [Hz] |  | 
 | 100 | 250 | 1000
Average gradient <G> [MV/m] | 65 | 32 | 30.4
Max klystron available output power [MW] | 50 | 50 | 10
Required klystron power per module PK [MW] | 39 | 42.5 | 8.5
RF pulse [µs] | 1.5 | 0.15 | 1.5
SLED | ON | OFF | ON
Av. diss. power per structure [kW] | 1 | 0.31 | 2.2
Peak input power per structure [MW] | 68 | 10.6 | 14.8
Av. Input power per structure [MW] | 44 | 10.6 | 9.6
Module energy gain [MeV] | 234 | 115 | 109

## Slide 3
50 MW, 1.5 µs, 100 Hz
Accelerating gradient and Linac energy reduced by a factor 2 @ 250 Hz rep rate;
The SLED has to be bypassed;
Klystron operated always at its nominal working point (good!);
Max rep rate very much dependent on modulator rise/fall times τtrans
KLYSTRON
SLED
MODE CONVERTER
MODE CONVERTER
CIRCULAR WAVEGUIDE
MODULATOR HALL
LINAC HALL
1 klystron x LINAC Module
<Eacc> = 65 MV/m
SLED bypassed
50 MW, 150 ns, 250 Hz
KLYSTRON
MODE CONVERTER
MODE CONVERTER
CIRCULAR WAVEGUIDE
MODULATOR HALL
LINAC HALL
1 klystron x LINAC Module
<Eacc> = 32 MV/m
HIGH REP. RATE 1st SCENARIO: pulse shortening with high peak power klystrons
Ref. CPI VKX-8311A
Operation probably possible with an optimization of the modulator rise/fall times

## Slide 4
1 kHz rep rate capability, with linac energy up to ≈ 47% of the max value;
R&D activity in progress @CANON and CPI on high rep. rate klystrons towards 10 MW, 1.5 µs, 1 kHz
10 MW, 1.5 µs, 1 kHz, operation probably possible in the near future
Reference RF source CANON Commercially available
<Eacc> = 30.4 MV/m @ 1 kHz
10 MW, 1.5 µs,
1 kHz
SLED
MODE CONVERTER
MODE CONVERTER
CIRCULAR WAVEGUIDE
MODULATOR HALL
LINAC HALL
HIGH REP. RATE 2nd SCENARIO:
LOW POWER HIGH REP. RATE KLYSTRONS

## Slide 5
Switching or combining 2 sources would preserve high gradient at low rep rate;
If source combination is possible, gradients > 30 MV/m available at rep rates ≤ 250 Hz;
10 MW, 1.5 µs, 1 kHz, operation probably possible in the near future
Reference RF source CANON
<Eacc> = 30.4 MV/m @ 1 kHz
10 MW, 1.5 µs,
1 kHz
SLED
MODE CONVERTER
MODE CONVERTER
CIRCULAR WAVEGUIDE
MODULATOR HALL
LINAC HALL
CPI VKX-8311A
RF smart combiner / switch
50 MW, 1.5 µs,
100 Hz
HIGH REP. RATE 3rd SCENARIO:
COMBINATION OF HIGH REP. RATE AND LOW REP. RATE KLYSTRONS
2 klystrons x LINAC Module
<Eacc> = 65 MV/m @ 100 Hz

## Slide 6
1st OPTION: DUAL MODE
Parameter | LINAC 1 | LINAC 2 | TOTAL
Number of structures | 32 | 60 | 92
Number of modules | 8 | 15 | 23
Number of klystrons | 8 (CPI) | 15 (CPI) | 23
Linac active length [m] | 29 | 54 | 83
Rep. rate [Hz] | 100 (250) |  | 
<Eacc> per struct. [MV/m] | 65 (32) |  | 
Energy gain per module [MeV] | 234 (115) |  | 
Max. Energy gain [MeV] | 1872 (921) | 3510 (1728) | 5382 (2649)
LINAC 1
LINAC 2
X-BAND
X-BAND
Single rf source
single linac run in two operating modes
Cheapest
Limited increase in repetition rate (SLED by-passed)
Linac optics needs to operate at two gradient
CPI
KLYSTRON
SLED
<Eacc> = 65 MV/m @ 100 Hz
<Eacc> = 32 MV/m @ 250 Hz

## Slide 7
2nd OPTION: DUAL LINAC
HIGH REP. RATE KLYSTRONS
(ref. CANON)
SLED
CPI
KLYSTRON
SLED
<Eacc> = 30.4 MV/m @ 1 kHz
<Eacc> = 65 MV/m @ 100 Hz
Parameter | LINAC 1 | LINAC 2 | TOTAL
Number of structures | 68 | 60 | 128
Number of modules | 17 | 15 | 32
Number of klystrons | 17 (HRR) | 15 (CPI) | 32
Linac active length [m] | 61 | 54 | 137
<Eacc> per struct. [MV/m] | 30.4 | 65 | -
Rep. rate [Hz] | 1000 | 100 | -
Energy gain per module [MeV] | 109 | 234 | -
Max. Energy gain [MeV] | 1853 | 3510 | 5363
LINAC 1
LINAC 2
X-BAND
X-BAND
two distinct linacs with different rf sources
SXR@ 1 kHz
HXR@ 100 Hz
SXR@ 900 Hz and HXR@ 100 Hz running in parallel

## Slide 8
3rd OPTION: DUAL SOURCE
HIGH REP. RATE KLYSTRONS
(ref. CANON)
SLED
<Eacc> = 30.4 MV/m @ 1 kHz
<Eacc> = 65 MV/m @ 100 Hz
Parameter | LINAC
Number of structures | 92
Number of modules | 23
Number of klystrons | 23 (HRR) + 23 (CPI)
Linac active length [m] | 83
<Eacc> per struct. [MV/m] | 30.4 (@1 kHz), 65 (@ 100 Hz)
Rep. rate [Hz] | 100-1000
Energy gain per module [MeV] | 109 (@1 kHz), 234 (@ 100 Hz)
Max. Energy gain [MeV] | 2507 (@1 kHz), 5382 (@ 100 Hz)
LINAC
X-BAND
X-BAND
CPI
KLYSTRON
Single linac with two sources
SXR@ 1 kHz
HXR@ 100 Hz
SXR and HXR CANNOT run in parallel

## Slide 9
MODULE LAYOUT
The accelerating module layout with 0.9 m long accelerating structures has been completed for the two options: low energy and high energy
Courtesy Gianluca Di Raddo

## Slide 10
MODULE LAYOUT
Courtesy Gianluca Di Raddo