## Slide 1
Introduction/Motivation and current wire HW
Adriana Rossi on behalf of the BBLR team
with material from O. Aberle, A. Bertarelli, C. Boccard, F. Carra, L. Gentini, Y. Papaphilippou, A. Poyet, K.Skoufaris, G. Sterbini
HL-LHC WP2/WP13 meeting on Wire Compensation, Fermilab, 17 October 2019
Notes: Good morning,
thank you for the opportunity to present on behalf of the team the results of the Beam-beam long-range in LHC
1

## Slide 2
2
This meeting
Scope of this meeting is to present the latest experimental and simulation results at LHC with the present demonstrator of wire for Beam-Beam Long Range Compensation.
Present the predictions for the HL-LHC, together with first ideas for the wire hard-ware design and possible implementation.
Building upon the existing collaboration between TRIUMF and CERN, look for a framework for future contributions from TRIUM to HL-LHC for BBLR wire compensation.
HL-LHC WP2/WP13 meeting on Wire Compensation, Fermilab, 17 October 2019

## Slide 3
3
This meeting
LHC
Adriana Rossi : Motivations and present wire demonstrator
Guido Sterbini : MD results during LHC Run II and plans for Run III
Axel Poyet : Modelling of MD results and effect of crossing angles
HL-LHC
Kyriacos Skoufaris : Simulations for HL-LHC configuration
Dobrin Kaltchev : Correction of resonant driving terms with wires
Yannis Papaphilippou : Scenarios and timeline for wire compensation at the HL-LHC
Alessandro Bertarelli : Wire HW design for HL-LHC
Oliver Kester: TRIUMF contribution to the BBLR Compensation Project for HL-LHC
HL-LHC WP2/WP13 meeting on Wire Compensation, Fermilab, 17 October 2019

## Slide 4
4
Outline
Brief introduction to BBLR compensation with wire
Recall the demonstrator HW: wire in-jaw collimator
Installation phases of the demonstrators in LHC
Integration in the HL-LHC
Summary and conclusions
HL-LHC WP2/WP13 meeting on Wire Compensation, Fermilab, 17 October 2019

## Slide 5
5
Long-Range Beam-Beam
LRBB interactions limit accelerator performance
  Perturb motion at large betatron amplitudes, where particles come close to opposing beam
  Produce beam blow-up and deterioration of beam lifetime
  Causes amplitude dependent detuning
  Limit closing crossing angle and therefore luminosity
Courtesy of
G.Sterbini
HL-LHC WP2/WP13 meeting on Wire Compensation, Fermilab, 17 October 2019

## Slide 6: LRBB Wire compensation
Beam-beam (LR) kick (round Gaussian beam + crossing in both planes)
with X/Y (beams separation)
Can be approximated by an “infinite” wire with X/Y (wire separation)
≈1 for large separation
Courtesy of
Y.Papaphilippou
6
HL-LHC WP2/WP13 meeting on Wire Compensation, Fermilab, 17 October 2019

## Slide 7
Recall of design of the demonstrator: wire in-jaw collimator
Requirements for BBLR compensation coming from scaling lows [S.Fartoukh et al., Phys. Rev. ST Accel. Beams 18, 121001 (2015)]
  High current -> cooling
  Approaching the beam at few mm distance
  Specific optics (initially βx/βy~0.5 and 2 on both sides of IP )
Design: Wires embedded into operational TCTP type collimators :
  Joule heating can be cooled by the collimator jaw cooling system
  The wire can approach the beam while being protected
  TCT at almost the right beta ratio
  Maintain TCTP collimator complete functionality!
7
Simulations and experiments explored wider range of parameters and configurations: see talks of G.Sterbini, A.Poyet, K.Skoufaris
HL-LHC WP2/WP13 meeting on Wire Compensation, Fermilab, 17 October 2019

## Slide 8
Engineering Department
EN
Wire-Embedded TCTW
Vacuum tank
Jaws
Actuation system
Tungsten inserts
(Inermet® IT180)
BPM button housing
Cooling pipes CuNi10
Glidcop Al-15 housing and back stiffener
BBLRC wire
Glidcop “T” support
8
Jaw/wire movement
In the plane of beam crossing the jaw position can be moved with a measured reproducible accuracy of 5 µm and with < 200µrad tilt
Possibility to move the wire in the transverse plane (collimator 5th axis) to align on orbit ~ 500µm from BPM dedicated measurements
HL-LHC WP2/WP13 meeting on Wire Compensation, Fermilab, 17 October 2019

## Slide 9
Thicker wire
Wire-Embedded TCTW
Cable dimensions (for 350A nominal current):
Transition 30°
MgO
ø3.45mm
0.41mm
Cu
316L
ø2.48mm
0.3mm
Cu
316L
MgO
Total diameter outside the jaw: ø5mm
Total diameter inside the jaw: ø3.6mm
0.26mm
0.365mm
Wire is brazed to a Glidcop “T shape” support
  Brazing maximizes wire cooling
Tungsten block and “T” support connected in series with the housing via screws
Increase of diameter where the wire is not in direct contact with the jaw (extremities)
Also clamped to cooling pipes when it’s not in the jaw
Note gap between wire and tungsten (0.1÷0.2 mm)
Engineering Department
EN
9
HL-LHC WP2/WP13 meeting on Wire Compensation, Fermilab, 17 October 2019
Wire-in-jaw
3 mm wire/jaw surface distance ~ 3 beam sigmas
Wire-beam distance should be minimized to achieve best compensation performance
New solution for HL-LHC (see talk of A. Bertarelli)

## Slide 10
Tests with spare collimator jaw
10
Max. temperature at IW=350 A: 161 oC
Courtesy of F. Carra
Top view
≈1 m
A. Rossi, Joint LARP CM28/HiLumi Collaboration Meeting, Napa Valley – 24-26 April 2017
HL-LHC WP2/WP13 meeting on Wire Compensation, Fermilab, 17 October 2019
Measurements of wire temp. and voltage drop with and without cooling
Notes: The wire-beam distance has to be of the order of few mm.
10

## Slide 11
Vertical centering with 3 pilot LHC bunches and orbit vertical bump (steps of 0.5mm)
Pressure (VPG.935.B4.R5) below threshold
Checking jaw temperature and movement with wire current ON
Tests at the LHC (G. Sterbini et al.)
11
HL-LHC WP2/WP13 meeting on Wire Compensation, Fermilab, 17 October 2019

## Slide 12
TCL
TCTPH
TCTPV
TAN
D2
TCL
TCTPH
TCTPV
D2
TAN
EYETS 2016-17 – replacement of TCTPH.4R5.B2 and TCL.4L5.B2
3D integration view: 4L5 top and 4R5 bottom.
TCTPH.4R5.B2
TCL.4L5.B2
TCTPH.4R5.B2
B1
B2
IP5
BBCWE.4L5.B2
BBCWI.4L5.B2
BBCWE.4R5.B2
BBCWI.4R5.B2
TCL.4L5.B2
12
HL-LHC WP2/WP13 meeting on Wire Compensation, Fermilab, 17 October 2019
See G.Sterbini’s talk

## Slide 13
TCL
TCTPH
TCTPV
TAN
D2
YETS 2017-18 – replacement of TCTPV.4R1.B2 and installation of new TCLVW.A5L1.B2
3D integration view: 4R1
TCLVW.A5L1.B2
TCTPV.4R1.B2
B1
B2
IP1
BBCWT.5L1.B2
BBCWB.5L1.B2
BBCWB.4R1.B2
BBCWT.4R1.B2
13
HL-LHC WP2/WP13 meeting on Wire Compensation, Fermilab, 17 October 2019
3D integration view: 5L1
TCLVW.A5L1.B2
Q4
Q5

## Slide 14
Compensation (TCT ops opening) provides a reduction of B2 (3 trains) losses by ~20%.
Almost full compensation, even at reduced crossing angle, for 1 regular bunch whereas head-on bunch not degraded.
IPAC19, G. Sterbini, contributed talk WEYYPLM3
A. Poyet
A. Poyet
See G.Sterbini’s talk
14
HL-LHC WP2/WP13 meeting on Wire Compensation, Fermilab, 17 October 2019
3 bunches, 5-6sigma distance
3 trains, TCT operational settings

## Slide 15: LS2 intervention before Run III Moving of two wire collimators for BBLR compensation from B2 to B1 on IR1 and IR5
15
HL-LHC WP2/WP13 meeting on Wire Compensation, Fermilab, 17 October 2019
Before LS2 After LS2
Clear potential to improve also B1 as shown for B2 during MDs
Gain in operational experience with wires during operation in Run III and prove potential for HL-LHC (wires used operationally)

## Slide 16
16
HL-LHC WP2/WP13 meeting on Wire Compensation, Fermilab, 17 October 2019
INTEGRATION of the BBLRW AT HL-LHC IP1/5
extraction from 3-D Model: ST0990131_01
Half-cell 5R1/5R5
Half-cell 5L1/5L5

## Slide 17
17
HL-LHC WP2/WP13 meeting on Wire Compensation, Fermilab, 17 October 2019
RACKS IN IP1(=IP5) ZONE (S.Maridor)

## Slide 18: Future for HL-LHC
18
HL-LHC WP2/WP13 meeting on Wire Compensation, Fermilab, 17 October 2019
See the rest of the meeting!

## Slide 19: Summary and conclusions
19
HL-LHC WP2/WP13 meeting on Wire Compensation, Fermilab, 17 October 2019
Wires have been identified as possible BBLR compensation as early as in the late 1990s
The first proof of concept was actually implemented in the SPS
Wire-in-jaw collimators are being successfully used to test compensation at LHC and simulation work have been able to reproduce experimental results (see future talks)
Results extrapolated to HL-LHC show the possibility of improving standard operations with larger dynamic aperture, more comfortable working point in the tune space, and enhanced performance. Without Carb Cavities, part of the luminosity lost could be recovered.
We hope to rise TRIUMF interest in the project and obtain support to introduce this option at the HL-LHC

## Slide 20: Thank you for your attention Acknowledgments also to (not exhaustive)
20
HL-LHC WP2/WP13 meeting on Wire Compensation, Fermilab, 17 October 2019
D. Amorim, G. Arduini, H. Bartosik, R. Bruce, X. Buffat, L. Carver, G. Cattenoz, L. Ceccone, S. Deschamps, W. Devauchelle, E. Effinger, S. Fartoukh, M. Fitterer, N. Fuster, M. Gasior, M. Gonzales, A. Gorzawski, G.-H. Hemelsoet, M. Hostettler, G. Iadarola, R. Jones, D. Kaltchev, K. Karastatis, S. Kostoglou, I. Lamas Garcia, T. Levens, A. Levichev, L. E. Medina, A. Mereghetti, E. Métral, D. Mirarchi, R. Mompo, J. Olexa, Y. Papaphilippou, D. Pellegrini, M. Pojer, L. Poncet, S. Redaelli, B. Salvachua, H. Schmickler, F. Schmidt, M. Solfaroli, R. Tomas, G. Trad, A. Valishev, D. Valuch, D. Wollmann, C. Xu, C. Zamantzas, P. Zisopoulos and all participants to the design, production and commissioning of the wire compensator prototypes (WP2, WP5, WP13 and LHC MD coordinators).

## Slide 21
Y. Papaphilippou and F. Zimmermann, “Weak-strong beam-beam simulations for the Large Hadron Collider”, in Phys. Rev. ST Accel. Beams 2, 104001 (1999).
Y. Papaphilippou and F. Zimmermann, “Estimates of diffusion due to long-range beam-beam collisions”, in Phys. Rev. ST Accel. Beams 5, 074001 (2002).
J.-P. Koutchouk, CERN-LHC-Project-Note 223 (2000); Proc. PAC2001, Chicago, p. 1681 (2001).
F. Zimmermann, “10 years of wire excitation experiments in the CERN SPS“, in Contribution to the ICFA Mini-Workshop on Beam-Beam Effects in Hadron Colliders, CERN, Geneva, Switzerland, 18-22 Mar 2013, CERN Yel-low Report CERN-2014-004, pp.153-166.
S. Fartoukh et al, “Compensation of the long-range beam-beam interactions as a path towards new configurations for the high luminosity LHC” in Phys. Rev. ST Accel. Beams 18, 121001 (2015).
M.Garlasche, A.Bertarelli, F.Carra, “Energy deposition (E.Skordis) and Structural Analysis of Wire-in-Jaw TCTP collimators”, presented at LHC Collimation Working Group #181, 6 Oct 2014.
L.Gentini, “Wire-in-Jaw TCTP collimators recap on design” and O.Aberle “Tests and Assembly”, presented at LHC Collimation Working Group #203, 11 Apr 2016.
Some literature
21
HL-LHC WP2/WP13 meeting on Wire Compensation, Fermilab, 17 October 2019

## Slide 22
Wire current and temperature with cooling
C. Boccard BE-BI
@ 350A
Temperature profile at 200A
F. Carra EN-MME
65°C
75°C
50°C
260°C
160°C
Jaw @ 27°C
Sagitta 150µm
A. Rossi, Joint LARP CM28/HiLumi Collaboration Meeting, Napa Valley – 24-26 April 2017
HL-LHC WP2/WP13 meeting on Wire Compensation, Fermilab, 17 October 2019
22

## Slide 23
With cooling, the wire temperature as simulations: stable a few minutes after the current jump. Hottest spot at 120°C @ 350A
Without cooling, tests at 100/200/300A: Tw <200-300°C for Uw < 2-3V
Interlock set at 2.7V (note that U(350A)=2.5V)
23
A. Rossi BE/BI – 6th HL-LHC Collaboration Meeting – 14-16 November 2016
T(C)
Voltage across wire U(V)
Wire current and temperature without cooling
HL-LHC WP2/WP13 meeting on Wire Compensation, Fermilab, 17 October 2019
Time (hh:mm)
T(C)
U(V)
Notes: The wire-beam distance has to be of the order of few mm.
23