## Slide 1: Designing the cross section of the MBXF prototype
Kento Suzuki
WP3 meeting, 04/09/2019

## Slide 2: Contents
Review of design procedure for MBXFS2 and 3
  Supplemental slides can be found at
    https://indico.cern.ch/event/844249/contributions/3552239/attachments/1901676/3140152/20190725_CERN-KEK_meetingv2.pdf
Determination of the correction b3
  Coil deformation
  Data– calc. discrepancy at nominal current
  3D effect
Expected b3 integral of the prototype

## Slide 3: MBXF short models so far
Yoke
Collar
Cryostat
Coil blocks
HX hole
MBXFS1 (80 MPa)
MBXFS2 (115 MPa)
MBXFS3 (115 MPa)
HX Φ 61
HX Φ 60
Tested in 2016-2017
Tested in 2018
Under testing
ROXIE 2D input | MBXFS1 | MBXFS2 and 3
f1 (deg) | 1.026 | 1.135
f 2 (deg) | 27.852 | 27.872
f3 (deg) | 50.308 | 50.297
f4 (deg) | 70.635 | 70.699
a1 (deg) | 0 | 0
a2 (deg) | 26.000 | 26.000
a3 (deg) | 52.351 | 52.421
a4 (deg) | 68.002 | 68.002
Azimuthal insulation thickness (mm) | 0.135 | 0.130

## Slide 4: MFM results for Model#2 and #3
 | MBXFS2 | MBXFS3 | 
 | After the cold test (warm, z=0) | After yoking (z=-321.5) | After shell weld. (z=-312.6)
b3 | 18.88 | 21.96 | 21.88
b5 | -1.96 | -2.31 | -2.57
RE
SS
We saw ~20 units offset in b3 for both Model#2 and 3
~20 units

## Slide 5
M. Sugano, F2F meeting on 25/07/19
It was found that the wedge design in Model #2 and #3 was inadequate.
The detailed explanation can be found in
  https://indico.cern.ch/event/844249/contributions/3552239/attachments/1901676/3140152/20190725_CERN-KEK_meetingv2.pdf
For MBXFP: azimuthal cable insulation thickness : 0.122 mm (GFRP E=31.5 GPa) in the ROXIE2D design
  Ref.) 0.130 mm for Model #2 and #3

## Slide 6: Secondary effect: coil deformation
We have evidence that the coil is deviated from the perfect circular model
M. Sugano and K. Suzuki, D1 technical meeting on 10/07/19

## Slide 7: Designing MBXFP
Azimuthal cable insulation thickness : 0.122 mm (GFRP E=31.5 GPa)
ROXIE2D design optimization
at I=3 kA and T=1.9 K
OPERA3D calculation*
Verify integral bn at I=12 kA
Correction on b3 from :
Coil deformation
Data-calc. difference at 12 kA
3D effects
Correction to get final b3:
- Coil deformation
- Data-calc. different at 12 kA
(*) 3D effects are already included

## Slide 8: Measurement of the coil deformation
LDM
(CD22-35 )
Tilt sensor
Reference
gauge (R=75)
MBXFS2
Rotary table
Laser Displacement meter (LDM)
Stepping motor
XZ stage
CFRP pipe
Rotary table

## Slide 9: Measured inner diameter of MBXFS2
Insulation
CB1
CB2
CB3
CB4
1
2
3
4
5
6
1
2
3
4
5
7
6
7
CB4 region is hidden by the insulation and could not be measured
→ Regions of CB1,2 and 3 are used in the analysis
CB１
CB2
CB3
1
2
3
4
5
6
7

## Slide 10: Modeling coil inner surface
/ n.d.f = 2252/410
/ n.d.f = 956/193
diameter (mm)
diameter (mm)
angle (degree)
angle (degree)
a=167 um
 | MBXFS2, 1.9 K, I=3 kA, (ROXIE2D) |  |  |  | MBXFS2 Data at I=3 kA average up/down
 | Wrong wedge | Actual wedge | Actual wedge Oval: (a=167um) | Actual wedge Polynomial | 
b3 | 2.12 | 17.02 | 21.50 | 20.53 | 20.89
b5 | -3.18 | -3.12 | -4.05 | -3.16 | -1.95
b7 | 0.40 | -0.03 | -0.28 | -0.35 | -0.15
b9 | -0.27 | -0.13 | -0.21 | -0.25 | 0.08
Polynomial:
Oval :
+3.51

## Slide 11: Determination of geometrical correction: Δb3geom
Deviation from the ideal circular model is taken into account by introducing the corresponding correction amount of Δb3 (=)
As described, we chose unit as the baseline after comparison with MBXFS2.
  b3 difference between the different models (unit) were taken as uncertainty
We already measured b3 of MBXFS3 whose coil cross section is identical to that of MBXFS2. Nevertheless the measured b3 of MBXFS3 is 3 unit larger than MBXFS2 as shown in the bottom table
Therefore, we target an average of b3MBXFS2 and b3MBXFS3
The total correction amount related to the coil geometry is:
 | MBXFS2 (z=0) | MBXFS3 ( z=~-300) | 
 | After cold test | After yoking | After shell welding
b3 | 18.88 | 21.96 | 21.88
b5 | -1.96 | -2.31 | -2.57
Warm measurement
Production uncertainty
Coil model
uncertainty
Average of Model#2 and 3

## Slide 12: Designing MBXFP
Azimuthal cable insulation thickness : 0.122 mm (GFRP E=31.5 GPa)
ROXIE2D design optimization
at I=3 kA and T=1.9 K
OPERA3D calculation*
Verify integral bn at I=12 kA
Correction on b3 from :
Coil deformation (Δb3=+5.01)
Correction at I=12kA
3D effects
Correction to get final b3:
- Coil deformation (Δb3=+5.01)
- Correction at 12 kA
(*) 3D effects are already included

## Slide 13: Correction at I=12 kA
 | b3 at the center OEPRA fine model | b3 at the center Data (MBXFS2)
3kA (Geom) | 2.04 (I=3kA) | 20.89 (average of up/down)
12 kA | 15.17 | 36.04 (average of up/down)
12 kA – 3 kA | 13.13 | 15.15
Δb3= +2.02
OPERA3D does not reproduce ‘b3 increase’ (b312kA-b33kA) :
Iron saturation and cable displacement due to the Lorentz force
The data-calc. difference is simply assigned to the correction (2.02 unit)
15.15 for data
13.13 for calc.
Previous model

## Slide 14: 3D effect: Transition from 2D to 3D at I=3kA
FQ at z=0 | ROXIE 2D w/o persistent current | OPERA 3D 7m simplified* yoke
 | 3kA | 3kA
b3 | 2.12 | 2.09
b5 | -3.18 | -3.24
b7 | 0.40 | 0.43
b9 | -0.27 | -0.29
b11 | 0.18 | 0.20
2D model predicts the 3D-geometrical FQ well
No correction is necessary for transition from b32D to b33D
(*) Assume no difference in FQ for lower field current between simplified and fine yoke models

## Slide 15: 3D effect : b3 profile along the beam axis
b3 contribution from the coil-end region
due to highly saturated yoke at nominal current
Δ
=
= 4.10 units
At I=12kA, b3 in the straight part is affected by highly saturated yoke at the coil end even for 7m-long (MBXFS2-3 cross section model)
The following shape difference at nominal current operation is taken into account for the correction amount Δb3
3000 A (no saturation)
12047 A
SS

## Slide 16: Summary of the correction to the b3 integral
LE
RE
SS
Numerator
OPERA3D prediction
OPERA3D prediction
Input from
ROXIE2D
Transition
from
2D to 3D
Geometrical correction
Correction at 12 kA
3D shape
5.01 unit
0 unit
2.02 unit
4.10 unit

## Slide 17: Determination of correction b3
Target: -4 unit

## Slide 18
K. Suzuki, D1 technical meeting on 10/07/19

## Slide 19: Optimization result : Δb3=-4 unit
 | For prototype design (2D_v6.a) |  | 
 | Objectives | 3000 A | 12070 A
B1 (T) | - | 1.559041 | 5.569903
b3 | -4 | -3.99870 | -6.03259
b5 | -3 | -3.00004 | 0.36068
b7 | 0 | -0.00541 | -0.48401
b9 | 0 | -0.05577 | 0.37743
b11 | 0 | -0.09511 | -0.13606
 | MBXFS2 and 3 | Prototype (proposal)
f1 | 1.1346 | 1.2957
f2 | 27.8721 | 27.9748
f3 | 50.2969 | 50.4723
f4 | 70.6992 | 70.8718
a2 | 26.0000 | 27.2648
a3 | 52.4212 | 52.3461
a4 | 68.0015 | 69.0283
Azimuthal insulation thickness (mm) | 0.130 | 0.122

## Slide 20: OPERA 3D model
7M model w/ CERN cryostat (perfect alignment)
Estimated BL: 35.005 Tm @ 12.07 kA

## Slide 21: Field profile b3

## Slide 22: Designing MBXFP
Azimuthal cable insulation thickness : 0.122 mm (GFRP E=31.5 GPa)
ROXIE2D design optimization
at I=3 kA and T=1.9 K
OPERA3D calculation*
Verify integral bn at I=12 kA
Correction on b3 from :
Coil deformation (Δb3=+5.01)
Correction at I=12kA (Δb3=+2.02)
3D effects (Δb3shape=+4.01)
Correction to get final b3:
Coil deformation (Δb3=+5.01)
Correction at 12kA (Δb3=+2.02)
(*) 3D effects are already included

## Slide 23: Final b3 integral
Before correction
After
correction
( I = 12 kA )
( I = 12 kA )
(unit) | (unit) |  |  | 
Z=0 | RE | SS | LE | Total
-3.40 | -3.50 | 1.05 | -2.82 | -5.26
Z=0 | RE | SS | LE | Total
-3.40 | -3.50 | 1.05 | -2.82 | -5.26
(unit) | (unit) |  |  | 
Z=0 | RE | SS | LE | Total
3.63 | -3.50 |  | -2.82 | 
Z=0 | RE | SS | LE | Total
3.63 | -3.50 |  | -2.82 | 
Final b3 integral is expected to be within the requirement
Expected
final b3,SS
2.02

## Slide 24: Expected integral for MBXFP
 | Acceptance criteria |  | Expected integral
 | lower limit | upper limit | 
b2 | -0.800 | 0.800 | -0.01
b3 | -2.900 | 2.900 | 
b4 | -0.500 | 0.500 | -0.00
b5 | -1.500 | 1.500 | 0.19
b6 | -0.240 | 0.240 | -0.00
b7 | -0.660 | 0.660 | -0.81
b8 | -0.110 | 0.110 | 0.00
b9 | -0.260 | 0.260 | -0.18
b10 | -0.030 | 0.030 | 0.00
b11 | -0.076 | 0.076 | -0.34
a2 | -0.800 | 0.800 | -0.03
a3 | -2.900 | 2.900 | 1.59
a4 | -0.500 | 0.500 | 0.01
a5 | -1.500 | 1.500 | -0.15
a6 | -0.240 | 0.240 | 0.00
a7 | -0.660 | 0.660 | 0.14
a8 | -0.110 | 0.110 | 0.00
a9 | -0.260 | 0.260 | -0.02
a10 | -0.030 | 0.030 | -0.01
a11 | -0.076 | 0.076 | 0.02
 | Acceptance criteria |  | Expected integral
 | lower limit | upper limit | 
b2 | -0.800 | 0.800 | -0.01
b3 | -2.900 | 2.900 | 
b4 | -0.500 | 0.500 | -0.00
b5 | -1.500 | 1.500 | 0.19
b6 | -0.240 | 0.240 | -0.00
b7 | -0.660 | 0.660 | -0.81
b8 | -0.110 | 0.110 | 0.00
b9 | -0.260 | 0.260 | -0.18
b10 | -0.030 | 0.030 | 0.00
b11 | -0.076 | 0.076 | -0.34
a2 | -0.800 | 0.800 | -0.03
a3 | -2.900 | 2.900 | 1.59
a4 | -0.500 | 0.500 | 0.01
a5 | -1.500 | 1.500 | -0.15
a6 | -0.240 | 0.240 | 0.00
a7 | -0.660 | 0.660 | 0.14
a8 | -0.110 | 0.110 | 0.00
a9 | -0.260 | 0.260 | -0.02
a10 | -0.030 | 0.030 | -0.01
a11 | -0.076 | 0.076 | 0.02

## Slide 25: Conclusion
Reviewed our design procedure found to be inadequate
Performed the measurement of coil deformation to define a correction amount of b3
Further corrections were considered for designing the cross section of the prototype
Evaluated field quality with the new cross section, and resultant b3 is confirmed to be within 2.9 units

## Slide 27: Summary of the field integral
 |  | OPERA Fine Yoke |  |  |  | 
 |  | RE | SS | LE | Total | z=0
ver.6.1.0 12070 A | B1 | 1.778 Tm | 31.456 Tm | 1.771 Tm | 35.005 Tm | 5.577 T
 | b3 | -3.50 units | 7.29 units | -2.83 units | 0.96 units | 3.63 units
 | b5 | -0.24 | 0.19 | 0.24 | 0.19 | -0.18
 | b7 | -0.31 | -0.41 | -0.10 | -0.81 | 0.05
 | b9 | -0.28 | 0.29 | -0.19 | -0.18 | 0.11
 | b11 | -0.13 | -0.12 | -0.09 | -0.34 | 0.18

## Slide 28: Field profile – b5

## Slide 29: Field profile – b7

## Slide 30: Field profile – b9

## Slide 31
M. Sugano, F2F meeting on 25/07/19
for GFRP E=27GPa

## Slide 32: Procedure of designing the MBXFP cross section
GFRP oversize has to be 0.82 mm to achieve pre-stress of 115 MPa
Assuming young’s modulus of GFRP is 31.5 GPa (MBXFS3) Cable-insulation thickness in the azimuthal direction shrinks 0.122 mm
Design has to start from the FINAL cross section in ROXIE2D
In the cable data, 0.122 mm must be adopted for azimuthal cable-insulation thickness. Then the cable position is determined by using optimization algorithm in ROXIE2D
Deduce the bare size of wedges (mechanical work)
Calculate arc lengths of GFRP wedges from the final cross section at the room temperature, and stretch it according to the Hooke’s law () where P=115 MPa and E=31.5 GPa
Rutherford cable
In this way, eventually we will get the target coil cross section
0.122 /0.123
at 115 MPa
0.155 at 0 MPa
Bare size

## Slide 33: Measurement of the coil inner surface
Emitter axis
Coil
LDM
y
x
Coil inner surface was measured using an laser displacement meter (LDM)
The LDM is fixed to the rotary table, and placed inside the magnet
As the table rotates we can measure distance to the coil inner at each angle step

## Slide 34: d(θ) measurement for MBXFS2
LDM was positioned to z=-14 ( the magnet center is at z=0)
Measurement procedure:
  Rotation angle step was set to 0.18 degree
  Took an average of 1000 samples at each angle
  29 rotations in total
RE
LE
Z
-14

## Slide 35
Setup
LDM
(CD22-35 )
Tilt sensor
Reference
gauge (R=75)
Measurement was performed in this summer.
A reference gauge (R=75) is put in front of the magnet to ensure an effect from inclination of LDM, which might result in overestimation of the oval size
Tilt sensor is also attached to the rotary table as well as LDM, which is used to monitor the inclination of the table throughout the measurement
MBXFS2
Rotary table

## Slide 36: Analysis method
To eliminate an effect from ‘off-center’ of the LDM, the coil inner diameter is reconstructed as follow:
Performed an analysis validation using the reference gauge (R=75) and reconstructed d(θ) from the measured r(θ)
  Oval size a is derived by a fit of d(θ) using a cos function
  From the fitting we evaluated the measured oval a is less than 10 um, and confirmed validity of the analysis
r(θ)
d(θ)
d0=149.12 mm
a=-8.97 um
Reference gauge (R=75)
Sinusoidal curve due to ‘off-center’ of LDM
Fit function:
Reconstruct d(θ)

## Slide 37: Modeling coil inner surface
To model the shape of the inner surface following two formulas are introduced:
  Oval model :
  Polynomial model :
    Well describe the inner surface shape of the mechanical short model (see p.39)
    p1-p4 were derived from fitting the mechanical short model and reused for MBXFS2
Fit regions are limited to CB1,2 and 3
Similar reduced was obtained for both model
/ n.d.f = 2252/410
/ n.d.f = 956/193
diameter (mm)
diameter (mm)
angle (degree)
angle (degree)
a=167 um

## Slide 38: ROXIE2D prediction
Implement the two models (oval and poly.) into ROXIE2D and calculate the corresponding multipoles
As shown in the table, we got a good agreement with the measured b3 when poly. model was used
Baseline is to use the polynomial model
  Δb3 = +3.51
Difference between b3oval and b3poly is taken as uncertainty in modeling the coil inner shape
 | MBXFS2, 1.9 K, I=3 kA, phi_R and alpha_R are set to 0 |  |  |  | 
 | original | modified xsec | modified xsec w/ oval (a=167um) | modified xsec w/ poly | MBXFS2 data average up/down
b3 | 2.12 | 17.02 | 21.50 | 20.53 | 20.89
b5 | -3.18 | -3.12 | -4.05 | -3.16 | -1.95
b7 | 0.40 | -0.03 | -0.28 | -0.35 | -0.15
b9 | -0.27 | -0.13 | -0.21 | -0.25 | 0.08
Design variables: ΦR=αR=0
Cable insulation thickness : 0.123 mm
Define position for each cable

## Slide 39: Fitting to the inner diameter of the mechanical short model
Polynomial function
f=Σpi x θi (i=0-4)
Diameter (mm)
Angle (degree)