## Slide 1
Caterina Biscari
ALBA Synchrotron
ECFA-EPS Joint Session
Technology path towards future colliders

## Slide 2
Inputs to the Strategy on accelerators
e+e- colliders
hh colliders
ep colliders
FCC
Gamma factories
Plasma acceleration
Muon colliders
Beyond colliders
Technological developments
Input to this talk mainly from Granada Symposium
Thanks to all those who submitted inputs, plus speakers, plus participants
Questions on Accelerator Science and Technology
What is the best implementation for a Higgs factory? Choice and challenges for accelerator technology: linear vs. circular?
Path towards the highest energies: how to achieve the ultimate performance (including new acceleration techniques)?
How to achieve proper complementarity for the high intensity frontier vs. the high-energy frontier?
Energy management in the age of high-power accelerators?
Disclaimer
Only main technologies
will be mentioned

## Slide 3: Linear colliders technology highlights
rf cavities
nanobeam

## Slide 4: Features of Normal conducting and Superconducting RF
Normal conducting (CLIC) | Superconducting (ILC)
Gradient: 72 to 100 MV/m - Higher energy reach, shorter facility | Gradient: 31.5 to 35 (to 45) MV/m, - Higher efficiency, steady state beam power from RF input
RF Frequency: 12 GHz - High efficiency RF peak power - Precision alignment & stabilization to compensate wakefields | RF Frequency: 1.3 GHz - Large aperture gives low wakefields
Q0: order < 105, - Resistive copper wall losses compensated by strong beam loading – 40% steady state rf-to-beam efficiency | Q0: order 1010, - High Q - losses at cryogenic temperatures
Pulse structure: 180 ns / 50 Hz | Pulse structure: 700 µs / 5 Hz
Fabrication: - driven by micron-level mechanical tolerances | Fabrication - driven by material (purity) & clean-room type chemistry
- High-efficiency RF peak power production through long-pulse, low freq. klystrons and two-beam scheme | - High-efficiency RF also from long-pulse, low-frequency klystrons
Courtesy: W. Wuensch

## Slide 5
Components:
Laboratory with commercial
Accelerating structures
pulse compressors
alignment
Stabilization, etc.
Full commercial supply
X-band klystrons
solid state modulator,
Systems Facilities:
(100 MeV-range)
XBoxes at CERN
(NEXTEF KEK)
Frascati
NLCTA SLAC
Linearizers at Electra, PSI, Shanghai and Daresbury
Test stand at Tsinghua
Deflectors at SLAC, Shanghai, PSI and Trieste
NLCTA
SmartLight
FLASH
C-band (6 GHz),
low-emittance
GeV-range facilities
Operational:
SACLA
SwissXFEL (8 GeV)
CLIC
Normal Conducting Linac Technology Landscape
X-band (12 GHz)
GeV-range facilities
Planning:
EuPraxia
e-SPS
CompactLight
~ 100 (+/-20) MV/m
Courtesy: W. Wuensch
A. Yamamoto, 190513bb

## Slide 6: Advances in SRF Technology for Accelerators
2000
2020
1980
Progress (1988~)
TRISTAN
LEP-II
HERA
CEBAF
CESR
KEKB
BES
cERL
In Operation:  # cavities
SNS: 1 GeV
CEBAF 12 GeV  80
ISAC-II, ARIEL
Super-KEKB
Eu-XFEL  800
Under Construction:
LCLS=II  300
FRIB  340
PIP-II  115
ESS 150
Shine  600
To be realized:
HL-LHC-Crab  20
EIC
ILC-250  8,000
FCC
CEPC/SPPS
> 2,000 SRF cavities realized, in last 10 years !

## Slide 7: Challenges in SRF Cavity Technology
Bulk-Nb:
  High-G and -Q optimization
    Low-T treatment w/ or w/o N-infusion.
  Large-Grain (LG) directly sliced from ingot
    For possible less contamination and cost-reduction
Thin-film Coating
  Nb thin-film coating on Cu-base cavity structure
    Important for lower frequency and/or low-beta application.
    A New approach to realize flatter Q-slope (higher-Q)
    High Power Impulse Magnetron Sputtering (HiPIMS) ,
    instead of
    DC Magnetron Sputtering (DCMS)
  Nb3Sn / MgB2 film coating on Nb or Cu
    To reach much higher G, with higher Bc (Bsh)
A. Yamamoto, 190513bb

## Slide 8: RF technology
Accelerator Technologies are ready to go forward for lepton colliders (ILC, CLIC, FCC-ee, CEPC), focusing on the Higgs Factory construction to begin in > ~5 years.
SRF accelerating technology is well matured for the realization including cooperation with industry.
Continuing R&D effort for higher performance is very important for future project upgrades.
  Nb-bulk, 40 – 50 MV/m: ~ 5 years for single-cell R&D and the following 5 – 10 years for 9cell cavities statistics to be integrated. Ready for the upgrade, 10 ~ 15 years.
FEL communities develop NC + SC rf cavities
Operating (SwissFEL, EuXFEL,…)
in construction (LCLS,…)
in design stage
And so do ERL (PERLE,..)

## Slide 9: ATF/ATF2: Accelerator Test Facility
ILC
Develop nano-beam technology for ILC/CLIC
Goal: Realize small beam-size and theStabilize beam position
1.3 GeV S-band e- LINAC (~70m)
Damping Ring (140m)
Low emittance e- beam
 | B Energy [GeV] | Vertical Size
ILC-250 | 125 | 7.7 nm
CLIC-380 | 190 | 2.9 nm
ATF2 (achieved) | 1.3 | 41 nm (-->8 nm eq. at ILC)
FF: Nano beam-size
Courtesy: N. Terunuma
Advances in light sources
(diffraction limited storage rings)
Demonstrated by MaxIV
In progress at ESRF, Sirius, APS, ALS,….

## Slide 10: Challenges of Linear Colliders Higgs Factories
Luminosity Spectrum
(Physics)
~1034
δE/E ~1.5% in ILC
Grows with E: 40% of CLIC lumi 1% off
Challenging e+ production (two schemes)
CLIC high-current drive beam bunched at 12 GHz
(klystrons + 1.4 BCHF)
Beam Current
(RF power limited, beam stability)
Record small DR emittances
0.1 μm BPMs
IP beam sizes
ILC 8nm/500nm
CLIC 3nm/150nm
Beam Quality
(Many systems)
beamstrahlung

## Slide 11: Overview of CLIC and ILC parameters
CLIC illustrations | CLIC parameters | ILC parameters | ILC illustrations
 | E: 380, 1500, 3000 GeV (L: 11-50 km) Lum: 1.5-5.9 1034 -2 cm-2 s-1 * Prep. phase 2020-2025 Constr.+comm. 7y, ready before 2035 Cost: CLIC-380: 5.9 BCHF, Upgrades: deltas of 5 and 7 BCHF Power: ~ 170 MW – 580 MW** | E: 250, 500, 1000 GeV (L: 20-40 km) Lum: 1.35 (2.7) – 1.8(3.6) 1034 cm-2 s-1* Prep. phase 2020-2023(4) Constr.+comm. 9-10y, ready before 2035 Cost: ILC-250: 4.9-5.3 BILCU, ILC-500: 8 BILCU (2012 $) Power: ~ 130 – 300 MW | 
CLIC y: 75% of 180 days | NCRF X-band now established and industrially available, used in small systems and being introduced in larger ones, relevant reference experience with C-band for larger systems (Swissfel). | SCRF in extensive use in several FELs with parameters close to ILC parameters, the primary one being the E-XFEL at DESY. Technology optimization underway, linking to evolving SCRF R&D for grad. and Q. | ILC y: 75% of 240 days
 | Nanobeam addressed in design & specifications, benchmarked simulations, low emittance ring progress, extensive prototype and method development (for alignment, stabilization, instrumentation, algorithms and feedback systems, system and facility tests : FACET, light-sources, FELs, ATF2) Extensive prototyping of all parts of these accelerators, for lab-test, use/test in test-facilities, light-sources or FELs (magnets, instrumentation, controls, vacuum, etc) |  | 
 | CERN hosted international project (follow LHC model) | Japan hosted international project, initial ideas about European capabilities available (link) | 
* Doubling by increasing frequency (to be) studied, ** Power at 1.5 and 3 TeV not updated from CDR 2012
Staged approach to higher energies

## Slide 12: Circular colliders technology highlights
Size
Synchrotron radiation
High field magnets

## Slide 13: Proton or lepton collisions
14 TeV lepton collisions
Are comparable to 100 TeV proton collisions
D. Schulte

## Slide 14: e+ e- colliders
Synchrotron radiation power, mitigated by long tunnel (100 km)
Limit set to 100 MW @ FCC-ee (60 MW @ CepC) by limiting the current => L decreases as E increases
new beam-beam instability; short beam lifetime => large acceptance
High efficient RF sources:
  Klystron 400/800 MHz η from 65% to >85%
High efficiency SRF cavities:
  10-20 MV/m and high Q0; Nb-on-Cu, Nb3Sn
Crab-waist collision scheme:
  Super KEK-B nanobeams experience will help
Energy Storage and Release R&D:
  Magnet energy re-use > 20,000 cycles
Efficient Use of Excavated Materials:
  10 million cu.m. out of 100 km tunnel
  Shiltsev

## Slide 15: Luminosity Challenge (e+ e-)
Luminosity cannot be fully demonstrated before the project implementation
Luminosity is a feature of the facility not the individual technologies
Have to rely on experiences, theory and simulation and foresee margins
FCC-ee and CEPC are based on experience from LEP, DAPHNE, KEKB, PEP II, superKEKB, …
Gives confidence that we understand performance challenges
New beam physics occurs in the designs,
  e.g. beamstrahlung is unique feature of FCC-ee and CEPC
    Identified and anticipated in the design, should be able to trust simulations
The technologies required are improved versions of those from other facilities
Linear colliders are based on experiences from SLC, FELs, light sources, …
Gives confidence that we understand the performance challenges
Gives us confidence that we can do better than SLC
Still performance goal more ambitious, e.g. beam size of nm scale
  Creates additional challenges and requires additional technologies, e.g. stabilization
A part of the technologies are improved versions of those from other facilities
Some had to be purpose-developed for linear colliders

## Slide 16: Maturity (e+e-)
CEPC and FCC-ee, LHeC
  Do not see a feasibility issue with technologies or overall design
  But more hardware development and studies essential to ensure that the performance goal can be fully met
    E.g. high power klystrons, strong-strong beam-beam studies with lattice with field errors, …
ILC and CLIC
  Do not see a feasibility issue with technology or overall design
  Cutting edge technologies developed for linear colliders
    ILC technology already used at large scale
    CLIC technology in the process of industrialization
  More hardware development and studies required to ensure that the performance goal can be full met
    e.g. undulator-based positron source, BDS tuning, …
Do not anticipate obstacle to commit to either CEPC, FCC-ee, ILC or CLIC
  But a review is required of the chosen candidate(s)
  More effort required before any of the projects can start construction

## Slide 17: pp colliders (+ ion-p, e-p)

## Slide 18: Advances in SC Magnets for Accelerators
2000
2020
1980
Past:
ISR-IR
Tevatron (Fermilab)
TRISTAN-IR (KEK)
HERA (DESY)
Nuclotron (JINR)
LEP-IR (CERN)
KEKB-IR (KEK)
Present:
RHIC (BNL)
LHC (CERN)
SRC (RIKEN) …..
Under Construction
FAIR (GSI) …......
HL-LHC (CERN)
NICA (JINR)
Future:
EIC (e-Ion)
FCC-hh / HE-LHC
SppC
Dipole
IR Quadrupole
Tevatron-D. HERA-D. RHIC-D. LHC.D (NbTi) HL-LHC 11T-D (Nb3Sn)
ISR-IRQ, LEP-IRQ TRISTAN/KEKB-IRQ LHCC-IRQ (NbTI) HL-LHC-IRQ (Nb3Sn)
SC-Cyclotron
Fast-cycleShnchr.

## Slide 19: Nb3Sn Conductor development for Accelerators (1998 ~ )
After 10 years of development, the US and EU development produced the Nb3Sn conductor for HILUMI
ITER
US-CDP
CARE-NED
EuCARD
HL-LHC
HL-LHC specs
FCC
FCC specs
Courtesy, G. de Rijk
A. Yamamoto

## Slide 20: High field magnet development
LHC1.5
12 T Nb3Sn dipoles HiLumi technology in LHC: 21 TeV c.o.m.
7 T Nb-Ti dipole (low cost LHC, 4.2 K):
44 TeV c.o.m. (100 km)
Energy tripler 100km
2040
In LHC, 14 T dipoles give 23.5 TeV
But timeline is NOT the same
HTS

## Slide 21
Bordry
The 1st Series, 5.5 m long Dipole, powered as a single aperture in the initial test: Reached
  Bc = 11.2 T (at nominal current)
    I-nominal, after 1 quench,
  Bc = 12.1 T (at ultimate current)
    I-ultimate) after 6 quenches.
+ Nb3Sn Quadrupole (MQXF) at IR
US: 4.5 m Prototype:
Completed and tested
CERN: 1-m short Models:
Successfully demonstrated the performance
CERN: 7 m Prototype under development
+MgB2 18.5 kA Superconducting Link Demonstrated

## Slide 22: s.c. magnet technology
Nb3Sn superconducting magnet technology for hadron colliders, still requires step-by-step development to reach 14, 15, and 16 T.
It would require the following time-line (in my personal view):
  Nb3Sn, 12~14 T: 5~10 years for short-model R&D, and the following 5~10 years for prototype/pre-series with industry. It will result in 10 – 20 yrs for the construction to start,
  Nb3Sn, 14~16 T: 10-15 years for short-model R&D, and the following 10 ~ 15 years for protype/pre-series with industry. It will result in 20 – 30 yrs for the construction to start, (consistently to the FCC-integral time line).
  NbTi , 8~9 T: proven by LHC and Nb3Sn, 10 ~ 11 T being demonstrated. It may be feasible for the construction to begin in > ~ 5 years.
Continuing R&D effort for high-field magnet, present to future, should be critically important, to realize highest energy frontier hadron accelerators in future.
Intensify HTS accelerator magnet development

## Slide 23
14 T magnet tested at FNAL!
15 T dipole demonstrator
Staged approach: In first step pre-stressed for 14 T (as planned for the first stage)
Second test foreseen in fall 2019 with additional pre-stress for 15 T
60-mm aperture
4-layer graded coil
84% on the laodline at 1.9 K
92% on the loadline at 4.2 K

## Slide 24
The difference between a 14 T and a 16 T magnet is very large, in terms of quantity of conductor needed, number of coils, and complexity of the construction. Though, on paper, a 16 T magnet is possible and is costing about twice the cost of a LHC magnet for twice the field. Achieving such a construction on a large series may be extremely difficult. A two layer design with a target field in the range of 12 T to 14 T is considered by the magnet community present during the FCC week as ‘consensus’ for a collider in the next decades
The design work has shown that all the considered options have a potential for FCC. This has motivated the decision of exploring experimentally all options to answer the outstanding questions of which design meets best the requirements, which margin field level (~12-14 T) should be selected
In the last three years, the FCC Conductor Development Program coordinated by CERN has succeeded in engaging the Japanese (Jastec and Furukawa via the KEK coordination), the Russian (TVEL) and the Korean (KAT) companies in developing for the first time very high-performance Nb3Sn wire. Critical current densities of up to about 1250 A/mm2 at 16 T have been achieved, and kilometers length of wire have been produced in industry and delivered to CERN for first cabling trials
In the US, the FCC current density target (1500 A/mm2 at 16 T) has been achieved! Industrialization and cost reduction has yet to come
14 T magnet tested at FNAL!

## Slide 25
R&D of 12T Twin-aperture Dipole Magnet
Components and assembly
3d coil layout
NbTi+Nb3Sn, 2*ф10 aperture
All HTS, 2*ф40 aperture
3D magnetic field distribution
Magnetic flux distribution
Nb3Sn+HTS, 2*ф20 aperture
R&D Roadmap for the next 10~15 years

## Slide 26
Goal：
1) To increase the Jc of iron-based superconductor (IBS) by 10 times, reduce the cost to 20 Rmb/kAm @ 12T & 4.2K, and realize the industrialization of the conductor;
2) To reduce the cost of ReBCO and Bi-2212 conductors to 20 Rmb/kAm @ 12T & 4.2K;
3) Realization and Industrialization of IBS magnets and SRF cavities.
Working groups：1) Fundamental sciences study; 2) IBS conductor R&D; 3) ReBCO conductor R&D; 4) Bi-2212 conductor R&D; 5) Performance evaluation; 6) Magnet and SRF technology.
Domestic Collaboration for HTS R&D
“Applied High Temperature Superconductor Collaboration (AHTSC)” formed in Oct. 2016.
Including 18 institutions and companies in China. Regular meeting every 3 months.
Qingjin XU

## Slide 27: HTS in Europe
C. Senatore, FCC week

## Slide 28: Beam vacuum systems: HTS coated conductors for FCC-hh beam screen impedance reduction
3 x improvement at 8 GHz compared to copper, expected 20 x improvement at 1 GHz (f3/2)
Synchrotron irradiation @ ALBA: no Tc degradation, neither permanent nor transient under photon flux
REBCO coated conductors are layered structures on a flexible metallic substrate
Soldering of REBCO tapes on the vacuum chamber
Dielectric Resonator
All experiments on samples, supported by theoretical modelling, indicate that the Coated Conductors solution attains FCC-hh performance goals (impedance reduction in high magnetic field) and accelerator compatibility (e-cloud, SR radiation tolerance…)
Ready to undertake scaling-up to
real-scale proof-of-concept device

## Slide 29: Energy Recovery Linacs
- Joint 802 MHz cavity development [LHeC+FCC]
- Very preliminary ideas on FCC-ee design with ERL technique: [extension to higher energy, less SR power, higher lumi > WW]
Llatas, Litvinenko, Roser FCC Brussels
LHeC: 1 TeV ep collider with 1034 luminosity: P/10! Dump at injection.
Possible injector to FCC-ee in recirculating mode [O.Bruening]
Existing test facilities
PERLE BINP, CERN, Daresbury, Liverpool, Jlab, Orsay+. Could be 6 GeV injector to FCC-ee 
ERLs in: Berlin, BINP, Cornell, Daresbury, Darmstadt, Jlab, KEK, Mainz..
High current and E ~ 1GeV: low energy physics [1000 x L(ELI)!, lithography, photofission
ERL: technology for possible applications in HEP, low energy and industrial areas
From M.Klein,

## Slide 30: Technical Challenges in Energy-Frontier Colliders proposed
 |  | Ref. | E (CM) [TeV] | Luminosity [1E34] | AC- Power [MW] | Cost-estimate Value* [Billion] | B [T] | E: [MV/m] (GHz) | Major Challenges in Technology
 | FCC-NbTi | (to be filled) | ~ 100 | < 30 |  |  | ~ 6 |  | ...Find the people who want to do it
CC hh | FCC-hh | CDR | ~ 100 | < 30 | 580 | 24 or +17 (aft. ee) [BCHF] | ~ 16 |  | High-field SC magnet (SCM) - Nb3Sn: Jc and Mechanical stress Energy management
 | SPPC | (to be filled) | 75 – 120 | TBD | TBD | TBD | 12 - 24 |  | High-field SCM - IBS: Jcc and mech. stress Energy management
CC ee | FCC-ee | CDR | 0.18 - 0.37 | 460 – 31 | 260 – 350 | 10.5 +1.1 [BCHF] |  | 10 – 20 (0.4 - 0.8) | High-Q SRF cavity at < GHz, Nb Thin-film Coating Synchrotron Radiation constraint Energy efficiency (RF efficiency)
 | CEPC | CDR | 0.046 - 0.24 (0.37) | 32~ 5 | 150 – 270 | 5 [B$] |  | 20 – (40) (0.65) | High-Q SRF cavity at < GHz, LG Nb-bulk/Thin-film Synchrotron Radiation constraint High-precision Low-field magnet
LC ee | ILC | TDR update | 0.25 ( -1) | 1.35 (– 4.9) | 129 (– 300) | 4.8- 5.3 (for 0.25 TeV) [BILCU] |  | 31.5 – (45) (1.3) | High-G and high-Q SRF cavity at GHz, Nb-bulk Higher-G for future upgrade Nano-beam stability, e+ source, beam dump
 | CLIC | CDR | 0.38 (- 3) | 1.5 (- 6) | 160 (- 580) | 5.9 (for 0.38 TeV) [BCHF] |  | 72 – 100 (12) | Large-scale production of Acc. Structure Two-beam acceleration in a prototype scale Precise alignment and stabilization. timing
*Cost estimates are commonly for ”Value” (material) only.

## Slide 31: Technical Challenges in Energy-Frontier Colliders proposed
 |  | Ref. | E (CM) [TeV] | Luminosity [1E34] | AC- Power [MW] | Cost-estimate Value* [Billion] | B [T] | E: [MV/m] (GHz) | Major Challenges in Technology
 | FCC-NbTi | (to be filled) | ~ 100 | < 30 |  |  | ~ 6 |  | ...Find the people who want to do it
CC hh | FCC-hh | CDR | ~ 100 | < 30 | 580 | 24 or +17 (aft. ee) [BCHF] | ~ 16 |  | High-field SC magnet (SCM) - Nb3Sn: Jc and Mechanical stress Energy management
 | SPPC | (to be filled) | 75 – 120 | TBD | TBD | TBD | 12 - 24 |  | High-field SCM - IBS: Jcc and mech. stress Energy management
CC ee | FCC-ee | CDR | 0.18 - 0.37 | 460 – 31 | 260 – 350 | 10.5 +1.1 [BCHF] |  | 10 – 20 (0.4 - 0.8) | High-Q SRF cavity at < GHz, Nb Thin-film Coating Synchrotron Radiation constraint Energy efficiency (RF efficiency)
 | CEPC | CDR | 0.046 - 0.24 (0.37) | 32~ 5 | 150 – 270 | 5 [B$] |  | 20 – (40) (0.65) | High-Q SRF cavity at < GHz, LG Nb-bulk/Thin-film Synchrotron Radiation constraint High-precision Low-field magnet
LC ee | ILC | TDR update | 0.25 ( -1) | 1.35 (– 4.9) | 129 (– 300) | 4.8- 5.3 (for 0.25 TeV) [BILCU] |  | 31.5 – (45) (1.3) | High-G and high-Q SRF cavity at GHz, Nb-bulk Higher-G for future upgrade Nano-beam stability, e+ source, beam dump
 | CLIC | CDR | 0.38 (- 3) | 1.5 (- 6) | 160 (- 580) | 5.9 (for 0.38 TeV) [BCHF] |  | 72 – 100 (12) | Large-scale production of Acc. Structure Two-beam acceleration in a prototype scale Precise alignment and stabilization. timing
*Cost estimates are commonly for ”Value” (material) only.
Major Technical Challenges:
Hadron Colliders:
High-field magnet
Energy management
Lepton Colliders:
SRF cavity: High-Q and -G (to prepare for upgrade)
NRF acc. Struct.: large scale, alignment, tolerance, timing
Energy management

## Slide 32: Advanced technologies
Muon collider
Plasma acceleration
Credit: Frank Tsung, UCLA

## Slide 33: Proton-driven Muon Collider Concept
Short, intense proton bunches to produce hadronic showers
Pions decay into muons that can be captured
Muon are captured, bunched and then cooled
Acceleration to collision energy
Collision
Muon-based technology represents a unique opportunity for the future of high energy physics research: the multi-TeV energy domain exploration.
Two schemes for m production
Proton (like in the figure)
Positrons, still requiring consolidation

## Slide 34: Answers to the Key Questions (D. Schulte)
Can muon colliders at this moment be considered for the next project?
  Enormous progress in the proton driven scheme and new ideas emerged on positron one
  But at this moment not mature enough for a CDR, need a careful design study
  done with a coordinate international effort
Is it worthwhile to do muon collider R&D?
  Yes, it promises the potential to go to very high energy
  It may be the best option for very high lepton collider energies, beyond 3 TeV
  It has strong synergies with other projects, e.g. magnet and RF development
  Has synergies with other physics experiments
  Should not miss this opportunity?
What needs to be done?
  Muon production and cooling is key => A new test facility is required.
    Seek/exploit synergy with physics exploitation of test facility (e.g. nuSTORM)
  A conceptual design of the collider has to be made
  Many components need R&D, e.g. fast ramping magnets, background in the detector
  Site-dependent studies to understand if existing infrastructure can be used
    limitations of existing tunnels, e.g. radiation issues
    optimum use of existing accelerators, e.g. as proton source
  R&D in a strongly coordinated global effort

## Slide 35: Proposed tentative timeline
1
3
5
7
9
11
13
15
17
2
4
6
8
10
12
14
16
Design
Construct
Test Facility
Design
Technologies
Baseline design
Exploit
Design optimisation
Project preparation
Design / models
Prototypes / t. f. comp.
Approve
Exploit
Prototypes / pre-series
R&D detectors
Prototypes
CDRs
MDI & detector simulations
Large Proto/Slice test
TDRs
Ready to construct
Ready to commit
to collider
Cost know
Ready to decide on test facility
Cost scale known
Technically limited
MACHINE
DETECTOR
Years?

## Slide 36: Plasma acceleration based colliders
Key achievements in last 15 years in plasma based acceleration using lasers, electron and proton drivers
Focus is now on high brightness beams, tunability, reproducibility, reliability, and high average power
The road to colliders passes through applications that need compact accelerators (Early HEP applications, FELs, Thomson scattering sources, medical applications, injection into next generation storage rings … )
Many key challenges remain as detailed in community developed, consensus based roadmaps (ALEGRO, AWAKE, Eupraxia, US roadmap,…)
Strategic investments are needed:
Personnel – advanced accelerators attract large numbers of students and postdocs
Existing facilities (with upgrades) and a few new ones (High average power, high repetition rate operation studies; fully dedicated to addressing the challenges towards a TDR for a plasma based collider)
High performance computing methods and tools
Drive beams
Lasers: ~40 J/pulse
Electrons: 30 J/bunch
Protons: SPS 19kJ/pulse, LHC 300kJ/bunch
Witness beams
Electrons: 1010 particles @ 1 TeV ~few kJ

## Slide 37: ALEGRO
Mission of the ALEGRO community:
Foster and trigger Advanced Linear Collider related activities for applications of high-energy physics.
Provide a framework to amplify international coordination, broaden the community, involving accelerator labs/institutes
Identify topics requiring intensive R&D and facilities.
Goal:
Long-term design of a e+/e-/gamma collider with up to 30 TeV: the Advanced Linear International Collider (ALIC)
Construction of dedicated Advanced and Novel Accelerators (ANA) facilities are needed over the next 5 to 10 years in order to reliably deliver high-quality, multi-GeV electron beams from a small number of stages.
  Today: Existing facilities explore different advanced and novel accelerator concepts and are proof-of-principle experiments.
Advanced LinEar collider study GROup, ALEGRO: formed at initiative of the ICFA ANA panel in 2017.
EuPRAXIA
Horizon 2020 EU design study funded in 2015.
Deliverable: Conceptual Design Report by Oct 2019
The EuPRAXIA Strategy for Accelerator Innovation:
The accelerator and application demonstration facility EuPRAXIA is the required intermediate step between proof of principle and production facility.
Current initiatives of coordinated programs:
EuPRAXIA, ALEGRO, AWAKE.

## Slide 38
ALEGRO delivered a document detailing the international roadmap and strategy of Advanced Novel Accelerators (ANAs).

## Slide 39: Status of Today and Goals for Collider Application
 | Current | Goal
Charge (nC) | 0.1 | 1
Energy (GeV) | 9 | 10
Energy spread (%) | 2 | 0.1
Emittance (um) | >50-100 (PWFA), 0.1 (LFWA) | <10-1
Staging | single, two | multiple
Efficiency (%) | 20 | 40
Rep Rate (Hz) | 1-10 | 103-4
Acc. Distance (m)/stage | 1 | 1-5
Positron acceleration | acceleration | emittance preservation
Proton drivers | SSM, acceleration | Emittance control
Plasma cell (p-driver) | 10 m | 100s m
Simulations | days | Improvements by 107
Achieved Individually
and
NOT
simultaneously

## Slide 40: Energy Efficiency
Energy efficiency is not an option, it is a must!
Energy efficiency and energy management must be addressed.
Investing in dedicated R&D to improve energy efficiency pays off in terms of savings and societal return through development of technologies which serve the society at large.
District heating, energy storage, magnet design, RF power generation, cryogenics, SRF cavity technology, beam energy recovery are areas where energy efficiency can significantly be improved.
Higher-temperature high-gradient Nb/Cu accelerating cavities and highly-efficient RF power sources developed in the frame of the FCC-ee R&D programme will find numerous other applications; could improve the sustainability and performance for accelerators of nearly all types and sizes around the world.
The resource-saving strategy includes studies to avoid water cooling wherever possible and developing schemes to supply waste heat to nearby consumers. A pilot program at LHC is on-going.
The detailed technical design of the FCChh will also investigate energy recovery opportunities within the accelerator infrastructure, for example, by working with industrial partners on either storing heat for later use or its conversion into mechanical or electrical energy.

## Slide 41: Example: He consumption @FCC-hh
Nelium (Neon+ Helium) for cooling down to 40 + He for going to 1.9K
The most power-hungry element @ FCC-hh is the cryogenic refrigeration system needed to cool the 16 T superconducting magnets down to 1.9 K.
With respect to an LHC-class system, which would for an FCC-hh collider consume 290 MW of electrical power, the nelium technology and temperature choices lead to a reduction by 50 MW or 17% in the baseline configuration. Slowly ramping up the field of the magnets and with constant power substantially reduces the power demand, for all main dipoles from 270 MW for a constant-voltage ramp of 20 minutes to 100 MW for a constant-power ramp of 30 minutes.
The external peak power demand during the ramp phase can be reduced further by recovering the energy stored in the superconducting magnets at the end of a cycle (50 MWh for the main dipoles), to buffer it locally, and to reuse it during the subsequent ramp-up. Losses in electricity transmission will be reduced by cooperating with industry to bring medium voltage DC distribution systems to market grade so that they can power the accelerator subsystems.
R&D on High efficiency klystrons to go from 65% to 80% in power conversion efficiency (with LC communities)
SC thin-film coating technology for operating high-gradient RF cavities at higher temperature, lowering the electricity need.
Yearly energy consumption forecast of 4 TWh, compared to 1.4 TWh expected for the HL-LHC.

## Slide 42: Figure of merit for proposed lepton colliders
Chart: 
| 0.25 | 0.5 | 1
ILC | 1.0465 | 1.118 | 1.7193
CLIC | 0.89286 | 1.0165 | 1.0017
FCC-ee | 177.6062 | 20.2166 | 6.0284 | 0.91176
MAP-MC | 0.004 | 0.5787 | 1.913 | 4.4444
Disclaimers:
This is not the only possible figure of merit
The presented numbers have different levels of confidence/optimism; they are still subject to optimisations
(2 IPs)
FCC-ee
ILC
CLIC
MC
Numbers for baseline proposals
electricity cost ~200 euro per Higgs boson (F. Zimmerman)

## Slide 43: Proposed HEP Projects and Grid Power Consumption
 | ECM [TeV] | L / IP [1034cm-2s-1] | PGrid [MW] | power driving effects
FCC-ee (Z) | 0.091 | 230 | 259 | SR Power: 50MW/beam
FCC-ee (t) | 0.365 | 1.5 | 359 | SR power: 50MW/beam
FCC-hh | 100 | 30 | 580 | SR power: 2.4MW/beam @ 50K, cryogenics
ILC | 1 | 4.9 | 300 | beam power: 13.6 MW/beam, cryogenics
CLIC | 3 | 5.9 | 582 | beam power: 14 MW/beam
muon coll. | 6 | 12 | 270 | mu decay, 1.6MW/drive beam, cycling magnets, but scaling advantages, least developed
 need more R&D towards efficient concepts & technology, and energy management
Notes: Here is a number of collider proposals. They are all optimized for fantastic luminosity, but they consume enormous amounts of power as well. Unfortunately all have good physics reasons why the consumption is so high to achieve the required luminosity.
Mitigating the large power consumption is a topic that is in my interest for a long time, and this be quite important for a public acceptance of such a project.

## Slide 44: Comparisons
Project | Type | Energy [TeV] | Int. Lumi. [a-1] | Oper. Time [y] | Power [MW] | Cost
ILC | ee | 0.25 | 2 | 11 | 129 (upgr. 150-200) | 4.8-5.3 GILCU + upgrade
 |  | 0.5 | 4 | 10 | 163 (204) | 7.98 GILCU
 |  | 1.0 |  |  | 300 | ?
CLIC | ee | 0.38 | 1 | 8 | 168 | 5.9 GCHF
 |  | 1.5 | 2.5 | 7 | (370) | +5.1 GCHF
 |  | 3 | 5 | 8 | (590) | +7.3 GCHF
CEPC | ee | 0.091+0.16 | 16+2.6 |  | 149 | 5 G$
 |  | 0.24 | 5.6 | 7 | 266 | 
FCC-ee | ee | 0.091+0.16 | 15+10 | 4+1 | 259 | 10.5 GCHF
 |  | 0.24 | 5 | 3 | 282 | 
 |  | 0.365 (+0.35) | 1.5 (+0.2) | 4 (+1) | 340 | +1.1 GCHF
LHeC | ep | 60 / 7000 | 1 | 12 | (+100) | 1.75 GCHF
FCC-hh | pp | 100 | 30 | 25 | 580 (550) | 17 GCHF (+7 GCHF)
FCC-NbTi | pp | 37.5 | 10 | 20 | 240 | 14 GCHF (including tunnel)
HE-LHC | pp | 27 | 20 | 20 |  | 7.2 GCHF
new
‘Traditional-technologies’ colliders

## Slide 45: Personal (A. Yamamoto) View on Relative Timelines
Timeline | ~ 5 | ~ 10 | ~ 10 |  |  | ~ 15 |  | ~ 20 |  | ~ 25 | ~ 30 | ~ 35 | 
Lepton Colliders |  |  |  |  |  |  |  |  |  |  |  |  | 
SRF-LC/CC | Proto/pre-series | Construction | Construction |  |  |  |  | Operation |  |  | Upgrade |  | 
NRF—LC | Proto/pre-series | Construction | Construction | Construction |  |  |  | Operation |  |  | Upgrade |  | 
Hadron Collider (CC) |  |  |  |  |  |  |  |  |  |  |  |  | 
8~(11)T NbTi /(Nb3Sn) | Proto/pre-series |  | Construction |  |  |  |  | Physics Experiment | Operation |  |  | Upgrade | Upgrade
12~14T Nb3Sn | Short-model R&D |  |  |  | Proto/Pre-series |  |  |  | Construction | Construction to Physics Experiment | Operation |  | 
14~16T Nb3Sn | Short-model R&D |  |  |  |  |  | Prototype/Pre-series |  |  |  | Construction | Construction | 
Note: LHC experience: NbTi (10 T) R&D started in 1980’s --> (8.3 T) Production started in late 1990’s, in ~ 15 years
14T Nb3Sn magnets ready for a collider following
HL-LHC ?

## Slide 46
Ursula Bassler @ Granada

## Slide 47: Special thanks to
Akira Yamamoto, Frank Zimmerman, Philip Burrows, Vladimir Shiltsev, Mike Seidel, Erk Jensen, Lucio Rossi, Daniel Schulte, Wim Leemans, Edda Gschwendtner, Mike Lamont, Michael Benedikt, Steinar Stapnes, Ursula Bassler, Fredry Bordry, Max Klein, plus many others
and
Lenny Rivkin

## Slide 48
Back up slides

## Slide 50
Ours is a very dynamic field!
(Luminosity upgrades for ILC, CLIC)
e+e- colliders
Project | Start construction | Start Physics (Higgs)
CEPC | 2022 | 2030
ILC | 2024 | 2033
CLIC | 2026 | 2035
FCC-ee | 2029 | 2039 (2044)
LHeC | 2023 | 2031
Proposed dates from projects
Would expect that technically required time to start construction is O(5-10 years) for prototyping etc.

## Slide 51
FCC integrated project technical schedule
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
34
35
36
37
38
39
40
41
42
43
15 years operation
Project preparation &
administrative processes
Funding & governance strategy
Geological investigations, infrastructure detailed design and tendering preparation
Tunnel, site and technical infrastructure construction
FCC-ee accelerator R&D and technical design
FCC-ee detector construction, installation, commissioning
FCC-ee detector technical design,
collaborations
Permis-sions
Detector R&D and
concept development
FCC-ee accelerator construction, installation, commissioning
FCC-hh detector construction, installation, commissioning
FCC-hh detector R&D, technical design
Update Permission,
Funding
FCC-hh accelerator construction, installation, commissioning
FCC-ee dismantling, CE & infrastructure adaptations FCC-hh
~ 25 years operation
FCC-hh accelerator R&D and technical design
SC wire and 16 T magnet R&D, model magnets, prototypes, preseries
16 T dipole magnet series production
Superconducting wire and high-field magnet R&D
70
LS4
LHC run 3
LS 3
LHC run 4
LS5
LHC run 5
LHC run 6
FCC integrated project is fully aligned with HL-LHC exploitation and provides for seamless continuation of HEP in Europe with highest performance EW factory followed by highest energy hadron collider.

## Slide 52
ESG request for parameters of a
lower-energy hadron collider
parameter | FCC-hh |  | FCC-hh-6T | HE-LHC | HL-LHC | LHC
collision energy cms [TeV] | 100 |  | 37.5 | 27 | 14 | 14
dipole field [T] | 16 |  | 6 | 16 | 8.33 | 8.33
beam current [A] | 0.5 |  | 0.6 | 1.1 | 1.1 | 0.58
synchr. rad. power/ring [kW] | 2400 |  | 57 | 101 | 7.3 | 3.6
peak luminosity [1034 cm-2s-1] | 5 | 30 | 10 (lev.) | 16 | 5 (lev.) | 1
events/bunch crossing | 170 | 1000 | ~300 | 460 | 132 | 27
stored energy/beam [GJ] | 8.4 |  | 3.75 | 1.4 | 0.7 | 0.36
NbTi technology from LHC, magnet with single-layer coil providing 6 T at 1.9 K:
  Corresponding beam energy 18.75 TeV or 37.5 TeV c.m.
  Significant reduction of synchrotron radiation wrt FCC-hh (factor 50) and corresponding cryogenic system requirements.
Luminosity goal 10 ab-1 over 20 years or 0.5 ab-1 annual luminosity:
  Beam current 0.6 A or 20% higher than for FCC-hh, 1.2E11 ppb (FCC-hh: 1.0 ppb).
  Stored beam energy 3.75 GJ vs 8.4 GJ for FCC-hh.
Analysis of physics potential, technology requirements and cost ongoing.
https://indico.cern.ch/event/727555/contributions/3447469/attachments/1867359/3071163/190624_Overview_of_the_FCC_Study_ap.pdf

## Slide 53: Proposed Schedules and Evolution