## Slide 1: MEDical Isotopes Production Facility at ESS (ESS-MEDIPF)
Yong Joong LEE (ESS)
September 19, 2019
PRISMAS-MAP (mediso-sepa) H2020 General meeting

## Slide 2: Mission Statement: ESS-MEDIPF
Exploration of a potential to position ESS as a key research infrastructure providing a high flux proton and neutron sources for medical radioisotopes production, while not compromising the performance and availability of the facility’s main mission.

## Slide 3: ESS Target Satation
Proton beam (2 GeV/5 MW)
Proton Beam Instrumentation
Proton Beam Window (PBW)
Moderator Reflector
Target Wheel
Target Wheel Drive Unit
Beam Extraction Unit

## Slide 4: Radiation Environment
Thermal Neutrons:
  Max. available flux: ∼5∙1014 n/cm2/s
Fast Neutrons:
  Max. available flux: ∼5∙1014 n/cm2/s
Protons: 2 GeV
  Available intensity: ∼1 𝞵A/cm2

## Slide 5: Potential Target Locations
Potential Location | Description | Potential Location | Description
A | In the vicinity of cold/thermal moderator | D | In the vicinity of the spallation target
B | In the water pre-moderator | E | Proton beam upstream
C | In the beryllium reflector | F | Used beam intercepting devices
E
D
C
B
A
A

## Slide 6: Potential Access Point #1: Unused Beam Port E1
Isotopes production target uploading and unloading via unused beam port E1
Space for a hot cell for the radioactive target handling in the Experimental Hall
Requires design modification of Neutron Beam Port Plug

## Slide 7: Potential Access Point #2: Moderator Twister Shaft
Isotopes production target uploading and unloading via Moderator-Reflector Plug
Space for a hot cell for the radioactive target handling on the High Bay
Requires design modification of Moderator-Reflector Plug
Picture courtesy by FZJ

## Slide 8: Benchmark against research reactors: ILL/JHR
Potential Target Location | Source Partcles | normalised flux to ILL/JHR Max | Access Route | brightness reduction
A | Neutron: E < 1 eV |  0.1 | Beam Port E1 | < 0.5%
 | Neutron: E > 1 MeV |  0.1 |  | 
 | Neutron: E > 10 MeV |  10 |  | 
B | Neutron: E < 1 eV |  0.5 | Twister | < 2.0%
 | Neutron: E > 1 MeV |  0.5 |  | 
 | Neutron: E > 10 MeV |  10 |  | 
C | Neutron: E < 1 eV |  0.5 | Twister | < 0.5%
 | Neutron: E > 1 MeV |  0.1 |  | 
 | Neutron: E > 10 MeV |  10 |  | 
D | Neutron: E < 1 eV |  0.1 | Twister | < 2.0%
 | Neutron: E > 1 MeV |  1.0 |  | 
 | Neutron: E > 10 MeV |  10 |  | 
E | Proton: E  2 GeV |  100 | Twister | < 0.1%
 | Neutron: E > 1 MeV |  0.5 |  | 
 | Neutron: E > 10 MeV |  10 |  | 
F | Proton: E  2 GeV |  100 | Active Cells | < 0.1%
 | Neutron: E > 1 MeV |  0.1 |  | 
 | Neutron: E > 10 MeV |  10 |  | 

## Slide 9: Benchmark against high power proton machines
Target Location | Source Particles | normalised flux to ISOLDE-MEDICIS | normalised flux to PSI-ERAWAST | brightness reduction
E | Proton: E < 2 GeV |  1 | -- | < 0.1%
F | Proton: E < 2 GeV | -- |  1 | < 0.1%

## Slide 10: Case Study
Representative radiation intensity
  Thermal neutron flux: 1014 n/cm2/s
  Fast neutron flux (10 MeV < E < 20 MeV): 1013 n/cm2/s
  Proton intensity: 1 𝞵A/cm2
Reference isotopes yields after 1 week beamtime, for benchmarking:
Product | Target | Neutron Energy | Reaction Chain | E.o.B. yield [GBq/g]
Mo-99 | Mo-100 | 10 MeV < E < 20 MeV | Mo100(n,2n)Mo99 | 100
I-131 | Te-130 | E < 0.625 eV | Te130(n,g)Te131(β-)I131 | 100
Lu-177 | Yb-176 | E < 0.625 eV | Yb176(n,g)Yb177(β-)Lu177 | 1000
Ac-225 | Ra-226 | 5 MeV < E < 15 MeV | Ra226(n,2n)Ra225(β-)Ac225 | 10
Ac-225 | Th-232 | Proton: 2 GeV | Th232(p,x)Ra225(β-)Ac225 | 10

## Slide 11: Way Forward
Identification of isotopes of high demands and target materials that ESS proton and neutron spectra at chosen target locations could be efficiently utilized
  ESS-MEDIPF intends to provide isotopes of high demands for research and clinical applications, which are otherwise not available in enough quantity
  Within the PRISMAS-MAP collaboration frame, the functional scope of the ESS-MEDIPF will be worked out in a way that it will become an important asset to the existing European research infrastructure
Identification of extraction methods for identified isotopes
  The neutrons have a large energy spectra from thermal to GeV, inducing a large radioisotopes inventories
  Renovative methods for extracting targeted isotopes should be studied within PRISMA MAPS collaboration frame.
Identification of target locations, conceptual design of the target station and handling concepts

## Slide 12
Thank you for your attention