## Slide 1: Bus Tape FDR
Concern #1: still need to identify producer as Alatflex have had problems.
  Carl investigating two new US companies and Altaflex + outsourcing.
  Producing prototypes with CS Electronics (China)
  Producing prototypes at CERN in Rui’s (new) workshop.
Concern #2: Distortions along short direction of tape
  See next slides.

## Slide 2: Tape Dimensions
Lock points added wrt MFFs.
  Modules mounted wrt lock points.
In x-direction:
  If tape too short or too long, would need to use very large angle for bond wires
In y-direction
  If distortion too large silicon sensor will be too close to LV pads on either the data or the power side of the stave.
MFF1
MFF2
y
x
1.5 mm

## Slide 3: Y-distortion
Use local fiducials
Line from MFF1 to MFF2
Calculate distance di from LFIDi to line.
Plot di measured – nominal vs x for two sides of tape
MFF1
MFF2
LFIDi
di
High y
Low y
y
x
Cut |DY| < 300 mm

## Slide 4: New Co-cure jig (Rui)
Add row of holes & slots in tape in sacrificial area of tape.
Use invar jig with dowel pins to ensure tape is held straight during co-cure.
Dowel pins become glued in during co-cure but can be removed with tapping.
Edge of tape after sacrificial area cut
4 mm diameter hole in tape
HV lines near edge of tape