Simulation of electron transport within electron cooler and hollow e. lenses using Warp – Status report
Technical Student:	Ondrej Sedlacek
Supervisor:	Adriana Rossi

---
I feel like I do not like the footing color… Play with the footing a bit more...
Outline
Introduction
  - My project & goal
  - Warp and its features
Current state of work
Next steps
Summary

---
Project
Simulation of an electron beam transport with Warp
  Hollow electron lenses	Electron cooler
Change to AD cooler – get pic

---
Project
Simulation of an electron beam transport with Warp
  Hollow electron lenses	Electron cooler
Change to AD cooler – get pic
L. Joergensen, G.Tranquille, Design
Par. Of the new AD E. Cooler, CERN-AD Electron Cooler Consolidation Review
D.Perini, C.Zanoni, CERN-ACC-NOTE-2017-0004

---
Goal of the project – expand...
D.Perini, et. al.,
CERN-IPAC2019
doi:10.18429/JACoW-
IPAC2019-MOPTS099
Simulate and compare
Probe a complex part
G.Tranquille et al., AD e. cooler, CERN – AD Electron Cooler Consolidation Review

---
Goal of the project – expand...
D.Perini, et. al.,
CERN-IPAC2019
doi:10.18429/JACoW-
IPAC2019-MOPTS099
Simulate and compare
  - Solenoid transport
  - Bending of the beam
  - Electron gun
Probe a complex part
G.Tranquille et al., AD e. cooler, CERN – AD Electron Cooler Consolidation Review

---
Goal of the project – expand...
D.Perini, et. al.,
CERN-IPAC2019
doi:10.18429/JACoW-
IPAC2019-MOPTS099
Simulate and compare
  - Solenoid transport
  - Bending of the beam
  - Electron gun
Probe a complex part
Bend
G.Tranquille
et al., ELENA,
CERN, IPAC2016
G.Tranquille et al., AD e. cooler, CERN – AD Electron Cooler Consolidation Review

---
Examples of currently used simulations

---
Warp
Designed for
  - Plasma & high current density particle beams
  - Space-charge effects in bent accelerator lattices
Main properties
  - Particle-in-cell (PIC)
  - Open-source
  - Python code (Fortran partly inside)
    - Possible MAD-style lattice input
  - Intensely developed & used
  - Supports parallel computation
Beam simulation tool
 D. P. Grote et al, IEEE 2014, DOI: 10.1109/TPS.2014.2308546

---
Warp
Designed for
  - Plasma & high current density particle beams
  - Space-charge effects in bent accelerator lattices
Main properties
  - Particle-in-cell (PIC)
  - Open-source
  - Python code (Fortran partly inside)
    - Possible MAD-style lattice input
  - Intensely developed & used
  - Supports parallel computation
Why Warp?
Beam simulation tool
 D. P. Grote et al, IEEE 2014, DOI: 10.1109/TPS.2014.2308546

---
Low res. …
Which might be important if the edge field is important
Warp features./[-]
Cartesian and Warped-Cartesian coordinates
Adaptive mesh refinement
Cylindrical coordinates – longitudinal coordinate replaced by angle
Subgrid (Submesh) conductor edge resolution
  - Important for the boundary position dependent field
 D. P. Grote et al, IEEE 2014, DOI: 10.1109/TPS.2014.2308546

---
Warp - example of use cases
Evolution of space-charge dominated beam
Multi-charge state beams
 D. P. Grote et al, IEEE 2014, DOI: 10.1109/TPS.2014.2308546
NDCX-II - LBNL
Lawrence Berkley National Laboratory
Plasma acceleration
 D. P. Grote et al, HB2012, THO3B04
Berkeley Lab Laser Accelerator - BELLA
Project-X - Fermilab
Injection
Transport
-Dynamics
 D. P. Grote et al, Phys. Plasmas 2011, DOI: 10.1063/1.3663841
BELLA - Berkley

---
Main parameters
1. AD Electron Cooler / HEL:
2. Current
3. Accelerating field
4. Magnetic fields at gun/bend/main
5. Main vacuum chamber radius
6. Length
7. Langmuir radius
8. Cyclotron and plasma freq.

---
Current state of work

---
Still in the learning process of the warp and the physics attached, but I’m getting a grip on it...
Current state work status
- Working simulation of beam injection (constant current) and evolution within a straight section with two solenoid
- Injecting beam into magnetic field – checked the magnetization
- Transport from one solenoid mag. Field into another – radius follows the formula
- Comfortable with the syntax:
  - Injecting with arbitrary (user defined) particle distribution
  - Creating magnetic elements (mainly solenoid or arbitrary gridded field)
  - Creating conductors (mainly pipe)
- Have build saving and analyzing infrastructure for the beam probing/diagnostics (maybe obvious and not needed to mention)?
- Precision study?

---
Timeline
Bending
Electron gun
Solenoid transport

---
Timeline
Bending
Electron gun
Solenoid transport
Solenoid transport
Transport in single solenoid

---
Current state of work – Transport in Solenoid
Solenoid:
1T
Particle (macro)
density
Initial parameters:
Beam created in space
Big help from:
Danila Nikiforov

---
Current state of work – Transport in Solenoid
Solenoid:
1T
Particle (macro)
density
Oscillations:
Due to Bush theorem violation
Initial parameters:
Beam created in space
Big help from:
Danila Nikiforov

---
Current state of work – Transport in Solenoid
Solenoid:
1T
Particle (macro)
density
Magnetized beam:
Straight profile
Initial parameters:
Injection: Ideal constant current
Big help from:
Danila Nikiforov

---
Timeline
Bending
Electron gun
Solenoid transport
Add a pipe
Solenoid transport
Transport in single solenoid

---
Timeline
Bending
Electron gun
Solenoid transport
Add a pipe
Solenoid transport
Transport in single solenoid
Add second solenoid

---
Current state of work
Solenoids:
 1T	&	4T
Pipe: grounded conductor
Particle (macro)
density
Compression: by a factor of 2
Initial parameters:
Injection: Ideal constant current
Big help from:
Danila Nikiforov

---
Timeline
Bending
Electron gun
Solenoid transport
Add a pipe
Ideal Sol. transport
Transport in single solenoid
Add second solenoid

---
Next steps
Bending
Electron gun
Solenoid transport
Add a pipe
Ideal Sol. transport
Transport in single solenoid
Add second solenoid
Realistic parameters of AD cooler

---
Summary
- Simulate the Electron Cooler and Hollow electron lenses with Warp
  - Compare the results with other simulations and measurements if possible
- Probe and focus on the bending
- Constructed simulation of Double solenoid transport with ideal parameters
  - Inject arbitrary distribution
  - Constructed a grounded pipe – Conductor
  - Added Solenoids
  - Tested the simulation against compression formula
- Next Steps will include: Include real parameters of AD cooler, construct an Electron gun, construct & prob the Bending.
  - After finishing the AD cooler move Hollow electron lenses

---
Nonuniform forces in the bend
Asymmetric forces due to the B field gradient
Centrifugal forces
Asymmetric electric field due to
the decentering of the beam inside
the grounded vacuum chamber
Displacement of beam in the pipe
   - grounded pipe → external e-field
   - beam tries to compensate → beam potential becomes asymmetric
A. Barnyakov, D. Nikiforov, M. Arsentyava, A. Levichev, 8th HL-LHC Collaboration Meeting
a
2.8 a
R

---
Kinetic energy with vs without pipe

---
Hollow electron lenses - back
- Beam scrapping of protons
  - Part of the colimator system for HL-LHC
Beam core experiences no field
Beam halo experiences nonlinear transverse kicks
Shiltsev, BEAM06,CERN-2007-002 Shiltsev et al., EPAC08