## Slide 1: Status of R&D on Linear Collider
4th meeting of CERN-KEK committee
March 29, KEK
T. Higo (Accelerator, KEK)

## Slide 2: Contents
CERN situation
Basic idea behind KEK X-band R&D
History of X-band R&D
Production of test structures
Test facilities
High gradient test results
Expansion of test facility
Basic studies related to breakdown
Expansion of our collaboration

## Slide 3: CERN situation
Multi-TeV machine after LHC
Feasibility study is needed to judge
Key judgment of energy around 2012
Optimization of parameters reached 12GHz in late 2006, presented at APAC in India
Tight collaboration for normal-conducting high-gradient approach among CERN, SLAC and KEK

## Slide 4: Present target area of KEK for collaboration on CLIC
Key technologies for CLIC accelerator
  High gradient acceleration
    Present focus in collaboration
    Most benefit to both sides
  RF generation from drive beam
  Low emittance
  ……..

## Slide 5: History of X-band structure developments at KEK
Early 1990 by KEK
  Established fabrication technology1.3m DS
Late 1990 with SLAC
  Realized discharge problem
By 2004 ITRP with SLAC
  Proved 50MV/m in 60cm HDDS with HOM suppression
2007 and later among CERN/SLAC/KEK
  CLIC oriented R&D at X-band toward twice gradient
  Collaboration among three laboratories

## Slide 6: Reasoning of X-band collaboration
KEK
  High-frequency technology for higher energy as one of the missions of high energy accelerator laboratory
  Study ground for physical mechanism governing and preventing high gradient acceleration, discharge
CERN
  Demand of high power facility at 12GHz to prove high gradient
  There are only two places now to efficiently run, SLAC and KEK, at very close frequency, 11.4GHz
  Expand the collaboration to support the technology

## Slide 7: Formal history of collaboration
  2006: Dec. at APAC in India, X-band choice
2007: Started structure collaboration meeting
  Jun. 1st Collab. mtng at CERN
2008: Addendum in CERN/KEK MoU, ICA-JP-0103
  May 2nd collab. Mtng at KEK
  Addendum 2 in MoU, ICA-JP-0103
    Collaboration of High Gradient Accelerator Technology Centered at Fabrication and Tests of X-band Accelerating Structures
  Supported accelerating structure fabrication and test
  Dec. 3rd Collab. mtng at UK
2009: Pursue under collaboration research contract
  Established collaboration research contract to support KEK activities
2010: Continue and expand collaboration
  Mar. Collab. mtng in China
  May 4th Collab. mtng at CERN

## Slide 8: Actual history of collaboration
2007: Started structure collaboration meeting in June
  Structure fabrication started discussion
  Moved test facility to the present area
2008: Addendum in CERN/KEK MoU, ICA-JP-0103 in Aug.
  Structure fabrication (QuadX1, T18X2, TD18X2)
  Establishment of high power facility, Nextef
2009: Pursue under collaboration research contract
  Structure fabrication (C10X2, CD10X2, T24X2, TD24X2)
  Structure test (T18X1, QuadX1, TD18X1)
  Started preparation of extension of Nextef by pulse compression
2010: Continue and expand collaboration
  Structure fabrication (under discussion)
  Structure test (cont. TD18, followed by T24, TD24, ……)
  Establishment of high power facility for basic studies
Red: main financial support from CERN

## Slide 9: Preparation of accelerator structures based on GLC/NLC technologies
Technology established for GLC/NLC
  KEK precision machining followed by SLAC assembly
  This is the best starting point for higher gradient.
  Extensive study is ongoing among CERN, SLAC and KEK
Nominal test flow
  Precision machining
  Chemical polish
  Diffusion bonding and brazing
  Baking in vacuum at 650C
  High gradient test at KEK and SLAC

## Slide 10: Fabrication of damped structures
KEK fabricated all parts.
SLAC made assembly.

## Slide 11
Vacuum Baking of T18_vg2.4_DISC
650° C
10 days
at SLAC
From Sami, Mar. 1

## Slide 12: TD18 first pair #2(KEK) & #3(SLAC)
#3 being tested at SLAC NLCTA
#2 being tested at KEK
Nextef
Design = CLIC-C

## Slide 13: Sent from SLAC and installed at Nextef

## Slide 14: Requirement to high gradient test
Evaluate at more than one laboratory
  Independent evaluations
  Equivalent to “S0” idea for ILC
  Aiming at obtaining statistical info and reproducible technology with scientifically proven mechanism
  Start at SLAC and KEK then include CERN test stand
Requirement for facility
  Long-term operation with 100MW or more
Actual facilities
  SLAC NLCTA with pulse compression
  KEK Nextef with two klystrons
  CERN 12GHz test stand (in this year)

## Slide 15: Test facilities of KEK
KT-1
Nextef
Now located at the J-Arc of the KEKB Injector

## Slide 16: KEK: Nextef Configuration
KT-1
X-band
Nextef
X-band
A

## Slide 17: Nextef operation since 2007

## Slide 18: Nextef inside shield room

## Slide 19: High gradient test of three CLIC-C prototype structures
Disk-based un-damped
  T18_Disk Oct. 2008~June 2009
  4000hr, 9 months
Quad-based heavily damped
  TD18_Quad_#5 Sep. 2009~Nov. 2009
  1000hr, 3 months
Disk-based heavily damped
  TD18_Disk_#2 Dec. 2009~
  1200hr, 4 month+

## Slide 20: Proof of 100MV/m with a pair of un-damped 18cell prototype structures
Roughly the same breakdown rates were observed for a pair of structures.
Will pursue the same comparison again for the second pair.
C. Adolphsen, US-HG@ANL, 2009
#2 test at KEK
#1 test at SLAC

## Slide 21: Quad fabrication and test
With 50 micron rounding
Fine assembly
Made in Japan
High gradient test in chamber
Must be cheap mass production but high gradient is not yet proved.

## Slide 22: Gradient limited at 50~60MV/m
All with 50nsec
Difficult to reach 100MV/m!!

## Slide 23: Optical inspection after test
No.18 Q2-2 to match Q1-1
No clear understanding of poor performance!
We will send it to CERN for SEM inspection.
We continue the study of this idea with CERN.

## Slide 24: TD18_Disk_#2
Aim: Prove heavily damped structure
  Electric gradient: possibility to realize 100MV/m
Design geometry
  Heavy damping slots with wide opening
  Big increase of gradient toward downstream
  Big pulse heating temperature rise at the damping port opening
  No longitudinal cut but disk-based as T18 structures
Fabrication in practice
  Milling surface in many places
  Fabrication flow the same as T18

## Slide 25: Slow processing on TD18 at KEK

## Slide 26: Fast processing but high BDR on TD18 at SLAC
But higher breakdown rate than T18 (un-damped).
Should continue to study the mechanism.
Should study TD24 with lower magnetic field.
Pulse width 230ns
Green line for TD18
Others for T18
Faya wang
100311

## Slide 27: Nextef for prototype structure tests KT1 for basic studies
7 10 1 4 7 10 1 4 7 10 1 4 7 10 1 4 7 10
2008 2009 2010 2011 2012
T18_Disk_#2
TD18_Quad_#5
TD18_Disk_#2
T18_Disk_Disk #3
T24_Disk_#3
TD24_Disk_#
Narrow waveguide test
High power components test
Narrow waveguide test
Basic studies at shield-B
RF delivery from KT1 to shield-B
KT1
Nextef
Pulse compression

## Slide 28: Nextef expansion plan
KT-1
X-band
Nextef
X-band
A
B
Pulse compressor
Nextef  PC  A
KT-1  B

## Slide 29: Mode Launcher for basic studies
From Sami, Mar. 1
Reusable coupler for basic studies made in 2009 by SLAC for KEK under US-Japan cooperation program.
Basic studies are to be made at shield-B.

## Slide 30: X-band collaboration
KEK
Structure fabrication
Infrastructure & test @ Nextef
CERN financially supports
Structure fabrication
High power test
System expansion
SLAC conducts
Structure fabrication
High power test
Basic research
US-Japan
CERN/KEK collaboration
CLIC
US-HG
IHEP: Components and acc str.
Tsinghua: Choke-mode design
Testing at KEK, SLAC, CERN(2011~),
or in China
Asian collaboration
KEK budget
16M\
US-Japan
6.5/2M\
CERN/KEK collaboration
31M\
Budget in JFY2009

## Slide 31: Conclusion
Collaboration between CERN and KEK is very critical for the feasibility proof of CLIC 100MV/m
Nextef is strengthening its high power production by introducing pulse compressor to stably run high gradient test for CLIC prototypes
New test area is being established to conduct basic studies to obtain a firm scientific understanding needed for CLIC
Collaboration is being expanded into an Asian laboratories with KEK as a foot stone
Financial support from CERN is very critical for the present KEK X-band activities