## Slide 1: POLAR2 Mechanics Overview on Integration

## Slide 2
Outline
SiPM & Module design (to set the constraints)
POLAR2 Frame assembly
POLAR2 Envelope & Interface definitions

## Slide 3
SiPM & Module design
Towards POLAR2

## Slide 4
SiPM & Module design
SiPM Module design inherited from POLAR1
Photomultiplier
(64 channels)
51.5mmx51.5mm
SiPM
(64 channels)
49.8mm x 49.8mm
POLAR1
POLAR2
SiPM back side
POLAR1_FEE
POLAR1_FEE
POLAR2 work based on POLAR1 design (Module + Frame)…with optimization

## Slide 5
SiPM & Module design
SiPM Module design (FEE + flex)
SiPM part
FEE with flex
FEE size not yet frozen
DPNC is working on it…
Direct soldering wrt SiPM grid
Flex to be optimized (length, bending)
Decoupling for thermal design purpose
49.8mm
49.8mm

## Slide 6
SiPM & Module design
Aluminium
+ TPG
(glued to the SiPM)
SiPM Module design (Cooling system with Peltier… under study!)
1rst prototype is under testing
Peltier to be evaluated
Peltier device

## Slide 7
SiPM & Module design
Copper bar or
heat pipe
FEE thermal
(PGS or TPG)
SiPM Module design (Spacer)
Key issue: bring the Peltier power to the outside
Force cooling power to the SiPM area (front side)
Minimize the thermal resistance on the back side

## Slide 8
SiPM & Module design
SiPM Module design (End Cap, adaptation to POLAR1)
End cap will apply pressure force to the module
Therm a Gap (TAG) seal as for POLAR1
TAG Thickness will be limited
Only few Kg force needed

## Slide 9
SiPM & Module design
SiPM Module design (into the CFRP socket, 1mm thick, T300 fiber)
FEE
Centring grid
64 bars aligned wrt siPM (thanks to the grid)
Grid opened on 1 side to ease the flex bending

## Slide 10
SiPM & Module design
SiPM Module design (into the CFRP socket, 1mm thick, T300 fiber)
Module estimated weight: 500 gr.
Leading to 50 Kg overall (100 modules)

## Slide 11
SiPM & Module design
SiPM Module design (2 centring grids)

## Slide 12
POLAR2 Frame Assembly

## Slide 13
POLAR2 Frame Assembly
An “100 modules” design fitting inside the envelope (see next!)
Aluminum frame (CNC machined)

## Slide 14
POLAR2 Frame Assembly
An “100 modules” design (main constraint... access door)
360 mm radius
350mm
315mm

## Slide 15
POLAR2 Frame Assembly
An “100 modules” design (key issue: Module design & Frame)
Wall thickness for M3 screws

## Slide 16
POLAR2 Frame Assembly
An “100 modules” design (access to FEE connector and heat exchange…not shown)
Mix of CNC machining and electro erosion by wire
AW7075T7351 aluminium type (stabilized)
1mm Bottom shoulders for module fixation

## Slide 17
POLAR2 Frame Assembly
An “100 modules” design (aluminium Frame, POLAR2 primary structure!)
Main mechanical interface (Electronics, Space frame..)
Rigidity provided by overall thickness (74mm)
Max envelope: 650mmx590mmx74mm
Estimated weight: 14 Kg only
POLAR1 Frame

## Slide 18
POLAR2 Frame Assembly
An “100 modules” design (preliminary FEA)
Conservative approach: 10 G normal to grid
Simply supported on 4 points (at M16 corners)
SiPM modules non structural weight (50Kg)
Top cover not considered here…
Looks quite OK: 60 microns deformation / 50 Mpa VonMisses stresses
Simplified FE model

## Slide 19
POLAR2 Frame Assembly
An “100 modules” design (Top Cover & Back end Electronics)
CFRP top cover
(to be redesigned!)
Back end electronics box
+ services
Design of top cover ongoing
Electronics box is purely conceptual…

## Slide 20
POLAR2 Frame Assembly
An “100 modules” design (Top Cover & Back end Electronics)
Fixation by
M4 side screws
+
4x M16 screws
Bottom patch panel

## Slide 21
POLAR2 Frame Assembly
An “100 modules” design (Top Cover & Back end Electronics… exploded view)
M16 fixations on rigid corners

## Slide 22
POLAR2 Frame Assembly
An “100 modules” design (Top Cover & Back end Electronics)
Fixation to Space Frame by 4x M16 bolts
Space Frame designed to support POLAR2 and grabbing system

## Slide 23
POLAR2 Envelope
&
Interface definitions

## Slide 24
POLAR2 Envelope definition
POLAR2 design (drawing and dimensions)

## Slide 25
POLAR2 Interface definition
POLAR2 design (Interfaces to the Chinese Space Station)
Mechanical I/F to the space frame (and to CSS)
Services I/F to CSS (power, signal..)
I/F with Thermal Heat Exchanger (on CSS?)
What is the expected thermal environment?