## Slide 2: Single Bunch Instabilities at Injection Energy
L. Sabato, G. Iadarola
luca.sabato@cern.ch
Acknowledgements: L. Mether, K. Paraschou
22nd November 2019 E-Cloud Meeting 71

## Slide 3: Outline
Introduction
Convergence Studies
Bunch Length and RF Voltage Amplitude
Effect of SEY and Bunch Charge
Chromaticity and Damper
Octupoles
Conclusions and Future Developments

## Slide 4: Outline
Introduction
Convergence Studies
Bunch Length and RF Voltage Amplitude
Effect of SEY and Bunch Charge
Chromaticity and Damper
Octupoles
Conclusions and Future Developments

## Slide 5
LHC measurements
The possibility of lowering the RF voltage at injection is being considered to cope with RF power limitations
  An extensive simulation study has been conducted to address the impact on e-cloud driven instabilities
In the simulations the bunch length has been adapted to the RF voltage following the dependence measured at the LHC
  In all simulations the longitudinal distribution is matched to the bucket
Simulated
H. Timko, presentation at LMC meeting, 5 Sep 2018
Introduction

## Slide 6
Electrons in the arc quadrupoles are expected to be the strongest contributor (quadrupolar field concentrates a large electron density at the beam location)
  Instabilities driven by e-cloud in the quadrupoles will be considered in the following
Introduction

## Slide 7
  m and m
  Energy: 450 GeV
  Magnetic Field (Arc Quadrupoles): 12.1 T/m
  Electron density: from build-up simulation
  SEY 1.30 - 1.40
  Bunch Intensity: 1.2e11 - 2.3e11 protons per bunch
  Scan: 𝜎t (0.341 - 0.254 ns) / RF voltage (3 - 8 MV)
Introduction: Simulation Parameters

## Slide 8
Blow-up time: time required for observing an emittance blow-up of 12% (2.5 µm ➔ 2.8 µm)
No EC kick on the vertical plane
The maximum number of turns is fixed: 20,000
Introduction: Instability Study Observables
Blow-up time
2.8

## Slide 9: Outline
Introduction
Convergence Studies
Bunch Length and RF Voltage Amplitude
Effect of SEY and Bunch Charge
Chromaticity and Damper
Octupoles
Conclusions and Future Developments

## Slide 10
The motivation of these convergence studies is to find the lower acceptable values for the numerical parameters:
  number of slices of the bunch
  number of MacroParticles (MPs) / slice
  number of kicks (or segments) for each e- cloud element
  number of electron MPs for each kick
  transverse grids (Multigrid [1])
Bunch length
10
9
8
7
6
5
4
3
2
1
Convergence Studies
MP1
MP2
MP3
MPN
…
[1] E. Belli, “PyPIC: the multigrid solver”, EC Meeting #32 – September 2, 2016

## Slide 11
Strategy
Scan every numerical parameter, using conservative values for the other parameters:
    Slices = 750
    MPs/slice = 5,000
    Segments = 8
    e- MPs = 500,000
    Transverse Grid: T0
Convergence Studies

## Slide 12
Old setting 150 slices is not adequate
500 slices is chosen
Convergence Studies: Slices
Instability detected when transverse emittance increases from 2.5 mm to 2.8 mm
(presence of coherent motion verified)
No instability observed over 20k turns

## Slide 13
To understand why such a large number of slices is required we look at the electron evolution during the individual pinch
Electron density average (|y| < 0.25𝜎y and x = 0) along the bunch
Single passage simulation confirms: 150 slices are not enough
Smaller electron density peak (around 20%) during the pinch ➔ bunch more stable
Convergence Studies: Pinch

## Slide 14
No surprise found
2,500 MPs/slice is chosen
Convergence Studies: MPs/Slice
No instability observed over 20k turns

## Slide 15
Convergence Studies: Kicks
No surprise found
8 kicks is chosen
No instability observed over 20k turns
Kicks

## Slide 16
500,000 e- MPs is chosen
Convergence Studies: e- MPs
No instability observed over 20k turns

## Slide 17
Tinj
T0
Value | Value | Value
0.5 | 0.5 | 0.5
10.5 (15𝜎) | 10.5 (15𝜎) | 10.5 (15𝜎)
0.139 (0.2𝜎) | 0.0697 (0.1𝜎) | 0.0349 (0.05𝜎)
0.4 | 0.4 | 0.4
10 | 10 | 10
40 | 40 | 40
Convergence Studies: Transverse Grid
Parameter | Value
f (magnification factor) | 0.3
Internal grid coverage [mm] | 6.95 (10𝜎)
Internal grid cell size [mm] | 0.139 (0.2𝜎)
External grid cell size [mm] | 0.8
N_nodes_discard | 5
N_min_Dh_main | 10
Beam chamber
Internal grid
External grid

## Slide 18
Convergence Studies: Transverse Grid
T0 is chosen
  Internal grid coverage: 6.95 mm (10𝜎)
  Internal grid cell size: 0.139 mm (0.2𝜎)
  External grid cell size: 0.8 mm
No instability observed over 20k turns
Still running (3)

## Slide 19
Convergence Studies: 16% - 26%
No instability observed over 20k turns
Scans of the length of the quadrupoles (equivalent to have stronger electron cloud kicks) for each numerical parameter
They confirm the previous conclusions

## Slide 20
378 multi-core simulations
Total computational time: ~ 32672 CPUcores*days
It took months using the full CNAF cluster
~127 GB stored
Convergence Studies: Summary

## Slide 21
Numerical Parameter | Chosen Value
Slices/bucket | 500
MPs/Slice | 2,500
Segments | 8
e- MPs | 5e5
Transverse Grid | T0 Internal grid coverage: 6.95 mm (10𝜎) Internal grid cell size: 0.139 mm (0.2𝜎) External grid cell size: 0.8 mm
Convergence Studies: Chosen Parameters

## Slide 22: Outline
Build-up
Convergence Studies
Bunch Length and RF Voltage Amplitude
Effect of SEY and Bunch Charge
Chromaticity and Damper
Octupoles
Conclusions and Future Developments

## Slide 23
Increasing VRF and decreasing the bunch length, the bunch is more stable
   Which is dominant?
Bunch Length and RF Voltage Amplitude
No instability observed over 20k turns for: VRF > 5 MV,
SEY = 1.3
1.2 x 1011 p/bunch

## Slide 24
Increasing VRF, we change
Faster synchrotron tune Qs Bunch length
Stabilising mechanism EC dynamics
Longer bunches  more e-
Shorter bunches  less e-
Bunch Length and RF Voltage Amplitude

## Slide 25
Bunch Length and RF Voltage Amplitude
We can block the build-up, without changing the bunch length, in order to see which effect is dominant
Increasing VRF, we change
Faster synchrotron tune Qs Bunch length
Stabilising mechanism EC dynamics
Longer bunches  more e-
Shorter bunches  less e-

## Slide 26
The slope as a function of the RF remains when fixing the bunch length:  the dominant stabilizing factor is the change of Qs
Fixed bunch length (same electron pinch)
Changing VRF (matched bunch, changing Qs, long. emittance)
Bunch Length and RF Voltage Amplitude
1.2 x 1011 p/bunch, SEY = 1.3

## Slide 27: Outline
Build-up
Convergence Studies
Bunch Length and RF Voltage Amplitude
Effect of SEY and Bunch Charge
Chromaticity and Damper
Octupoles
Conclusions and Future Developments

## Slide 28
Increasing the SEY, the bunch is more unstable
No instability for 2.3e11 ppb in this entire range of parameters
Effect of SEY and Bunch Charge

## Slide 29
Increasing the SEY, the bunch is more unstable
No instability for 2.3e11 ppb in this entire range of parameters
Effect of SEY and Bunch Charge

## Slide 30: Why no Instability at High Intensity?
The electron density average, close to the bunch, during the pinch is significantly smaller for high intensity
Effect of SEY and Bunch Charge
1.2 x 1011 p/b, SEY=1.3
1.2 x 1011 p/b, SEY=1.4
1.2 x 1011 p/b, SEY=1.5
2.3 x 1011 p/b, SEY=1.3
2.3 x 1011 p/b, SEY=1.4
2.3 x 1011 p/b, SEY=1.5

## Slide 31: Outline
Build-up
Convergence Studies
Bunch Length and RF Voltage Amplitude
Effect of SEY and Bunch Charge
Chromaticity and Damper
Octupoles
Conclusions and Future Developments

## Slide 32
Scanned around these points
Chromaticity and Damper

## Slide 33
VRF = 4 MV
SEY = 1.3 – 1.4
Feedback damping time is 10 turns
No instability observed over 20k turns for Q’ > 12.5!
Chromaticity and Damper
For the case of LHC intensity (which an instability could be observed) the effectiveness of different mitigation measures has been investigated:
  The instability is strongly mitigated by increasing the chromaticity settings

## Slide 34
VRF = 4 MV
SEY = 1.3 – 1.4
Feedback damping time is 10 turns
Chromaticity and Damper
No instability observed over 20k turns for Q’ > 12.5!
For the case of LHC intensity (in which an instability could be observed) the effectiveness of different mitigation measures has been investigated:
  The instability is strongly mitigated by increasing the chromaticity settings
  The transverse feedback is mostly ineffective  cannot damp intra-bunch motion

## Slide 35
Pickup D-signal
Example: VRF = 4MV, SEY = 1.4, Q’ = 2.5…?
Feedback ON
z [m]
Chromaticity and Damper
Strong intra-bunch motion  transverse feedback is mostly ineffective

## Slide 36: Outline
Build-up
Convergence Studies
Bunch Length and RF Voltage Amplitude
Effect of SEY and Bunch Charge
Chromaticity and Damper
Octupoles
Conclusions and Future Developments

## Slide 37
Octupoles
Explored starting from this point

## Slide 38
38
VRF = 4 MV
SEY = 1.4
Damper = 10 turns
For the case of LHC intensity the octupole current has also been scanned (between -78 A and 78 A)
   less effective compared to chromaticity
Octupoles
I = 78 A
I = -78 A

## Slide 39: Outline
Build-up
Convergence Studies
Bunch Length and RF Voltage Amplitude
Effect of SEY and Bunch Charge
Chromaticity and Damper
Octupoles
Conclusions and Future Developments

## Slide 40: Conclusions
  Extensive convergence studies at injection are carried out
  Decreasing VRF the bunch is more unstable
    dominant factor is the de-stabilising effect due to the change of the synchrotron tune
  No instability for 2.3e11 ppb in the entire range of parameters
    electron density average is smaller for high intensity
  Damper does not affect significantly the blow-up time (unable to suppress intra-bunch motion)
  Positive chromaticity strongly mitigates the instability
  Octupoles are less effective compared to chromaticity

## Slide 41: Thanks for your attention

## Slide 45: Spares

## Slide 46
Electron dynamics
Proton bunch
oscillations
Head
Tail
The electron motion is fast enough to act as a coupling mechanism between the head and the tail of the bunch (dominated by electrons at the beam location)
  Stronger at injection energy due to lower beam rigidity
Introduction: Motivation

## Slide 47
The motivation of these convergence studies is to find the lower acceptable values for the numerical parameters:
  transverse grids
Introduction: Numerical Parameters

## Slide 48
The motivation of these convergence studies is to find the lower acceptable values for the numerical parameters:
  transverse grids
    Single grid
      PyPICmode = ‘FiniteDifference_ShortleyWeller’
      Dh_sc_ext
Introduction: Numerical Parameters

## Slide 49
[1] E. Belli, “PyPIC: the multigrid solver”, EC Meeting #32 – September 2, 2016
The motivation of these convergence studies is to find the lower acceptable values for the numerical parameters:
  transverse grids
    Multigrid [1]:
Introduction: Numerical Parameters

## Slide 50
The motivation of these convergence studies is to find the lower acceptable values for the numerical parameters:
  transverse grids
    Multigrid:
Courtesy of
E. Belli
Introduction: Numerical Parameters

## Slide 51
The motivation of these convergence studies is to find the lower acceptable values for the numerical parameters:
  transverse grids
    Multigrid:
      PyPICmode = ‘ShortleyWeller_WithTelescopicGrids’
      f_telescope
      target_grid
        target_size_internal_grid_sigma
        target_Dh_internal_grid_sigma
      N_nodes_discard
      N_min_Dh_main
      Dh_sc_ext
Introduction: Numerical Parameters

## Slide 52
The motivation of these convergence studies is to find the lower acceptable values for the numerical parameters:
  transverse grids
    Multigrid:
      f_telescope: Magnification factor between grids (0 < f < 1)
Courtesy of
E. Belli
Introduction: Numerical Parameters

## Slide 53
Courtesy of
E. Belli
The motivation of these convergence studies is to find the lower acceptable values for the numerical parameters:
  transverse grids
    Multigrid:
      target_grid: dictionary with the internal grid parameters: ‘x_min_target’, ‘x_max_target’, ‘y_min_target’, ‘y_max_target’, ‘Dh_target’
Introduction: Numerical Parameters

## Slide 54
The motivation of these convergence studies is to find the lower acceptable values for the numerical parameters:
  transverse grids
    Multigrid:
      target_grid: dictionary with the internal grid parameters
Can be given also in terms of transverse sigma of the beam:
        target_size_internal_grid_sigma
        target_Dh_internal_grid_sigma
Introduction: Numerical Parameters

## Slide 55
The motivation of these convergence studies is to find the lower acceptable values for the numerical parameters:
  transverse grids
    Multigrid:
      N_nodes_discard: number of nodes at the edge of the internal grids which are discarded in the field interpolation
Courtesy of
E. Belli
Introduction: Numerical Parameters

## Slide 56
The motivation of these convergence studies is to find the lower acceptable values for the numerical parameters:
  transverse grids
    Multigrid:
      N_min_Dh_main: minimum size of the first internal grid, in number of points of the step of the main grid
Courtesy of
E. Belli
Introduction: Numerical Parameters

## Slide 57
The motivation of these convergence studies is to find the lower acceptable values for the numerical parameters:
  transverse grids
    Multigrid:
      Dh_sc_ext: step of the external grid
Introduction: Numerical Parameters

## Slide 58
  Scan: 4𝜎t (1.37 – 1.02 ns) / RF voltage (3 - 8 MV)
[1] H. Timko, “Injection Voltage Reduction In the LHC” – September 5, 2018
Introduction: Numerical Parameters

## Slide 59
Computational Time
The simulations are: 108.
The finished simulations are: 108. The killed simulations are: 0.
Total computational time: 858 days (8 cores).
28.5 GB stored.
Convergence Studies: Slices

## Slide 60
Computational Time
The simulations are: 72.
The finished simulations are: 72. The killed simulations are: 0.
Total computational time: 818 days (8 cores).
24.6 GB stored.
Convergence Studies: MPs/Slice

## Slide 61
Computational Time
The simulations are: 72.
The finished simulations are: 72. The killed simulations are: 0.
Total computational time: 748 days (number of cores depends on segments).
25.7 GB stored.
Convergence Studies: Segments

## Slide 62
Computational Time
The simulations are: 54.
The finished simulations are: 54. The killed simulations are: 0.
Total computational time: 645 days (8 cores).
19.7 GB stored.
Convergence Studies: e- MPs

## Slide 63
T0
Parameter | Value
f (magnification factor) | 0.3
SN [mm] | 6.95 (10𝜎)
ΔhN [mm] | 0.139 (0.2𝜎)
Δh0 [mm] | 0.8
N_nodes_discard | 5
N_min_Dh_main | 10
Convergence Studies: Transverse Grid
…
2*S0
2*S1
2*SN
ΔhN
Δh0
Δh1

## Slide 64
Computational Time
Convergence Studies: Transverse Grid
The simulations are: 72.
The finished simulations are: 69. The killed simulations are: 0.
Total computational time: 1035 days (8 cores).
25.4 GB stored.
The slowest simulation needs 35 days to reach 20,000 turns.
The fastest simulation needs 26 days to reach 20,000 turns.
(last download 19/11/2019)

## Slide 66
Convergence Studies: 16% - 26%
Slices MPs/Slice
Segments e- MPs

## Slide 67
Convergence Studies: 16% - 26%
Transverse Grids

## Slide 69
It can be related to the number of electrons around the chamber centre (from build-up simulations)
Useful Parameter in PyECLOUD
cen_density [e-/m3]: electron volumetric density in a sphere around the chamber centre with radius r_center (input simulation parameter)
r_center = 1 mm
  Why no Instability at High Intensity?
x
y
r_center

## Slide 70: Build-up: Full Plot
  Why no Instability at High Intensity?

## Slide 71: Build-up: Full Plot
The combined build-up status are: 196 – 204 bunches
Build-up in saturation
  Why no Instability at High Intensity?

## Slide 72: Build-up: Zoom Plot
  Why no Instability at High Intensity?

## Slide 73: Build-up: Zoom Plot
Mask: points only when the number of the proton bunch is larger than 10% of the maximum
  Why no Instability at High Intensity?

## Slide 74: Build-up: Zoom Plot
2.5e13 e-/m3
Average of these values
  Why no Instability at High Intensity?

## Slide 76
76
VRF = 6 MV
SEY = 1.4
Damper = 10 turns
Chromaticity

## Slide 78
VRF = 4 MV
SEY = 1.3 – 1.4
Feedback damping time is 10 turns
Chromaticity and Damper
No instability observed over 20k turns for Q’ > 12.5!
For the case of LHC intensity (which an instability could be observed) the effectiveness of different mitigation measures has been investigated:
  The instability is strongly mitigated by increasing the chromaticity settings
  The transverse feedback is mostly ineffective cannot damp intra-bunch motion

## Slide 79
SEY = 1.3, Q’ = 0
SEY = 1.3, Q’ = 2.5
For the case of LHC intensity (which an instability could be observed) the effectiveness of different mitigation measures has been investigated:
  The instability is strongly mitigated by increasing the chromaticity settings
  The transverse feedback (bunch-by-bunch, damping time of 10 turns) is mostly ineffective  cannot damp intra-bunch motion
Chromaticity and Damper

## Slide 80
Positive chromaticity strongly mitigates the instability
The damper does not affect significantly the blow-up time (unable to suppress intra-bunch motion)
VRF = 4 MV
SEY = 1.3 – 1.4
Feedback damping time is 10 turns
No instability observed over 20k turns for Q’ > 12.5!
Chromaticity and Damper

## Slide 81
SEY = 1.4, Damper ON
Chromaticity and Damper