## Slide 1: Multi-species simulations with cross-ionization: investigation of numerical runaway
L. Mether and G. Iadarola
Acknowledgements: K. Poland, G. Rumolo

## Slide 2: Motivation
  Throughout 2017 operation, abnormal losses were observed in the LHC
  Located in the 16th half-cell left of Point 2 (‘16L2’)
68 premature dumps with the following signature occurred during 2017:
Sudden onset of high beam losses in 16L2
Coherent beam motion with extremely fast rise times
Beam dump either due to losses on the collimation system or directly in 16L2
To stay operational, the LHC was limited to fewer than the nominal number of bunches for most of the 2017 run. Several 16L2 events occurred also in 2018.
X. Buffat
L. Ponce et al.

## Slide 3: Sequence of events in 16L2
The problems in 16L2 are thought to have been caused by air frozen inside the beam chamber, through the following sequence of events:
The macro-particle undergoes a phase transition to a gas, leading to a a high local gas density
A macro-particle of frozen air (N2, O2) is detached,
possibly triggered by e-cloud,
and enters the beam
The beam ionizes some of the gas in its path. Its interaction with the
The beam ionizes some of the gas in its path. Its interaction with the generated electrons/ions causes the fast instabilities
frozen air
beam
macro-particle
electron
gas
ion
A. Lechner

## Slide 4: Sequence of events in 16L2
The problems in 16L2 are thought to have been caused by air frozen inside the beam chamber, through the following sequence of events:
The macro-particle undergoes a phase transition to a gas, leading to a a high local gas density
A macro-particle of frozen air (N2, O2) is detached,
possibly triggered by e-cloud,
and enters the beam
The beam ionizes some of the gas in its path. Its interaction with the
The beam ionizes some of the gas in its path. Its interaction with the generated electrons/ions causes the fast instabilities
Our aim is to model the last part of this sequence of events:
If we assume a high gas density in the beam chamber, can we reproduce the observations in a consistent manner?
Previous studies and development (2017-18):
Implementation of multi-species simulations
Multi-species build-up and stability simulations with beam-induced ionization of N2 gas
See e.g. LBOC #82
Recent model ingredient (2019):
Implementation of cross-species ionization
First simulation study with cross-ionization
See e-cloud meeting #69

## Slide 5: Cross-species ionization model
For the implementation of the cross-species ionization, we wanted to keep the same simplifying assumptions as are made for the beam-induced ionization
Assume a uniform gas density in the chamber (no neutral macro-particles, no collisions  not full-scale plasma simulations)
Consider single ionization only

## Slide 6: First cross-ionization simulations
450 GeV, SEY=1.25
Cross-ionization starts to have a significant impact as of gas densities of 1020 m-3
An unexpected self-sustaining behaviour is observed for a gas density of 1020 N2/m3 – is it physical?
Sudden drops of the electron density occur for higher gas densities – are they physical?

## Slide 7: First cross-ionization simulations
450 GeV, SEY=1.25
Cross-ionization starts to have a significant impact as of gas densities of 1020 m-3
An unexpected self-sustaining behaviour is observed for a gas density of 1020 N2/m3 – is it physical?
Sudden drops of the electron density occur for higher gas densities – are they physical?
In this presentation we try to address these questions. We focus mainly on the case with gas density 1020 N2/m3

## Slide 8: Energy evolution
As a first consistency check, we monitor the total energy in the system
Previously only the kinetic energies of each cloud were saved
Calculation and saving of the electrostatic energy was implemented as
   energy of the total charge system, not individual clouds

## Slide 9: Energy evolution
After the last bunch passage no external energy is injected into the system
The total energy should stay constant or decrease
Instead, an increase is observed in every energy component
The evolution after the bunch train is unphysical
Unphysical evolution correlates roughly with neutralisation of system
The wall is a net energy absorber

## Slide 10: Energy evolution
During the bunch train passage, external energy is injected only during individual bunch passages
An energy increase is observed also between bunch passages
The evolution becomes unphysical already during the bunch train passage
The wall is a net energy absorber

## Slide 11: Detailed studies
To investigate the unphysical evolution, detailed studies were performed
Saved full simulation state at regular intervals along the simulation
Restarted simulations from saved states could be run interactively in small steps, allowing the examination of different quantities along the simulation
Both time-consuming and data-intensive
On the next slides some observations from these studies…

## Slide 12: E-field evolution
There appears to be a correlation between the artificial energy growth, the (quasi-) neutralization of the system and increasingly noisy e-fields
Bunch passage 1
[V/m]

## Slide 13: E-field evolution
There appears to be a correlation between the artificial energy growth, the (quasi-) neutralization of the system and increasingly noisy e-fields
Bunch passage 10
[V/m]

## Slide 14: E-field evolution
There appears to be a correlation between the artificial energy growth, the (quasi-) neutralization of the system and increasingly noisy e-fields
Bunch passage 20
[V/m]

## Slide 15: E-field evolution
There appears to be a correlation between the artificial energy growth, the (quasi-) neutralization of the system and increasingly noisy e-fields
Bunch passage 30
[V/m]

## Slide 16: E-field evolution
There appears to be a correlation between the artificial energy growth, the (quasi-) neutralization of the system and increasingly noisy e-fields
Bunch passage 35
[V/m]

## Slide 17: E-field evolution
There appears to be a correlation between the artificial energy growth, the (quasi-) neutralization of the system and increasingly noisy e-fields
Bunch passage 40
Here the energy evolution is already unphysical
[V/m]

## Slide 18: E-field evolution
There appears to be a correlation between the artificial energy growth, the (quasi-) neutralization of the system and increasingly noisy e-fields
Bunch passage 45
Here the energy evolution is already unphysical
Also the e-field magnitude becomes suspiciously large
[V/m]

## Slide 19: E-field evolution
There appears to be a correlation between the artificial energy growth, the (quasi-) neutralization of the system and increasingly noisy e-fields
Bunch passage 48
Here the energy evolution is already unphysical
[V/m]
Also the e-field magnitude becomes suspiciously large

## Slide 20: E-field evolution
There appears to be a correlation between the artificial energy growth, the (quasi-) neutralization of the system and increasingly noisy e-fields
Bunch passage 49
Here the energy evolution is already unphysical
[V/m]
Also the e-field magnitude becomes suspiciously large

## Slide 21: E-field evolution
There appears to be a correlation between the artificial energy growth, the (quasi-) neutralization of the system and increasingly noisy e-fields
Bunch passage 50
Here the energy evolution is already unphysical
[V/m]
Also the e-field magnitude becomes suspiciously large

## Slide 22: E-field evolution
There appears to be a correlation between the artificial energy growth, the (quasi-) neutralization of the system and increasingly noisy e-fields
Bunch passage 51
Here the energy evolution is already unphysical
[V/m]
Also the e-field magnitude becomes suspiciously large

## Slide 23: E-field evolution
There appears to be a correlation between the artificial energy growth, the (quasi-) neutralization of the system and increasingly noisy e-fields
It looks like the simulation suffers from numerical heating, where local noise in the electric field artificially accelerates the electrons  unphysical energy growth
Bunch passage 51
Here the energy evolution is already unphysical
[V/m]
Also the e-field magnitude becomes suspiciously large

## Slide 24: Numerical heating
Well known phenomenon in PIC plasma codes
Can typically be avoided by ensuring the stability conditions:
  Based on saved average quantities, these conditions are satisfied in our simulation
However, it is based on assumption of thermal Maxwell-Boltzmann distribution
Generally a problem for “cold” plasmas, with no spread in velocities
  e.g. astrophysical plasmas

## Slide 25: Regeneration
To keep the number of macro-particles manageable during simulations (with exponentially increasing number of particles), macro-particles are merged throughout the simulation, to keep their number within requested limits
When merged in large steps, a correlation is observed between the merging events (regenerations) and the slope of the (unphysical) energy growth

## Slide 26: Regeneration
To keep the number of macro-particles manageable during simulations (with exponentially increasing number of particles), macro-particles are merged throughout the simulation, to keep their number within requested limits
When merged in large steps, a correlation is observed between the merging events (regenerations) and the slope of the (unphysical) energy growth
The regenerations inject more noise into the system

## Slide 27: Regeneration
To keep the number of macro-particles manageable during simulations (with exponentially increasing number of particles), macro-particles are merged throughout the simulation, to keep their number within requested limits
When merged in large steps, a correlation is observed between the merging events (regenerations) and the slope of the (unphysical) energy growth
The regenerations inject more noise into the system
With smaller regenerations, no evident correlation occurs. The unphysical evolution is slightly damped and postponed, but not mitigated

## Slide 28: Cross-ionization imbalance
Another source of artificial imbalance is introduced in the system by the cross-ionization
In principle the same amount of electrons and ions should be generated
Since a probabilistic algorithm is used, which depends on the macro-particle weight of each cloud, small fluctuations in the numbers occur
The introduced imbalance is small compared to the number of particles in the clouds

## Slide 29: Cross-ionization imbalance
Another source of artificial imbalance is introduced in the system by the cross-ionization
In principle the same amount of electrons and ions should be generated
Since a probabilistic algorithm is used, which depends on the macro-particle weight of each cloud, small fluctuations in the numbers occur
The introduced imbalance is small compared to the number of particles in the clouds
But not so small with respect to the net charge (electrons - ions), which essentially determines the fields
An option was implemented to enforce the algorithm to use the same probabilities for all clouds, removing the imbalance, but this didn’t cure the simulation

## Slide 30: Noise reduction
To decrease numerical noise, the number of macro-particles needs to be increased
A clean e-cloud build-up simulation typically requires around 250 000 macro-particles
For these studies the number was pushed up to 8 million per cloud
In order to keep the computational time within reasonable limits a parallelization scheme had to be introduced in the build-up simulation (not available up to now)
The parallelization is done on the particle-by-particle operation and is effective only for a very large number of particles

## Slide 31: Macro-particle number scan
We scan the number of macro-particles per cloud
The numerical breakdown can be pushed to later in the bunch train with increasing macro-particle numbers
Before the breakdown, the simulation is converged wrt the macro-particle number

## Slide 32: Macro-particle number scan
We scan the number of macro-particles per cloud
The numerical breakdown can be pushed to later in the bunch train with increasing macro-particle numbers
Before the breakdown, the simulation is converged wrt the macro-particle number

## Slide 33: Macro-particle number scan
We scan the number of macro-particles per cloud
The numerical breakdown can be pushed to later in the bunch train with increasing macro-particle numbers
Before the breakdown, the simulation is converged wrt the macro-particle number
The first part of the simulation can be trusted

## Slide 34: Time step scan
We scan the time step, keeping a large number of macro-particles
Here electric fields are updated at each step (in typical build-up simulations updates can be done every 5-10 time steps)
The numerical breakdown can be pushed to later in the bunch train also with decreasing simulation time step
Before the breakdown convergence wrt the time step is decent
Simulating 60 bunch passages has taken about 10 days

## Slide 35: Time step scan
We scan the time step, keeping a large number of macro-particles
Here electric fields are updated at each step (in typical build-up simulations updates can be done every 5-10 time steps)
The numerical breakdown can be pushed to later in the bunch train also with decreasing simulation time step
Before the breakdown convergence wrt the time step is decent

## Slide 36: Time step scan
We scan the time step, keeping a large number of macro-particles
Here electric fields are updated at each step (in typical build-up simulations updates can be done every 5-10 time steps)
The numerical breakdown can be pushed to later in the bunch train also with decreasing simulation time step
Before the breakdown convergence wrt the time step is decent
The first part of the simulation can be trusted

## Slide 37: Grid cell size scan
We keep a large number of macro-particles and a time step of 5 ps and scan the grid size
The dependence on the grid cell size is non-linear
  For a fixed number of macro-particles, going to a smaller cell size makes the fields more noisy and the numerical instability set in earlier, but a larger cell size is also prone to numerical instability
Before the breakdown, the simulation is converged also wrt to the grid cell size

## Slide 38: Grid cell size scan
We keep a large number of macro-particles and a time step of 5 ps and scan the grid size
The dependence on the grid cell size is non-linear
  For a fixed number of macro-particles, going to a smaller cell size makes the fields more noisy and the numerical instability set in earlier, but a larger cell size is also prone to numerical instability
Before the breakdown, the simulation is converged also wrt to the grid cell size

## Slide 39: Grid cell size scan
We keep a large number of macro-particles and a time step of 5 ps and scan the grid size
The dependence on the grid cell size is non-linear
  For a fixed number of macro-particles, going to a smaller cell size makes the fields more noisy and the numerical instability set in earlier, but a larger cell size is also prone to numerical instability
Before the breakdown, the simulation is converged also wrt to the grid cell size
The first part of the simulation can be trusted

## Slide 40: Higher gas densities
Increasing the gas density by a factor of 10 to 1021 m-3, the numerical breakdown occurs already at the beginning of the simulation

## Slide 41: Higher gas densities
Increasing the gas density by another factor of 10 to 1022 m-3, the numerical breakdown occurs during the first bunch passage
Sudden drops of the electron density occur when the simulation is already compromised

## Slide 42: Conclusions
We have identified the limit of our simulation model due to numerical heating
For a gas density of 1020 m-3 the simulation is converged for about 50 bunch passages
We cannot currently simulate gas densities above 1020 m-3, as the breakdown occurs after only a few bunch passages
The simulation is converged wrt numerical parameters until the runaway starts
This indicates that this model is sufficient to cover the evolution until that point
To improve the simulation further neutrals would need to be tracked and collisions modelled  full-scale plasma simulations (would require huge development efforts)

## Slide 43: Conclusions
Based on what we have so far, we can conclude that
Cross-ionization increases the electron and ion densities up to at least 1017 m-3
Based on previous instability simulation studies (with a different initial state without cross-ionization, but similar average electron and ion densities), this could be compatible with the observed instabilities
Refined instability simulations could be done starting from the results of build-up simulations with cross-ionization with a reasonable effort (a few more weeks of work)

## Slide 45: Further ingredients
Neutrals
Collisions respecting momentum conservation laws
  Impact ionization (could we take into account the ionization energy) e- + N2
  Coulomb collisions between charged particles (compensate for underestimation within individual cells in PIC) e- + e- , N2+ + N2+ , e- + N2+
  Elastic collisions e- + N2 , N2 + N2
  Charge exchange and momentum transfer N2+ + N2

## Slide 46: Time steps
A PyECLOUD build-up simulation has 2 different time steps
The main time step that determines the propagation of the beam etc typically set to Δt ≈ 25 ps
A time step for updating the electric fields from the charge distribution typically set to Δt_sc = 5 * Δt ≈ 125 ps
In the cross-ionization simulations the time steps were set much smaller than for a standard build-up simulation
Δt = 5 ps
Δt_sc = 5 * Δt = 25 ps
Still, it was found that even more
frequent updates of the electric fields are required
A convergence scan wrt the time step with Δt_sc = Δt was performed