## Slide 1: EoI 114: Development of Resistive electrodes for MPGD detectors for future collider experiments. EoI 126: Application of Diamond Like Carbon (DLC) coating in Gas Electron Multipliers (GEM) based detectors for future experiments and applications. Eraldo Oliveri – Piet Verwilligen CERN – INFN BA
++

## Slide 2: Participating Institutes
EoI 126
Institute / company | Main contact person | E-mail
CERN EP-DT-DD GDD | Eraldo Oliveri | eraldo.oliveri@cern.ch
CERN EP-DT-EF MPT | Rui De Oliveira | rui.de.oliveira@cern.ch
IFPIL | Maryna Chernyshova | maryna.chernyshova@ifpilm.pl
AGH UST | Bartosz Mindur | bartosz.mindur@agh.edu.pl
USTC | Yi Zhou | zhouyi@mail.ustc.edu.cn
KOBE | Atsuhiko Ochi | ochi@kobe-u.ac.jp
Institute / company | Main contact person | E-mail
INFN Bari (UniBA – CNR) | Piet Verwilligen | piet.verwilligen@ba.infn.it
CERN | Archana Sharma | archana.sharma@cern.ch
INFN Lecce (UniSAL) | Anna Paola Caricato | annapaola.caricato@le.infn.it
INFN Pavia (UniPV, UniBG) | Ilaria Vai | ilaria.vai@pv.infn.it
Techtra | Piotr Bielowka | piotr.bielowka@techtra.pl
EoI 114

## Slide 3: The background
  The Gas Electron Multiplier (GEM) proved to be a very successful detector concept adopted by several HEP & non-HEP experiments
  Resistive electrodes, recognizing limitations in terms of rate capability and charging up, improve detector stability of single amplification stage MPGDs (micromegas, mRWELL) and might be the bridge to higher gains (reach wire-chambers gain of ~105)
  Diamond Like Carbon (DLC) coating techniques are currently explored by several groups in the gaseous detector community to develop new structures and new detectors profiting from coating properties (e.g. robustness, resistivity,…) and on the possibility of controlling them.
++

## Slide 4: Aim, motivations, interests
EoI 114’s aim: Investigate the use of carbon based materials to develop spark-free high-gain GEM detectors with resistive electrodes, exploring both high resistivity (DLC) and low resistivity (multilayer-graphene) layers.
  Verify detectors on small scales O(5-100 cm2); study and understand material (DLC / Graphene) properties with well-controlled techniques to define optimal parameters
EoI 126’s aim: Explore possible advantages coming from the application of DLC coatings in GEM based detectors.
  Special attention to scalability to large area system, maximum achievable detection rate (i.e. low resistivity DLC coating) and radiation hardness
Complementarity of the two EoIs: 114 is concentrated on high precision & high quality methods to make resistive electrodes on small scales; 126 will work with resistive electrodes produced by techniques that allows scaling
++

## Slide 5
Interests:
Quantify the improvements in discharge quenching and robustness (e.g. permanent shorts) for resistive GEMs, resulting in safer operation in harsh environments.
Find optimal value for resistivity that allows protection and preserves rate capability
Development of low-material budget detector
Not limited to GEMs: High Quality resistive layers will find application in many MPGDs
Development of GEM foils with resistive electrodes will allow electrically transparent structures  new ways of signal pickup, improve timing, …
Successful transfer & etching of Multilayer-Graphene will allow new detector concepts: ion blocking, resistive-mesh, …
Common interest and added value for the community:
Technological development of DLC coating on different substrates.
Studies of DLC properties (e.g. photoemission properties) that can be picked up in any kind of detection system, not necessarily GEM and not necessarily gaseous.
Radiation hardness studies on DLC.
Low material budget detector with “metal free” electrodes.
Aim, motivations, interests

## Slide 6
Aspect that will be investigated (EoI 126):
  Foil protection against discharges (limiting energy & quenching, robustness and GEM survivability, limiting affected areas during sparks);
  Improvement of foil sectorization to reduce dead area between sectors;
  Mitigation of discharge propagation between electrodes and toward the readout;
  FE protection implemented on readout board;
  Radiation hardness of DLC-GEMs.
Aspect that will be investigated (EoI 114):
  Production of high-quality DLC with Ion Beam Deposition and Pulsed Laser Deposition;
  Emphasis on the adhesion of DLC to polyimide and control of holesize during etching;
  Scale production techniques up to 10 cm x 10 cm;
  Resistance of Graphene to polyimide etching liquids: KOH and ethyl-diamine;
    This will allow Graphene to play role of Cu not only during detector operation, but also during detector production: Photolithography & Plasma Etching of Graphene.
  Characterization of 10 cm x 10 cm DLC (high-res) and Graphene (low-res) GEM foils.

## Slide 7: Partners Involvement
++
EoI 126:
Characterization and qualification measurements/studies/interests:
    CERN GDD (high rate and low material budget, large area tracking and triggering devices for future HEP experiments, radiation hardness and robustness..)
    IFPILM (high rate, no intrinsic fluorescence, ITER-oriented research in plasma physics, harsh radiation environment, robustness, ...)
    AGH UST (high rate, X-ray imaging, robustness, no intrinsic fluorescence, energy and space resolution,... )
Component production
    CERN MPT (MPGD component manufacturing: GEM/readout/…, new structures, new procedure)
    USTC & KOBE (*) (optimization of DLC coating: properties, adhesion on different materials,..)
(*) Industrial partners linked to USTC/KOBE will support technological development on DLC deposition techniques

## Slide 8: Partners Involvement
++
EoI 114:
Production of DLC and Graphene layers (10 x 10 cm2):
  DLC with 10-100MOhm/sq by PLD or IBD INFN BA&LE – UniSAL -BA
  HQ Multilayer Graphene with 30-100 Ohm/sq CNR-Nanotech – UniBA
Etching of DLC UniBA - CERN
Etching of ML-Graphene:
  Test of chemical resistance of KOH and ethyl-diamine solutions of graphene
  Photolithography of Graphene (hole pattern) CNR-IFN – UniBA
  Oxygen Plasma Etching of Graphene CNR-NanoTech – UniBA
  Graphene-Polyimide Etching CERN
Test Prototype detectors with Resistive GEM foils
  X-rays and UV-laser INFN BA – INFN Pv
Industrial Partner: Techtra
  Will be involved in the photo-lithography and plasma etching phases of DLC and Graphene coated Polyimide
  I see the possibility for Technology transfer of etching of DLC-PI foils (to be discussed with the partners)

## Slide 9: Resources, Infrastructures,…
++
Infrastructures:
  Well-equipped laboratories for DLC production; Detector production & test
  Laboratories for detector test: CERN GDD, IFPILM, AGH UST (EoI 126) INFN BA, INFN PV (EoI 114)
  Production facilities: CERN MPT workshop (MPGD components manufacturing), USTC/KOBE (DLC coatings) (EoI 126) CNR-Nanotech – UniBA (Graphene), INFN-BA (IBS DLC), INFN-LE (PLD DLC) (EoI 114)
EoI 126 Deliverables:
  Deliverable 1: Double side DLC GEM: full single foil characterization, discharge propagation, rate capability, radiation hardness.
  Deliverable 2: Light multi GEM-DLC based detector prototype, potentially scalable up to relevant sizes for HEP experiments.
EoI 114 Deliverables:
  Deliverable 1: Characterization of 10cm x 10 cm GEM made with DLC electrodes.
  Deliverable 2: Assessment of potentiality of multilayer graphene as GEM detector electrode.
  Deliverable 3: Characterization of 10cm x 10 cm GME made with ML-Graphene electrodes.
Timeline:
  Phase 1 (2 years) – exploring phase: EoI 126: characterization of components, validation of proposed optimizations, preliminary prototypes. EoI 114: first 10x10 deposition with IBS; design setup for 10x10 with PLD; assessment of Graphene.
  Phase 2 (2 years) – final prototypes: EoI 126: built a final DLC GEM based prototype , scalable to large area, based on the outcome of phase 1 (GEM, readout,…). EoI 114: production & test of prototypes with IBS and PLD; production of 10x10 Graphene prototype.

## Slide 10: Resources, Infrastructures,…
++
Task ID | Task | Partner | Total number of PMs | EC contribution (in kEUR) (a) | Matching funds (in KEUR) (b) | Total Costs (kEUR)
114 | Development of resistive electrodes for MPGD detectors for future collider experiments. | INFN BA, INFN LE, INFN PV, CERN, Techtra | 52 | 173 | 347 | 520
126 | Application of Diamond Like Carbon (DLC) coating in Gas Electron Multipliers (GEM) based detectors for future experiments and applications. | CERN GDD, MPT IFPILM, AGH UST, USTC, KOBE | 48 | 148 | 296 | 444
Resources:
  Manpower will be covered by all the involved institutes.
  EoI 126: EC contribution for prototypes and material.
    It may support measurement campaigns between EU institutes.
  EoI 114: EC contribution for 2-y post-doc and prototypes and material:
    Production: Pyrolithic Carbon Targets, Gas, New PLD setup to cover 10 x 10 cm2, Photolithography masks, Graphene;
    Prototypes: Readout boards, frames, polyimide, Travel to CERN for etching sessions;
    Tests: measurement cables, gas, some specific advanced instrumentation (e.g. APIC w/ MCA).
  Table below gives summarizes the total number of PMs = Matching Funds.

## Slide 11: Back-up
++

## Slide 12: Resources, Infrastructures,…
++
Task ID | Task | AREA | Partner | Total number of PMs | Total number of PMs | EC contribution (in kEUR) (a) | EC contribution (in kEUR) (a) | Matching funds (in kEUR) (b) | Matching funds (in kEUR) (b) | Full costs (in kEUR) (a) + (b)
126 | Application of Diamond Like Carbon (DLC) coating in Gas Electron Multipliers (GEM) based detectors for future experiments and applications. | Gaseous Detectors | CERN GDD,MPT IFPILM, AGH UST, USTC, KOBE | 48 | 11,11 22 4 0,0 | 148 | 32,32 64 20 0,0 | 296 | 64,64 128 40 0,0 | 444
114 | Development of resistive electrodes for MPGD detectors for future collider experiments. | Gaseous Detectors | INFN Bari INFN Lecce INFN Pavia CERN, Techtra | 52 | 26 10 10 3,3 | 173 | 100 35 20 9,9 | 347 | 173 70 70 17,17 | 520
Task ID | Task | Partner | Contribution | Total number of PMs | EC contribution (in kEUR) (a) | Matching funds (in KEUR) (b) | Total Costs (kEUR)
114 | Development of resistive electrodes for MPGD detectors for future collider experiments. | INFN BA, INFN LE INFN PV CERN, Techtra | 50% 20% 20% 5%, 5% | 52 | 173 | 347 | 520
126 | Application of Diamond Like Carbon (DLC) coating in Gas Electron Multipliers (GEM) based detectors for future experiments and applications. | CERN GDD, MPT IFPILM, AGH UST, USTC, KOBE | 22.5%, 22.5% 45% 10% 0%, 0% | 48 | 148 | 296 | 444
Caution! These estimates are only indicative, final numbers will depend on scientific program and available funding