## Slide 1: Inspired by Physics - How to Design a Flying Jumbo Jet - in Just One Hour
CBI-ER, December 17, 2019, Markus Nordberg
Development & Innovation Unit (CERN)

## Slide 4: WHY ARE WE DOING THIS?
Like the experiments at CERN, the aerodynamic design of aircraft are also much determined by the laws of physics
We wish to give an example of physics-driven experimentation process, requiring cross-disciplinary collaboration
Here, we wish to bring in business management, engineering and design, but driven by physics (i.e. special case)
They all contribute, even if the driver here is aerodynamics
Prototyping is a good way to start to learn about the design process (even if incremental)
If we are able to design a stupid jumbo, well, then we can ….
… better judge what looks disruptive rather than just incremental
Physics driven Design Thinking is Fun

## Slide 5: PLEASE REMEMBER THAT …
… Modern aircraft designers are not taught like this
  (The difference between this intro and designing real airliners is only about 10 000 hours … But make no mistake, our jumbo will fly)
… Modern aircrafts are not designed by MSc-level students
… You will not be a certified aircraft designer after this course
… Folks at CERN can’t do anything
  (Alas - but they do know how far the laws of physics will take you)

## Slide 6: LET US START

## Slide 7: WHO DESIGNED THIS?

## Slide 8: OR THIS?

## Slide 9: USUALLY GROUP DESIGNING COMES UP WITH THINGS LIKE THESE

## Slide 10: NATURE SEEMS TO KNOW ITS SHAPES WELL

## Slide 11: ALL YOU NEED TODAY TO KNOW ABOUT THE THEORY
Finesse F = L/D
Aspect Ratio Ar = b²/S
b
S
codecogs
Shape (F)
Performance (engines)

## Slide 12
F = ma
or, assuming air ~ fluid
W/S ~ 0.3 x σ x v²
Where:
W = weight of the object (N)
S = wing area (m²)
σ = density of air; 1.1 kg/m³ at sea level, 0.4 kg/m³ at 10 km altitude
v = (constant) cruising speed (m/s)
So at low altitudes
W/S ~ 0.4 x v²

## Slide 13
How fast did Daedalus fly?
W/S ~ 0.4 x v²
(at low altitudes)
W = weight of the object (750N)
S = wing area (2 m²)
v = cruising speed (m/s) ~ 30 m/s = 110 km/h

## Slide 14
Did my Uncle Alport’s Opel Really Fly?
W/S ~ 0.4 x v²
(at low altitudes)
W = weight of the object (8500N)
S = wing area (7 m²)
v = cruising speed (m/s) ~ 55 m/s = 200 km/h

## Slide 15: WHAT DOES OUR JUMBO NEED TO DO?
Transport a lot of cargo (originally)
Fly non-stop long distances (Europe-US)
Be fuel-efficient (i.e. good aerodynamics, good Ar and F)
Take off and land in existing (big) airports
Return back to home base the same day
Fast turnaround time (cargo handling, aircraft servicing)
+ Other criteria (not relevant for us today)

## Slide 16
Let us Start with the Aerodynamics
Looking for inspiration from:
heavy migrating birds
high Aspect Ratio (Ar) and Finesse (F)
H. Tennekes (2009)
H. Tennekes (2009)

## Slide 21: INITIAL INPUT PARAMETERS (ROUGH GUESS)
We assume 6h service + 3h turnaround + 15h flying time per day (ie. 2 x 7.5 h)
Distance Frankfurt – New York is ~ 6300 km + small margin (say, 200 km) => v < 870 km/h
W/S ~ 0.3 x σ x v² < 7000 N/m²
Ar = b²/S, large airport taxiways are max. 80 m wide (max b!)
An average albatross Ar ~ 19 => S ~ 340 m² => W ~ 2600 kN (260 tn)

## Slide 22
DESIGN CYCLE
Range
R
Cruising (C) speed
v
Wing load
W/S
Thrust & Weight
T, W
Aspect Ratio
Ar -> b -> S
Engine fuel consumption
fc (SFC)

## Slide 23
PERFORMANCE OF CIVIL AIRCRAFTS IN 1960s
Wikipedia

## Slide 24: OUTPUT JUMBO PARAMETERS (1st CYCLE)
For the time being, let us not worry about minor details such as the landing gear, stabilizers, engine nacelles, or the length and diameter of the fuselage, landing speed or minimum runway distances etc …
Let us optimize on Cargo

## Slide 25: OK NOW YOU GO & IMPROVE (2nd CYCLE)

## Slide 26
SO THERE WE ARE …

## Slide 27: WHAT DO WE TAKE AWAY FROM ALL OF THIS?
Apart perhaps its engine performance, the jumbo (design) is basically incremental
Socio-economic needs drive such large aircraft designs
Less than five engineering parameters determine the aerodynamic design of a large aircraft – but of course there is plenty more to design (interior, cockpit, services etc.)
Performance of large birds does not seem to fall under the spell of neoclassical economics and business thinking -> Not much help in optimizing aircraft design?

## Slide 28
THANK YOU
Questions? Comments?
Contact information:
Email: markus.nordberg@cern.ch
Skype: phone-markus

## Slide 29
ASSIGNMENT

## Slide 30
10
20
Finesse
Please design a passenger aircraft that fulfills the following needs:
Highly economical to fly (F higher than 20)
Cruising speed less than current large jets (but above TGV)
Can land and take off from existing airports or fields
Integral element of a new, compelling business model
Its appearance is perceived as unique or distinctive in the market
40
H. Tennekes (2009)

## Slide 31
List of engines
https://en.wikipedia.org/wiki/List_of_aircraft_engines
To obtain fuel consumption in tn/h,
= (TSFC x Thrust (kN) x 3600)/100’000
EVOLUTION OF JET ENGINE (FUEL CONSUMPTION)
PPRuNe Forum

## Slide 32
To obtain fuel consumption in mg/Ns, multiply by 28

## Slide 33
DESIGN CYCLE
Range
R
Cruising (C) speed
v
Wing load
W/S
Thrust & Weight
T ~ W/3.5
Finesse
~ 6 x √Ar
-> S
Engine fuel consumption
fc (SFC)

## Slide 34
DESIGN PARAMETERS OF MODERN CIVIL JETS
Wikipedia

## Slide 35: LET US START (EXERCISE)

## Slide 36
BE INSPIRED BY NATURE AND PHYSICS…

## Slide 37
… BUT LET’s NOT GET TOO CARRIED AWAY