## Slide 1: Super-FGD Electronics
FEB / MCB status
Y. FAVRE 15/11/2019

## Slide 2
FEB status :
  Baseline is 24V for FEB (no more LV module for a crate)
Writing specification, goal is 1st draft for end of the year:
  Writing bloc diagrams for architecture
  Connectivity :
    256 SiPMs => 512 signals => critical, need backplane definition to confirm LLR proposal (last meeting) => need mechanical integration study
    SYNC and OCC (DAQ) signals less critical
  FPGA pinout & I/O constraints (voltages) for CITIROC, ADC, MCB, OCC
  FPGA early power estimation
  Power tree consolidation of LLR proposal (DC/DC and LDOs)
Exploring parts placement for the board architecture wrt analog area (more critical):
  Mother board with 4 CITIROC + FPGA + power and 1 Mezzanine board with 4 other ASICs ? Connectivity with backplane ?
  Other (standard single board) ?
24V input to LV DC/DC with air coil:
  Difficult to estimate the impact on the FEB (induced radiation noise on analog stage, no risk on conductive noise due to low-noise LDO, based from B-MIND feedback)
  Design of the converters with standard ICs, including shielding case
  Replace B-MIND DC/DC converters by air coil DC/DC buck mockup and measure noise to evaluate the risk for Super-FGD FEB design => easier iterations
  When OK => put on the Super-FGD design

## Slide 3
MCB status, SYNC and DAQ protocol:
  MCB based on B-MIND
B-MIND MCB has limitations and complicates DAQ unpacking
=> simplify the SYNC protocol and add features (TDC) and more info in order to facilitate DAQ unpacking and event building
1st draft of MCB specification written:
  Update bloc diagram, protocol and signals by end of the year
DAQ:
  The FEB data will be very similar to B-MIND (even simpler with MCB enhancement)
  => OCC protocol for input data can be based on B-MIND protocol
  OCC protocol for output data need to be defined in order to specify the architecture of the OCC:
    Final DAQ (events) needs to be defined
    Limit of Software and Firmware (what is inside OCC) must be found
    This will define DAQ protocol for OCC output data
    => quite critical since defines OCC specification