## Slide 1: Run 3 optics (for the p-p runs)
S. Fartoukh, N. Karastathis
Acknowledgments: all LCR3WG members + LPC
Main outcome of the Run 3 configuration WG
Main Optics changes w.r.t. Run 2
Optics files description for the combined ramp & squeeze
Optics files description for the squeeze (b* levelling)
Chromatic properties
Next steps

## Slide 2: Main outcome of the Run 3 machine configuration WG https://indico.cern.ch/category/10387/
The preparation of the HL-LHC beam will take place in Run III
 Up to 2.1E11 p/b (ge=1.55 mm for BCMS) at SPS extraction in 2023 (1.3-1.4E11 max in 2021, 1.8E11 in 2022)
 versus 1.7-1.8E11 p/b acceptable for most of the existing LHC HW (on-going work)
LMC 06.03.2019
“The machine configuration should not limit the performance of the LHC in Run 3” (LMC recommendation)

## Slide 3
 Telescopic optics are needed to be deployed in the ramp for Landau damping the brighter (and more rigid) Run 3 beam.
 Two categories of octupoles in s81/12/45/56: the “optically strong” (with increased peak ) and the “optically weak” (with decreased peak ).
Beam 1/2 | “Strong“ OF.b1/OD.b2 | Weak OF.b1/OD.b2 | Strong OD.b1/OF.b2 | Weak OD.b1/OF.b2
Sector 45 (81) | 22.R4(8), 26.R4(8), 30.R4(8), 34.R4(8), 30.L5(1), 26.L5(1), 22.L5(1) | 24.R4(8), 28.R4(8), 32.R4(8), 32.L5(1), 28.L5(1), 24.L5(1) | 25.R4(8), 29.R4(8), 33.R4(8), 31.L5(1) | 31.R4(8), 33.L5(1), 29.L5(1), 25.L5(1)
Sector 56 (12) | 31.R5(1), 33.L6(2), 29.L6(2), 25.L6(2) | 25.R5(1), 29.R5(1), 33.R5(1), 31.L6(2) | 22.R5(1), 26.R5(1), 30.R5(1), 34.R5(1), 30.L6(2), 26.L6(2), 22.L6(2) | 24.R5(1), 28.R5(1), 32.R5(1), 32.L6(2), 28.L6(2), 24.L6(2)
Total | 7+4 = 11 | 6+4 =10 | 4+7 =11 | 4+6=10
 Anti-telescopic optics (r  1/r) also works, with the peak b-beating wave shifted by one FODO cell, i.e. the strong octupoles becoming weak, and vice et versa (strictly speaking the direct anharmonicity is reduced by 10%).
a) First optics constraints: Impedance

## Slide 4
[Run II – like collimator settings, new low impedance collimator included]
Coherent modes
still inside (with tele-index)
Comparison between telescopic and anti-telescopic optics
in terms of stability diagram
W/o telescopic (or anti-telescopic) optics, the MO threshold can be (at least) 550 A
in Run 3 (@ Q’=15+/-2, worst case) for a beam brightness of 1 (1.8e11 p/b within 1.8 mm)
N. Mounet
550A (with safety
factor of 2)
Q’=15
Q’=13

## Slide 5
Half-crossing angle vs b* in IR1/5[from ~100 mrad up to ~160 mrad]
and corresponding bunch charge evolution @ 2E34
First validation (using preliminary b* levelling optics sequence)
The WP can even be kept cst over the full
levelling period !
b) 2nd optics constraints: peak Lumi and IT lifetime
L ≤ 2E34 @ 1.8e11 p/b
 b* dynamic range of up to 500-600% (1-1.5 m 25 cm), similar to HL-LHC (vs. 20% in 2018) !
∫ Ldt ≤ 300 fb-1 in total, i.e. “only” ~100-150 fb-1 left for Run III w/o any dedicated measures
 V-Xing polarity management in ATLAS and operating at minimal X-angle vs. b* (BBLR limit)
Taking
[9.2 s @ 1.15e11 p/b from Run II experience, 12.0 s @ 1.8e11 p/b from HL-LHC studies]
@ L=2E34
[considering the less performing parameter case, i.e. 2484 collisions and ge=2.5 mm]

## Slide 6
b* levelling in telescopic mode is much preferred by the FP experiments (AFP & PPS)
Cst R-matrix from the IP to the Roman Pot’s (within the OMC knobs ..)
In telescopic squeezing mode: “tele-index range” = “b* range”
Considering
(i) a tele-index of 2-2.5 recommended EoR (stability of non-colliding beams for 1.8E11 p/b),
(ii) a b* dynamic range of up to 5-6 in SB (1.8 p/b colliding @ 2E34)
(iii) a typical range of [1/3, 3-4] for the tele-index (optics flexibility/match-ability/correct-ability),
 The only possible approach is to start b*-levelling from an anti-telescopic optics
c) Third main optics constraint: Forward physics experiment
Even w/o constraint from impedance (no telescope in the ramp), a b* levelling range of up to 5-6 in telescopic mode would require to start from an anti-telescopic optics at the EoR.
 b* levelling is the plan A to prepare HL-LHC
Another possibility would be to bet on offset-levelling (with a much smaller b*-levelling fraction in tele-mode, as in 2018), but leading to some difficulty (m-scan, instabilities may be)
 Offset levelling is the back-up (unless to fine tune the lumi unbalance between ATLAS and CMS)

## Slide 7
.. Betting on the best (1.8e11 p/b within 1.8 mm at Flat top) and investing for HL-LHC (b*-levelling), this is how the ramp and the b*-levelling sequence should look like in Run 3:
EoR = Beginning of SB parameters | 2021 | 2022-2023
Max beam brightness [1011 /mm] | 1.4/1.8 | (up to) 1.8/1.8=1
Full bunch lengh [ns] | 1.2 | 1.2
b* [m] at IP1 & IP5 | 1.0 | 1.5
Half-crossing angle [mrad] | 110.4 [12.1 s for ge=2.5 mm] | 101.7 [13.6 s for ge=2.5 mm]
Max Lumi [1034]@ beginning of SB [for ge=1.8 mm and 2736 collisions at IP1/5] | 1.68 | 1.98
EoR pre-squeezed b* [m] (IPQ settings in IR1/5) | 0.6 | 
EoR Tele-index (IPQ settings in IR8/2/4/6) | 0.6/1.0 =0.60 | 0.6/1.5 = 0.40
Single-bunch MO threshold [A] (with margin factor of 2) | 375 | 355
EoR Beam and Optics Parameters

## Slide 8
IR2
Ramp (2022):
  Pre-squeeze down to b*=1.5/10/1.5/1.5 m at IP1/2/5/8
  Combined Pre-squeeze and anti-tele squeeze at constant b* =1.5 m down to a tele-index of 0.40, i.e b*pre-squeeze = 0.4×1.5=0.6 m
b* levelling in Tele mode from 1.5 m to 20 cm (28 cm @ 7 TeV from aperture constraint), i.e. rtele = 0.4  3.0
IR8
IR1

## Slide 9: Main optics changes (and similarities) w.r.t. Run 2
Same injection optics as in Run 2 (the impact of BBLR on DA still OK at 1.8E11 p/b)
Pre-squeeze
  New pre-squeeze sequences in IR1 and IR5 from b*=11 m down to 60 cm to maximise the normalised dispersion at the RPs for AFP & PPS (the min. 1.5 mm gap should now be reachable for all RP’s, while sticking to the Run 2 MP rules, TBC)
  “New” IR8 optics transition down to b*= 1.5 m from the 2018 ion cycle (IR2 unchanged w.r.t. Run 2)
Anti-tele and Tele-squeeze of IR2/8/4/6 from r=0.4 (anti-telescope) up to r=3.0 (telescope)
  All new, in particular smoother in IR2 and IR4, at b*=1.5 m in IR8 (vs. 3 m in Run 2), and at constant b’s at the TCDQ in IR6 … BUT big MKD-TCDQ phase advance deviation for the anti-tele-squeeze part (up to 115o vs. 94o nominal)
  Higher leakage from the TCDQ for ASD, but only at high b* > 60 cm (normalised TCT widely open)
  OK from collimation (LHC Collimation Working Group #242) but green light still pending from the LBDS team

## Slide 10
New IR1/5 pre-squeeze from b*=11 m to 60 cm (possible extension down to 40 cm)
Beam 1
Beam 2
Roman Pots: dispersion slightly increased v.s Run 2 (no miracle) but b x sensibly reduced

## Slide 11
IR2/4/6/8 anti-telescopic squeeze (r=1.0  0.4)
Beam 1
Beam 2
IR8
IR2
IR6
IR4
IR6
IR4
IR2
IR8

## Slide 12
IR2/4/6/8 telescopic squeeze (r=1.0  3.0)
Beam 1
Beam 2
IR8
IR2
IR6
IR4
IR6
IR4
IR2
IR8

## Slide 13: Ramp & Squeeze in 2021 & 2022-2023
Optics file name |  | b* [m] in IR1/2/5/8 |  | Tele-index (& pre-squeezed b* [m] ) |  | Ramp & Squeezing modes |  | 
2021 | 2022-2023 | 2021 | 2022-2023 | 2021 | 2022-2023 | 2021 | 2022-2023 | 
Opticsfile.1 |  | 11.000/10.000/11.000/10.000 |  | 1.000 (11.00) |  | Nominal 2018 injection optics |  | 
Opticsfile.2 |  | 10.000/10.000/10.000/10.000 |  | 1.000 (10.00) |  | Combined Ramp & Pre-Squeeze at constant tele-index=1 down to b* = 1.5 m at IP1/5/8 (10 m at IP2) |  | 
Opticsfile.3 |  | 9.600/10.000/ 9.600/ 9.600 |  | 1.000 (9.60) |  |  |  | 
Opticsfile.4 |  | 9.100/10.000/ 9.100/ 9.100 |  | 1.000 (9.10) |  |  |  | 
Opticsfile.5 |  | 8.300/10.000/ 8.300/ 8.300 |  | 1.000 (8.30) |  |  |  | 
Opticsfile.6 |  | 7.100/10.000/ 7.100/ 7.100 |  | 1.000 (7.10) |  |  |  | 
Opticsfile.7 |  | 5.900/10.000/ 5.900/ 5.900 |  | 1.000 (5.90) |  |  |  | 
Opticsfile.8 |  | 4.900/10.000/ 4.900/ 4.900 |  | 1.000 (4.90) |  |  |  | 
Opticsfile.9 |  | 4.100/10.000/ 4.100/ 4.100 |  | 1.000 (4.10) |  |  |  | 
Opticsfile.10 |  | 3.300/10.000/ 3.300/ 3.300 |  | 1.000 (3.30) |  |  |  | 
Opticsfile.11 |  | 2.600/10.000/ 2.600/ 2.600 |  | 1.000 (2.60) |  |  |  | 
Opticsfile.12 |  | 2.100/10.000/ 2.100/ 2.100 |  | 1.000 (2.10) |  |  |  | 
Opticsfile.13 |  | 1.700/10.000/ 1.700/ 1.700 |  | 1.000 (1.70) |  |  |  | 
Opticsfile.14 |  | 1.500/10.000/ 1.500/ 1.500 |  | 1.000 (1.50) |  |  |  | 
Opticsfile.15 |  | 1.506/10.000/ 1.506/ 1.500 |  | 0.870 (1.31) |  | Ramp and Pre-Squeeze and Anti-Tele-Squeeze at quasi-constant b* ~ 1.5 m at at IP1/5/8 (10 m at IP2) |  | 
Opticsfile.16 |  | 1.508/10.000/ 1.508/ 1.500 |  | 0.769 (1.16) |  |  |  | 
Opticsfile.17 |  | 1.502/10.000/ 1.502/ 1.500 |  | 0.686 (1.03) |  |  |  | 
Opticsfile.18 |  | 1.500/10.000/ 1.500/ 1.500 |  | 0.600 (0.90) |  |  |  | 
Opticsfile.19 | Opticsfile.19 | 1.200/10.000/ 1.200/ 1.500 | 1.501/10.000/ 1.501/ 1.500 | 0.600 (0.72) | 0.506 (0.76) | Ramp and Pre-Squeeze at constant tele-index r=1.667 b* = 1.0 m & r = 0.600 EoR |  | Ramp and Pre-Squeeze and Anti-Tele-Squeeze at b* ~ 1.5 m b* = 1.5 m & r = 0.400 EoR
- | Opticsfile.20 | - | 1.501/10.000/ 1.501/ 1.500 | - | 0.440 (0.66) |  |  | 
Opticsfile.20 | Opticsfile.21 | 1.000/10.000/ 1.000/ 1.500 | 1.500/10.000/ 1.500/ 1.500 | 0.600 (0.60) | 0.400 (0.60) |  |  | 
20 matched points in 2021, and 21 matched points in 2022-2023. The first 18 optics are the same.
/afs/cern.ch/eng/lhc/optics/runIII/RunIII_dev/2021/PROTON (2021 optics)
/afs/cern.ch/eng/lhc/optics/runIII/RunIII_dev/2022/PROTON (2022-2023 optics)

## Slide 14: b* levelling in 2021 & 2022-2023 (prepared down to b*=20 cm)
Optics file name |  | b* [m] in IR1/2/5/8 |  | Tele-index (& pre-squeezed b* [m] ) |  | Comment | 
2021 | 2022-2023 | 2021 | 2022-2023 | 2021 | 2022-2023 | 2021 | 2022-2023
- | Opticsfile.21 | - | 1.500/10.000/ 1.500/ 1.500 | - | 0.400 (0.60) | Purely Telescopic Squeeze from b*=1.5 m (1.0 m in 2021) down to 20 cm, i.e. at constant quadrupole settings in IR1 and IR5 (60 cm pre-squeezed b*) | 
 | Opticsfile.22 |  | 1.330/10.000/ 1.330/ 1.500 |  | 0.451 (0.60) |  | 
 | Opticsfile.23 |  | 1.160/10.000/ 1.160/ 1.500 |  | 0.517 (0.60) |  | 
Opticsfile.20 | Opticsfile.24 | 1.000/10.000/ 1.000/ 1.500 |  | 0.600 (0.60) |  |  | 
Opticsfile.21 | Opticsfile.25 | 0.840/10.000/ 0.840/ 1.500 |  | 0.714 (0.60) |  |  | 
Opticsfile.22 | Opticsfile.26 | 0.710/10.000/ 0.710/ 1.500 |  | 0.845 (0.60) |  |  | 
Opticsfile.23 | Opticsfile.27 | 0.600/10.000/ 0.600/ 1.500 |  | 1.000 (0.60) |  |  | 
Opticsfile.24 | Opticsfile.28 | 0.510/10.000/ 0.510/ 1.500 |  | 1.176 (0.60) |  |  | 
Opticsfile.25 | Opticsfile.29 | 0.430/10.000/ 0.430/ 1.500 |  | 1.395 (0.60) |  |  | 
Opticsfile.26 | Opticsfile.30 | 0.360/10.000/ 0.360/ 1.500 |  | 1.667 (0.60) |  |  | 
Opticsfile.27 | Opticsfile.31 | 0.300/10.000/ 0.300/ 1.500 |  | 2.000 (0.60) |  |  | 
Opticsfile.28 | Opticsfile.32 | 0.250/10.000/ 0.250/ 1.500 |  | 2.400 (0.60) |  |  | 
Opticsfile.29 | Opticsfile.33 | 0.220/10.000/ 0.220/ 1.500 |  | 2.727 (0.60) |  |  | 
Opticsfile.30 | Opticsfile.34 | 0.200/10.000/ 0.200/ 1.500 |  | 3.000 (0.60) |  |  | 
/afs/cern.ch/eng/lhc/optics/runIII/RunIII_dev/2021/PROTON (2021 optics)
/afs/cern.ch/eng/lhc/optics/runIII/RunIII_dev/2022/PROTON (2022-2023 optics)
11 matched points in 2021 (down to 20 cm) and 14 matched points in 2022-2023. The last 11 optics are the same.
.. Detailed b*-levelling strategy still to be agreed (e.g. how many b* stops with state-of-the-art optics correction ?)

## Slide 15: Chromatic properties [2022-2023 cycle]
Fully satisfactory W functions over the cycle (although net impact of IR8)
Beam 1
Beam 2
IR8
IR5
IR1

## Slide 16: Chromatic properties [2022-2023 cycle]
Non-linear chromaticity from the triplet  well-controlled over the cycle
Beam 1
Beam 2

## Slide 17: Chromatic properties [2022-2023 cycle]
Spurious dispersion from crossing angle (simplified simulation at constant max. X-angle over the full cycle)
Beam 1
Beam 2
ON_DISP knob
Dispersion (impact of IR8 not corrected)

## Slide 18
OP (LSA)
Demonstrate the feasibility of the new ramp (within dI/dt and d2I/dt2 PC limits)
Timing table of the squeeze (b* levelling mode)
Collimation
Loss maps & ASD simulations over the cycle
TCT operational scenario, e.g. constant in mm at FT vs b*, maybe fine-tuned to minimize the allowed minimum gap of the Roman Pots (within the MP rules).
Optics & OP (OMC, collimation, LBDS,..)
 Is that OK for the commissioning teams? Commissioning strategy: how many optics with sate-of-the-art optics corrections, how many with full validation (LM, ASD tests, etc.), b* stop selections, etc ..
Beam-beam (in collision)
DA, tune scan, MO, Q’,… If applicable refine the parametric X-angle functions in b*-levelling mode… but it should work without need of further iteration.
Pacmann effect on orbit, b-beating, etc. at 1.8e11 p/b
Collective effects
Confirm the beam stability over the full cycle (including low-mu Runs), and decide on the octupole polarity
…
Next steps

## Slide 19: Back-up

## Slide 20
DA at injection for 1.8e11 p/b (keeping the 2017/2018 injection optics)
Even with huge margin taken in emittance (ge=2.5 mm)
the DA killer remains the octupole (at Q’=15), not the BBLR
[in terms of tune spread needed for Landau damping: 40 A @ ge=2.5 mm means 55 A @ ge=1.8 mm at ~cst DA in s]

## Slide 21: Some pre-checks to compare tele and anti-tele optics (1/3)
Telescopic EoR optics with r=2.5
Anti-telescopic EoR optics with r=1/2.5
Tune scan comparison at “small” emittance (1.8 mm) [different b* but same norm. X-angle]
/afs/cern.ch/eng/lhc/optics/runII/2018/RunIII_DEV/optics_EoR.madx
/afs/cern.ch/eng/lhc/optics/runII/2018/RunIII_DEV/optics_EoR_antitele.madx

## Slide 22: Some pre-checks to compare tele and anti-tele optics (2/3)
Telescopic EoR optics with r=2.5
Anti-telescopic EoR optics with r=1/2.5
Tune scan comparison at “large” emittance (2.5 mm) [different b* but same norm. X-angle]
/afs/cern.ch/eng/lhc/optics/runII/2018/RunIII_DEV/optics_EoR.madx
/afs/cern.ch/eng/lhc/optics/runII/2018/RunIII_DEV/optics_EoR_antitele.madx

## Slide 23: Some pre-checks to compare tele and anti-tele optics (3/3)
Stability diagram comparison (no BBLR), changing rtele into 1/rtele
N. Mounet
H-plane
H-plane
V-plane
V-plane
MO<0
(-350 A)
MO >0
(+350 A)
Coherent modes
well inside
Coherent modes
inside (with tele-index)

## Slide 24: Best possible performance reach and IT life time (4/4)
Possible running scenarios exist with 27 MGy with round optics (25 MGy with flat optics) after 420 fb-1, offering a possible extension for a 4th year, preferably with flat optics and 500 ++ fb-1
OPTICS | ROUND | FLAT*) | ROUND + 2024 FLAT*) (+2024 ROUND) | FLAT*) + 2024 FLAT*)
MAGNET | PEAK DOSE [MGy] |  |  | 
Integrated lumi [inc. 190 fb-1 from Run I/II] | after 412 fb-1 | after 419 fb-1 | after 520 (518) fb-1 | after 527 fb-1
Q1 IR1 | 21 | 20.5 |  | 
Q1 IR5 | 19 | 18 |  | 
Q2A IR1 | 25.5 | 25 | 32 (32.5) | 31.5
Q2A IR5 | 19.5 | 17 |  | 
Q2B IR1 | 14 | 17.5 |  | 
Q2B IR5 | 26.5 | 21.5 | 31 (34) | 26
Q3 IR1 | 12 | 14 |  | 
Q3 IR5 | 18.5 | 16.5 |  | 
Round optics in 2021 (V/H crossing in IR1/5) with LHCf good X-angle polarity in ATLAS
 Then 2 scenarios for 2022/2023
Round (V/H crossing in IR1/5)
X-angle polarity inversion in ATLAS from 2022 to 2023
Flat (H/V crossing in IR1/5)
X-angle polarity inversion in CMS from 2022 to 2023
Finally 2 possible 2024 extensions
Round optics
Flat optics
F. Cerutti
10th LCR3 meeting
*) CMS IP shift assumed to be corrected for flat optics (i.e. machine perfectly realigned)