## Slide 1: WP4 C-band injector rf system design
Second CompactLight Annual Meeting,
Athens 21-24/01/2020
M. Diomede (INFN-LNF)
on behalf of the WP3 C-band injector working team*
* D. Alesini, A. Vannozzi, G. Muti, F. Cardelli, E. Gazis, E. Trachanas, M. Croia, A. Gallo, M. Diomede, M. Ferrario, C. Vaccarezza, A. Giribono, L. Ficcadenti, J. Scifo, L. Pellegrino, B. Spataro.

## Slide 2
A C-BAND INJECTOR LAYOUT
Considered layout (not in scale)
1.6 cell RF gun operating at 200-240 MV/m cathode peak field
3 C-band TW structures, 2 with solenoids around, operating at 40 MV/m average accelerating gradient (as example, PSI-like structures)
X-band accelerating module
2 m
Gun solenoid
TW structures solenoids
Linearizer (X,Ka?)

## Slide 3
DESIGN CRITERA FOR THE C-BAND GUN
The design and fabrication of the new gun has been driven by the same criteria used in the design of room temperature high gradient X-band structures developed in the last 20 years in the framework of linear collider projects (NLC, JLC and CLIC). There are four main quantities that play a crucial role in the BDR control: the peak electric field, the modified Poynting vector (Sc), the RF pulse length (tp) and the pulsed heating (T). The gun has been designed keeping under control these quantities.
Mode launcher
(with comp. of quad. component)
Standard couplers on the full cell cannot be adopted because of the high pulsed heating due to the high magnetic field on the coupling holes and, therefore, a mode launcher type coupler has been considered. To reduce the dipole and quadrupole field components induced in the mode launcher a modified design of the mode launcher itself will be necessary. Holes on the mode launcher coupler to allow the laser injection will be also implemented.

## Slide 4
C-BAND GUN POWERING SCHEME
KLY
<0.200 s 40 MW
circ
Ecath | 240 MV/m
Δf0- | ≈ 90 MHz
Q0 | 12000
 | 3
Pdiss @240MV/m | 12 MW
 | 69 [MV/mMW0.5]
PIN @240MV/m | 31 MW
T @ 200 ns | <30 oC
RF pulse length | <200 ns
Av diss power | 2000-200 W
Rep. Rate | 1000-100 Hz
Ecath | 240 MV/m
Δf0- | ≈ 90 MHz
Q0 | 12000
 | 3
Pdiss @240MV/m | 12 MW
 | 69 [MV/mMW0.5]
PIN @240MV/m | 31 MW
T @ 200 ns | <30 oC
RF pulse length | <200 ns
Av diss power | 2000-200 W
Rep. Rate | 1000-100 Hz
RF pulses of few tens of MW at 200 ns allow reaching Ecath>200 MV/m.
Because of its higher efficiency, a C-band RF Gun is also suitable for application requiring repetition rates in the 500 Hz ÷ 1 kHz range
Moreover, to feed the SW gun a C-band circulator is necessary to protect the klystron from the power reflections during transients (a commercially available C-band circulator exists and will be purchased from CML to allow the high-power tests).
[1] D. Alesini et al., TUPTS024, IPAC 19

## Slide 5
FULL C-Band gun 2D DESIGN

## Slide 6
FULL C-Band gun 2D DESIGN: RESULTS
fπ | 5712 MHz | 
∆f | 82 MHz | 
¦(Es/Ec)¦ | 0.904 | 
¦Sc¦ | 4.544 W/µm2 | 6.543 W/µm2
Ec/√P | 69 | 
Q0 | 12289 | 
∆T @180 ns | 21 deg | 30 deg
fπ | 5712 MHz | 
∆f | 82 MHz | 
¦(Es/Ec)¦ | 0.904 | 
¦Sc¦ | 4.544 W/µm2 | 6.543 W/µm2
Ec/√P |  | 
Q0 | 12289 | 
∆T @180 ns | 21 deg | 30 deg
(@200 MV/m)
(@240 MV/m)

## Slide 7
3D ELECTROMAGNETIC DESIGN
(@200 MV/m)
(@240 MV/m)
A first version of the mode launcher coupler (w/o quadrupole compensation) has been designed.
The S11 put in evidence the presence of the only two modes.
The position of the coupler can be varied according to the BD/solenoid design.
On axis injection with external mirrors is possible.
BD calculations considering the tail of the electric field into the circular waveguide need to be done
laser
laser

## Slide 8
1 KHz OPERATION
(@200 MV/m)
(@240 MV/m)
Assuming equivalent transients given by solid state modulators similar to that measured on SPARC C-band klystrons (ttrans1.2 s) we obtain:
In this case we reduce the RF pulse but we are dominated by the modulator transients. Looking at the values of the high power C-band klystron Canon (Toshiba) E37212 that are specified for 100 Hz, 50 MW, tRF_MAX=2.5 s, ttrans=2.5 s, we obtain Pcoll_MAX58kW.
Mode launcher case
9 MW

## Slide 9
THERMAL ANALISYS (1 KHz REGIME)
Courtesy
L. Pellegrino
We started a thermo-mechanical analysis to investigate the feasibility of the 1 KHz operation.
We use the ansys code. In the figure a preliminary calculation in the case of a 1 KW dissipated power is shown.

## Slide 10
2 m long sections (PSI-LIKE)
(@200 MV/m)
(@240 MV/m)
RF system | 
Operating frequency [GHz] | 5.712
Klystron pulse length [us] | 3
Klystron peak power (Net) [MW] | 50 (40)
Pulse rate [pps] | 100
Q0 of BOC | 216000
Qe of BOC (optimized) | 24700
Acc. Structure |  | 
Phase advance | 2pi/3 | 
Cell length [mm] | 17.495 | 
Number of cells | 114 | 
Total length [m] | 1.9945 | 
Average iris radius [mm] | 6.6 | 
Tapering angle [deg] | 0.02 | 
Iris radius (first - last) [mm] | 6.945 – 6.255 | 
Shunt imp. [MOhm/m] | 78.5-85 | 
Q | 10209-10170 | 
Group velocity/c [%] | 2-1.4 | 
Filling time [ns] | 403 | 
Repetition rate [Hz] | 100 | 1000
BOC | ON | Bypassed
Kly. Pow./struct. [MW] | 13 | 8
Avg. acc. gradient [MV/m] | 40 | 15.6
100 Hz: 40 MV/m w/ 1 klystron for 3 structures (considered 20 MW per structure).
1 kHz: <20 MV/m w/ 1 klystron for 1 structure (BD check is required).
PRELIMINARY BETTER RESULTS W/ SHORTER STRUCTURES.
Canon E37212

## Slide 11: WP4 Task 1: Layout and optimization of the linac rf system
Second CompactLight Annual Meeting,
Athens 21-24/01/2020
M. Diomede (INFN-LNF)
On behalf of the XLS WP4 Study group @ LNF

## Slide 12
Baseline (1 RF source):
Twin bunches (2-colors)
RF in dual mode
  SXR @250Hz
  HXR @100Hz
Variable pol.
Upgrade-1 (2 RF sources):
RF in dual source (combined)
  SXR @1kHz
  SXR & HXR NOT in parallel
Upgrade-2 (2 RF sources):
RF in dual linac
100 Hz kicker
  SXR & HXR @100Hz
Seeding (self-, external)
Layouts

## Slide 13
Parameter | Value
Frequency [GHz] | 11.9942
Phase advance per cell [rad] | 2/3
Shunt impedance R [MΩ/m] | 90-131
Effective shunt Imp. Rs [M/m] | 387
Group velocity vg [%] | 4.7-1.0
Pout/Pin | 0.215
Filling time [ns] | 144
Number of cells per structure | 108
Unloaded SLED Q-factor Q0 | 180000
External SLED Q-factor QE | 23000
# structures per module Nm | 4
Module active length Lmod [m] | 3.6
Average iris radius <a> | 3.5
Iris radius input-output [mm] | 4.3-2.7
Structure length Ls [m] | 0.9
Accelerating cell length [mm] | 8.332
ACCELERATING STRUCTURE AND MODULE: PARAMETERS
 | Rep. rate [Hz] |  | 
 | 100 | 250 | 1000
Average gradient <G> [MV/m] | 65 | 32 | 30.4
Max klystron available output power [MW] | 50 | 50 | 10
Required input power per module PK [MW] | 39 | 42.5 | 8.5
RF pulse [µs] | 1.5 | 0.15 | 1.5
SLED | ON | OFF | ON
Av. diss. power per structure [kW] | 1 | 0.31 | 2.2
Peak input power per structure [MW] | 68 | 10.6 | 14.8
Av. Input power per structure [MW] | 44 | 10.6 | 9.6
Module energy gain [MeV] | 234 | 115 | 109

## Slide 14
Thermal analysis with CST of the average cell
100 Hz
4 channels
1 kHz
4 channels
1 kHz
8 channels
Collaboration with L. Faillace (INFN)
Water temperature: 30°C
Pdiss=9 W
Pdiss=19 W
Pdiss=19 W

## Slide 15
Short range wakefield with ECHO (EuPRAXIA case)
Wake potential

## Slide 16
Short range wakefield with ECHO (EuPRAXIA case)
Fitted formula
a=3.5mm
A=1.48
s2 =9.948 × 10−5
Wake function

## Slide 18
HIGH REPETITION RATE OPERATION
The high repetition rate operation is limited by two effects:
The average dissipate power in the structure: is someting manageable.
The main limitation for the rep rate increasing comes from the power released on the tube collector which can not exceed a limit value corresponding to the nominal working point (with some margin).
The klystron operational rep rate can be increased at expenses of the saturated RF power (by decreasing the tube HV) and/or the pulse duration
Klystron efficiency vs. power derating
The amount of rep rate increase obtainable by reducing the HV and the RF saturation power is limited by the tube efficiency decrease.
The amount of rep rate increase obtained by reducing the pulse duration depends very much on the actual value of the dead time τtrans, which is a characteristics of the modulator.

## Slide 19
Accelerating gradient and Linac energy reduced by a factor 2 @ 250 Hz rep rate;
The SLED has to be bypassed;
Klystron operated always at its nominal working point (good!);
Max rep rate very much dependent on modulator rise/fall times τtrans
HIGH REP. RATE 1st SCENARIO: pulse shortening with high peak power klystrons

## Slide 20
1 kHz rep rate capability, with linac energy up to ≈ 47% of the max value;
R&D activity in progress @CANON and CPI on high rep. rate klystrons towards 10 MW, 1.5 µs, 1 kHz
10 MW, 1.5 µs, 1 kHz, operation probably possible in the near future
Reference RF source CANON Commercially available
HIGH REP. RATE 2nd SCENARIO:
LOW POWER HIGH REP. RATE KLYSTRONS

## Slide 21
Switching or combining 2 sources would preserve high gradient at low rep rate;
If source combination is possible, gradients > 30 MV/m available at rep rates ≤ 250 Hz;
10 MW, 1.5 µs, 1 kHz, operation probably possible in the near future
Reference RF source CANON
HIGH REP. RATE 3rd SCENARIO:
COMBINATION OF HIGH REP. RATE AND LOW REP. RATE KLYSTRONS

## Slide 22
1st OPTION: DUAL MODE
Parameter | LINAC 1 | LINAC 2 | TOTAL
Number of structures | 32 | 60 | 92
Number of modules | 8 | 15 | 23
Number of klystrons | 8 (CPI) | 15 (CPI) | 23
Linac active length [m] | 29 | 54 | 83
Rep. rate [Hz] | 100 (250) |  | 
<Eacc> per struct. [MV/m] | 65 (32) |  | 
Energy gain per module [MeV] | 234 (115) |  | 
Max. Energy gain [MeV] | 1872 (921) | 3510 (1728) | 5382 (2649)
Single rf source
single linac run in two operating modes
Cheapest
Limited increase in repetition rate (SLED by-passed)
Linac optics needs to operate at two gradient

## Slide 23
2nd OPTION: DUAL LINAC
Parameter | LINAC 1 | LINAC 2 | TOTAL
Number of structures | 68 | 60 | 128
Number of modules | 17 | 15 | 32
Number of klystrons | 17 (HRR) | 15 (CPI) | 32
Linac active length [m] | 61 | 54 | 137
<Eacc> per struct. [MV/m] | 30.4 | 65 | -
Rep. rate [Hz] | 1000 | 100 | -
Energy gain per module [MeV] | 109 | 234 | -
Max. Energy gain [MeV] | 1853 | 3510 | 5363
two distinct linacs with different rf sources
SXR@ 1 kHz
HXR@ 100 Hz
SXR@ 900 Hz and HXR@ 100 Hz running in parallel

## Slide 24
3rd OPTION: DUAL SOURCE
Parameter | LINAC
Number of structures | 92
Number of modules | 23
Number of klystrons | 23 (HRR) + 23 (CPI)
Linac active length [m] | 83
<Eacc> per struct. [MV/m] | 30.4 (@1 kHz), 65 (@ 100 Hz)
Rep. rate [Hz] | 100-1000
Energy gain per module [MeV] | 109 (@1 kHz), 234 (@ 100 Hz)
Max. Energy gain [MeV] | 2507 (@1 kHz), 5382 (@ 100 Hz)
Single linac with two sources
SXR@ 1 kHz
HXR@ 100 Hz
SXR and HXR CANNOT run in parallel

## Slide 25
ACCELERATING STRUCTURE AND MODULE: PARAMETERS

## Slide 26
Short range wakefield with ECHO (EuPRAXIA case)
Wake potential
Wake function

## Slide 27
Short range wakefield with ECHO (EuPRAXIA case)
Fitted formula
a=3.5mm
A=1.48
s2 =9.948 × 10−5