## Slide 1: BSM search in rare muon decay: the MEG II experiment
Kei Ieki
on behalf of MEG II collaboration
JSPS
Core-to-Core Program

## Slide 2: Why ?
MEG
MEG II
DeeMe
COMET-I
Mu3e-I
Mu3e-II
COMET-II
Mu2e
μNeN
BSM prediction
(SUSY-seesaw etc.)
New physics predicts Br(~ , which is close to the current upper limit
Because it is a good probe of BSM!
Flavor violation is observed in neutrinos. There is no fundamental rule which prohibits flavor violation.

## Slide 3: Muon as a probe of BSM
Other golden modes can be used
for model discrimination
Correlation with muon g-2 also suggests existence of
G. Isidori, F. Mesia, P. Paradisi, D. Temes, Phys. Rev. D 75 (2007) 115019.
(B-field)
Correlation between and g-2

## Slide 4: MEG II experiment
e
Utilizes world’s highest intensity continuous beam @ PSI 
( 2.3 from MEG)
Goal: Br sensitivity upgrade from MEG
Accidental BG (∝beam rate2) limits the sensitivity  Improve detector resolutions by x2 (energy, timing, direction)
PSI proton cyclotron
MEG detector

## Slide 5: Signal and BG
e
Signal
Accidental BG
from
from
or
52.8MeV
Same timing
Back to back
e
Good energy, time and position resolutions are required

## Slide 6: Detector upgrades from MEG
upgrade

## Slide 7: drift chamber
upgrade
16 modules
single volume
Measures momentum and direction
Resolution is limited by multiple scattering  extremely low material is used
High rate BG at low momentum  suppressed by gradient B-field

## Slide 8: drift chamber
1728 anode wires in 6-8mm interval, 9 layers  many hits per track  good resolution ( ~ 130 keV, ~ 5 mrad expected)
No extra material between timing counter  efficiency 2
Cylindrical stereo wire chamber (stereo angle: )
Low mass ( X0 along track) low multiple scattering  good resolution Gas: He(90%)+iC4H10(10%), Wire: 20 W(Au) for anode, 40 or 50 Al(Ag) for cathode
Example of signal

## Slide 9: timing counter
upgrade
Measures timing
Fast plastic scintillators
15 bars x2
256 counters x2

## Slide 10: timing counter
Fast plastic scintillator + SiPM
Increased segmentation  many hits per track
 good resolution
= 38.5 ps already achieved
6 SiPMs series connection
~8 for signal
series connection makes the waveform sharp
To improve time resolution:
- Use many SiPMs  high light yield
- Connect them in series  less readout ch, short risetime

## Slide 11: LXe detector
upgrade
Measures energy, timing, position
900l liquid xenon
2-inch PMTs
15mm SiPMs

## Slide 12: LXe detector
Uniformity of sensor coverage and granularity improved!  Energy and position resolution improves by factor of 2 in MC
Energy resolution
2%  0.7~1.5%
Example of BG event in beam run
(part of the detector was readout)

## Slide 13: BG tagging detector
upgrade
New detector for tagging BG
Detects low energy from
Plastic scintillator (timing) + LYSO crystals (energy) + SiPMs
All events
High energy removed
time coincidence
BG
successfully identified

## Slide 14: Trigger & DAQ
New DAQ + trigger system
developed by PSI+INFN: WaveDAQ
- Waveform (1-2 GHz) readout of ~9000 channels with DRS chip
(Domino Ring Sampler)
- Trigger is integrated  Reduced rack space,
Sophisticated trigger (High energy , coincidence with back-to-back)
- Amplifier, shaper and HV supply for SiPMs
WaveDREAM board
Mass production in this year

## Slide 15: Status in 2020
Overall status
- Detector construction is finished, commissioning is ongoing.
- Timing counter and BG tag detector are ready for physics run.
Pilot run in the end of 2020
- Establish stable operation of drift chamber - LXe detector resolution measurement with ~55 MeV from from beam (
Commissioning of drift chamber and LXe detector is ongoing
- For drift chamber, we successfully removed broken/potentially bad wires (due to corrosion). Anomalous current was observed  under investigation
- In LXe detector, photon detection efficiency of SiPMs is found to be reduced (~0.08% per 1-hour beam) likely due to surface damage by VUV photons. Annealing (heating) was found to be effective to recover it.
Corona discharge in drift chamber
Recovery of SiPM detection efficiency

## Slide 16: Summary
is a good probe for new physics. e.g. SUSY-seesaw: Br( ~ O( MEG II goal: Br( < 6
MEG II experiment utilizes world’s most intense continuous beam @ PSI.
Detectors are constructed and commissioning is ongoing.
Commissioning runs with beam will continue in 2020. Physics run will follow soon after.

## Slide 17: Backup slides

## Slide 18: PDE degradation problem
Mean PDE vs. time
Decrease of MPPC PDE was observed while commissioning with from .
 surface damage by VUV light from LXe scintillation?
Accumulation of holes near SiO2-Si interface
 reduction of carrier collection efficiency
Similar phenomena is known for UV photo diode.
2017
2018
2019
~1.31012 photons / day / MPPC
SiO2
Si
VUV photons
()

## Slide 19: SiPM annealing
2016.7.7
Reverse bias, room light
Vover~7V, ~11mA
Accumulated charges can be removed by annealing (heating).
 Generate Joule heat by applying reverse bias on MPPC under light (We need special HV source to apply high current.)
We should not exceed
temperature limits:
MPPC 100 deg.
PCB 120 deg.
CFRP 45 deg.
Glue 65 deg.
CFRP
PCB
MPPC