## Slide 1
BASE
Annual Report 2019
Plans for the 2020 run
Future Proposal
SPSC – CERN/Switzerland – 2020 / 01 / 21
Stefan Ulmer
RIKEN,
Chief Scientist, Fundamental Symmetries Laboratory, RIKEN
Spokesperson BASE collaboration, CERN
2019 / 01 / 21

## Slide 2: BASE – Collaboration
Mainz: Measurement of the magnetic moment of the proton, implementation of new technologies (laser cooling and BASE-STEP).
CERN-AD: Measurement of the magnetic moment of the antiproton and proton/antiproton q/m ratio
Hannover/PTB: QLEDS-laser cooling project, new technologies
C. Smorra et al., EPJ-Special Topics, The BASE Experiment, (2015)
Institutes: RIKEN, MPIK, CERN, University of Mainz, Tokyo University, GSI Darmstadt, University of Hannover, PTB Braunschweig

## Slide 3
Precise CPT test with baryons
S. Ulmer, et al., Nature 524, 196 (2015)
To be improved by another factor of 10 to 100
Rexp,c = 1.001 089 218 755 (64) (26)
Observation of spin flips with
a single trapped proton
Application of the double
Penning-trap technique
S. Ulmer, et al., PRL 106, 253001 (2011)
A. Mooser, et al., PLB 723, 78 (2013)
Reservoir trap for antiprotons
C. Smorra, et al., Int. Journ. Mass Spec. 389, 10 (2015).
Idea: Enable operation with antiprotons independent of accelerator run times.
Most precise antiproton/proton
g-factor measurments
A. Mooser, et al., PRL 110, (2013)
Partly comparable work by J. DiSciacca, G. Gabrielse et al.. (ATRAP/TRAP collaboration)
C. Smorra et al., Nature 550, 371 (2017)
g/2 = 2.792 847 344 1 (42)
3000-fold improvement compared to previous measurement
G. Schneider et al., Science 358, 1081 (2017).
g/2 = 2.792 847 344 62 (82)
Achievements since 2011
Constraining Antiproton Lifetime
Dark Matter / Antimatter Interaction
C. Smorra et al., Nature 575, 310 (2019)
30-fold improvement compared to previous measurement
Proton:
Antiproton:
First limits on dark matter / antimatter coupling, orders of magnitudes more stringent than astrophysics limits.
S. Sellner et al., NJPhys. 19, 083023 (2017)
30-fold improved constraints on directly measured antiproton lifetime

## Slide 4: This Talk
M. J. Borchert et al., Measurement of Ultralow Heating Rates of a Single Antiproton in a Cryogenic Penning Trap, Phys Rev. Lett. 122, 043201 (2019).
J. A. Devlin et al., Superconducting Solenoid System with Adjustable Shielding Factor for Precision Measurements of the Properties of the Antiproton, Phys. Rev. Appl. 12, 044012 (2019).
C. Smorra, et al., Direct limits on the interaction of antiprotons with axion-like dark matter, Nature 575, 310 (2019).
Progress and developments during the 2019 run
  Improved charge-to-mass ratio measurement
  Implementation of phase-sensitive frequency measurements
BASE future proposal
  Improved magnetic moment measurement
  Implementation of a transportable trap for antiprotons
  Installation of an offline laboratory

## Slide 5: Timeline 2019
01
02
03
04
05
06
07
08
09
10
11
12
Peak ratio measurements and systematic studies
dip ratio measurements
Installation of new experiment frame
Dispersive frequency measurements
Antiproton lifetime measurements
Phase methods with protons
Development of upgrades for R1/LS2
Data analysis of Q/M ratio and lifetime
Time-base data analysis of g-factor
Characterization of Shielding Coils

## Slide 6: Main Tool: Penning Trap
axial confinement:
radial confinement:
Cyclotron Frequency
Axial | 
Magnetron | 
Modified Cyclotron | 
Invariance-Relation
Axial Motion
Modified Cyclotron Motion
Magnetron Motion
Cyclotron frequency connects measurable quantity to fundamental properties of trapped charged particle

## Slide 7: Measurements in Penning traps
Cyclotron Motion
Larmor Precession
Determinations of the q/m ratio and g-factor reduce to measurements of frequency ratios -> in principle very simple experiments –> full control, (almost) no theoretical corrections required.
g: mag. Moment in units of
nuclear magneton
S. Ulmer, A. Mooser et al. PRL 106, 253001 (2011)
S. Ulmer, A. Mooser et al. PRL 107, 103002 (2011)
simple
difficult
FFT
Amp
Amp
Rp
Lp
Cp
Resonator
Low Noise Amp
FFT
Image Current Detection
currents: 1 fA
Single Antiproton Signal

## Slide 8: Experiment

## Slide 9: The BASE Trap System
RT
PT
CT
AT
HV Electrodes
Degrader
Spin flip coil
Electron gun
Pinbase
Access to beamline
Particles not continuously available
Trap for efficient cyclotron cooling
S. Ulmer et al., BASE TDR, CDS (2013).
pbar lifetime > 11 a

## Slide 10: A special place (in the universe?) – the BASE trap
We have
  A vacuum of 5e-19 mbars
    comparable to pressures in the interstellar medium
  Antiproton storage times of several 10 years.
  Not more than 3000 atoms in a vacuum volume of 0.5l
  Order 100 to 1000 trapped antiprotons
  A local inversion of the baryon asymmetry
BASE ANTIMATTER INVERSION | 
local volume | 0.00013 m3
Baryons in local trap volume | 1.65*10-7
Antibaryon in local trap volume | 100
Antibaryon/Baryon Ratio | 5.9*108
Ratio Inversion | 3.8*1012
With this instrument: Investigate properties of antimatter very precisely

## Slide 11: Limits on Antiproton/Dark Matter Coupling
the axion
  introduced to solve the strong CP problem (Peccei/Quinn)
  candidate for dark matter (QCD-axion and other hypothetical axion-like particles)
Not understood why they survived
Know it exists (), but microscopic properties have yet to be understood.
BASE study: Could the appearance of matter/disappearance of antimatter and dark matter be in any sense related?
Need a model which allows us to study this question
Gravitational lensing
Galactic rotation
Structures in CMWB

## Slide 12: Axion Wind Model
First of all: a quick comment on axion / fermion coupling
J. Kim, G. Carosi, https://arxiv.org/pdf/0807.3125.pdf
A very “simplistic” translation of this “derivative interaction”: the axion dissociates to photons which interact with SM-particles.
Cold dark matter – axion like particles – are gravitationally bound to galaxies.
They produce an “oscillating background”, comparable to diffuse light, which oscillates at a frequency
This type of interaction would look like a “pseudo”-magnetic field which leads to frequency modulations in the antiproton Larmor frequency at the axion frequency.

## Slide 13: Illustration of the concept:
Antiproton/axion coupling would induce a frequency modulation
of the measured Larmor frequency.
Analysis: Compare hypotheses H0 – no oscillation / H1 – oscillation at certain g-amplitude
Define test statistic based on Nyman/Pearson Lemma (likelihood ratio test)
Derive constraints based on CLs method ((p-value)/(power of test))
Most important is still that we have a measurement

## Slide 14: Limits from SN-1987A
Bremsstrahlung type axion emission in SN
SN-1987A
SN-1987A-remnant
Addition: We derive limits on six previously unconstrained coefficients of the Standard Model Extension (Lorentz Violation for antimatter)
Coefficient | Limit
 | GeV
 | GeV
- | /GeV
 | /GeV
 | /GeV
 | /GeV
Coefficient | Limit

## Slide 15
Extract antiprotons and H- ions, compare cyclotron frequencies
antiproton
H- ion
Rtheo = 1.001 089 218 754 2(2)
Park
electrode
Park
electrode
Precision
trap
Reservoir
trap
Measure &
Measure &
inspired by G. Gabriesle et al., PRL 82, 3199 (1999).
Charge to Mass Ratio Measurement
6521 frequency ratios
Notes: Gabrielse idea to use H- ions

## Slide 16: Recent Progress
100mHz
55mHz
2014 measurement
Jan 2018
Better stabilisation of cryoliquid pressure, temperature improves magnetic stability
Mechanical upgrade more stable and lower heat load means fewer vibrations
peak measurement technique
2.5 Hz
frequency (Hz)
signal (a. lin. u.)
25 mHz
New magnetic shielding system
J. A. B.-Harrington et al.
M. J. Borchert et al.
Next step:

## Slide 17: Implementation of Phase Sensitive Detection
Compared to dip method: Not limited by power supply noise
Compared to peak method: Reduced systematics, reduced noise, faster measurement cycles.
M. Borchert
Hannover/RIKEN
J. Devlin
CERN/RIKEN
Reached in the best cases frequency scatters on the order of 330 p.p.t. per shot
2014 BASE Sideband
2019 BASE Sideband
2019 BASE Phase
Completed campaigns
Phase methods
development

## Slide 18: Summary of Achievements / Request
2014 measurement
2018 measurement
Current status with AD off
Noise limit with AD on
Final resolution: 15 p.p.t. to 20 p.p.t.
Goal of next measurement should be at the level of 1 p.p.t. to 5 p.p.t.
Given the AD noise level of 600 p.p.t. this will require measurement time of years
Strategy to only work during accelerator shutdown is not attractive and not very goal oriented.
We request an offline-laboratory at CERN, which will be supplied with antiprotons from the AD, using a transportable trap.
current sideband limit

## Slide 19: Laboratory Requirements
Wish list – Magnetically Calm
  Access to a bridge crane with a lifting capability of at least 2 T, better 5 T.
  Access to liguid nitrogen.
  Access to liquid helium and helium recovery line.
  Power supplies comparable to those in the current BASE experiment zone.
  The option to connect to CERN’s uninterruptable power supply.
  A well deﬁned, calm, isolated mains ground.
  The laboratory should have at least the size of the current BASE experiment zone (at least 40 m2, wish 80 m2).

## Slide 20: Transportable Trap – BASE STEP
All these methods have already been demonstrated by
Christian Smorra
1.8 m
Magnet cryostat
electronics
Differential pumping section
Portable reservoir trap with 10000 antiprotons
non-destructive extraction
Emergency power connection desired
„Compact“ design, weight below 1000 kg
2020
2021
2022
2023
April 2020:
Project start
18 month
Magnet procurement
Commissioning in Mainz
12 month
April 2022:
Starting at CERN
Commissioning at CERN
6 month
April 2023:
Online Operation
Antiproton operation
BASE magnetic moment measurement
30 month
Yet open: Extraction mechanism (under development at Mainz)
Regarding the implementation of the instrument into the AD hall we need advice by the SPSC.

## Slide 21: Possible Locations for BASE-STEP
ATRAP I zone. Offered as an option in a discussion with CERN’s engineering department.
STEP could be installed in front of BASE
Will interfere with BASE experiments
Option 2 – BASE-STEP in independent experiment zone is certainly very attractive.

## Slide 22: Flash: IUPAP Prize for AMO Physics 2019
For their outstanding contribution to determine the most precise comparison of the proton-to-antiproton charge-to-mass ratios and the most precise comparison of the proton and antiproton magnetic moments, constituting two different world-record tests of the fundamental charge, parity, and time reversal symmetry in these systems
Christian Smorra
Andreas Mooser

## Slide 23: The Magnetic Moment of the Antiproton
first measurement more precise for antimatter than for matter...
A. Mooser et al., Nature 509, 596 (2014)
C. Smorra et al., Nature 550, 371 (2017)
G. Schneider et al., Science 358, 1081 (2017)
updated shortly after antiproton measurement.

## Slide 24: BASE – «Short Term» Goal – Magnetic Moment
Drive:
CERN 2017
Mainz 2017
CERN 2017
CERN 2016
B-field:
CERN
Mainz
TOTAL:
With the current magnet at CERN and the implemented magnetic shielding system, regardless whether AD is on or off, we could reach Dg/g=0.8 p.p.b. -> Improved measurement 80 p.p.t. to 200 p.p.t.
Indicates a possible width of 650 p.p.t.

## Slide 25: Error Budgets of previous measurements
Estimate on the effect of fitting was too conservative, can be done much better (10 times)
Direct methods (phase) will suppress this by factor of 50
Much better methods available to determine axial temperature
better methods
better methods
12 p.p.t.
4 p.p.t.

## Slide 26: …if we do all the other homework…
Improved Magnet Stabilization
More homogeneous trap center
Reduced noise in AT / better cryo-electronics.
Local shim coils
Cooling trap with improved cyclotron cooler for fast sub-thermal cooling
Improved axial detectors
Working ELENA interface
Two particle method planned – background B / double trap

## Slide 27: Cooling trap
Smaller trap: Improves particle / detector coupling by a factor of 10
Superimposed magnetic bottle with temperature resolution of 8Hz/K makes real-time cooling possible.
Improved cyclotron detector: Higher Q and lower temperature (3K)
Sub-thermal cooling cycles: minutes compared to hours seem possible.
cold particle (50mK)
hot particle (1K)
high-fidelity spin state resolution
fidelity at 65%, not useful for measurements

## Slide 28: Planned experiment scheme
Cooling trap assisted two particle measurement of the antiproton g-factor
g-factor particle
Transport
Transport
Cooling trap
Sub thermal cooling
Key: Larmor and cyclotron frequency measured SIMULTANEOUSLY in a more homogeneous magnetic field. Two particle systematics eliminated.
Confident that we will be able to achieve our target precision.

## Slide 29: Planned Developments
Current antiproton magnetic moment measurements are limited by particle preparation time and particle mode temperature
Expect: With traditional methods another 50-fold improvement is possible, afterwards: limit of traditional methods will be reached!
Sympathetic Cooling of Antiprotons
Couple protons/antiprotons sympathetically to laser cooled 9Be+ ions and imprint Doppler temperatures to the antiproton
Publication: K. R. Brown, C. Ospelkaus, Y. Colombe, A. C. Wilson, D. Leibfried, D. J. Wineland, Nature 471, 196 (2011).
Was demonstrated for 9Be+ ions in Paul traps – implement same in Penning traps
Chart: Current Time Budget
| Cooling | Maintenance | Measurement | Shuttling
Time Budget Double Trap | 80 | 5 | 10 | 5
Chart: Laser Time Budget
| Cooling | Maintenance | Measurement | Shuttling
Time Budget Double Trap | 5 | 5 | 85 | 5
Effort at University of Hannover and PTB
Recent dramatic progress: Detection of a single laser cooled 9Be+ ion, in a Penning trap system which is fully compatible with the BASE trap system at CERN
M. Niemann, J. M. Cornejo, C. Ospelkaus et al.
>100-fold improved antiproton cooling time seems to be in reach
Transportable Antiproton Traps
Idea:
Move antiprotons into precision laboratory with magnetically calm environment for experiments with much higher precision
C. Smorra, S. Ulmer, et al.

## Slide 30: Possible Timeline
antiproton Q/M

## Slide 31: Scenarios…
confident that we will be able to measure the antiproton magnetic moment to order 100 p.p.t. precision.
Proton/Antiproton charge-to-mass ratio measurements with different systematic effects. Maybe slightly more precise…
Currently no perspective to further improve these values in the AD hall.
…without the BASE offline lab…
…with the BASE offline lab…
…no obvious limits regarding fractional precision, sub-p.p.t. measurements will become possible.
Many new technologies involved, transport trap, laser cooling, …additional «classical Penning trap measurements possible»… (proton mass, electron mass, etc…)
Sky is the limit…:-)

## Slide 32: Flash – Center for Time, Constants, and Fundamental Symmetries
Inauguration
Combine precision traps, clocks and lasers to challenge the Standard Model at the low energy frontier
7 500 000,- over five years
PI’s
Blaum
Ulmer
Peik
Katori
Pfeiffer
Crespo
Schmidt
Udem
Hänsch

## Slide 33: Summary and Outlook
2019 Run: Q/M measurement / Lifetime measurement / Improved experiment stability / implemented phase methods
Publications: Lowest heating rates in traps / better magnetic shielding / direct constraints on antimatter-dark matter coupling.
Future program: 100 p.p.t. measurement of the antiproton magnetic moment, offline laboratory, transportable trap system.
BASE 2016
BASE 2017

## Slide 34
C. Smorra
RIKEN
S. Ulmer RIKEN
Thanks for your attention!
M. Borchert
Hannover/RIKEN
J. Harrington
MPIK/RIKEN
K. Blaum, Y. Matsuda,
C. Ospelkaus, W. Quint,
J. Walz, Y. Yamazaki
M. Bohman
RIKEN/MPIK
M. Wiesinger
RIKEN/MPIK
J. Devlin
RIKEN
S. Gavranovic
Mainz
E. Wursten
CERN / RIKEN
S. Erlewein
MPIK/RIKEN
M. Fleck
RIKEN/U. Tokyo
M. Sato
RIKEN/U. Tokyo
D. Popper
Mainz

## Slide 35: THANKS Tommy Eriksson…
…for 7 fantastic years of AD physics
…we wish you a happy retirement!!!

## Slide 36: Single Trap – Double Trap – Triple Trap
single-trap method
multi-trap method
!!! measured !!!
!!! measured !!!
Chart: 
| Cooling | Maintenance | Measurement | Shuttling
Time Budget Double Trap | 80 | 5 | 10 | 5
Chart: Time Budget Two Particle
| Cooling | Maintenance | Measurement | Shuttling
Time Budget Double Trap | 20 | 5 | 70 | 5
two years compared to two months…

## Slide 37: Limits on Exotic Physics – ONE example
Test the Standard Model (CPT invariance) by comparing the fundamental properties of protons and antiprotons with high precision
sensitive: comparisons of particle/antiparticle magnetic moments in traps
Dirac equation
CPT-odd modifications
++
Pseudo-magnetic field, with different coupling to matter and antimatter, respectively
V. A. Kostelecky, N. Russell, 0801.0287v10 (2017).
Would correspond to the discovery of a boson field which exclusively couples to antimatter.