## Slide 1: Beam-Gas Curtain (BGC) monitor for the Hollow e-lens
Ray VENESS for the BGC collaboration
e-Beam meeting, 15th Jan 2020

## Slide 2: Contents
Brief introduction to the principles
BGC collaboration
Key experimental and simulation results
  Experiments with electrons
  Experiments with protons
Instrument design
  Gas jet simulations
  Synchrotron radiation background
Next steps
Summary

## Slide 3: Beam-Gas Curtain: Principles
The challenge:
On-line monitoring of co-axial proton (blue) and electron (orange) beams in a hollow e-lens configuration (ie., in the presence of a strong solenoid magnetic field and with limited available space)

## Slide 4: Beam-Gas Curtain: Principles
Laminar, supersonic gas ‘curtain’ traverses the beams
Gas jet atoms or molecules are excited by beam interactions and emit photons (Beam Induced Florescence or ‘BIF’)
Key parameters influencing BIF are beam intensities, gas jet density and thickness, beam-gas cross section. The cross section is a function of gas species, particle type and energy. In addition, a spectral range of different florescence transitions are excited depending on gas species

## Slide 5: Beam-Gas Curtain: Principles
The light emitted from the BIF is imaged with an ex-vaccua optical system consisting of lens, image intensifier and CCD camera.

## Slide 6: Beam-Gas Curtain: Principles
Eliptical image of two beams on the ‘virtual screen’
True 2D beam image seen by the camera when viewed at 90° to the beam axis

## Slide 7: The BGC collaboration
Cockcroft institute/Liverpool Uni. (C.Welsch et al.)
  Expertise in gas jet diagnostics, experiment and theory
    Full instrument set-ups with 5 keV/650 uA electron gun and diagnostics
  BGC instrument developer and supplier
    HL-UK funding for gas jet 2016-2020
    HL-UK phase 2 funding just approved for 100% in-kind supply of the final instruments for HL
GSI, Darmstadt (P.Forck et al.)
  Expertise in optics and fluorescence simulations and experiment for diagnostics
    Fluorescence measurements with 13.8 MeV protons at TU Munchen
CERN
  Project management, engineering design, integration
  Expertise in Monte-Carlo simulations for gas and SR
  Expertise and experiments at close to nominal conditions
    LHC background gas fluorescence measurements at 450 GeV and 7 TeV for p+ and ions
    HEL test stand with high-intensity 10 keV electrons (Summer 2020)
BGC on INDICO at https://indico.cern.ch/category/9896/

## Slide 8: Expected signal integration times for electron and proton beam profiles
From: Development of a beam-gas curtain profile monitor for the high luminosity upgrade of the LHC. R.Veness et al. IBIC 2018

## Slide 9: Experiments with a 650 uA electron beam using the prototype at the Cockcroft Institute
HIPACE 300L/S
Turbo-molecular pump
HIPACE 700L/S
Turbo-molecular pump
Nozzle Chamber
Skimmer Assembly
Gas Separator
Skimmer Chamber
Imaging System
Interaction Chamber
Moveable Gauge Chamber
Dump Chamber
Third Skimmer
Courtesy A. Salehilashkajani, H.Zhang, C.Welsch

## Slide 10: Typical BIF image from a nitrogen jet
Integration time : 400 S
Calibration = 0.0147mm/pixel
FWHM = 1.2mm
FWHM = 1.2mm
Integration time : 4 S
Calibration = 0.147mm/pixel
Filter used for Nitrogen : 391 +/- 3nm, HW : 10 +/- 2nm
Number of photons per second from the jet: ~ 17
Electron beam signal is visible in just 4seconds via binning.
Gas jet
Electron beam
z
Integration time for the picture below : 400 S
Courtesy A. Salehilashkajani, H.Zhang, C.Welsch
Notes: Check fitlers

## Slide 11: Theoretical Photon Numbers vs Experimental
Emitter | Photon Number/s (LHC conditions) | Expected Photon Number/s (Lab conditions) | Experimental Photon Number per second
N2+ | 3.4E6 | 2.4E1 | 17
Ne | 2.5E4 | 1.76 | 1.6
Ar (750 & 751.5) | 2.9E4 | 1.17 | -
Ar+ ( 476) | 2.3E4 | 1 | 1.3
Ar+ (Broadband) | N/A | N/A | 4
LHC Conditions :
Cross sections calculated at 10KeV
Gas jet density assumed to be 2.5E16
Current assumed to be 5A
Lab Conditions :
Cross sections calculated at 5KeV (Assuming Linearity)
Gas jet density :
  Nitrogen: 7E14/m^3
  Argon: 4E15/m^3
  Neon: 6.5e15/m^3
Current assumed to be 0.65mA
Courtesy A. Salehilashkajani, H.Zhang, C.Welsch

## Slide 12
Courtesy S.Mazzoni, LHC Beam size review, Oct. 2019

## Slide 13
Courtesy S.Mazzoni, LHC Beam size review, Oct. 2019

## Slide 14
Courtesy S.Mazzoni, LHC Beam size review, Oct. 2019

## Slide 15
Courtesy S.Mazzoni, LHC Beam size review, Oct. 2019

## Slide 16
Courtesy S.Mazzoni, LHC Beam size review, Oct. 2019
Alignment of optics vs. beam
SR background in LHC
Beam-gas background in LHC
Data analysis and background subtraction

## Slide 17
Setup at TANDEM TU München
Advantage: Some 100 nA dc beam,
some days exclusive beam time
& protons 13.8 MeV
Blue underlay:
Measurement and statements from TU München

## Slide 18
Neon Spectra with Proton Impact at 14 MeV
Result for cross section:
Ne & low pressure p < 10-3 mbar:
 is constant
i.e. reflects beam profile
Absolute systematic error  sys = 50 %
Estimation of cross section for neutral Ne:
Proton p(14MeV) = 4  10-21 cm2
Energy loss from 14 MeV to 7 TeV by factor 0.1
 Bethe-Bloch scaling p(7TeV) = 0.1  p(14MeV) = 4.0  10-22 cm2
 Bethe-Born scaling p(7TeV) = 0.06  p(14MeV) = 2.3  10-22 cm2
Serban’s estimation p(7TeV) = 4.710-22 cm2  factor 2 too small (1.1 for B-Bloch)
(scaling from S8+ factor 6 too large)
Absolute value of fluorescence cross-section at LHC energies

## Slide 19: Full prototype Instrument LHC integration
Ex-vacua optics
Gas jet generation
Interaction chamber
Gas exhaust

## Slide 20: Gas jet simulations using MolFlow Code
Images courtesy of M.Ady/TE-VSC

## Slide 21: Gas injection design
Retractable target for optics

## Slide 22: Simulations for synchrotron radiation background used to design the interaction chamber
IP4
D4/D3 aperture separator magnets
BGC
X
S
Arcs
Arcs
Simulation courtesy of M.Ady/TE-VSC

## Slide 23
 | Degreased no coating | NEG | Amorphous carbon | LESS (Dundee) | Multilayer sputtering (Polyteknik)
 | ≈ 85% | ≈ 45% | ≈ 13% | ≈ 2% | ≈ 0.2%
 | ≈ 56% | ≈ 45% | ≈ 14% | ≈ 2% | ≈ 0.2%
Copper
Steel
Reflectivity at neon wavelength 584nm
Images: Johanna Glutting/BE-BI

## Slide 24: Prototype Interaction Chamber for LHC installation in LS2
This is the first stage of the LHC installation, planned for March 2020
It can be used in the first year of run 3 to continue to background gas fluorescence measurements
These measurements will benefit from the improved, blackened chambers and new optics design
Instrument can be completely isolated from the LHC with valves to allow for staged installation and operation

## Slide 25: LHC-BGC experimental roadmap
2019
2020
2021
2023
2022
Install the prototype interaction chamber in the LHC
Long shutdown 2
YETS
YETS
LS3
Transport prototype instrument from HEL stand to LHC
prototype commissioning & experimental programme in the LHC
Install prototype optics on LHC interaction chamber
Background gas tests in LHC
Prototype instrument testing on HEL e- stand

## Slide 26: LHC status
Interaction chamber under final preparation for installation from March 2020
Gas rack installed and piping installation planned
Cables installed for the full prototype instrument and vacuum system in LSS4L

## Slide 27: Current version of BGC integration in the HEL, LHC4L

## Slide 28: Summary
A beam-gas curtain instrument is being designed as the baseline monitor for overlap and beam(s) profile for the HEL
  Recently confirmed as a fully in-kind contribution as part of HL-UK2
A collaborative experimental programme is well developed to validate the design
  Parameters for integration times for electrons and protons
  Optimisation of the gas curtain density and gas selection
Further experiments are being prepared to test instrument performance for nominal beam conditions
  HEL test stand for electron profiles
  LHC prototype in background gas fluorescence mode
  Full LHC prototype for 7 TeV proton profiles

## Slide 29: Thanks for your attention

## Slide 30
Fluorescence of different gases
F. Becker, Ph.D. thesis, T.U. Darmstadt, Germany, 2009
Several Ne+ UV lines mainly corresponding to different [2s22p4(3P)]3p → 3s transitions with life times below 10 ns.
The strong UV/blue lines correspond to the B2Σu+ → X2Σg+ electronic transition band of N2+, life times are of about 60 ns.
Several Ne yellow/red lines mainly corresponding to different [2s22p5(2P)]3p → 3s transitions with life times of about 20 ns.
λ [nm]
Strongest emission from Ar+ blue/green lines mainly corresponding to different [3s23p4(3P)]4p → 4s transitions with life times of 10-20 ns.
Courtesy P.Forck/GSI
Fluorescence cross-section
Emission from ion or neutral?
Emission lifetime?
Photocathode efficiency?
Pumped by NEG surfaces or not?

## Slide 31: BGC principle
HEL schematic representation, courtesy of Johanna Glutting