## Slide 2
Beam phase detection
17/12/2019
H. Damerau, N. Pittet
Meeting on PS LLRF developments

## Slide 3
Overview
To and from10/20/40/80/200 MHz RF cavities
WCM and DR PUs
PSB, kickers Tomoscope, BSM, BI, etc.
Finemet cavity
Beam loops
2n frev clocks and SYNC
Reference dividers
frev,SPS fRF,SPS
Kickers, ref. processing, RF cavities
frev
fbeam, DR
fref
2n frev clocks and SYNC
Other digital signals
frev
B, dB/dt, White Rabbit
open loop
closed loop
RF
200 MHz cavity controller (6)
10 MHz cavity controller (11)
20/40/80 MHz cavity controller (7)
Ref. signal processing
10 MHz ret.
20/40/80 MHz ret.
PU proc. Df
PU proc. DR
RF sources for injection trains, etc.
Master clock
Synchronous reference dividers
Coupled bunch feedback
Freq. program

## Slide 4
Beam phase measurement
  Part of beam phase loop
  Measure (simulated) beam phase versus phase of (simulated) cavity returns at configurable harmonic(s)
  Multiple inputs
    Injection oscillator:  Beam replacement before injection
    Beam:  Sensitive pick-ups  Wall current monitor  80 MHz (2nd Nyquist zone) receiver
    Cavity return sums:  10 MHz, 20 MHz, 40 MHz, 80 MHz  Single 10 MHz cavity  Finemet cavity
  20 RF signals in total
Digital down-conversion to baseband I/Q
Detailed synoptic (6 modules VXS + mezzanines): link
Introduction

## Slide 5
Double-harmonic receiver with pre-selection
Data concentrator/selector matrix
Phase detection as part of beam loops
Introduction
Double harmonic receiver
RF1 in
Data concentrator/ selector matrix
Double harmonic receiver
RF2 in
Data concentrator/ selector matrix
Phase detection as part of beam loops
RFn in
…
…

## Slide 6
Phase loop: double phase detection
Df
Combined I/Q streams: beam
h1 (GSHL1)
Selector matrix
Selector matrix
Df
Combined I/Q streams: cavity
h2 (GSHL2)
Selector matrix
Selector matrix
Smooth switch
Phase loop amp.
To frev correction sum
Timings Functions
Set ‘present’ and ‘next’ configuration of signals
Smooth switch after only after phase detection

## Slide 7
Choice of hardware platform
  VXS-based plat-form developed for PSB, LEIR, ELENA, …
  Backplane: only clock and synchronization distribution
  Data exchange by Gigabit links (SFP)
    1 MHz update rate
    32 bit each for I and Q
    2 harmonic, 2 signals
    Net data rate: 256 Mbit/s
Introduction

## Slide 8
Convert RF signals to baseband I/Q data
  Beam synchronous down-conversion
  Two harmonics simultaneously: previous/present and next
Configuration: VXS carrier (PSB), FMC-ADC (PSB), FMC-SFP (COTS)
In: 4 RF signals
Out: 2 data streams containing baseband information of 2 signals at 2 harmonics, or 4 signals
Beam synchronous double-harmonic receiver
VXS Carrier (PSB)
Data stream selection matrix
Internal functions: HPL1/2, PLOFFSET1/2
FMC ADC
FMC SFP
RF in 1
RF in 2
RF in 3
RF in 4
Baseband I/Q, h1 and h2, 2 signals
Baseband I/Q, h1 and h2, 2 signals

## Slide 9
Conversion of direct sampled RF to I/Q baseband
Double-harmonic receiver block

## Slide 10
Synchronous receiver:
  VXS motherboard with ADC and SFP mezzanines
2 baseband I/Q data outputs: Operational and MD beam ctr. (2  2 harmonics  32 bit I/Q)
4 double-harmonic receivers: 2  4 I/Q streams (per output)
Preselection matrix to route I/Q signals from receivers to outputs:
  8 I/Q streams in  4 I/Q streams out
  Dynamic selection of signals during cycle
    Control function per output data stream
  Static selection
    Fixed registers for configuration
  Simple selection, no smooth switching
Double-harmonic receiver block

## Slide 11
Double-harmonic receiver block
Matrix selection functions
Matrix selection functions
256 MBit/s
256 MBit/s

## Slide 12
Data concentration of baseband I/Q data streams
  Reduce number of physical SFP connections
  Pack up to 4 baseband I/Q streams into single physical connection (SFP)
Configuration: VXS carrier (PSB), 2  FMC-SFP (COTS)
Detailed synoptic on DFS (3 modules): link
Beam control – non-synchronous concentration
Baseband I/Q, 4 streams
Baseband I/Q, 4 streams
Baseband I/Q, up to 4 streams
Baseband I/Q, 4 streams
VXS Carrier (PSB)
Data stream selection
Concentration of data streams
Internal functions: HPL1/2
FMC SFP
FMC SFP
Baseband I/Q, 4 streams
Baseband I/Q, 4 streams
Baseband I/Q, 4 streams
Baseband I/Q, 4 streams

## Slide 13
Beam control – non-synchronous concentration
256 MBit/s
256 MBit/s
Matrix selection functions
Matrix selection functions

## Slide 14
Beam control – non-synchronous concentration

## Slide 15
Smooth switch
4 input configuration?
Control through
  Internal function
  Internal ramp block
  Register (PPM)
Control configuration static per cycle
Potential issues
  Fast (inj.) and slow switching (manipulations)
  Switch between all inputs?

## Slide 16
LHC-type multi-bunch beam (triple splitting or BCMS)
Phase loop switching sequence
Signal 1 | Signal 2 | 
Injection synthesizer, h1 = hinj | Cavity return 10 MHz, h1 = hinj | Beam replaced by injection synthesizer before 1st injection Constant harmonic
Beam, h1 = hinj | Cavity return 10 MHz, h1 = hinj | Fast switch-over, timing linked to injection
Beam, h2 | Cavity return 10 MHz, h2 | RF manipulation
… | … | …
Beam, h = 21 | Cavity return 10 MHz, h = 21 | RF manipulation
Beam, h = 42 | Cavity return 20 MHz, h = 42 | 1st splitting at flat-top
Beam, h = 84 | Cavity return 20 MHz, h = 84 | 2nd splitting at flat-top

## Slide 17
Lead ion beam for LHC (example of 100 ns)
Phase loop switching sequence
Signal 1 | Signal 2 | 
Injection synthesizer, h1 = hinj | Cavity return 10 MHz, h1 = hinj | Beam replaced by injection synthesizer before 1st injection Constant harmonic
Beam, h1 = 16 | Cavity return 10 MHz, h1 = 16 | Fast switch-over, timing linked to injection
Beam, h2 | Cavity return 10 MHz, h2 | RF manipulation
… | … | …
Beam, h = 21 | Cavity return 10 MHz, h = 21 | RF manipulation
Beam, h = 169 | Cavity return 80 MHz, h = 169 | Re-bucketing, h = 21  169 Separate beam receiver channel, 80 MHz (2nd Nyquist zone)

## Slide 18
Multi-input, multi-harmonic beam phase detection
Main firmware blocks
  Double-harmonic receiver (DHRX)
  Dynamic matrix, set by functions (IQFM)
  Smooth switch (SSP4T)
  Data separator and combiner for Gigabit links
Next steps
Finalize layout and overview diagram
Integrate ejection synchronization loops
Define functions and timings
Define firmware framework
Summary and outlook

## Slide 19
Spare slides

## Slide 20
Beam loops calculation
  To be implemented in single VXS carrier board
  I/Q baseband streams of all relevant signals
  Generates digital closed-loop revolution frequency for distribution
Beam control – beam loops
S
From beam phase loop amplifier
From radial loop amplifier
From coarse and fine synchronization loop amplifiers
S
±Df
frev, open loop from frequency program
frev, closed loop to distribution