## Slide 1: Gamma ray analysis and GW follow-up observations
Masaki Mori, Yoichi Asaoka, Shoji Torii, Daisuke Zenita, Nick Cannady, Mike Cherry, Yuta Kawakubo for the CALET collaboration
CALET TIM at CNR-IFAC, Florence, February 04-06-27, 2020

## Slide 2: Gamma Ray Event Selection
electron
proton
gamma-ray
= Electron Selection Cut + Gamma-ray ID Cut w/ Lower Energy Extension
100 GeV Event Examples
Charge Z=0
Charge Z=1
Electromagnetic Shower
Hadron Shower
well contained, constant shower development
larger spread
Cannady et al., ApJS 238:5 (2018)

## Slide 3: Gamma-ray skymap
LE- mode, from 2015 November to 2018 May
(Contours show relative exposures)
Mori, Asaoka et al., ICRC2019

## Slide 4: Gamma-ray spectra
  “On-plane”: |l| < 80 & |b|< 8, “Off-plane”: |b|> 8
LE- mode
from 2015 November to 2018 May
Mori, Asaoka et al., ICRC2019+

## Slide 5: CTA 102 (AGN) light curve
(2016/1/13 2016/7/31 2017/2/16 2017/9/4 2018/3/23 2018/10/9 2019/4/27)
Modified Julian Day
Flux [cm-2s-1]
LE trig (> 1 GeV)
By Zenita
Red: CALET signal, Hatched: CALET upper limit (<10-7cm-2s-1)
Blue: Fermi-LAT

## Slide 6: CTA 102 (AGN) light curve
Modified Julian Day
Flux [cm-2s-1]
LE trig (> 1 GeV)
By Zenita
Red: CALET signal, Hatched: CALET upper limit (<10-7cm-2s-1)
Blue: Fermi-LAT
(2016/7/31 2016/11/4 2017/2/16 2017/5/27 2017/9/4)
[Flare period]

## Slide 7: Toward higher energies - Gamma-ray line? -
No result yet…

## Slide 8: Gamma-ray lines from DM annihilation
Kaluza-Klein
Tsuchida and Mori 2017
Bringmann and Calor 2013
Neutralino
(loop suppressed – low branching ratio)
M = 800GeV

## Slide 9: Limits by indirect searches
F. S. Queiroz, arXiv:1605.08788
[proposed]
Annihilation cross section

## Slide 10: 130 GeV line at the Galactic center?
Su & Finkbeiner, arXiv:1206.1616

## Slide 11: 130 GeV line at the Galactic center?
Su, Finkbeiner & Weniger, JCAP 01(2013)209
TS=18.8  4

## Slide 12: Fermi-LAT dark matter line analysis (update)

## Slide 13: CALET gamma-ray spectrum

## Slide 14: Effective area
Fermi LAT
https://www.slac.stanford.edu/exp/glast/groups/canda/lat_Performance.htm
CALET LE 
(Cannady+, 2018)

## Slide 15: Energy resolution
CALET electron
(Asaoka+ 2017)
Fermi LAT
https://www.slac.stanford.edu/exp/glast/groups/canda/lat_Performance.htm
7.5%@100 GeV
2.5%@100 GeV

## Slide 16: Angular resolution
CALET LE 
(Cannady+, 2018)
Fermi LAT
https://www.slac.stanford.edu/exp/glast/groups/canda/lat_Performance.htm
C68 [deg]
0.1@100 GeV
0.13@100 GeV
0.6@100 GeV
100 GeV

## Slide 17: Point spread function: CALET vs LAT
(scaled)

## Slide 18: Effective area at high energies
100 GeV
Gamma ray, LE trig
Electron, HE trig
Decreasing…
Cannady+, 2018
Adriani+, 2019
 How to recover?

## Slide 19: Efficiency in each step
By Zenita
100 GeV

## Slide 20: GW counterpart search

## Slide 21: LIGO-VIRGO observation 3
April 30, 2020

## Slide 22: Energy flux limit map for S190408an
90% C.L. upper limit on S190408an energy flux in the energy region 1–10 GeV and time window [T0-60s, T0+60 s] shown in the equatorial coordinates. The thick cyan line shows the locus of the FOV center of CAL, and the plus symbol is that at T0. Also shown by green contours is the localization significance map of S190408an reported by LIGO/Virgo.
10-6
Mori, Asaoka et al., ICRC2019

## Slide 23: CAL limits on electromagnetic emission from gravitational wave events
(LIGO/Virgo O3)
Mori, Asaoka et al., ICRC2019
†: LE-
New!

## Slide 24: GraceDB glossary
BBH - Binary black hole
BNS - Binary neutron star
NSBH - Neutron star black hole, a binary system composed of one neutron star and one black hole
Terrestrial - Classification for signals in gravitational-wave detectors that are of instrumental or environmental origin. Terrestrial signals are not astrophysical and not due to gravitational waves. Some examples of sources of terrestrial signals are statistical noise fluctuations, detector glitches, and ground motion.
MassGap - Compact binary systems with at least one compact object whose mass is in the hypothetical “mass gap” between neutron stars and black holes, defined here as 3-5 solar masses
Grace DB: https://gracedb.ligo.org/superevents/public/O3/

## Slide 25: CAL limits on electromagnetic emission from gravitational wave events
(LIGO/Virgo O3)
†: LE-
Extended to 12-SEP-2019

## Slide 26: CAL limits on electromagnetic emission from gravitational wave events
(LIGO/Virgo O3)
†: LE-
Extended further to 27-JAN-2020

## Slide 27: LIGO-VIRGO O3: Monthly variation
Grace DB: https://gracedb.ligo.org/superevents/public/O3/
Chart: LIGO-VIRGO triggers
| 43556 | 43586 | 43617 | 43647 | 43678 | 43709 | 43739 | 43770 | 43800 | 43831
GraceDB | 5 | 10 | 3 | 7 | 7 | 9 | 0 | 9 | 10 | 8
CALET GCN | 3 | 7 | 2 | 7 | 3 | 8 | 0 | 4 | 6 | 4

## Slide 28: Searching transient events
Judging ‘pairs’ using PSF
Gamma ray bursts, AGN flares, EM counterparts of GW, …
We define a ‘transient event’ as a gamma-ray pair coming from the same direction (within our angular resolution) in a 120-s time window.
See also poster PS3-243 (Cannady et al.) for GRB search by CALET/CAL
Mori, ICRC2019

## Slide 29: Transient gamma-ray monitor system
Running since 2018/08/20 at WCOC
Parallel processing (60 threads) – 40 min for 1hr data
Receive 1hr data
Produce high-level data
Select gamma ray candidates
Thread01
Produce high-level data
Select gamma ray candidates
Thread02
Produce high-level data
Select gamma ray candidates
Thread03
Produce high-level data
Select gamma ray candidates
Thread04
Produce high-level data
Select gamma ray candidates
Thread05
Produce high-level data
Select gamma ray candidates
Thread60
…
HE
Same direction?
LE
Same direction?
CGBM T060s
Same direction?
Classification of threads
Divide into threads
Mori, ICRC2019

## Slide 30: WCOC DQC “GAM_PAIRS”

## Slide 31: Summary
Gamma ray analysis is on-going.
We have to recover efficiencies toward higher energies to have enough statistics. Some new idea is necessary.
Dark matter line signal search could be sensitive thanks to our good energy resolution.
GW counterpart search results are regularly reported in GCN circulars, but we have only upper limits up to now.
Automated search for gamma-ray pairs are working at WCOC.

## Slide 32: Backups

## Slide 33: Gamma-ray spectra
  “On-plane”: |l| < 80 & |b|< 8
LE- mode
from 2015 November to 2018 May
Mori, Asaoka et al., ICRC2019

## Slide 34: Monitoring count rates of AGNs
Search for flares of known AGNs
Use events within 68% containment angles from AGNs listed in 3FGL (Fermi-LAT 4-year catalog)
Calculate count rates based on 28-day exposures assuming E-2 spectra
Exposures for CTA102 (2015/11-2018/09)
Count rates for CTA102 (2015/11-2018/09)

## Slide 35: Monitoring count rates of AGNs
Search for flares of known AGNs
Use events within 68% containment angles from AGNs listed in 3FGL (Fermi-LAT 4-year catalog)
Calculate count rates based on 28-day exposures assuming E-2 spectra
Fermi-LAT count rates for CTA102
Count rates for CTA102 (2015/11-2018/09)
2017/01/12

## Slide 36: Summary for part B
Selection algorithm for transient gamma-ray events has been developed with FOV cut and direction consistency. It could identify point sources.
503 CGBM triggers are analyzed (T060s) but no pairs were found.
Monitoring method for count rates of AGNs has been developed. It could identify CTA102 flare (2017/01).
Transient gamma-ray monitor system is running since 2018/08. It can detect transient events within 2hr from CGBM triggers by parallel processing.

## Slide 37: Analysis of TXS 0506+056/IceCube-170922A
2015/10/13-2018/05/31, LE run, FOV cut (fixed structure & robot arm)
CC track
EM track
Light curve
(1day/bin,
2months/tic)
Countmap
(within 2)
+ : TXS 0506+056
17/09/22
17/09/22

## Slide 38
Analysis of TXS 0506+056/IceCube-170922A
CC track
EM track
Integrated Exposure
Integrated Flux

## Slide 39
Analysis of TXS 0506+056/IceCube-170922A
CC track
EM track
Cf. Fermi-LAT: 3.6×10-7cm-2s-1 (0.1-300 GeV, Sep.15-27 2017; Atel #10791)
 dN/dE = 3.6×10-8 (E/GeV)-2 cm-2s-1GeV-1
Fermi-LAT flare
Fermi-LAT flare

## Slide 40: Effective Area and Sensitivity
Effective area as a function of energy. Four representing zenith angle ranges are shown.
Mostly axially symmetric except for FOV cut
Effective area is estimated as a function of incident angle (dx/dz, dy/dz) and energy.
Maximum effective area is achieved at around 5 GeV, but lower energy is more important for steep spectrum like E-2.
dx/dz
dy/dz
3-10GeV average
LE- trigger: > 1 GeV
HE trigger: > 10 GeV
CC Track
 Talk by Fujita (25pK202-10)

## Slide 41: CALET Collaboration

## Slide 42: CALET-CAL Detector
Fully active thick calorimeter (30X0) optimized for electron spectrum measurements well into TeV region
Imaging Calorimeter
Charge Detector
Total Absorption Calorimeter
plastic scintillator hodoscope, absolute charge measurement (including charge zero)
SciFi + tungsten plate (3X0),
reconstruction of arrival direction and initial shower development
PWO hodoscope (27X0),
energy measurements and particle identification
448mm
1TeV electron shower is fully contained in TASC
CHD
IMC
TASC

## Slide 43: Gamma Ray Event Selection
1. Geometry Condition
  - CHD-Top to TASC 1st layer (2cm margin)
2. Pre selection
  - Offline trigger
  - Shower concentration
  - Shower starting point
3. Track quality cut
  - Track hits >2
  - matching w/ TASC
4. Electromagnetic shower selection
  - shower shape
5. Gamma-ray ID
  - CHD/IMC-veto (combination of loose cuts)
FOV cut
= Electron Selection Cut + Gamma-ray ID Cut w/ Lower Energy Extension
An example of gamma-ray event candidate in flight data (reconstructed primary energy ~5GeV)

## Slide 44: Gamma Ray Event Selection
1. Geometry Condition
  - CHD-Top to TASC 1st layer (2cm margin)
2. Pre selection
  - Offline trigger
  - Shower concentration
  - Shower starting point
3. Track quality cut
  - Track hits >2
  - matching w/ TASC
4. Electromagnetic shower selection
  - shower shape
5. Gamma-ray ID
  - CHD/IMC-veto (combination of loose cuts)
FOV cut
= Electron Selection Cut + Gamma-ray ID Cut w/ Lower Energy Extension
To maximize the field of view (FOV), the requirements on acceptance condition was loosened as much as possible compared to electron analysis. However, penetration of CHD paddle by shower axis is required to ensure charge zero selection.

## Slide 45: Gamma Ray Event Selection
1. Geometry Condition
  - CHD-Top to TASC 1st layer (2cm margin)
2. Pre selection
  - Offline trigger
  - Shower concentration
  - Shower starting point
3. Track quality cut
  - Track hits >2
  - matching w/ TASC
4. Electromagnetic shower selection
  - shower shape
5. Gamma-ray ID
  - CHD/IMC-veto (combination of loose cuts)
FOV cut
= Electron Selection Cut + Gamma-ray ID Cut w/ Lower Energy Extension
FE : fractional energy deposit of TASC-Y6 relative to total TASC deposit
RE : Second moment of lateral energy deposit distribution relative to shower axis [cm]
“K-cut”
O. Adriani et al., PRL 119, 181101 (2017) supplemental material
cut

## Slide 46: Gamma Ray Event Selection
1. Geometry Condition
  - CHD-Top to TASC 1st layer (2cm margin)
2. Pre selection
  - Offline trigger
  - Shower concentration
  - Shower starting point
3. Track quality cut
  - Track hits >2
  - matching w/ TASC
4. Electromagnetic shower selection
  - shower shape
5. Gamma-ray ID
  - CHD/IMC-veto (combination of loose cuts)
FOV cut
= Electron Selection Cut + Gamma-ray ID Cut w/ Lower Energy Extension
⇒ reject charge 1 region
Electron MC
Proton
MC
-ray
MC

## Slide 47: Gamma Ray Event Selection
1. Geometry Condition
  - CHD-Top to TASC 1st layer (2cm margin)
2. Pre selection
  - Offline trigger
  - Shower concentration
  - Shower starting point
3. Track quality cut
  - Track hits >2
  - matching w/ TASC
4. Electromagnetic shower selection
  - shower shape
5. Gamma-ray ID
  CHD-veto
FOV cut
= Electron Selection Cut + Gamma-ray ID Cut w/ Lower Energy Extension
By removing Black parts, it is possible to reject majority of such background. More sophisticated rejection method is under development.
It was found that secondary gamma-ray produced in ISS structures are dominant source of background
Gamma-ray candidates in CALET FOV
LE Trigger
Fish-eye view of CALET FOV
45o
60o

## Slide 48: EM Track vs CC Track: Effective area

## Slide 49: EM Track vs CC Track : PSF

## Slide 50: Point Source Spectra: Sensitivity Validation
CALET Preliminary
The observed point source spectra are well consistent with Fermi-LAT’s parameterizations. Therefore, it was found that current selection criteria has a validated sensitivity and can be used to set limit on GW counterpart flux.

## Slide 51: Fermi LAT performance
https://www.slac.stanford.edu/exp/glast/groups/canda/lat_Performance.htm
Area
PSF
E/E
E/E

## Slide 52: GRB analysis following a CGBM trigger: an example
GRB 180126A: triggered by CGBM at T0=2018/1/26/ 2:16:38 UTC
 No gamma ray candidates within T060s
Exposure during 120s
Upper limits on energy flux (0 event)
Upper limits on energy flux (2 events, not a pair)
Upper limits are calculated assuming number of events N0 corresponding to 90% C.L.
0 event  N0 = 2.44
1 event  N0 = 4.36
2 events, not a pair  N0 = 4.38/0.68
CALET zenith