## Slide 1: Cavity Design Elliptical and non-elliptical cavities
Erk JENSEN, CERN
https://cernbox.cern.ch/index.php/s/E4qimjeXzf67RLS
Password: easischool

## Slide 2: Outline
From waveguide to cavity
Characterizing a cavity
Multipactor
Many gaps
Elliptical cavities
Higher Order Modes
Non-elliptical cavities
Power couplers
Tuners

## Slide 3: From Waveguide to Cavity

## Slide 4: Lorentz force
A charged particle moving with velocity through an electromagnetic field in vacuum experiences the Lorentz force .
The total energy of this particle is , the kinetic energy is .
The role of acceleration is to increase .
Change of (by differentiation):
Note: Only the electric field can change the particle energy!
Hendrik A. Lorentz 1853 – 1928

## Slide 5: Maxwell’s equations in vacuum
Source-free:
curl (rot, ) of 3rd equation and of 1st equation:
Using the vector identity and the 4th Maxwell equation, this yields:
i.e. the 4-dimensional Laplace equation.
James Clerk Maxwell 1831 – 1879

## Slide 6: Homogeneous plane wave
Wave vector :
the direction of is the direction of propagation,
the length of is the phase shift per unit length.
behaves like a vector.
z
x
Ey
φ

## Slide 7: Superposition of 2 homogeneous plane waves
+
=
Metallic walls may be inserted where without perturbing the fields. Note the standing wave in -direction!
This way one gets a hollow rectangular waveguide.

## Slide 8: Rectangular waveguide
Fundamental (TE10 or H10) mode
in a standard rectangular waveguide.
Example 1: “S-band”: ... ,
Waveguide type WR284 (2.84” wide), dimensions: 72.14 mm x 34.04 mm.
cut-off: .
Example 2: “L-band” : ... ,
Waveguide type WR650 (6.5” wide), dimensions: 165.1 mm x 82.55 mm.
cut-off: .
Both these pictures correspond to operation at 1.5 .
electric field
magnetic field
power flow:
power flow
power flow

## Slide 9: Waveguide dispersion – phase velocity
The phase velocity is the speed at which the crest (or zero-crossing) travels in -direction.
Note on the 3 animations on the right that, at constant , . Note also that at , !
With , !
1: a = 52 mm,
2:
a = 72.14 mm,
3:
a = 144.3 mm,
cutoff:
1
2
3

## Slide 10: Summary waveguide dispersion and phase velocity:
In a general cylindrical waveguide:
  Propagation in -direction:
  for TE, for TE
Example: TE10-mode in a rectangular waveguide of width :
.
In a hollow waveguide: phase velocity , group velocity , .

## Slide 11: Rectangular waveguide modes
TE10
TE20
TE01
TE11
TM11
TE21
TM21
TE30
TE31
TM31
TE40
TE02
TE12
TM12
TE41
TM41
TE22
TM22
TE50
TE32
plotted: E-field

## Slide 12: Radial waves
Also radial waves may be interpreted as superposition of plane waves.
The superposition of an outward and an inward radial wave can result in the field of a round hollow waveguide.

## Slide 13: Round waveguide
f/fc = 1.44
TE11 – fundamental
TM01 – axial field
TE01 – low loss

## Slide 14: Circular waveguide modes
TE11
TM01
TE21
TE21
TE11
TE31
TE31
TE01
TM11
plotted: E-field

## Slide 15: Waveguide perturbed by notches
perturbations (“notches”)
Reflections from notches lead to a superimposed standing wave pattern.
“Trapped mode”
Signal flow chart

## Slide 16: Short-circuited waveguide
TM010 (no axial dependence)
TM011
TM012

## Slide 17: Single WG mode between two shorts
short circuit
short circuit
Eigenvalue equation for field amplitude :
Non-vanishing solutions exist for :
With , this becomes .
Signal flow chart

## Slide 18: Simple pillbox
electric field (purely axial)
magnetic field (purely azimuthal)
(only 1/2 shown)
TM010-mode

## Slide 19: Pillbox cavity field (w/o beam tube)
The only non-vanishing field components :
h
Ø 2a
with
,

## Slide 20: Pillbox with beam pipe
electric field
magnetic field
(only 1/4 shown)
TM010-mode
One needs a hole for the beam passage – circular waveguide below cutoff

## Slide 21: A more practical pillbox cavity
electric field
magnetic field
(only 1/4 shown)
TM010-mode
Rounding of sharp edges (to reduce field enhancement!)

## Slide 22: A (real) elliptical cavity
electric field
magnetic field
(only 1/4 shown)
TM010-mode

## Slide 23: Characterizing a Cavity

## Slide 24: Acceleration voltage and
I define
The exponential factor accounts for the variation of the field while particles with velocity are traversing the cavity gap.
With this definition, is generally complex – this becomes important with more than one gap (cell).
For the time being we are only interested in .
The square of the acceleration voltage is proportional to the stored energy the proportionality constant defines the quantity called “-upon-”:
Attention – different definitions are used in literature!
electric field

## Slide 25: Transit time factor
The transit time factor is the ratio of the acceleration voltage to the (non-physical) voltage a particle with infinite velocity would see:
The transit time factor of an ideal pillbox cavity (no axial field dependence) of height (gap length) is:
(remember: )
Field rotates by 360° during particle passage.

## Slide 26: Stored energy
The energy stored in the electric field is
The energy stored in the magnetic field is
Since and are out of phase, the stored energy continuously swaps from electric energy to magnetic energy.
On average, electric and magnetic energy must be equal.
In steady state, the Poynting vector describes this energy flux.
In steady state, the total energy stored (constant) is

## Slide 27: Stored energy and Poynting vector
electric field energy
Poynting vector
magnetic field energy
John Henry Poynting
1852 – 1914

## Slide 28: Wall losses &
The losses are proportional to the stored energy .
The tangential on the surface is linked to a surface current (flowing in the skin depth ).
This surface current sees a surface resistance , resulting in a local power density flowing into the wall.
is related to skin depth as .
  Cu at has , leading to at 1 GHz, scaling with .
  Nb at has a typical at 1 GHz, scaling with .
The total wall losses result from .
The cavity (caused by wall losses) is defined as
Typical values:
  Cu at (normal-conducting): , should improve at cryogenic by a factor .
  Nb at (superconducting):
No! Anomalous skin effect!
improves only by a factor !

## Slide 29: Shunt impedance
Also the power loss is also proportional to the square of the acceleration voltage ; the proportionality constant defines the “shunt impedance”
Attention, also here different definitions are used!
Traditionally, the shunt impedance is the quantity to optimize in order to minimize the power required for a given gap voltage.
Now the previously introduced term “-upon-” makes sense:

## Slide 30: Geometric factor
With
and assuming an average surface resistance , one can introduce the “geometric factor” as
has dimension Ohm, depends only on the cavity geometry (as the name suggests) and typically is .
Note that (dimension , purely geometric)
is only used for SC cavities.

## Slide 31: Cavity resonator – equivalent circuit
Generator
Cavity
: coupling factor
: shunt impedance
: -upon-
Simplification: single mode
Z
Beam

## Slide 32: Power coupling - Loaded
Note that the generator inner impedance also loads the cavity – for very large more than the cavity wall losses.
To calculate the loaded (), losses have to be added:
The coupling factor is the ratio .
With , the loaded can be written
For NC cavities, often is chosen (power amplifier matched to empty cavity); for SC cavities, .

## Slide 33: Resonance
While a high results in small wall losses, so less power is needed for the same voltage.
On the other hand the bandwidth becomes very narrow.
Note: a 1 GHz cavity with a of has a natural bandwidth of 0.1 Hz!
… to make this manageable, is chosen much smaller!
0

## Slide 34: Loss factor
Voltage induced by a single charge :
Cavity
Beam
V (induced)
Energy deposited by a single charge :
Impedance seen by the beam

## Slide 35: Summary: relations , and
Accelerating voltage
𝑉_acc
Accelerating voltage
wall losses
𝑃_loss
wall losses
Energy stored
𝑊
Energy stored
Attention – different definitions are used in literature !

## Slide 36: Beam loading
The beam current “loads” the cavity, in the equivalent circuit this appears as an impedance in parallel to the shunt impedance.
If the generator is matched to the unloaded cavity (), beam loading will (normally) cause the accelerating voltage to decrease.
The power absorbed by the beam is .
For high power transfer efficiency RF  beam, beam loading must be high!
For SC cavities (very large , the generator is typically matched to the beam impedance!
Variation in the beam current leads to transient beam loading, which requires special care!
Often the “impedance” the beam presents is strongly reactive – this leads to a detuning of the cavity.

## Slide 37: Multipactor
The words “multipactor”, “to multipact” and “multipacting” are artificially composed of “multiple” “impact”.
Multipactor describes a resonant RF phenomenon in vacuum:
  Consider a free electron in a simple cavity – it gets accelerated by the electric field towards the wall
  when it impacts the wall, secondary electrons will be emitted, described by the secondary emission yield (SEY)
  in certain impact energy ranges, more than one electron is emitted for one electron impacting! So the number of electrons can increase
  When the time for an electron from emission to impact takes exactly ½ of the RF period, resonance occurs – with the SEY>1, this leads to an avalanche increase of electrons, effectively taking all RF power at this field level, depleting the stored energy and limiting the field!
For this simple “2-point MP”, this resonance condition is reached at or . There exist other resonant bands.
courtesy: Sarah Aull/CERN

## Slide 38: Multipactor (contd.)
Unfortunately, good metallic conductors (Cu, Ag, Nb) all have SEY>1!
1-point MP occurs when the electron impact where they were emitted
Electron trajectories can be complex since both and influence them; computer simulations allow to determine the MP bands (barriers)
To reduce or suppress MP, a combination of the following may be considered:
  Use materials with low SEY
  Optimize the shape of your cavity ( elliptical cavity)
  Conditioning (surface altered by exposure to RF fields)
  Coating (Ti, TiN, NEG, amorphous C …)
  Clearing electrode (for a superimposed DC electric field)
  Rough surfaces

## Slide 39: Many gaps

## Slide 40: What do you gain with many gaps?
The of a single gap cavity is limited to some . Now consider to distribute the available power to identical cavities: each will receive , thus produce an accelerating voltage of. (Attention: phase important!) The total accelerating voltage thus increased, equivalent to a total equivalent shunt impedance of .

## Slide 41: Standing wave multi-cell cavity
Instead of distributing the power from the amplifier, one might as well couple the cavities, such that the power automatically distributes, or have a cavity with many gaps (e.g. drift tube linac).
Coupled cavity accelerating structure (side coupled)
The phase relation between gaps is important!

## Slide 42: Brillouin diagram; Travelling wave structure
synchronous
2p
speed of light line,
w = b /c
p
p/2
p
p/2
b L
0
0
p/2
p
2p/3

## Slide 43: The elliptical cavity
The elliptical shape was found as optimum compromise between
  maximum gradient ()
  suppression of multipactor
  mode purity
  machinability
A multi-cell elliptical cavity is typically operated in -mode, i.e. cell length is exactly .
It has become de facto standard, used for ions and leptons! E.g.:
  ILC/X-FEL: 1.3 GHz, 9-cell cavity
  SNS (805 MHz)
  SPL/ESS (704 MHz)
  LHC (400 MHz)
At : , .
*): http://accelconf.web.cern.ch/AccelConf/SRF93/papers/srf93g01.pdf‎
D. Proch, 1993 *)

## Slide 44: Elliptical cavities

## Slide 45: Elliptical cavities – the de facto standard for SRF
FERMI 3.9 GHz
CEBAF 1.5 GHz
HEPL 1.3 GHz
TESLA/ILC 1.3 GHz
SNS , 0.805 GHz
KEK-B 0.5 GHz
CESR 0.5 GHz
LEP 0.352 GHz
S-DALINAC 3 GHz
HERA 0.5 GHz
cells
TRISTAN 0.5 GHz

## Slide 46: Practical RF parameters 1
Contour plot of
on the wall
on the wall
The ratio shows sensitivity of the shape to the field emission of electrons.
The ratio shows limit in Eacc due to the breakdown of superconductivity (quench, Nb: ).
Average accelerating gradient:
Contour plot of
courtesy: Jacek Sekutovicz/DESY

## Slide 47: Practical RF parameters 2
Both and are purely geometric parameters.
Like the shunt impedance , the product is a measure of the power loss for given acceleration voltage and surface resistance .
Minimize :
  operation at lower ,
  better surface cleanliness,
  lower residual resistance
Optimize geometry maximizing .
courtesy: Jacek Sekutovicz/DESY

## Slide 48: Single-cell versus multi-cell cavities
Advantages of single-cell cavities:
  It is easier to manage HOM damping
  There is no field flatness problem.
  Input coupler transfers less power
  They are easy for cleaning and preparation
Advantages of multi-cell cavities:
  much more acceleration per meter!
  better use of the power ()
  more cost-effective for most applications
courtesy: Jacek Sekutovicz/DESY

## Slide 49: Practical RF parameters 3
Cell-to-cell coupling will determine the width of the passbands in multi-cell cavities.
0
Brillouin diagram
courtesy: Jacek Sekutovicz/DESY
-mode
-mode

## Slide 50: Field flatness
Field amplitude variation from cell to cell in a multi-cell structure
Should be small for maximum acceleration.
Field flatness sensitivity factor for a structure made of cells:
  is related to the cell-to-cell coupling as and describes the sensitivity of the field flatness on the errors in individual cells.
courtesy: Jacek Sekutovicz/DESY

## Slide 51: Criteria for Cavity Design (1)
Here: Inner cells of multi-cell structures
Parameters for optimization:
  Fundamental mode: , , , , .
  Higher order modes: , .
The elliptical cavity design has distinct advantages:
  easy to clean (rinse)
  little susceptible to MP – can be conditioned …
Geometric parameters for optimization:
  iris ellipse half axes: , :
  iris aperture radius: ,
  equator ellipse half axes: ,
Problem: 7 parameters to optimize, only 5 to play with – some compromise has to be found!
courtesy: Jacek Sekutovicz/DESY

## Slide 52: Criteria for Cavity Design (2)
We see here that is a very “powerful” variable to trim the RF-parameters of a cavity.
Of course it has to fit the aperture required for the beam!
Criterion | RF parameter | Improves if | examples
high gradient operation |  |  | ILC, CEBAF 12 GeV HG
low cryogenic losses |  |  | CEBAF LL
High | , |  | B-factory RHIC cooling LHeC
Criterion | RF parameter | Improves if | examples
high gradient operation |  |  | ILC, CEBAF 12 GeV HG
low cryogenic losses |  |  | CEBAF LL
 |  |  | B-factory RHIC cooling LHeC
courtesy: Jacek Sekutovicz/DESY

## Slide 53: Effect of
for small and big iris radius
Smaller allows to concentrate where it is needed for acceleration
courtesy: Jacek Sekutovicz/DESY

## Slide 54: Example: cell optimization at 1.5 GHz
A. Mosnier, E. Haebel, SRF Workshop 1991

## Slide 55: Equator shape optimization
(and ) change when changing the equator shape.
courtesy: Jacek Sekutovicz/DESY

## Slide 56: Iris shape optimization
Both cells have the same: , , and .
changes with the iris shape
courtesy: Jacek Sekutovicz/DESY

## Slide 57: Minimizing HOM excitation
HOMs loss factors ( , )
courtesy: Jacek Sekutovicz/DESY

## Slide 58: Cell-to-cell coupling
courtesy: Jacek Sekutovicz/DESY

## Slide 59: Scaling the frequency
 | [MHz] | 2600
 | [Ω] | 57
 | [Ω/m] | 2000
 | [Ω] | 271
 | [MHz] | 2600
 | [Ω] | 57
 | [Ω/m] | 2000
 | [Ω] | 271
 | [MHz] | 1300
 | [Ω] | 57
 | [Ω/m] | 1000
 | [Ω] | 271
 | [MHz] | 1300
 | [Ω] | 57
 | [Ω/m] | 1000
 | [Ω] | 271
(or )
courtesy: Jacek Sekutovicz/DESY

## Slide 60: Historic evolution of inner cell geometry
 | [mm] | 35 | 30 | 30
 | [%] | 1.9 | 1.56 | 1.52
 | - | 1.98 | 2.30 | 2.36
 | [mT/(MV/m)] | 4.15 | 3.57 | 3.61
 | [Ω] | 113.8 | 135 | 133.7
 | [Ω] | 271 | 284.3 | 284
 | [Ω*Ω] | 30840 | 38380 | 37970
() | [V/pC/cm2] | 0.23 | 0.38 | 0.38
() | [V/pC] | 1.46 | 1.75 | 1.72
 | [mm] | 35 | 30 | 30
 | [%] | 1.9 | 1.56 | 1.52
 | - | 1.98 | 2.30 | 2.36
 | [mT/(MV/m)] | 4.15 | 3.57 | 3.61
 | [Ω] | 113.8 | 135 | 133.7
 | [Ω] | 271 | 284.3 | 284
 | [Ω*Ω] | 30840 | 38380 | 37970
 | [V/pC/cm2] | 0.23 | 0.38 | 0.38
 | [V/pC] | 1.46 | 1.75 | 1.72
Re-entrant, optimized
TESLA, optimized
1992
2002/04
2002/04
Example: ILC
courtesy: Jacek Sekutovicz/DESY
Low-loss (LL) optimized

## Slide 61: Cavity optimization example
courtesy: Frank Marhauser/JLAB

## Slide 62: Higher Order Modes

## Slide 63: Higher order modes
IB
R3, Q3,w3
R2, Q2,w2
R1, Q1,w1
...
...
external dampers
n1
n3
n2

## Slide 64: Pillbox: 1st dipole mode
electric field
magnetic field
(only 1/4 shown)
TM110-mode

## Slide 65: 7-cell 1.3 GHz structure for
Galek et al.: IPAC2013
Band diagram (top) and Q-factors (bottom)
Reminder:
0-mode -mode

## Slide 66: HOMs: Example 5-cell cavity
First passbands of HOMs typically dangerous
courtesy: Rama Calaga/CERN

## Slide 67: HOM dampers
Ferrite absorbers: broadband damper, room temperature
Waveguides: better suited for higher frequencies (size!)
Notch filters: narrow-band; target specific mode
Multi-cell cavities require broadband dampers!
ferrite absorber
waveguides
notch filter
bandpass filter
double notch

## Slide 68: Non-elliptical cavities
Special thanks to R. Laxdal (TRIUMF) and A. Facco (INFN & FRIB)

## Slide 69: Useful relations
Heavy Ions (, )
Protons/H- (, )

## Slide 70: Particle velocity vs. kinetic energy
electron @ 50 MeV
proton @ 91.8 GeV
electron @ 511 keV
proton @ 938 MeV
electron @ 5.4 keV
proton @ 1 MeV

## Slide 71: Accelerating electrons vs. accelerating ions

## Slide 72: Accelerating electrons vs. accelerating ions
Various building blocks – different technologies, each optimized for a certain velocity range
Ions
Common building blocks – all designed for .
Electrons

## Slide 73: Limitations of elliptical cavities
Elliptical cavities have been designed starting at for CW applications, for for pulsed (SNS, ESS).
The -mode requires cell-to-cell distance of , but outer diameter , i.e. at low the cavity looks more like bellows, sensitive to LFD!

## Slide 74: Non-elliptical SRF Community around the world

## Slide 75: Resonator types for low beta acceleration
Quarter wave resonator (QWR)
Half wave resonator (HWR)
Single spoke resonator (SSR)
Multi-spoke resonator (MSR)
For comparison: Elliptical cavities

## Slide 76: Coaxial resonator
Consider a coaxial geometry with grounded end plates, an inner conductor with radius and an outer conductor with radius .
A standing wave occurs with vanishing on the end walls at and .
The remaining non-zero field components are , , where ,
Peak voltage:

## Slide 77: Quarter-wave resonator (QWR)
The most popular coaxial TEM mode cavity is the quarter wave resonator – capacitively loaded transmission line
The inner conductor is open at one end with a resonant length of ,
For acceleration, is chosen.
The maximum voltage builds up on the open tip – the maximum current at the root.
A beam tube is arranged near the end of the tip.

## Slide 78: Half-wave resonator (HWR)
In the HWR the beam port is at the centre of the inner conductor of a coaxial resonator, coincident with the maximum voltage for .
Magnetic fields loop around the inner conductor with peak fields at the shorted ends.
For acceleration, is chosen.

## Slide 79: QWR vs. HWR
QWR is the cavity of choice for low beta applications where a low frequency is needed
  requires ~50% less structure compared to HWR for the same frequency – rf power loss is ~50% of HWR for same frequency and .
  allows low frequency choice giving larger longitudinal acceptance.
  twice that of HWR.
  Asymmetric field pattern introduces vertical steering especially for light ions that increases with velocity – avoid use for .
  Less mechanically stable than HWR due to unsupported end (microphonics).
HWR is chosen in mid velocity range () or where steering must be eliminated (i.e. high intensity light ion applications)
  produces twice rf losses for the same and .
  is 2x longer for the same frequency.
  Pluses are the symmetric field pattern and increased mechanical rigidity.

## Slide 80: HWR vs. Single Spoke Resonator (SSR)
A single spoke resonator (SSR) is another variant of the half-wave TEM mode cavity class.
In HWR the outer conductor is coaxial with the inner conductor (with diameter ) while in the spoke cavities the outer cylinder is co-axial with the beam tube with diameter . It means that for the SSR has a larger overall physical envelop than the HWR for the same frequency.
Thus for low beta applications () HWRs are chosen at , while SSRs are preferred at .
The spoke geometry allows an extension along the beam path to provide multiple spokes in a single resonator giving higher effective voltage, but with a narrower transit time acceptance.

## Slide 81: Cavity types – QWRs
Typical range:

## Slide 82: Cavity types – HWRs
Typical range:

## Slide 83: Cavity types – SSRs
Typical range:

## Slide 84: Cavity types – multi-cell
CH: Crossbar H-mode

## Slide 85: Accelerating cavity velocity/frequency chart

## Slide 86: Transit Time factor vs. for multiple gaps

## Slide 87: High- spoke cavities
High velocity spoke cavities with are being designed as alternative to elliptical cavities
Features:
  relatively compact
    between 20% and 50% smaller (radially) for low- cavities
    for high diameter close to TM counterparts
  allows low frequency at reasonable size
  mechanically stable – high shunt impedance

## Slide 88: Deflecting mode cavities

## Slide 89: Prototype HL-LHC Crab Cavity prototypes
“DQW” (vertical deflection)
“RFD” (vertical deflection)

## Slide 90: The real thing (HL-LHC Crab Cavity)
CERN-PHOTO-201708-196-10
CERN-PHOTO-2018-026-5

## Slide 91: Power Couplers

## Slide 92: Fundamental Power Coupler – FPC
The Fundamental Power Coupler is the connecting part between the RF transmission line and the RF cavity
It is a specific piece of transmission line that also has to provide the cavity vacuum barrier.
FPCs are amongst the most critical parts of the RF cavity system in an accelerator!
A good RF design, a good mechanical design and a high quality fabrication are essential for an efficient and reliable operation.
LHC FPC
SPL FPC
HL-LHC FPC
courtesy: Eric Montesinos/CERN

## Slide 93: Magnetic (loop) coupling
The magnetic field of the cavity main mode is intercepted by a coupling loop
The coupling can be adjusted by changing the size or the orientation of the loop.
Coupling:
coupling loop
courtesy: David Alesini/INFN

## Slide 94: Electric (antenna) coupling
The inner conductor of the coaxial feeder line ends in an antenna penetrating into the electric field of the cavity.
The coupling can be adjusted by varying the penetration.
Coupling
antenna
courtesy: David Alesini/INFN

## Slide 95: Tuners

## Slide 96: Small boundary perturbation
V
Perturbation calculation is used to understand the basics for cavity tuning – it is used to analyse the sensitivity to (small) surface geometry perturbations.
  This is relevant to understand the effect of fabrication tolerances.
  Intentional surface deformation or introduced obstacles can be used to tune the cavity.
The basic idea of the perturbation theory is use a known solution (in this case the unperturbed cavity) and assume that the deviation from it is only small. We just used this to calculate the losses (assuming would be that without losses).
The result of this calculation leads to a convenient expression for the (de)tuning:
V
ΔV
unperturbed:
perturbed:
Slater’s Theorem
John C. Slater 1900 – 1976

## Slide 97: Lorentz force detuning (“LFD”)
The presence of electromagnetic fields inside the cavity lead to a mechanical pressure on the cavity.
Radiation pressure:
Deformation of the cavity shape:
Frequency shift: ; typical:
This requires good stiffness – and the possibility to tune rapidly!

## Slide 98: Tuner principle
Slow tuners:
  compensate for mechanical tolerances,
  realized with stepper motor drives
Fast tuners:
  compensate Lorentz-force detuning and reactive beam loading
  realized with piezo crystal (lead zirconate titanate – PZT)
Tuning of SC cavities is often realized by deforming the cavity:
courtesy: Eiji Kako/KEK

## Slide 99: Blade tuner
courtesy: Eiji Kako/KEK
Developed by INFN Milano
Azimuthal motion transferred to longitudinal strain
Zero backlash
CuBe threaded shaft used for a screw nut system
Stepping motor and gear combination driver
Two piezo actuators for fast action
All components in cold location

## Slide 100: “Saclay” lever-arm tuner
courtesy: Eiji Kako/KEK
Developed by DESY based on the Saclay design
Double lever system (leverage 1.25)
Cold stepping motor and gear combination
Screw nut system
Two piezo actuators for fast action in a preloaded frame
All components in cold location

## Slide 101: Slide-jack tuner
courtesy: Eiji Kako/KEK
Developed by KEK for STF cryomodule
Slide-jack mechanism
Single high voltage piezo actuator for fast action
Warm stepping motor for easy maintenance
Access port for replacing piezo

## Slide 102: Microphonics
Driven by mechanical vibration in the environment.
QWRs are particularly problematic due to the pendulum action of the inner conductor, which can have very low mechanical frequencies ()
  need to reduce the RMS detuning to of the available BW to avoid nuisance
  the other option is to increase the BW (lower , costs power)
Mitigation:
  stiffening during design/manufacture
  centring the inner conductor by plastic deformation so that .
  adding passive dampers
  reduce environmental noise

## Slide 103: Frequency compensation/tuning
For QWRs a tuning plate at the open end near the beam tube is generally used.
For QWRs with removable tuning plate, a Nb puck can be welded to it – this reduces the cavity by increasing the equivalent .
This puck can be trimmed after final fabrication
tuning plate

## Slide 104: Thank you very much!