## Slide 1: From the Transatlantic Networking Workshop to the DAM Jamboree
David Foster
CERN-IT

## Slide 2: LHC Network Activities 2005-2010
LHCOPN designed to ensure T0-T1 data transport and provide capacity for (most) T1-T1 needs.
  Closed group of parties, CERN + T1’s
  Bounded problem with good estimates of needs
T2 connectivity uses general purpose IP connectivity.
  T2-T1, T2-T2
  Open problem with poor estimates of needs

## Slide 3: We have entered a new era
A workshop on transatlantic connectivity was held 10-11 June 2010 at CERN.
  http://indico.cern.ch/conferenceDisplay.py?confId=88883
  ~50 Participants representing major stakeholders in R&E networking
    ESNet, I2, Dante, NRENs, NSF, DOE, Industry, Major Labs etc
And revealed the following:
  Flows are already larger than foreseen at this point in the LHC program, even with lower luminosity
  Some T2’s are very large (not new).
    All US ATLAS and US CMS T2’s have 10G capability.
  Some T1-T2 flows are quite large (several to 10Gbps)
  T2-T2 data flows are also starting to become significant.
  The vision progressively moves away from all hierarchical models to peer-peer
    True for both CMS and ATLAS
    For reasons of reduced latency, increased working efficiency
  Expectations of network capability are reaching unrealistic proportions without forward planning.

## Slide 4: Problems and Opportunities
Networking Technology and Bandwidth is not the problem itself, but the flows are scaling up to occupy much of the existing infrastructures.
This will not be a problem if:
  You can clearly define what you need, now and over the next few years.
  “You” (or your agency) can pay for it.
  You can integrate it into a system, where the end-site facilities and networks operate together in a consistent fashion.

## Slide 5: 1. Define what you need
The networking community needs a much better definition of real requirements.
  Excessive use of general purpose networks will cause operators to take defensive action.
  International network architectures, with sufficient reliability and capacity to cope with the expected traffic growth and flow patterns need to be designed and implemented.
    This is not at all trivial; it needs planning and time
  Experiments must work with the network community to create a definition that will enable implementation of infrastructures to support T1-T2-T3 matrix flows.

## Slide 6: 2. Pay for it
Given an agreed architectural plan with capacity and other objectives (e.g. resilience and adaptability to shifting flows)
  Optimal solutions in terms of costs can be found;
    The limits of what could be afforded can be understood
  The funding bodies can plan for the resulting infrastructure, within feasible cost bounds.
  The sites can budget to connect.
This requires conviction and excellent justification of the costs from the experiments – In line with the justifications given for other parts of the LHC program
  and ultimately: Commitment from the funding bodies.

## Slide 7: 3. Integrate it into a system
Provisioning capacity and providing it to end sites is manageable
  If you can define what you need.
  If you can show how your needs follow from a well-defined comprehensive operational plan, with well-justified costs.
  And you can pay for it.
Using it effectively is more of a problem
  Site/Campus/Regional network issues
  End system hardware issues
  End system platform and interface issues (O/S, drivers, NIC, etc)
  End system application issues
  Experiments’ data movement and job placement software.
    Real end-end awareness is needed.

## Slide 8: We Need 3 Core Interrelated Activities
Data Architecture Vision
  Encompassing all substantial data movement operations, with clear throughput or time-to-complete goals
  Leading to clear (and effective) capacity planning
  System-wide view enabling key efficiencies: e.g. strategic data placement with some form of Content Distribution Network (not a new concept)
International Network Architecture
  Takes time to put in place.
End-end everything
  Monitoring
  Automated Operations
  Consistent site and network resource-use and/or performance optimization

## Slide 9: LHC Networking Activities 2010-2013 First Step
A small planning group that engages a small number of people to come up with an agreed plan for network bandwidth requirements for the experiments.
  That network architects can then translate into core infrastructure designs.
  That funding bodies can understand and plan for; based on a convincing, comprehensive operational model
  That sites can then understand how to connect to these infrastructures and any policy implications.
A design group that will understand the architectural and organisational issues around an additional international core infrastructure.
  The LHCOPN working group is a good start of key stakeholders.
  Needs to involve and inform T2/T3 stakeholders in some managed way.
This should be done now to ensure that the infrastructures will be in place for 2013 data taking.
  In time for a “STEP13” exercise in 2012
Must work closely with the other core activities.