## Slide 1: Description of the DFX device, scope & interfaces
P. Cruikshank on behalf of the WP6a team at CERN & SOTON
3 March 2020
Production Readiness Review of the DFX

## Slide 2: WP6a - DFX
Interface between SC Link and Diodes Cold Module
of the HL-LHC Inner Triplets
DFX
4 DFX devices to be installed
(5L, 5R, 1L, 1R)

## Slide 3: 1. INTRODUCTION: Direction of the slope P1 vs P5
Horizontal ref
POINT 5
Horizontal ref
POINT 1
L1: DFX has to compensate the slope
R1: DFX follows the slope
(Requirement coming from DFX cryo design)
L5: DFX follows the slope
R5: DFX has to compensate the slope
Extract from DFX integration review June 2019

## Slide 4
Superconducting
Link (~ 80m)
MgB2 cables
NbTi to NbTi
cable splices
NbTi cables of SC link
NbTi cables from triplet
Lambda
plate (WP3)
Horizontal
helium vessel
Vacuum
vessel
Helium
Vessel
safety
devices
Vacuum vessel
safety valve
MgB2 to NbTi
cable splices
Cryo instrumentation
(heaters, temp sensors)
Helium
supply
To DCM &
triplet
cryostat
Vertical
helium
vessel &
fountain
DFX in the HL-LHC tunnel
DFX – recall of main components

## Slide 5: WP6a DFX prototype …fully assembled configuration of the UK1 in-kind supply

## Slide 6: DFX - WP6a
DFX prototype usage at Cern:
Prototype test of cold power system (SC link, DFHX)
HL String
Stored as HL operational spare.
5 DFX & 5 DFM cryostats required:
Connection of MgB2 SC link to NbTi leads of cryomagnets in LHC tunnel
In-kind contribution from UK via collaboration with Southampton University (design & manufacture).
Design & supply of DFX prototype within UK1
4 DFX series & 5 DFM series in UK2 (not yet signed)
DFX CDR – 31/01/2019
DFX DDR – 20/06/2019
DFX PRR – 03/03/2020
DFX #1 delivery – Q4, 2020
Design & Manufacturing:
According to harmonized standards EN 13445
According to IS0-GPS drawing standards
Compliance with PED 2014/68/EU.
CE marking.
MIPs and quality records to be put in MTF.

## Slide 7: WP6a Master Plan

## Slide 8: DFX documentation for PRR
DFX Engineering Specifications and Drawings will be in released status prior to start of production
….with many thanks to Simon & Beatriz for all their support over the last week

## Slide 9: Interfaces overview
Tunnel, supports & Beam
SCLink interface
  Leads + Instru
  Jackets flanges
DCM interface
  Leads + Instru
  Jackets flanges
QXL interface
  Vacuum jacket flange
  Cryogenic lines
Instrumentation
  Sensors supports + IFS
  Splices + bus bars support
External services
  Vacuum equipment
  Pressure relief devices
DFX interfaces
  Outer & Inner jackets
  Cryogenics
  Supports
  External accessories
  Instrumentation & cables/splices
Beam reservation
Jumper
IFS
Splice
T&H
Tunnel Vault
DCM
Cryogenic lines
SCLink
NbTi leads
V
Vacuum equipment
He Safety device
NbTi leads

## Slide 10: SCLink interfaces
Vacuum & Helium jackets
  LHCDSH_C0002
Helium jacket end
  Ø200 x 700 mm + NbTi bus bars
Bus bars
  Design of supports between bus bars de-scoped from prototype deliverables
  DFX mechanical interfaces in helium vessel
    LHCLDQD_0003
NbTi-NbTi splices
  Fixed to helium vessel mechanical interfaces
    LHCLDQD_0003
    Edms 2317283
SCLink Vacuum Jacket flange
Bolted to DFX vacuum vessel
SCLink Helium Jacket flange
Welded to DFX He vessel
MgB2-NbTi
rigid protection
Ø 200
700
NbTi
bus bars
Ø 150

## Slide 11: DCM interface
D1-DFX Connection Module (DCM)
Vacuum & Helium Jackets
  ISOK-DN630 with standard O-ring
  Lip weld
  Interface Drawing: LHCLDQD_0004
Bus bars
  Part of WP3 lambda plate
Core
axis
3.6 m
555

## Slide 12: Cryogenic interfaces
Jumper & DFX interfaces
  Cryogenic interface for DFX, edms 2317868
  Semi-flexible link from DFX to QXL jumper to be detailed.
Temperature sensors supports
  Interface long CERNOX
Heaters Vishay® RH100 interfaces
Level gauges & DeltaP gauge interfaces agreed
Pressure relief devices

## Slide 13: Insulation vacuum interface
SCLink insulation vacuum volume
  Pumping equipment :
    valve + turbopump + primary pump
    LHCVPGFY0001
  Gauges interface
    3 gauges on one ISO DN100
    LHCVA___0076
  Relief plate interface
    ISO-K DN100
    LHCVV___0011
DFX insulation vacuum volume
  Pumping equipment
    Valve + Turbopump + Primary Pump
    LHCVPGFY0001
  Gauges interface
    3 gauges DN100
    LHCVA___0076
  Self-closing flap valve
    On DN200 nozzle
    ST0705009_01

## Slide 14: DFX Instrumentation, Edms 2087413
14
Mechanical supports
Wire Instrumentation Box (WIB)
IFS
  CERN supply
  3 external flanges
  5 tubes sorted by functions
    190 V-taps
    32 T-wires
    8 power wires
Vacuum instrumentation feedthrough ISO DN100
DFX Instrumentation Layout

## Slide 15: Civil Engineering & Transport Interfaces
CERN responsible for support to ground & ceiling in the LHC tunnel
Integration model validated
Ceiling loads, Edms 2224370
DFX support interfaces
  Threaded blocks in upper plate
  Transport lifting points
  Installation tooling TBD
Confirmed load transfer to civil engineering core
15

## Slide 16: Assembly and P.Test configuration in UK
SOTON design according to EN 13445 – Edms 2301702.
Compliance with PED 2014/68/EU.
System fully assembled in UK to validate assemblability, perform pressure test and validate behaviour for all pressure configurations.
To avoid welding/cutting operations at lip welds in UK, the design permits the closing of the helium vessel with elastomer seals (Edms 2332938) prior to cable integration at Cern.
Manufacture and pressure test conformity assessement (presence of UK NoBo) and receives CE marking.
Execution of lip welds at Cern during final assembly with SC cables (CE marking removed)

## Slide 17: Thanks for your attention !