## Slide 1: Upgrade of the vertex detector of the Belle II experiment
Jerome Baudot, for the VXD Upgrade R&D Working Group of the Belle II collaboration
Context of the current VXD
Opportunity for a VXD upgrade
On-going relevant R&Ds
Full simulations for optimisation

## Slide 2: The VXD roles within the Belle II setup
The vertex detector (VXD)
  Better vertexing ← lower boost Smarter tracking ← higher hit rate
  + Harsher radiation environment
  + Belle II trigger rate ~ 30 KHz
 The Belle II physics book PTEP 12 (2019) 123C01
with billions of , pairs
In “clean” environment of B-factory
SuperKEKB collider implementing the nano-beam scheme @ high currents
High collision rate
High beam-induced bkg
Granularity & Material
Radiation tol.
LHC
outer ITK
ee Higgs factory
vertex
Belle II
Physics program @ SuperKEKB with Belle II
  Thorough test of Std Model
  DIrect/indirect search for New Physics
  Hadronic Physics
  Based on accumulation of 50 ab-1 of e++e- at √s = MY(4S)
    within ~10 years → instantaneous luminosity close to 1036 cm-2.cm-1
The Belle II experiment
  “classical” B-factory detector + enhanced features

## Slide 3: The current VXD
Two technology system
  SVD = Double-Sided Strip Detector
    Read-out sensor connected on sensor = Origami
    Hit time-stamping σt ~ 2-3 ns
    Spatial resolution σs.p.~ 20 μm
  PXD = DEPFET sensors
    Very low material budget 0.2 % X0 / layer
    Small first layer radius = 1.4 cm
    Long integration time 20 μs / trigger rate & injection bkg
Strips 1.2 m2
Pixels 0.3 m2
65 cm long – 30 cm in diameter
    G.Rizzo SVD overview talk on Monday
      + Y.Uematsu Hit-time reconstruction poster
      + S.Hazra Particle identification Poster
 Q.Liu PXD overview talk on Monday
The plan is successful so far!  C.Praz Tracking performance and interaction point properties talk on Tuesday

## Slide 4: A decade of operation → Upgrades?
Short term ~ 2026
  Long shutdown for QCS upgrade
    Needed before next jump in luminosity
  Inner region needs to be opened up
    Current VXD moved anyway
  Opportunity for Belle II sub-det. upgrades
    Let’s investigate possibilities…
    short time → with currently ~available techno.
Longer term > 2030
  Further increase of peak luminosity
    Possibly beam polarization?
    Enhanced physics program with 250 ab-1
  A renewed detector is needed
    New set of requirements → not this talk!
Current SuperKEKB-Belle II projection (June 2020)
Target Lpeak
Target Lint
2026 Lint

## Slide 5: Current VXD & nominal luminosity
Beam-induced background extrapolations
  A long way to reach Data/MC ratio ~ O(1)
  Still with large uncertainties
    Drastic change of beam optics for max Lpeak
      βy* today 800 μm  nominal 300 μm
    Continuous injection effect not predicted
      currently too small for good estimate
Tracking / vertexing
  Track pattern recognition with SVD hits only required in // to tracking in Central Drift Chamber
  Then extrapolation to match PXD hits
    Also used for reduction of PXD output bandwidth
  Final pointing resolution somewhat limited by beam-pipe thickness
    0.8 % X0 ← partially required against synchrotron rad.
 Belle II VXD Open workshop July 2019
PXD DAQ limit
Good tracking limit
with hit-time rejection
Current prediction @ nominal Lpeak
Performances within limits BUT without much margin

## Slide 6: Requirements for short-term VXD upgrade
Vertexing & Tracking performances at least as good as current VXD
  Radius range 14 – 135 mm
  Single point resolution ≤10-15 μm
Robust against environment for inner layer (r=1.4 cm)
  Hit-rate ~ 120 MHz.cm-2
  Total Ionizing Dose ~ 10 Mrad / year
  NIEL fluence ~ 50x1012 neq.cm-2 / year
Possibly improve performances
  Impact parameter resolution
  Tracking efficiency (pT < 100 MeV) & Fake rate
  Faster High Level Trigger
    Simplified track pattern recognition
  Total material budget < (2x 0.2 + 4x 0.7) % X0
    total power budget < 1000 W
 Based on current extrapolation with safety factor (x5) bear In mind large uncertainties (previous slide)
For trend only (no uncertainties)
Timing if pixelated tracker ? rough estimate → 100 ns

## Slide 7: Current strategy
Thin & fine-pitch strips
CMOS pixel sensors
(various flavours)
SOI pixel sensors
New geometry implemented
General concepts
discussed
Full simulation
→ performances
R&D efforts
within Belle II Upgrade group
R&D groups
(outside Belle II welcome!)
All pixel layers with upgraded techno. ~ ALICE ITS2 concept
Keep Strips+Pixels with upgraded performances ~ current Belle II concept
standard Belle II geometry
DEPFET pixel sensors
Integration concept
for layer ~ 0.1-0.3 % X0
+
Effort built up to answer within ~1 year
Which concepts bring best performances?
Which technology fit requirements?
Which technology can allow install in ~2026?
CDR

## Slide 8: Thin and fine-pitch DSSD
Main R&D targets
  Handling higher hit-rate / SVD
    10 MHz/cm2 (radii>3 cm)
  Improved resolution σz & decrease material budget
  Longer trigger latency & rate
R&D paths
  Shorter strips
  Finer pitch
  Thinner sensor
R&D challenges
  Heat dissipation (larger #chan.)
  Noise reduction (lower signal)
  ENC = 650 e-
  Total power 2.8 mW/chan.
  127 MHz output
  σt ~ 8 ns
  2k-depth memory → latency ~16 μs
Solutions
  Double-Sided Sensors prototyped by Micron
  Front-End ASIC = SNAP128A under dvpmt
    Based on SliT chip for g-2 (J-PARC experiment)
    180 nm CMOS process
@ KEK
Sensor dim. | Thickness | Pitch P-side | Pitch N-side
40x125 mm2 60x125 mm2 | 300-320 μm | 50-75 μm | 160-240 μm
51.2x57.6 mm2 | 140 μm | 50 μm | 75 μm
Current
Upgrade
128 inputs
 First Sensor+FEE in 2021
(with intermediate strip)
 K.Nakamura Development of thin and fine-pitch DSSD poster

## Slide 9: DEPFET pixel sensors
Current Belle II - PXD
  First use of the technology in HEP experiment
  Many lessons learned
R&D directions
  Gain increase with shorter FET length L
    thinner oxide
    higher signal → improved rad. tolerance
  Rotating read-out direction + switcher intergration
    Speed x3
    Pixel size along beam x1/2
  Faster driving & read-out circuits
    Require advanced processed
    Speed x2
  All-silicon module improvements
    Microchannel cooling
    Thinner drivers
Within reach
  Tint: 20  3 μs
  Improved σz
  Mat. budget 0.21  0.15 % X0
45/62 mm along beam
DCD
Data handler
switcher
Drain Current Digitizer DCD
switcher
Belle II DEPFET collaboration

## Slide 10: DuTiP - SOI pixel sensors
Main R&D targets
  Low material budget
    Monolothic technolgy
  Handling high-rate
    Time-stamping < 100 ns
    Global-shutter style
 M.Yamada R&D status of monolithic SOI pixel sensor for vertex detector talk on Wed.
@ KEK
 Initial prototype DuTIP 1 submission in Nov.2020
Comparison with counter
2x timers
In pixel
7  0
~ ALPIDE FEE
Dual Timer Pixel concept
  16 MHz clock for TIMER
  2x 60 ns “integration” window
  Trigger latency 8 μs
  Occupancy << 0.1 %
SOI Implementation
  0.2 μm LAPIS
  Full depletion
  Pixel pitch 45x45 μm2
  Sensitive thickness 50-75 μm
Pixel layout
45 μm

## Slide 11: CMOS pixel sensor optionS
Sensor available 2020 | MIMOSIS-1 (CBM-MVD) | Belle II requirements “First guess” | MONOPIX-2 (ATLAS-ITK) | ATLASPix3 (ATLAS-ITK)
Time precision (ns) | 5000 | 50 to 100 | 25 | 25
Pixel pitch (m2) | 30x27 | 30x30 to 40x40 | 33x33 | 150x50
TID (Mrad) | 5 | 10 | 100 | 
Power (mW/cm2) | ~50 | < 100 to 200 | ~150 | ?
Trigger delay (s) | No trigger | 5 → 10 | long | 
180 nm HR-CMOS process
 Various R&D on-going outside Belle II
In test
IPHC
Submitted
Bonn, CERN, CPPM
180 nm HV-CMOS process
Tested Barcelona, CPPM, Geneva, Heidelberg, KIT, Liverpool
 Monolithic sessions on Wednesday
~full depletion
amp
comp
Timing / Trigger logic
sensing
node
In pixel
Periphery
(+ToT)
Demonstrated
  Monolithic & low power → low material budget granted
  Excellent granularity → σs.p.~ 5-10 μm
  Short integration → occupancy = O(10-3)
   1st dedicated version in 2021 ~ realistic

## Slide 12: Integration concept
Inner layers = full silicon module
  2 to 3 layers, radius < 4 cm
  Target 0.1 % X0 / layer
Outer layers ~ ALICE-ITS concept
  3 to 4 layers, radius 4-14 cm
  Target 0.3 % X0 / layer
C.Marinas G.Vidal
C.Gargiulo CERN - ALICE
@ IFIC, Valencia
Context = new geometry with all VXD fully pixelated

## Slide 13: Integration concept
Inner layers = full silicon module
  2 to 3 layers, radius < 4 cm
  Target 0.1 % X0 / layer
Outer layers ~ ALICE-ITS ladder concept
  3 to 4 layers, radius 4-14 cm
  Target 0.3 % X0 / layer
Context = new geometry with all VXD fully pixelated
C.Gargiulo CERN - ALICE
@ INFN-Pisa
Forward disks
  2 disks at z= 16.5 & 25.6 cm
  Target 0.3 % X0 / layer
Disk (Ring 2)
F.Bosi
M.Massa

## Slide 14: Simulated tracking performances
Context = new geometry with all VXD fully pixelated = VTX
Realistic pixel sensor model
  Digitizer assuming
    fully depleted thin layer 30 μm
    Pixel 33x33 μm2 with 7bits Time over Threshold
  Tuned with Monopix-1 beam data
    JINST 14 (2019) C06006
    Pitch 40x40 μm2
    ToT 6 bits
Results by T.Fillinger (Strasbourg), B.Schwenker (Göttingen), C.Wessel (Bonn)
θ=0o
θ=60o
Monopix-1 data from Bonn group Test-beam at DESY with 5 GeV e-

## Slide 15: Simulated tracking performances
Context = new geometry with all VXD fully pixelated = VTX
Realistic pixel sensor model
  Digitizer assuming
    fully depleted thin layer 30 μm
    Pixel 33x33 μm2 with 7bits Time over Threshold
  Tuned with Monopix-1 beam data
Geometry
  Taken from fast simulation
  5 or 7 barrel layers with/without 2 forward disks
  Crude layer description but with targeted material budget → per layer: 0.1 % X0 for radii <4 cm then 0.3 % X0
Full tracking chain
  VTX standalone
  CDC standalone
then combined
Results by T.Fillinger (Strasbourg), B.Schwenker (Göttingen), C.Wessel (Bonn)
All VTX layers included in pattern-reco. → other possible simpler/faster scheme
beneficial to High Level Trigger


## Slide 16: Simulated tracking performances
Context = new geometry with all VXD fully pixelated = VTX
Realistic pixel sensor model
  Digitizer assuming
    fully depleted thin layer 30 μm
    Pixel 33x33 μm2 with 7bits Time over Threshold
  Tuned with Monopix-1 beam data
Geometry
  Taken from fast simulation
  5 or 7 barrel layers with/without 2 forward disks
  Crude layer description but with targeted material budget → per layer: 0.1 % X0 for radii <4 cm then 0.3 % X0
Full tracking chain
  VTX standalone
  CDC standalone
then combined
Results by T.Fillinger (Strasbourg), B.Schwenker (Göttingen), C.Wessel (Bonn)
Preliminary

## Slide 17: Simulated tracking performances
Context = new geometry with all VXD fully pixelated = VTX
Preliminary
Realistic pixel sensor model
  Digitizer assuming
    fully depleted thin layer 30 μm
    Pixel 33x33 μm2 with 7bits Time over Threshold
  Tuned with Monopix-1 beam data
Geometry
  Taken from fast simulation
  5 or 7 barrel layers with/without 2 forward disks
  Crude layer description but with targeted material budget → per layer: 0.1 % X0 for radii <4 cm then 0.3 % X0
Full tracking chain
  VTX standalone
  CDC standalone
then combined
Results by T.Fillinger (Strasbourg), B.Schwenker (Giessen), C.Wessel (Bonn)

## Slide 18: Summary & Outlook
There is an opportunity for an upgraded vertex detector (VXD) in Belle II
  Shor-term target ~ 2026
  Main requirement = additional robustness / hit-rate & radiation environment
  Also opportunity to enhance vertexing & tracking performances
   Will benefit to physics with > 30 ab-1 still to accumulate over expected 50 ab-1
Initial work status
  R&D concepts on various strip / pixel & integration technologies on-going
  Full simulation for fully pixelated VXD option → first evaluation of expected performances
Still a lot to do in a short time
  Letters of Intent describing draft proposals @ end of 2020
  First dedicated prototypes in 2021 → CDR 2021
  Physics benchmarking with full simulation
  Then 5 years rush to development & install
 It is time to join, R&D contributors outside Belle II welcomed!

## Slide 19: SUPPLEMENTARY SLIDES

## Slide 20: Related talks at VERTEX 2020
Belle II related talk
  PXD
    Q.Liu Operational Experience and Performance of the Belle II Pixel Detector Talk on Monday 5th
  SVD
    G.Rizzo The Belle II SVD performance and operational experience in the first data taking Talk on Monday 5th
    Y.Uematsu A Study for Hit-time Reconstruction of Belle II Silicon Vertex Detector Poster on Monday 5th
    S.Hazra Particle identification in Belle II silicon vertex detector Poster on Monday 5th
  Tracking
    C.Praz Tracking performance and interaction point properties at the Belle II experiment Talk on Tuesday 6th
  R&D
    K.Nakamura Development of the thin and fine-pitch silicon strip detector aiming for the Belle II upgrade Poster on Monday 5th
Generic R&D on pixel
  Sessions on Wednesday 7th morning: Monolithic I Monolithic II
    M.Yamada R&D status of monolithic SOI pixel sensor for vertex detector Wednesday talk
    M.Barbero Depleted Monolithic Active Pixel Sensors in LFoundry 150 nm and TowerJazz 180 nm CMOS technologies: The Monopix developments talk
    - H-C.Augustin MuPix10: First Results from the Final Design talk

## Slide 21: SuperKEKB collider
Recipe to high luminosity
  & specific beam crossing features
    Crossing angle (83 mrad) + crab waist (80%)
High currents: > 1A
Nano-scale beam size: σx×σy ~ 10µm × 60 nm
βy*<< 1 mm
Cost = severe beam induced background
 | KEKB | SuperKEKB | 
 |  | 2020 | Nominal
Energy (GeV) LER/HER | 3.5 / 8 | 4 / 7 | 
Current (A) LER/HER | 1.6/1.2 | 0.7/0.6 | 2.8 / 2.0
βy* (mm) | 5.9 | 0.8 | 0.3
Instant. Lumi. (cm-2.s-1) | 2.1x1034 | 2.4x1034 | ~6x1035

## Slide 22: Belle II detector
Planned for better performances / Belle under:
  Higher beam-background rate
  Higher trigger rate (30 kHz)
electrons (7 GeV)
positrons (4 GeV)
KLong and muon detector (KLM)
Resistive Plate Chambers (barrel outer layers)
Scintillator + WLSF + SiPM’s (end-caps , inner 2 barrel layers)
Particle Identification
TOP detector system (barrel)
Prox. focusing Aerogel RICH (fwd)
Central Drift Chamber
He(50%):C2H6(50%), small cells, long lever arm, fast electronics
EM Calorimeter (CDC)
CsI(Tl), waveform sampling (barrel+ endcap)
Vertex Detector (VXD = PXD+SVD)
2 layers DEPFET pixels + 4 layers DSSD
Beryllium beam pipe
2cm diameter
Belle II collab ~1000 researches / 26 countries
SuperCond. Solenoid
1.5 T magnetic field
Final focusing magnets
new
new
new
new
upgraded
upgraded
new

## Slide 23
From Eugenio Paoloni, July 2019

## Slide 24: Details on beam-induced background
PXD
Extrapolations still under progress

## Slide 25: CMOS pixel sensor
Typical application-ready sensor (180 nm techno)

## Slide 26: Full pixelated VXD: Geometry details
5 layers + 2 disks

## Slide 27: Material budget full pixelated VXD

## Slide 28: About timeline: the ALPIDE-ITS case
~4 years from tech-proto to final sensor
Few remarks
  TJ180 nm exploration started in 2011
  This is not a small team
+3 years for assembly (ALICE-ITS ~10 m2)
P.Riedler CERN, PSI Seminar

## Slide 29: Tower Jazz 180 nm time response simulations
Front-end structure in-pixel
Simulated behavior (MALTA case)
  From I. Berdalovich, JINST 13 (2018) C01023
  Short recovery time for node requires Ibias~500 nA → 0.9 W/pixel
  ALPIDE with s timing reaches 0.040 W/pixel
amp
comp
logic
sensing
node
bias
current
100 ns
 Suggest gating injection for ~100-200 ns doable after comparator
Occur every 20 ms
10 µs
4 ms
Occur every 20 ms