## Slide 1: RADIATION CHALLENGES FOR THE MACHINE
Francesco Cerutti, on behalf of the
team
with contributions by L.S. Esposito, R. Garcia Alia, A. Lechner, G. Lerner, A. Tsinganis
acknowledging the input of many CERN colleagues
5th Workshop on LHCb Upgrade II zoom.us Mar 30th, 2020

## Slide 2: OUTLINE
Collision debris figures and features
Impact on superconducting magnets
of the triplet – D1 string
of the Matching Section
of the Dispersion Suppressor
and on electronics equipment

## Slide 3: THE COLLISION DEBRIS
150 W absorbed in the TAS absorber
650 W going through the TAS
of which
150 W absorbed in the triplet
950 W towards each (L&R) side
@ 1034 cm-2 s-1 , i.e. 8.5 108 s-1 inelastic collision rate
cold magnets
proton-proton inelastic reaction
with 7.5 10-10
Higgs bosons
7 TeV p + 7 TeV p
with 6.5 TeV beams (80mb) ~125 W (magnet end uncertainties) prediction at 1034 cm-2 s-1
vs 115-135 W measurements (TE-CRG-OP) in the triplet cold mass

## Slide 4: DEBRIS CAPTURE IN THE TRIPLET
lost in Q1
end of the
TAS shadow
right of ATLAS
high energy spectra are depopulated by charge particle (especially pion) interception in the successive quadrupoles
due to magnetic field bending

## Slide 5: MARGIN TO QUENCH AND LIFETIME
round optics
142.5 μrad
V crossing in ATLAS (IR1)
H crossing in CMS (IR5)
x
x
- different behavior reflecting the crossing plane variation for the same
magnetic configuration of the triplet (FDF in the horizontal plane for
positively charged particles coming from the IP)
- IR1 triplet (Q2a) approaches the design limit at nominal luminosity
peak dose [MGy] after 300 fb-1, relevant for triplet (i.e. coil insulator) lifetime
≤30 MGy
≤20 MGy
x
x
~20 MGy
50% +V & 50% -V crossing in ATLAS (IR1)

## Slide 6: TRIPLET: BLM BENCHMARKING
2012
4 TeV beams

## Slide 7: SPECTROMETER EFFECT
OFF
ON

## Slide 8: IR8: TRIPLETS
compensator dipoles
LHCb spectrometer
outside
the ring
D
[on the horizontal plane for the outgoing beam]
F
F
D

## Slide 9: IR8: MARGIN TO QUENCH & CRYOLOAD
145
45
45
35
total
power [W]
70
45
45
35
design limit
385 urad half horizontal crossing angle
@ 1034 cm-2 s-1
peak dose after 400 fb-1 to be evaluated vs. 30 MGy design
LIFETIME
D1

## Slide 10: TRIPLET: BLM BENCHMARKING
2012
4 TeV beams

## Slide 11: IR8: RECOMBINATION DIPOLE (D2)
outside
the ring
Q4 D2 D1 Q3 Q2 Q1
TANB

## Slide 12: D2 QUENCH MARGIN, CRYOLOAD, LIFETIME
@ 1.5 1034 cm-2 s-1 5 mW/cm3
with a total load of 35 W in the cold mass
after 400 fb-1 ≤20 MGy

## Slide 13: MATCHING SECTION
R5 (CMS)
need for designing a collimator (TCL) protection system
Looking for reference at Point 1&5 @ 1034 cm-2 s-1
major role played by TCL4/TCL5
Point 8 specificities: different optics, different crossing angle, different TAN,
injection kickers and septa around Q5R

## Slide 14: MATCHING SECTION: BLM BENCHMARKING
IR1
6.5 TeV beams

## Slide 15: DISPERSION SUPPRESSOR
14 
Point 8 specificities: different dispersion function, TCL6 lack
≤1 mW/cm3 @ 1.5L0
noticeable impact by TCL6 up to half-cell 9
pronounced sensitivity to aperture imperfections
14 
≤3 MGy after 400 fb-1

## Slide 16: DISPERSION SUPPRESSOR: BLM BENCHMARKING
IR5
Fill #5401 (October 2016)
TCLs @ 15-35-20 sigma
6.5 TeV beams

## Slide 17: RADIATION TO ELECTRONICS
scaling up to 50 fb-1/y, i.e. 25 times more
Relocations of sensitive equipment have already been foreseen (see plans for cryo racks)
New FLUKA simulations are going to be carried on with updated geometry, aiming at an improved benchmarking against RadMon data and to study new shielding options
with a reference limit
(R2E-safe) of 3 106 cm-2/y
At higher HEH fluences
a RHA procedure is needed
for equipment qualification
UL86
US85
UW85
UL84
vertically averaged from -1.1m to 2.4m
(0 is the beam height)
[cm-2]
x [cm]
Annual High Energy Hadron fluence
determining the Single Event Effect rate

## Slide 18: CONCLUSIONS
The LHCb upgrade to an instantaneous luminosity of 1.5 1034 cm-2 s-1 and an integrated luminosity of 400 fb-1 implies a TAS-like protection of Q1 and calls for the study of a physics debris collimator (TCL) system for Q5-Q7 as well as shielding solutions for the electronics equipment in the detector cavern proximity.
A systematic FLUKA study of both IP8 sides, implementing the updated detector model and crossing schemes, is being launched as the subject of a starting PhD.
An intentional triplet misalignment is known to offer on paper some potentiality, to be possibly assessed in this specific case.
The recently installed TANB, required by the Upgrade I, appears to offer an adequate D2 protection also in the long term.
The limited dose resistance of certain corrector magnets has to be reviewed in the IR8 context.