## Slide 1
Testing the effect of quadrupolar impedance
with Vlasov approach developed for e-cloud
G. Iadarola
Many thanks to:
N.. Biancacci, L. Mether, E. Métral, N. Mounet, G. Rumolo, L. Sabato, C. Zannini

## Slide 2
Dipolar impedance alone
Studied case:
4 st = 1.3 ns, reference intensity 1.2 x 1011 p/b
BB resonator (fr = 2 GHz, Rs=75 MW)
Synchrotron tune Qs = 4.9 x 10-3
Factor on bunch intensity
(Q-Q0)/Qs
Factor on bunch intensity
(Q-Q0)/Qs
The dashed line is the expected rigid-bunch tune shift estimated as:
Vlasov
PyHEADTAIL

## Slide 3
Factor on bunch intensity
(Q-Q0)/Qs
Factor on bunch intensity
(Q-Q0)/Qs
Studied case:
4 st = 1.3 ns, reference intensity 1.2 x 1011 p/b
BB resonator (fr = 2 GHz, Rs=75 MW)
Synchrotron tune Qs = 4.9 x 10-3
The dashed line is the expected rigid-bunch tune shift estimated as:
Vlasov
PyHEADTAIL
Dipolar + positive quadrupolar

## Slide 4
Factor on bunch intensity
(Q-Q0)/Qs
Factor on bunch intensity
(Q-Q0)/Qs
Studied case:
4 st = 1.3 ns, reference intensity 1.2 x 1011 p/b
BB resonator (fr = 2 GHz, Rs=75 MW)
Synchrotron tune Qs = 4.9 x 10-3
The dashed line is the expected rigid-bunch tune shift estimated as:
Dipolar + negative quadrupolar
Vlasov
PyHEADTAIL

## Slide 5
Instability risetimes
Vlasov
PyHEADTAIL
Factor on bunch intensity
Factor on bunch intensity
Destabilizing effect
Destabilizing effect

## Slide 6
Comparison
Dipolar alone
Dipolar + positive quadrupolar
Dipolar + negative quadrupolar
The behavior of the modes changes significantly (it is not simply a rigid shift)
This is the effect of the changing detuning along the bunch acting differently on different radial modes

## Slide 7
Conclusion
The new Vlasov solver agrees well with PyHEADTAIL for the case of dipolar and quadrupolar impedances
The quadrupolar impedance introduces complex changes in the behavior of the modes: different shifts for different radial modes as result of the detuning along the bunch
This can affect the instability threshold and have a destabilizing effect in a certain range of intensity
Thanks for your attention!