## Slide 1: Summary of power supply ripple observations in the LHC and impact on the HL-LHC
WP2, 19/05/2020
63rd TCC 13/12/2018:
https://indico.cern.ch/event/779650/contributions/3244747/attachments/1770859/2877607/TCC_noise_131218.pdf
S. Kostoglou, G. Sterbini, Y. Papaphilippou
With the valuable help of:
G. Arduini, C. Baccigalupi, H. Bartosik, M. C. Bastos, X. Buffat,
J. P. Burnet, R. De Maria, D. Gamba, L. Intelisano, T. Levens,
M. Martino, V. Montabonnet, N. Mounet, D. Nisbet, M. Soderen,
H. Thiesen, Y. Thurel, N. Triantafyllou, D. Valuch, J. Wenninger

## Slide 2: Motivation
LHC performance during Run I & II: proton losses and emittance growth ↑ than anticipated → mechanism that enhances diffusion → Noise effects
Power supply ripple in dipoles and quadrupoles:
  Observed in LHC & expected in HL-LHC
  50 Hz harmonics
    What is the source? Summary of 2018 observations.
    What is the impact on lifetime?
    How can we mitigate?
  Expected in HL-LHC
  Inner Triplet
    Do we expect an impact on the HL-LHC beam performance?
  Open questions and next steps.

## Slide 3: Motivation
LHC performance during Run I & II: proton losses and emittance growth ↑ than anticipated → mechanism that enhances diffusion → Noise effects
Power supply ripple in dipoles and quadrupoles:
  Observed in LHC & expected in HL-LHC
  50 Hz harmonics
    What is the source? Summary of 2018 observations.
    What is the impact on lifetime?
    How can we mitigate?
  Expected in HL-LHC
  Inner Triplet
    Do we expect an impact on the HL-LHC beam performance?
  Open questions and next steps.

## Slide 4: Beam spectrum at SB
“High frequency cluster”
“Low frequency cluster”
Low-f cluster up to 3.6 kHz.
High-f cluster ~7-8 kHz, in the regime frev-fx
Not aliases due to sampling error.
Not an artifact of the instrumentation system.
The effect is dipolar.
ADTObsBox
50 Hz harmonics
50 Hz harmonics
Status of noise studies in the LHC and expected impact for the HL-LHC, WP2 26/11/2019

## Slide 5: Beam spectrum at SB
“High frequency cluster”
“Low frequency cluster”
Low-f cluster + High-f cluster:
Multiple 50 Hz harmonics.
Similar phase modulation from the mains, with an amplitude proportional to the order of the harmonic.
Frequency evolution of all harmonics normalized with the order of the harmonic.

## Slide 6: Experiments with active filters
Projections
Amplitude evolution of beam harmonics up to 3.6 kHz (h=72)
ON/OFF active filters MB PC: impact on the harmonics of the low-f cluster.
All eight sectors contribute to this effect.
3.6 kHz is clearly passing to the beam, although way beyond the cutoff beam screen frequency [1,2].
[1] R. De Maria et al, Field fluctuation and beam screen vibration measurements in the LHC magnets
[2] M. Morrone M. Martino, et al, Magnetic frequency response of High-Luminosity Large Hadron Collider beam screens., Phys. Rev. ST Accel. Beams

## Slide 7: Experiments with active filters
Active filters enhance the high-order harmonics [1].
Amplitudes of the high-f cluster still lower than low-f cluster.
There is also the shielding from beam screen, vacuum chamber.
No impact on the high-f cluster in the beam was observed during AF tests but strong mitigation from ADT, see next slides.
Voltage spectrum from PC in sector 1-2
Multiples of 600 Hz
[1] J.P Burnet, Test results of RPTE LHC thyristor rectifier with active filter.

## Slide 8
maximum beam offset, equal to ~0.1 μm or 10-3 σ → Equivalent kick 0.09 nrad from single dipole at β=105 m, 1e-3 distance from tune (in the absence of a damper), corresponds to stability of 2e-9 for a single main bend.
ADTObsBox
B1
B2
Comparison between beams & planes
The horizontal plane of B1 is mainly affected.
Asymmetry between low & high f-cluster.

## Slide 9
Impact of ADT BW on 50 Hz
LBOC, 30/10/2012, D. Valuch
Impact of high-f cluster when the ADT BW is changed from extended to standard.
Change in the ADT BW during Adjust, reduction of high-f cluster.
Fill 7035 no change of ADT BW in Adjust. SB with extended BW.
Standard BW
Extended BW
Evian 2019, M. Soderen et al

## Slide 10
B2H
Standard setting
regular-BW cycle
Fill 7033, Stable beams
Impact of ADT BW on 50 Hz

## Slide 11
Special settings
Special cycle ADT extended-BW
Impact of ADT BW on 50 Hz
Fill 7035, Stable beams

## Slide 12
Special settings
Special cycle ADT extended-BW
Impact of ADT BW on 50 Hz
Fill 7035, Stable beams
Open question
Source of the high-f cluster:
Similar signature between low and high-f cluster.
Contrary to what was expected, larger amplitude of the high-f cluster.
Higher sensitivity of the beam’s response to frev-fx compared to fx?
UPS?
V. Chareyre, Assessment of the High Frequency Noise Produced by the UPS Systems in the LHC Machine

## Slide 13: Motivation
LHC performance during Run I & II: proton losses and emittance growth ↑ than anticipated → mechanism that enhances diffusion → Noise effects
Power supply ripple in dipoles and quadrupoles:
  Observed in LHC and expected in HL-LHC
  50 Hz harmonics
    What is the source? Summary of 2018 observations.
    What is the impact on lifetime?
    How can we mitigate?
  Expected
  Inner Triplet
    Do we expect an impact on the HL-LHC beam performance?
  Open questions and next steps.
Based on the source and that no modification is foreseen for the MB PC for HL-LHC, the 50 Hz harmonics will be present in the future.

## Slide 14: A note on tracking distributions
Aperture at 5σcoll (3.5 μm) → 6.7σ (2 μm)
Gaussian
q-Gaussian
Double Gaussian

## Slide 15: A note on tracking distributions
q-Gaussian
Aperture at 5σcoll (3.5 μm) → 6.7σ (2 μm)
Gaussian
q-Gaussian
Double Gaussian

## Slide 16: Lumped vs distributed model
Sixtracklib
Preliminary
Comparison of a dipolar excitation at 3.45 kHz and offset of 2 μm (larger than experimental observations) in Q7 PU with 2 models:
Lumped model: a single modulated kick at Q7.
Distributed model: modulated kick (same phase and amplitude) in 1232 LHC dipoles.
FFT
Losses, q=1.15
Emittance, q=1

## Slide 17
Intensity evolution with a realistic spectrum
“High frequency cluster”
“Low frequency cluster”
LHC
Spectrum in SB (considering the LHC spectrum).
Spectrum in simulations
Baseline
Realistic spectrum

## Slide 18
Intensity evolution with a realistic spectrum
“High frequency cluster”
“Low frequency cluster”
Baseline
Including the low-f cluster
Including the high-f cluster
Including both
LHC
Transverse*: q=1.15 , σq-gauss/σgauss = 1.05
Longitudinal: q=0.88, σq-gauss/σgauss = 0.95
*S. Papadopoulou: HSI lumi meeting 18/5/2018 BSRT calibration Fill 6699

## Slide 19
Spectrum of B2
Spectrum of B1
Reference
Considering the spectrum of B1 or B2 in simulations leads to an asymmetry in the intensity evolution for the two beams.
Intensity evolution of B1 & B2
LHC

## Slide 20
Considering the spectrum of B1 or B2 in simulations leads to an asymmetry in the intensity evolution for the two beams.
Intensity evolution of B1 & B2
LHC
Instantaneous lifetime from fit + moving average

## Slide 21
Considering the spectrum of B1 or B2 in simulations leads to an asymmetry in the intensity evolution for the two beams.
Intensity evolution of B1 & B2
LHC
Instantaneous lifetime at 90 s.

## Slide 22: Motivation
LHC performance during Run I & II: proton losses and emittance growth ↑ than anticipated → mechanism that enhances diffusion → Noise effects
Power supply ripple in dipoles and quadrupoles:
  Observed
  50 Hz harmonics
    What is the source? Summary of 2018 observations.
    What is the impact on lifetime?
    How can we mitigate?
  Expected
  Inner Triplet
    Do we expect an impact on the HL-LHC beam performance?
  Open questions and next steps.

## Slide 23: Mitigation
Attenuation of 50 Hz harmonics is expected due to upgrade of ADT system for Run 3.
ADT comb filter to increase the gain only around the most important 50 Hz harmonics instead of whole BW.
Main objectives for Run 3:
Better understanding of the source of the high-f cluster in Run 3 (Inject noise in a warm dipole?, impact of ADT gain, impedance related?UPS?..)

## Slide 24: Motivation
LHC performance during Run I & II: proton losses and emittance growth ↑ than anticipated → mechanism that enhances diffusion → Noise effects
Power supply ripple in dipoles and quadrupoles:
  Observed in LHC and expected in HL-LHC
  50 Hz harmonics
    What is the source? Summary of 2018 observations.
    What is the impact on lifetime?
    How can we mitigate?
  Expected in HL-LHC
  Inner Triplet
    Do we expect an impact on the HL-LHC beam performance?
  Open questions and next steps.

## Slide 25: Noise thresholds with DA scans
Sum in phase all triplets circuits
RMS sum
all triplets circuits
6D
Modulation frequency as a function of modulation depth, color-coded with minimum DA
HL-LHC
DA reduction
No impact even when considering multiple voltage tones simultaneously with amplitudes as derived by PC specifications

## Slide 26: Open questions & next steps
What is the source?
                Source of the low-f cluster are rectifier MB PC. Although the source and signature is the same, the mechanism driving the high-f cluster’s amplitude to be clearly identified with dedicated experiments in Run 3.
                Measurements needed to check if related to UPS noise.
Is there an impact on lifetime?
Impact on losses especially due to high-f cluster. LHC simulations show that the factor of 2 between the spectra of B1 and B2 can lead to a different intensity evolution of the two beams.
How can we mitigate?
    Expecting amplitude reduction of harmonics due to higher sensitivity ADT pickups.
    If not the case, more refined ADT filter configuration.
    Inject noise in a warm dipole.
    MB PC instrumentation in sector 1-2 very important to these studies. If possible, deploy in all sectors or to be cycled around the sectors after technical stops.
    Shielding not as effective as expected: Study voltage vs magnetic field transfer function in the 0-10 kHz regime for LHC MB and its vacuum chamber in SM18?
50 Hz

## Slide 27: Open questions & next steps
Do we expect an impact on the HL-LHC?
The threshold of DA reduction (ΔQ = 1e-5, depending on the frequency) orders of magnitude above PC specifications → no impact is expected (including both tune modulation due to power supply ripple and operation with high-chromaticity).
However, important non-linearities not included in the simulations → test limits by injecting noise in a single warm quadrupole e.g. Q4/Q5.
Inner triplet
Studies mainly focused on impact on lifetime → Emittance growth studies and comparison with analytical models.
50 Hz & Inner triplet

## Slide 28: Backup

## Slide 29: Motivation
LHC performance during Run I & II: proton losses and emittance growth ↑ than anticipated [1-4] → mechanism that enhances diffusion → Noise effects
[1] F. Antoniou, et al. Can we predict luminosity? 7th Evian Workshop on LHC beam operation 2016
[2] S. Papadopoulou, et al. Emittance, intensity and luminosity modeling and evolution, 8th Evian Workshop on LHC beam operation 2017
[3] S. Papadopoulou S, et al. What do we understand on the emittance growth? 9th Evian Workshop on LHC beam operation 2019
[4] S. Kostoglou, et al. Luminosity and lifetime modeling and optimization, 9th Evian Workshop on LHC beam operation 2019

## Slide 30: A note on tracking distributions
Initial distribution:
Transverse:
sampling from a uniform distribution up to 7σ.
Aperture at 5σcoll (3.5 μm) → 6.7σ (2 μm)
Assign weights depending on PDF of simulated distribution.
Longitudinal:
δp/p extending in the whole bucket height.

## Slide 31: A note on tracking distributions
Initial distribution:
Transverse:
sampling from a uniform distribution up to 7σ.
Aperture at 5σcoll (3.5 μm) → 6.7σ (2 μm)
Assign weights depending on PDF of simulated distribution.
Longitudinal:
δp/p extending in the whole bucket height.
Gaussian
q-Gaussian
Double Gaussian
Weights
Double Gaussian: 5% population for > 3.5 σ1 →σ2=2.38 σ1
Collimator

## Slide 32: A note on tracking distributions
q-Gaussian
Double Gaussian

## Slide 33
Intensity evolution of B1 & B2
 | Instantaneous lifetime at 90 s (h) |  |  | 
Transverse | q=1 | q=1.05 | q=1.1 | q=1.15
Reference | 1560.242 | 279.463 | 75.677 | 28.434
Spectrum of B1 | 889.798 | 188.705 | 56.24 | 22.274
Spectrum of B2 | 1433.508 | 264.628 | 72.584 | 27.423
*S. Papadopoulou: HSI lumi meeting 18/5/2018 BSRT calibration Fill 6699
21.66%
18.77%
25.68%
22.31%
*Transverse: σq-gauss/σgauss = 1.05
Longitudinal: q=0.88, σq-gauss/σgauss = 0.95