Strategy for RF Breakdown Protection of the Linac4 RFQ
Rolf Wegner, Bartosz Bielawski

---
Outline
Detection of Breakdowns and Breakdown Clusters
Recovery from Breakdown Clusters
Beam inhibition
Recovery algorithm
Simulation examples
Conclusions

---
RFQ Breakdown Detection
Detection:
background: Endoscope inspection showed plenty of BD craters
=> current protection for RFQ is not sufficient (vacuum, klystron, modulator)
breakdowns (BD) are discharges that are caused by strong EM fields
plasma of electrons and copper ions acts as short circuit
=> feeding RF power is reflected
detection: if this reflected power exceeds an adjustable threshold level
=> fast interlock is generated within the pulse (~50 μs / pulse ~1000 μs)
=> RF and Beam stopped (BIS –> Source RF)
auto-reset for next pulse (isolated BD)
if a BD cluster (consecutive BDs) or a high BD Rate (BDR) is observed
=> no further auto-reset, Recovery is needed
traceability: alarms will be generated on interlocks + Timber logging
implementation ongoing (RF section: CS, LRF, MK)

---
RFQ Breakdown Detection
BD cluster detection:
BD clusters / high BDR will be detected using history and bins
Bin 1 (BD cluster) : 3rd BD within 25 pulses
=> Recovery Level 1 (trying a quick recovery ~1 min)
Bin 2 (high BDR) : 8th BD within 9’000 pulses (3 hours, BDR ~ 1e-3)
=> Recovery Level 3 (sensitive recovery ~30 min)
Monitoring of BDs on different time scales (per hour, per day) over several days in Inspector
Monitoring of BDs in Timber
Refinement during Linac4 startup

---
Recovery from Breakdowns
Recovery, general remarks, Beam inhibition:
BDs can damage the surface and can leave craters / sharp edges
=> EM field enhancement, further discharges are provoked
Recovery: edges can be smoothed by field emission
=> apply EM fields with lower strength (to avoid discharges)
=> slowly ramping amplitude up to nominal level
=> beam needs to be inhibited (lower transmission => losses)
RFQ needs to be pulsed without beam
=> BIS interlock will be kept active (RFQ BIS user_permit = FALSE)
=> change of RF controls required to decouple BIS interlock and RF pulse permit (many thanks Jan for the clear recommendation)
=> implementation: BIS user_permit = AND (current logic, extra FESA bit)
     so that the beam can be disabled while RFQ is pulsing

---
Recovery from Breakdowns
Recovery algorithm, I:
synergy with CLIC high gradient structure conditioning / BD recovery
=> many thanks to the CLIC team for helpful input (W. Wuensch, L. Millar)
in Recovery Mode the LLRF Feed-back is opened (open loop).
Level 1/2 shall quickly bring back the RFQ into operation, ~1/5 min.
If more than a certain number of BDs are detected during recovery, the next, more sensitive Recovery Level is entered.
On each entry into a Level, the amplitude is reduced by a defined factor and ramped-up in small steps over a number of pulses for each step.
When the nominal amplitude is reached, LLRF feedback is closed and the RFQ is pulsed for a certain time before going back to operational mode.

---
Recovery from Breakdowns
Recovery algorithm, II:
Recovery Level 4 as most sensitive, “normal” Recovery Mode takes about 1 hour.
If still not sufficient, the amplitude is further reduced and RF experts shall be contacted by the Operator while the RFQ is pulsing
(Recovery Level 5).
If still too many BDs occur, the RFQ is stopped (Locked state).

---
Recovery from Breakdowns
Level	new amplitude	# pulses hold	ΔA / A / ramp-up	# pulses FB closed	sum pulses	approx. time	allowed BDs
1	95% * Anominal	2	0.5%	20	40	1 min	2
2	95% * Acurrent	4	0.25%	50	130..210	~5 min	3
3	95% * Acurrent	10	0.1%	200	700..1700	15 to 35 min	5
4	75% * Anominal	10	0.1%	500	3000	60 min	7
5	to keep RFQ pulsing while expert is contacted
	65% * Anominal	10	0.1%	1000	4500	90 min	7
locked	emergency stop
=> Refinement will be done during start-up for Run3.

---
RFQ BD Recovery - examples
Single BDs are ignored if not too frequent.

---
RFQ BD Recovery - examples
3rd BD triggers recovery mode, level 1
E => 95%*E_nom, ramped-up in open loop followed by closed loop 100%*E_nom
6th BD (3rd within recovery level 1) triggers recovery mode, level 2
no further BDs => ramp-up from 95%*E_nom to 100%*E_nom and closed loop
back to normal operation. Next BD ignored as isolated BD.

---
RFQ BD Recovery - examples
3rd BD triggers recovery mode, level 1
6th BD (3rd inside recovery mode, level 1) triggers level 2
11th BDs triggers recovery mode, level 3
ramp-up from ~85% E_nom to 100% and Feed-Back loop closed
back to normal operation after 1’700 pulses (34 min)

---
RFQ BD Recovery - examples
32th BD triggers recovery modes up to locked state = stop pulsing, something very wrong.

---
RFQ BD Recovery - examples
In reality a reduction in electric field will reduce the Breakdown rate strongly.
Assuming here a 10th power dependency BDR ~ (E/Enom)^10 (conservative).
=> the lower number of BDs leads the recovery mode only reach level 4 in this example.

---
RFQ BD Recovery – LBE data
Simulating BD detection and recovery algorithm on the LBE run data
assuming BDR ~ (E/Enom)^10 (conservative)
The presented algorithm will detect BD clusters, will protect the RFQ and will automatically recover its performance.

---
Conclusions
A system to detect Breakdowns (BDs) and to interlock within concerned pulses is being implemented.
On isolated BDs the interlock will be automatically cleared to continue beam operation.
When BD clusters or a high BDR are observed the RFQ will be switched to an automatic Recovery.
2 bins will be used as primary trigger (first implementation).
Beam will be inhibited during Recovery via RFQ BIS user_permit=FALSE.
4 Recovery Levels will treat “normal” cases with different amplitude reduction factors and ramp-up functions.
2 additional Levels will cover special cases.
Refinement will be done during start-up for Run3.
The implementation is ongoing and will be presented by Bartosz.