## Slide 1: Update on longitudinal impedance studies for HL-LHC
Theodoros Argyropoulos, Ivan Karpov and Elena Shaposhnikova
Special Joint HiLumi WP2/WP4 Meeting, 26 May 2020

## Slide 2: Recap on longitudinal stability studies
Loss of Landau damping (LD) in longitudinal plane is important intensity limitation in LHC.
Threshold observed in measurements cannot be explained by Sacherer approach
Based on accurate semi-analytic calculations, threshold depends on “cut-off” frequency
Which threshold should be used for HL-LHC?
= 12 MV, beam energy 450 GeV

## Slide 3: Van Kampen modes
Parameter scan using MELODY:
5 azimuthal modes
500 mesh points in energy of synchrotron oscillations
Resonator impedance Q=1

## Slide 4: Van Kampen modes
Parameter scan using MELODY:
5 azimuthal modes
500 mesh points in energy of synchrotron oscillations
Resonator impedance Q=1

## Slide 5: Van Kampen modes
Parameter scan using MELODY:
5 azimuthal modes
500 mesh points in energy of synchrotron oscillations
Resonator impedance Q=1
Coherent modes
Incoherent band
Lower azimuthal modes have lower thresholds

## Slide 6: Van Kampen modes
Parameter scan using MELODY:
5 azimuthal modes
500 mesh points in energy of synchrotron oscillations
Resonator impedance Q=1
Coherent modes
Incoherent band
Lower azimuthal modes have lower thresholds
Different radial modes within one azimuthal mode

## Slide 7: Van Kampen modes
Parameter scan using MELODY:
5 azimuthal modes
500 mesh points in energy of synchrotron oscillations
Resonator impedance Q=1
Coherent modes
Incoherent band
Lower azimuthal modes have lower thresholds
Different radial modes within one azimuthal mode
More modes are present for higher resonator frequency

## Slide 8: Mode pattern at threshold
Density modulation is localised around bunch centre
Peak of the spectrum around half of resonant frequency

## Slide 9: Mode pattern at threshold
Density modulation is localised around bunch centre
Peak of the spectrum around half of resonant frequency

## Slide 10: Mode pattern above threshold

## Slide 11: Mode pattern above threshold

## Slide 12: Mode pattern above threshold

## Slide 13: Mode pattern above threshold
Modes widen above threshold and become very similar for different

## Slide 14: Comparison with BLonD
Procedure:
Generation of matched bunch,
tracking for 1e5 – 1e6 turns,
storing mean and std value of particle coordinates
Number of macroparticles - 1e6
Number of slices per bucket – 256
Coherent modes
Incoherent band
Very good agreement between semi-analytic calculations and macroparticle simulations
Can these modes be excited?

## Slide 15: Comparison with BLonD
Procedure:
Generation of matched bunch,
tracking for 1e5 – 1e6 turns,
storing mean and std value of particle coordinates
Number of macroparticles - 1e6
Number of slices per bucket – 256
Very good agreement between semi-analytic calculations and macroparticle simulations
Can these modes be excited?
Coherent modes
Incoherent band

## Slide 16: Residual oscillations after a kick
Procedure:
Generation of matched bunch,
Initial offset of 1 deg.
tracking for 40k turns,
storing mean value of particle coordinates
Number of macroparticles - 20e6
Number of slices per bucket – 256

## Slide 17: Comparison for 4 and 8 GHz
Similar residual oscillations for intensities >> threshold

## Slide 18: Comparison for 4 and 8 GHz
4 GHz
8 GHz
4 GHz
8 GHz
Scan around threshold is not fully conclusive. Potentially even more macroparticles is needed.

## Slide 19: Noise excitation
Procedure:
Generation of matched bunch,
Monochromatic phase modulation with amplitude 0.01 deg. (10 times smaller than noise level!)
tracking for 100k turns,
storing mean and rms value of particle coordinates
Number of macroparticles - 1e6
Number of slices per bucket – 256

## Slide 20: Results for GHz
Coherent oscillations can be driven by noise
Lowest radial mode is excited at most

## Slide 21: Results for GHz
Similar results to 4 GHz case. Higher-order radial modes are less excited.

## Slide 22: Example with higher noise amplitude
Phase modulation with amplitude 0.1 deg. at frequency 0.967
Controlled emittance blow-up can affected by interaction of noise with coherent modes

## Slide 23: Summary
“Cut-off” or resonant frequency defines the threshold of loss of Landau damping and corresponding mode pattern. Accurate impedance model is need for threshold evaluation.
Presence of Van Kampen modes was verified in macroparticle simulations.
Modes can be excited by the kick (injection error) and can be driven by noise (might have impact on controlled emittance blow-up).

## Slide 24: Thank you for your attention!

## Slide 29: Phase noise

## Slide 30: 4 GHz 1.17 ns