## Slide 1: CLIC requirements
Beam structure | ~300 bunch/BX
 | 1 bunch train every 20 ms
 | Bunch length 0.5 ns
 | Train length ~150ns
Low mass | Readout thinned to → 50 um No active cooling (air cooling)
Pixel size | 10 to 20 µm square pixels
Power consumption | 100 mW/cm2 → 100 to 400nW/pixel
Radiation | No radiation hardness
Average hit rate | 0.04 hit/mm2/ns
Maximum hit rate | (x5 average hit rate) → 0.2 hit/mm2/ns

## Slide 2: Pixel consumption per pixel (target 100mW/cm2)
As a conclusion: Power pulsing/gating will be needed in this project (1/20 should be feasible…)

## Slide 3: Average/Maximum hit rate
An important parameter for the CLIC front-end is to understand whether we have to deal with double hits per bunch train per pixel
I used the hit rate numbers given by Dominik and Erik (previous slide)
For the following plots I assumed:
  1 hit generates a 3 pixel cluster independently of the pixel size
  Particle arrival follows a uniform distribution
  Hits are uniformly distributed along the whole detector

## Slide 4: Average hit rate probability per pixel per bunch train

## Slide 5: Maximum hit rate probability per pixel per bunch train

## Slide 6: Summary
20 µm pixel:
  400 nW/pixel → (x20) 8 µW/pixel
  Average hit rate per pixel per bunch train:
    0.0072 1 hit probability per pixel
    0.00005184 2 hit probability per pixel
    0.000000373248 3 hit probability per pixel
  Maximum hit rate per pixel per bunch train:
    0.036 1 hit probability per pixel
    0.001296 2 hit probability per pixel
    0.000046656 3 hit probability per pixel