## Slide 1
Two-bunch operation for Compact Light:
sub-harmonic transverse deflector system design
and long-range transverse wakefield optimization
Xiaowei Wu, Walter Wuensch
xiaowei.wu@cern.ch
27.5.2020

## Slide 2
outline
  1. Introduction to Compact Light
  2. Sub-harmonic transverse deflector system design
  3. Long-range transverse wakefield optimization

## Slide 3
Layout of Compact Light
1000 Hz soft X-ray
100 Hz hard X-ray
A compact free electron laser based on X-band technology
Two-bunch operation for pump-and-probe experiment
Produce 100 Hz hard X-ray (2.0 - 16.0 keV) and 1000 Hz soft X-ray (0.25 - 2.0 keV) with same installed linac
Design project funded by European Union Horizon 2020
Injector
Main linac
FEL structure
X-band structure
C-band gun&injector

## Slide 4
Compact Light X-band structure
 | Rep. rate [Hz] | 
 | 100 | 1000
Average gradient <G> [MV/m] | 65 | 30.4
Max klystron available output power [MW] | 50 | 10
Required input power per module PK [MW] | 39 | 8.5
RF pulse [µs] | 1.5 | 1.5
Av. diss. power per structure [kW] | 1 | 2.2
Peak input power per structure [MW] | 68 | 14.8
Av. Input power per structure [MW] | 44 | 9.6
Module energy gain [MeV] | 234 | 109
* Courtesy by M. Diomede
Parameter | Value
Frequency [GHz] | 11.9942
Phase advance per cell [rad] | 2/3
Shunt impedance R [MΩ/m] | 90-131
Effective shunt Imp. Rs [M/m] | 387
Group velocity vg [%] | 4.7-1.0
Pout/Pin | 0.215
Filling time [ns] | 144
Number of cells per structure | 108
# structures per module Nm | 4
Module active length Lmod [m] | 3.6
Average iris radius <a> | 3.5
Iris radius input-output [mm] | 4.3-2.7
Structure length Ls [m] | 0.9
108-cell 2/3 traveling-wave structure

## Slide 5
Compact Light linac module
4 X-band structures in 1 rf module
Dual rf source (100 Hz and 1000 Hz)
With pulse compressor to increase the peak power
Module energy gain: 234 MeV@100 Hz
109 MeV@1000 Hz
* Courtesy by M. Aicheler

## Slide 6
1000 Hz soft X-ray
100 Hz hard X-ray
Linac layout
Linac0
Linac1
Linac2
Linac3
H/S XR
3 C-band 2(4)X-band
16 X-band
8 X-band
68 X-band
1-str beween quads
2-str beween quads
2-str beween quads
4-str beween quads
300 MeV
100 Hz
1.16 GeV
5.25 GeV
150 MeV
1000 Hz
0.55 GeV
2.46 GeV
1.59 GeV
0.75 GeV
BC1
BC2
hard X-ray
soft X-ray
Main linac
main linac works at 67 deg off crest

## Slide 7
  1. Introduction to Compact Light
  2. Sub-harmonic transverse deflector system design
  3. Long-range transverse wakefield optimization
outline

## Slide 8
Bunch splitter before FEL structure
1000 Hz soft X-ray
100 Hz hard X-ray
y=drifting length
x=2.5 mm
Splitter
Need a splitter to separate the two bunches into two FEL lines
Distance between the two bunches should be over 2.5 mm at the entrance of septum

## Slide 9
Gun 6 GHz C-Band
Linac
12 GHz X-Band
Sub-harmonic delfector
3GHz
S-band
Δt = n τgun, n = 1,3,5...
Δs = n λgun
E
E
E┴
drifting length
2.5 mm
Sub-harmonic delfector
Sub-harmonic delfector and spacing between two bunches
Spacing between the two bunches should be 2, 6, 10, 14… X-band rf cycles
n (C-band) | Δt | Δs
1 | 166 ps | 50 mm
3 | 500 ps | 150 mm
5 | 833 ps | 250 mm
7 | 1.16 ns | 350 mm
9 | 1.5 ns | 450 mm
n (X-band) | n (S-band)
2 | 0.5
6 | 1.5
10 | 2.5
14 | 3.5
18 | 4.5
* Courtesy by N. Thompson

## Slide 10
TM110 mode in transverse deflecting cavity
TM010 mode
Accelerating mode
Dipole mode
Transverse kick to beam
TM110 mode
Transverse magnetic field of TM010 and TM110 in pillbox cavity

## Slide 11: Transverse deflecting cavity (TDC) design
Hard X-ray mode: 5.5 GeV bunch
x=2.5 mm, y is drift length
y=drifting length
x=2.5 mm
TDC
Traveling-wave structure
Voltage of deflector could be reduced if we increase the drift length
Longer drift length makes standing-wave deflecting cavity possible
Three options for the transverse deflecting cavity
1. Traveling-wave structure
2. Standing-wave structure, 3-cell structures
3. Standing-wave structure, 5-cell structures
SLAC type LOLA TDC
TM110, 2/3 mode
Length=2.4 m
Filling time~ 300 ns
Standing-wave structure
INFN type 5-cell structure
Tsinghua University type 3-cell structure
Loew, G. A., & Altenmueller, O. H. DESIGN AND APPLICATIONS OF RF DEFLECTING STRUCTURES AT SLAC. 1965
Shi, J. phD thesis. 2009
Alesini, D., et al. RF deflector design and measurements for the longitudinal and transverse phase space characterization at SPARC. Nucl. Instrum. Methods Phys. Res. A, 568(2), 488-502. 2006
Notes: 700 ns SW filling time

## Slide 12
Power capability
Spherical pulse compressor | 
frequency | 2.998 GHz
Q0 | 100000
Coupling factor | 7
Compression ratio | 15
Peak power gain | 7.15
Average power gain | 5.29
CPI S-band Klystron (VKS8262G1):
7.5 MW, 5.0 μs, 400 Hz flat pulse
already applied in IFIC S-band test stand in Valencia
With spherical pulse compressor:
39.7 MW, 300 ns (Avg. without loss) compressed pulse
Esperante Pereira, Daniel, et al. "Construction and Commissioning of the S-Band High-Gradient RF Laboratory at IFIC." J. Phys. Conf. Ser.. Vol. 1067. 2018.

## Slide 13
Drift length [m] | Deflecting voltage [MV] | Traveling wave (2/3) |  | 
 |  | Input power [MW] | Stru. Length w/ PC [m] | Stru. Length w/o PC [m]
0.5 | 13.75 | 6 | 1.45 | 3.65
1.0 | 6.875 | 6 | 0.70 | 1.64
1.5 | 4.583 | 6 | 0.46 | 1.06
2.0 | 3.438 | 6 | 0.35 | 0.79
Traveling-wave transverse deflecting structure design
Freq [GHz] | 2.998
R [MΩ/m] | 20
Q | 12000
vg/c [%] | 3
Increasing the drift length can reduce the length of traveling-wave structure
Work at 2/3 mode
6 MW 4.5 μs klystron pulse
30 MW 300 ns compressed pulse
y=drifting length
x=2.5 mm
TW TDC
Notes: 1 m=111 ns

## Slide 14
R [MΩ] | Freq [MHz] | Q
3.03 | 2996 | 15337
TM110 Eigen mode results
R [MΩ] | Freq [MHz] | Q
5.02 | 2996 | 15271
3-cell structure
5-cell structure
Standing-wave transverse deflecting structure design

## Slide 15
Use race track shape coupling hole
4.14 MV deflecting voltage @ 6 MW input power
Maximum surface field around 100 MV/m
Filling time~820 ns
3-cell standing-wave TDC coupler design

## Slide 16: TDC System design
HXR mode: 5.5 GeV bunch
x=2.5 mm, y is drift length
Klystron: VKS8262G1 model built by CPI
Maximum rf peak power of 7.5 MW6 MW within loss
Pulse length of up to 5 μs
Repetition rate of 400 Hz
Pulse compressor: spherical pulse compressor
Increase the average power:
6 MW, 4.5 us 40 MW, 300 ns (Avg.)
2998 MHz | Traveling-wave (2/3) | Standing-wave
Cell number | N | 3/5
Single cell length [m] | 0.033 | 0.05
Structure length [m] | N*0.033 | 0.15/0.25
Shunt impedance [MΩ/m] | 15.3 | 20
Power capability
y
x=2.5 mm
TDC
RF parameters
Traveling-wave structure
Standing-wave structure
Two options for the transverse deflecting cavity
1. Traveling-wave structure
2. Standing-wave structure
Notes: 700 ns SW filling time

## Slide 17
Drift length [m] | Deflecting voltage [MV] | Input power [MW] | Traveling-wave (2/3) |  | Standing-wave
 |  |  | Stru. Length w/ PC [m] | Stru. Length w/o PC [m] | Stru. length [m]
1.66 | 4.14 | 6 | 0.42 | 1.06 | 0.15
Use the maximum output power (6 MW with loss) from VKS8262G1
1. Klystron, pulse compressor, 0.42 m traveling-wave structure
2. Klystron, circulator, 0.15 m standing-wave structure
PC
TW
6 MW
0.8~1 us
30 MW
70 ns (AVG)
0.42+1.66=2.08 m
Traveling-wave
Klystron
SW
6 MW
0.7~1 us
0.15+1.66=1.81 m
Standing-wave+Circulator
Klystron
Cir
Notes: 700 ns~800 ns SW filling time
50 ns 0.44 m TW filling time

## Slide 18
  1. Introduction to Compact Light
  2. Sub-harmonic transverse deflector system design
  3. Long-range transverse wakefield optimization
outline

## Slide 19
Long-range transverse wakefield problem
In the two-bunch operation, wakefield excited by the first bunch will affect the second bunch
Baseline design is cylinder tapering cavity without heavy damping part
Check the wakefield at 2nd, 6th, and 10th X-band rf cycle (sub-harmonic at S-band)

## Slide 20
*The GdfidL Electromagnetic Field Simulator: bruns@gdfidl.de
Numerical and analytical results have a good agreement
We can estimate the wake by analytical methods and then use GdfidL to verify
  The long-range transverse wakefield goes down automatically 
    X-band linac structure has a tapered iris design
    Structure cells have different dipole mode frequency
  Wake at 2nd rf cycle is much higher than the requirement (40 V/pC/mm/m) 
  Wake at 6th rf cycle is a bit higher than the requirement
  Wake at 10th rf cycle is around 20 V/pC/mm/m
1. Analytical results from formula
Dipole wake:
2. Numerical results from GdfidL*
P. B. Wilson, SLAC-PUB-4547
Long-range transverse wakefield of the Compact Light X-band structure

## Slide 21
  Detuning by using non-linear frequency distribution
  Adjust the dipole mode frequency distribution by changing the coupling irises and the diameters of the cells
  Optimize the wake by changing the curvature of the aperture distribution
    Linear distribution (Blue) is the existing baseline design
    Enhanced-bandwidth distribution (Pink) reduces the wake at 6th rf cycle
    Gaussian-like distribution (Red) reduces the wake at 10th rf cycle
  Baseline design’s aperture:
  from 4.278 mm to 2.722 mm
Wakefield optimization
Notes: Adjust the frequency of the dipole mode by diameter of the cell
如何引出利用aperture来改变geometry？
Developed by the linear accelerator society and well applied in the linear collider people
Enhanced-bandwidth
Gaussian-like

## Slide 22
Enhanced-bandwidth distribution optimization at 6th rf cycle
Cycle number (X-band) | Wt [V/pC/mm/m] | Enhanced Wt [V/pC/mm/m]
6 | 45.3 | 25.7
10 | 21.2 | 41.5
GdfidL results
Possible for 6th rf cycle operation but delicate
Notes: -1.8

## Slide 23
Gaussian-like distribution optimization at 10th rf cycle
Cycle number (X-band) | Wt [V/pC/mm/m] | Gaussian Wt [V/pC/mm/m]
6 | 45.3 | 64.5
10 | 21.2 | 1.8
GdfidL results
Even lower wakefield at 10th rf cycle and robust
Notes: 3.4

## Slide 24
Long-range transverse wake at 10th rf cycle in the linear tapering design
Robust and low wakefield at 10th rf cycle
Apply linear iris thickness distribution to the Gaussian-like aperture design
Origin design has a constant iris thickness
This could reduce the average wake around 10th rf cycle

## Slide 25
CompactLight | baseline design | Gaussian aperture linear iris thickness
Frequency [GHz] | 11.9942 | 
RF pulse [µs] | 1.5 | 
Net kly. power (w/ loss) [MW] | ≈40 | 
Average iris radius <a> | 3.5 | 
Iris radius a [mm] | 4.3-2.7 | 
Iris thickness t [mm] | 2.0 | 2.0-2.24
Average gradient <G> [MV/m] | 65 MV/m (w/ margin) | 65 MV/m (no margin)
Structure length Ls [m] | 0.9 | 
Shunt impedance R [MΩ/m] | 90-131 | 90-125
Effective shunt Imp. Rs [M/m] | 387 | 378
Group velocity v_g/c [%] | 4.7-1 | 4.7-0.9
Filling time [ns] | 144 | 146
Max. Mod. Poy. Vec. - 10-6 bpp/m limit [%] | -32.7 | -29.7
* Courtesy by M. Diomede
RF parameter comparison between two taperings
No big difference on rf parameters
Apply Gaussian-like aperture and linear iris thickness distribution to the baseline design
Choose 10 X-band rf cycles as the two bunch spacing