## Slide 1: CSC Track Finder upgrade
Focusing on algorithm logic now
  Design
  Performance evaluation
Hardware details will come later

## Slide 2: CSC Track Finder upgrade
Current design is totally adequate for LHC luminosity
  2 LCTs (di-muon signal) + 1 (background) = 3 LCTs per Port Card per BX
With luminosity upgrade, we expect ~7 LCTs per Port Card per BX.
  Preliminary simulated data, no measurements so far
  Reality could be worse
Port Card becomes a bottleneck
Solution:
  Keep 2 Trigger Primitives per chamber
  Bring all LCTs to SP (18 per Port Card per BX), no filtering
    May keep the filtering option in Port Cards, in case it’s needed
See this talk by Darin Acosta for explanation of above numbers
  Based on simulations performed by A. Safonov and V. Khotilovich (TAMU)
Notes: Explanation of Port Card as choking point for upgraded luminosity, proposed solution

## Slide 3: SP upgrade
Conversion of trigger primitives to
coordinates
Extrapolation units
Track assembly
Sorting, ghost cancellation
Pt, φ, η calculation
Current SP logic structure
Multiple Bunch Crossing Analysis
BX adjustment to 2nd trig. primitive

## Slide 4: Trig. Primitives  Coordinates
Currently performed in large 2-stage LUTs
Unacceptable for upgrade – too much memory
  4MB per trig. primitive
  6 times more trig. primitives in upgraded design
  Need ~400 MB per SP
Wiregroup pattern
Strip pattern
Chamber ID
φ
η
LUT

## Slide 5: Trig. Primitives  Coordinates
For upgrade:
  Make conversion inside FPGA
  Combine LUTs and logic to reduce memory size
  We receive Trig. Primitives from all chambers
    no need to analyze Chamber ID
    saves precious LUT input bits
  Use different angular coordinates – φ with half-strip resolution and θ
    Why θ ?
      Allows for uniform angular extrapolation windows, no need to adjust them depending on θ
    Why φ with half-strip resolution?
      Makes conversion easier, for 80-strip 10° chambers (ME1/2, ME2/2, ME3/2, ME4/2) as easy as one addition with fixed value.
      Easier to handle in FPGA

## Slide 6: Wiregroup  θ
Wiregroup
5 to 7-bit
θ
8-bit
LUT
32 to 128 cells
θ conversion
all chambers except ME1/1
ME1/1 θ conversion
θ corrected and duplicated  because of wire tilt (if chamber has 2 trig. primitives)
Strip1
6-bit
LUT
Strip2
6-bit
LUT
+
+
θ corrections
4-bit
Wiregroup
6-bit
θ2
8-bit
θ1
8-bit
WG2 θ1
WG2 θ2
LUT
WG MSB
2-bit
WG MSB
2-bit
WG1 θ1
WG1 θ2

## Slide 7: Strip  φ
Use built-in multiplier or LUT. “F” factor depends on chamber type
CLCT pattern 4-bit
Initial φ
10-bit (fixed)
Half-Strip
7 or 8-bit
φ in sector
10-bit
×F
Chamber | Strip angle | F
ME1/2, ME2/2, ME3/2, ME4/2 | 0.1333° | 1 (no multiplication)
ME2/1, ME3/1, ME4/1 | 0.2666° | 2 (shift)
ME1/1a | 0.2222° | 1.667
ME1/1b | 0.1695° | 1.272
ME1/3 | 0.1233° | 0.925
LUT
φ correction
2-bit
corrected
φ in sector
12-bit
+

## Slide 8: Pattern-based detection
Investigating another approach:
  Pattern-based detection
  Separately in φ and θ
  Once the patterns are detected, merge them into complete 3-D tracks
Benefits:
  Logic size reduction
  Size does not explode if 3 track segments per chamber are needed
  Certain processing steps become “natural”, logic for them is greatly simplified or removed
    Multiple Bunch Crossing Analysis
    Ghost Cancellation
    Assigning timing on second track segment

## Slide 9: Pattern-based detection
Target: importing all available trig. primitives from all CSCs
Status: this section complete (initial attempt)
Starting integration and tests with CMSSW very soon
Trig. primitives to θ and φ conversion
Raw hit construction
Raw hit persistence (time extension)
φ and θ pattern detectors
best pattern selectors (3 in each zone,
total 12 best φ and 18 best θ patterns)
φ and θ pattern merging into 12 track candidates
selection of best three tracks,
precise φ, η, Pt assignment

## Slide 10: Raw hit reconstruction: layers and zones
4 layers of chambers make up detector layers
Split the sector into zones according to phi and theta coverage
phi
theta

## Slide 11: Zone boundaries
Chart: 
| MB1 | ME1/1 | ME1/2 | ME1/3 | ME2/1 | ME2/2 | ME3/1 | ME3/2 | ME4/1 | ME4/2
high | 128 | 50 | 85 | 124 | 47 | 107 | 39 | 96 | 34 | 88
low | 88 | 5 | 46 | 98 | 5 | 52 | 5 | 44 | 6 | 38
close | 88 | 5 | 46 | 98 | 5 | 52 | 5 | 44 | 6 | 38
Chart: 
| ME1a/1 | ME1a/2 | ME1a/3 | ME1a/4 | ME1a/5 | ME1a/6 | ME1a/7 | ME1a/8 | ME1a/9 | ME1b/1 | ME1b/2 | ME1b/3 | ME1b/4 | ME1b/5 | ME1b/6 | ME1b/7 | ME1b/8 | ME1b/9 | ME2/1 | ME2/2 | ME2/3 | ME2/4 | ME2/5 | ME2/6 | ME2/7 | ME2/8 | ME2/9 | ME3/1 | ME3/2 | ME3/3 | ME3/4 | ME3/5 | ME3/6 | ME3/7 | ME3/8 | ME3/9
high | 99 | 174 | 249 | 98 | 173 | 248 | 88 | 163 | 238 | 324 | 399 | 474 | 323 | 398 | 473 | 313 | 388 | 463 | 175 | 325 | 475 | 98 | 173 | 248 | 323 | 398 | 473 | 176 | 326 | 476 | 98 | 173 | 248 | 323 | 398 | 473
low | 17 | 92 | 167 | 18 | 93 | 168 | 28 | 103 | 178 | 242 | 317 | 392 | 243 | 318 | 393 | 253 | 328 | 403 | 15 | 165 | 315 | 18 | 93 | 168 | 243 | 318 | 393 | 16 | 166 | 316 | 18 | 93 | 168 | 243 | 318 | 393
close | 17 | 92 | 167 | 18 | 93 | 168 | 28 | 103 | 178 | 242 | 317 | 392 | 243 | 318 | 393 | 253 | 328 | 403 | 15 | 165 | 315 | 18 | 93 | 168 | 243 | 318 | 393 | 16 | 166 | 316 | 18 | 93 | 168 | 243 | 318 | 393
Theta
7 bit
Phi
9 bit

## Slide 12: Raw hit construction
Based on simple decoders
Phi and theta coordinates converted to positional codes (hits)
Put into zones according to chamber that they came from

## Slide 13: Raw hit persistence
Each raw hit is time-extended to 4 BX
The hits overlap in time, so delayed track segments can be taken into account by pattern detectors
This used to be BXA functionality

## Slide 14: Pattern detectors
One of the patterns
Phi pattern detection is in double strips, to save logic
  Detection precision seems to be sufficient
  Full 12-bit phi will be assigned to the best tracks
Phi patterns are constructed so that:
  They accommodate max 10 degree bending (ME1-ME2)
  High-PT (straightest) tracks are detected most precisely
  As bending increases, the precision becomes worse
  Minimum two layers must be hit
Quality code:
  The more layers – the better
  Patterns with ME1 hit have priority
Theta patterns are similar but simpler
  No bending in theta direction
1234
16
8
4
2
1
1
1
2
4
8
16
Number of di-Strips ORed
Station
Possible φ pattern envelope structure
ME

## Slide 15: Remaining steps
Best pattern selection in each zone
Merging phi and theta patterns into 12 track candidates
Three best tracks selection
Precise parameter assignment

## Slide 16: Performance evaluation
Bobby Scurlock has integrated code into CMSSW
Working on pattern mask optimization now
Getting ready for performance plots
Meanwhile:
  new Verilog to CPP converter is finished: features:
    supports most of Verilog 2001 features, including test fixtures
    generates compact C++ that compiles with GCC and Microsoft VC++
    generated C++ is traceable to the original Verilog code
    transfers author's comments from the source Verilog to the generated C++
    expands Verilog by allowing array inputs/outputs
    performance of the generated C++ looks OK, to be evaluated later
    adapting upgraded TF logic design for the new converter is in progress, will be finished soon.