## Slide 1: CTF3 collaboration technical meeting CLIC Two-beam Module Program in CTF3
G. Riddone, 06.05.2010
(contributions from Two-beam module team and several collaborators: CEA/Saclay, Dubna/JINR, HIP, CIEMAT, LAPP, Pakistan, UnM, UPPSALA, IFIC Valencia, SLAC, Fermilab)

## Slide 2: Content
Introduction to module
CLIC feasibility issues and motivation
Phases towards the CLEX modules
  TBTS
  Prototype modules in the lab (Modules-LAB)
  Prototype modules in CLEX (Modules-CLEX)
Conclusions

## Slide 3: CLIC two-beam module
ACCELERATING STRUCTURE +100 MV/m, 64 MW
PETS -6.5 MV/m, 136 MW
NUMBER OF CLIC MODULES
20924
QUADRUPOLES:
Main Beam – 3992
Drive Beam – 41848
ACCELERATING
STRUCTURES - 142812
PETS - 71406

## Slide 4: CLIC feasibility issues
Demonstration of novel scheme of two beam acceleration in compact modules integrating all technical systems for RF production, beam measurement and acceleration including alignment, stabilisation and vacuum at their nominal parameters.

## Slide 5: Steps towards two-beam acceleration modules
Two-beam test stand (PETS and ac. structures)
Prototype modules in LAB
Prototype modules in CLEX
Demonstration of the two-beam acceleration with one PETS and one accelerating structure at nominal parameters in CLEX
Demonstration of the two-beam module design. This implies the assembly and integration of all components and technical systems, such as RF, magnet, vacuum, alignment and stabilization, in the very compact 2-m long two-beam module
Demonstration of the two-beam acceleration with two-beam modules in CLEX
Address other feasibility issues in an integrated approach
  Industrialization and mass production study

## Slide 6: Two-beam modules - Strategy
CLIC Modules (LAB) (as much as possible close to CLIC modules)
4 modules: 2010-2011
CLIC Modules (CLEX)
(Eucard – NCLinac –WP9.2/9.3)
(to be adapted to test infrastructures)
3 modules: 2010-2012
CLIC PROTOTYPE MODULES
RF structures
Pre-alignment
Stabilisation
Vacuum
Stand-alone tests
TBTS

## Slide 7: TBTS – Phase 2
NOW: phase 2.1
FUTURE
Phase 2.2: two accelerating structures TD24 with WFM (CEA)
The accelerating structures are currently under procurement (aim: ready to be installed by Q4, 2010)
PETS
AS
(TD24)

## Slide 8: CLIC module types
Type 0
(only RF structures)
Type 1
(1 short MB Q)
Type 4
(1 long MB Q)
A. Samoshkin
The test module types 0-1-4 are representative of all module types

## Slide 9: Modules-LAB: objectives
Integration of all technical systems (dummy RF structures and quadrupoles can be used – real dead weight and interfaces to other systems)
  Assembly of RF structures with all features
Validation of different types of girders and movers
Pre-alignment of girders/quadrupoles in the module environment, including fiducialisation
Full metrology of the module components
Stabilization of main beam quad in the module environment
Validation of interconnections under different simulated thermal loads
Vibration study of all systems and identification of vibration sources
Measurement of resonant frequencies (both in lab and in the tunnel/underground area)
Simulation of several thermal cycles: measurements of thermal transients (e.g. how long it takes to achieve a new equilibrium state), fiducialisation verification
Transport of the module and verification of alignment

## Slide 10: Modules-LAB Installation of first two modules in the building 162

## Slide 11: Modules-LAB
Phase 1
Phase 2
Phase 3
Pre-alignment validation with dummy elements
Interconnections - pumping (static conditions)
Repositioning
Measurements of resonant frequencies
Transport and thermal cycles
Measurements of resonant frequencies
Stabilization (Q) and pre-alignment compatibility
Vibration study of all system and vibration sources
2010

## Slide 12: Modules-CLEX: objectives
Two-beam acceleration in compact modules integrating all technical systems for RF production, beam measurement and acceleration including alignment, stabilisation and vacuum at their nominal parameters.
Accelerating structure alignment on girder using probe beam
Wakefield monitor (WFM) performance in low and high power conditions, and after a breakdown
Investigation of the breakdown effect on the beam
Alignment and stabilization systems in a dynamic accelerator environment
RF network phase stability especially independent alignment of linacs
Vacuum system performance, both static and dynamics with rf
Cooling system, especially dynamics due to beam loss and power flow changes
Validation of assembly, transport, activation, maintenance etc.

## Slide 13
From CLIC module to CLEX module
CLIC module type 0
(1PETS feeding 2 AS)
PETS
PETS
CLEX module type 0
(1PETS feeding 2 AS)
Double length PETS

## Slide 14: Module-CLEX: Phase 3
3.1 / Nominal power and pulse length for 1 PETS and 2 AS
Recirculation
12 A and 240 ns
3.2 / No modifications on the module type 0 HW
No Recirculation
Current increase from 12 A to 19.2 A
Pulse length reduced from 240 ns to 140 ns
Phase 3 foresees the installation and testing of 1 module type 0: AS equipped with WFM (5 um accuracy / few WFM in the 1st powered AS)

## Slide 15: Module-CLEX/ Phase 3: type 0 module installation
15
PROBE BEAM LINE
DRIVE BEAM LINE (opt.1)
DRIVE BEAM LINE (opt.2)
A. Solodko

## Slide 16: CLEX/Phase 3: module integration
16
Test Module type 0 integration into CLEX
A. Solodko
Double length PETS

## Slide 17: Modules-CLEX: Phase 4
No modifications on the module type 0
Addition of new modules - type 1 and 4
Increase of current from 19.2 A to 22 A
Modification on the module type 1
(2 CLIC PETS)
Needed klystrons and PC

## Slide 18: Phase 4: module installation
18
PROBE BEAM LINE
DRIVE BEAM LINE
A. Solodko

## Slide 19: Phase 4: module integration
19
3 Modules integration into CLEX
A. Solodko

## Slide 20: Proposed schedule

## Slide 21: Conclusions
Two-beam acceleration module is one of the feasibility issues
We have established a program to address this issue, through different steps:
  TBTS
  Lab (4 modules from 2010)
  CLEX (3 modules from 2011) [also part of EuCARD – WP9.2 (G. Riddone /WP9.3 (A. Jeremie))  compact modules integrating all technical systems for RF production, beam measurement and acceleration
Procurement of key components for Modules-LAB under way (girders, Q, RF structures)
Prototype module design was frozen in Q1 2010 – a lot of work and limited resources: contribution from several collaborators is essential  Type 0 by end of 2010