## Slide 1: ECON @ LLR & Split Sorting network IP synthesis Stratus HLS + Genus w/ RD53 libs
L. Pacheco, T. Romanteau, J.-B. Sauvan
LLR CNRS/Ecole Polytechnique
D. Čoko, A. Kristić, J. Musić, J. Ožegović, I. Puljak
University of Split - FESB
Fermilab – LLR – Split meeting, 15 May 2020

## Slide 2: BestChoice algorithm
One of three algorithms in ECON-T
  Super Trigger Cell
  Threshold-Sum
  BestChoice
Development at LLR
  Based upon Batcher odd-even mergesort algorithm
  High-Level Synthesis
  Source code written in SystemC
  Translated to RTL Verilog using Stratus HLS
  Tested in SystemC and Python
Synthesis and functional verification at Split
  CERN Digital Flow, TSMC65LP and RD53 tech libs
  Cadence Genus (RTL synthesis)
  Cadence Incisive (simulation)
  Tested at RTL and gate-level
https://indico.cern.ch/event/862245/contributions/3632336/attachments/1943107/3222874/hirschauer_ECON_ASICs_HGCALweek_12nov2019.pdf

## Slide 3: BestChoice algorithm - Functionality
Functionality:
  48 parallel TC charge inputs
  parallel output for sorted TC charges outputs
  parallel output for TC addresses
Requirements:
  low power consumption
  low latency
  simple and flexible design
16 different architectures were considered:
  1-stage pipeline (2 BX latency) vs 0-stage pipeline (1 BX latency)
  23 TC outputs vs 48 TC outputs
  40 MHz clock vs 160 MHz clock
  Compressed data (7 bits) vs uncompressed data (18 bits)
1-stage pipeline architecture (Latency 2 BX) with 48 outputs
  Selected as the final architecture
  Meets timing constraints at all TID levels

## Slide 4: BestChoice algorithm - Development
Development:
  each architecture fully synthesized and tested
    SystemC -> RTL -> Gate-level -> simulation
  final candidate selected in agreement with FNAL:
    48 TC output
      allows for better flexibility
      23 TC output version showed no significant benefits
    18-bit inputs and outputs
      allows for better resolution
      7-bit version needs another compression block
    2 BX latency
      significant reduction in power consumption compared to 1 BX latency
    40 MHz clock
      simplicity (single clock)
      160 MHz would need another clock or a PLL block
Why Batcher odd-even mergesort algorithm?
  Best algorithm for parallel processing
  Lowest amount of resources
  Small number of comparators

## Slide 5: Synthesis and simulaton workflow
Verilog RTL
Tech libraries
SDC constraints
Genus
Synthesis tool
Verilog
Gate-level netlist
SystemC
sources
Tech library
Timing constraints
Stratus HLS
Incisive Simulator
Verilog testbench
Output values and addresses
Input values and addresses
  SDC constraints:
    Clock period: 25.0 ns
    Input and output delays set to zero
    Inputs driven from a D flop (DFQD1)
    Output loads set to 0.01 pF
  Technology libraries:
    Stratus HLS: TSMC65LP BC
    Genus: TSMC65LP WCL, 0.9V + RD53 libs

## Slide 6: Synthesis reports: 1-stage pipeline (Latency 2BX)
Technology library |  | RD53 |  |  |  |  |  | TSMC65LP | 
GENUS TARGET LIB. |  | 100 Mrad |  | 200 Mrad |  | 500 Mrad |  | WCL0D9 | 
HLS TOOL |  | VIVADO | STRATUS | VIVADO | STRATUS | VIVADO | STRATUS | VIVADO | STRATUS
Gates | Sequential | 2,233 | 2,261 | 2,233 | 2,261 | 2,233 | 2,261 | 2,233 | 2,261
 | Inverter | 5,565 | 6,182 | 5,607 | 6,490 | 8,131 | 7,355 | 6,480 | 7,276
 | Buffer | 429 | 457 | 490 | 658 | 1,176 | 1,006 | 183 | 207
 | Logic | 31,387 | 31,945 | 33,267 | 34,005 | 41,141 | 38,038 | 37,031 | 37,578
 | Total | 39,614 | 40,845 | 41,597 | 43,414 | 52,681 | 48,660 | 45,927 | 47,322
Area [mm2] | Net | 69,099 | 72,306 | 72,559 | 76,267 | 87,468 | 83,164 | 77,484 | 79,937
 | Cell | 128,675 | 132,018 | 138,247 | 146,082 | 202,951 | 175,793 | 158,169 | 163,425
 | Total | 197,774 | 204,324 | 210,806 | 222,349 | 290,419 | 258,957 | 235,653 | 243,362
Power [mW] | Dynamic | 24.219 | 25.047 | 25.78 | 27.977 | 38.123 | 32.751 | 16.707 | 17.583
 | Leakage | 0.001 | 0.001 | 0.001 | 0.002 | 0.004 | 0.004 | 0.001 | 0.001
 | Total | 24.22 | 25.048 | 25.78 | 27.979 | 38.127 | 32.755 | 16.708 | 17.584
Critical path [ps] | Input to Reg | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
 | Reg to Output | 24,629.4 | 24,603.5 | 24,543.5 | 24,521.3 | 24,330.5 | 24,349.3 | 24,431.2 | 24,432.4
 | Reg to Reg | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
 | Input to Output | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A
Synthesis time |  | 28:00 | 34:27 | 28:00 | 37:12 | 35:20 | 34:22 | 27:49 | 32:53

## Slide 7: BestChoice algorithm - Testing
compare
IDENTICAL ✓
Input file with random TC charge values
Python testbench
BC algo in Python
SystemC testbench
BC algo in SystemC
Verilog testbench
BC algo at Gate-level
Output file with sorted charge values
Output file with addresses
Output file with sorted charge values
Output file with addresses
Output file with sorted charge values
Output file with addresses
compare
IDENTICAL ✓
compare
IDENTICAL ✓
compare
IDENTICAL ✓
Verilog testbench
BC algo at RTL level
Output file with sorted charge values
Output file with addresses
compare
IDENTICAL ✓
compare
IDENTICAL ✓

## Slide 8: Conclusion
BestChoice algorithm block synthesis
  Stratus HLS synthesis with TSMC65LP Best-Case library
    A Worst-Case library was used last time
    This one generates a less constrained RTL
  Genus synthesis with
    RD53 SS, 1.08V, 0°C, 100/200/500 Mrad TID
    TSMC65LP Worst Case 0.9V library
  No timing violations
  All testbench tests have passed successfully
  RTL Verilog and Test Bench available on CERN GitHub repo:
  https://gitlab.cern.ch/dcoko/econ-t-bestchoice-algorithm/

## Slide 9: Backup

## Slide 10: Synthesis reports: Stratus HLS -> Genus
Technology library |  | RD53 |  |  |  |  |  | TSMC65LP | 
GENUS TARGET LIB. |  | 100 Mrad |  | 200 Mrad |  | 500 Mrad |  | WCL0D9 | 
SYNTHESIS PHASE |  | Initial | Post-synth | Initial | Post-synth | Initial | Post-synth | Initial | Post-synth
Gates | Sequential | 2,305 | 2,261 | 2,305 | 2,261 | 2,305 | 2,261 | 2,305 | 2,261
 | Inverter | 13,229 | 6,182 | 13,229 | 6,490 | 13,229 | 7,355 | 13,229 | 7,276
 | Buffer | 0 | 457 | 0 | 658 | 0 | 1,006 | 0 | 207
 | Logic | 47,392 | 31,945 | 47,392 | 34,005 | 47,392 | 38,038 | 47,392 | 37,578
 | Total | 62,926 | 40,845 | 62,926 | 43,414 | 62,926 | 48,660 | 62,926 | 47,322
Area [mm2] | Net | 1,118 | 72,306 | 1,118 | 76,267 | 1,118 | 83,164 | 1,118 | 79,937
 | Cell | 256,520 | 132,018 | 256,520 | 146,082 | 256,520 | 175,793 | 256,520 | 163,425
 | Total | 257,638 | 204,324 | 257,638 | 222,349 | 257,638 | 258,957 | 257,638 | 243,362
Power [mW] | Dynamic | N/A | 25.047 | N/A | 27.977 | N/A | 32.751 | N/A | 17.583
 | Leakage | N/A | 0.001 | N/A | 0.002 | N/A | 0.004 | N/A | 0.001
 | Total | N/A | 25.048 | N/A | 27.979 | N/A | 32.755 | N/A | 17.584
Critical path [ps] | Input to Reg | 11,735.0 | 0.0 | 8,501.3 | 0.0 | 3,470.6 | 0.0 | 8,009.1 | 0.0
 | Reg to Output | 24,574.4 | 24,603.5 | 24,486.1 | 24,521.3 | 24,317.8 | 24,349.3 | 24,371.2 | 24,432.4
 | Reg to Reg | 16,169.4 | 0.0 | 14,024.2 | 0.0 | 10,651.1 | 0.0 | 13,644.3 | 0.0
 | Input to Output | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A
Synthesis time |  | 34:27 |  | 37:12 |  | 34:22 |  | 32:53 | 

## Slide 11: Synthesis reports: Vivado HLS -> Genus
Technology library |  | RD53 |  |  |  |  |  | TSMC65LP | 
GENUS TARGET LIB. |  | 100 Mrad |  | 200 Mrad |  | 500 Mrad |  | WCL0D9 | 
SYNTHESIS PHASE |  | Initial | Post-synth | Initial | Post-synth | Initial | Post-synth | Initial | Post-synth
Gates | Sequential | 2,307 | 2,233 | 2,307 | 2,233 | 2,307 | 2,233 | 2,307 | 2,233
 | Inverter | 13,310 | 5,565 | 13,310 | 5,607 | 13,310 | 8,131 | 13,310 | 6,480
 | Buffer | 0 | 429 | 0 | 490 | 0 | 1,176 | 0 | 183
 | Logic | 48,251 | 31,387 | 48,251 | 33,267 | 48,251 | 41,141 | 48,251 | 37,031
 | Total | 63,868 | 39,614 | 63,868 | 41,597 | 63,868 | 52,681 | 63,868 | 45,927
Area [mm2] | Net | 1,118 | 69,099 | 1,118 | 72,559 | 1,118 | 87,468 | 1,118 | 77,484
 | Cell | 261,151 | 128,675 | 261,151 | 138,247 | 261,151 | 202,951 | 261,151 | 158,169
 | Total | 262,269 | 197,774 | 262,269 | 210,806 | 262,269 | 290,419 | 262,269 | 235,653
Power [mW] | Dynamic | N/A | 24.219 | N/A | 25.78 | N/A | 38.123 | N/A | 16.707
 | Leakage | N/A | 0.001 | N/A | 0.001 | N/A | 0.004 | N/A | 0.001
 | Total | N/A | 24.22 | N/A | 25.78 | N/A | 38.127 | N/A | 16.708
Critical path [ps] | Input to Reg | 13,199.2 | 0.0 | 10,390.2 | 0.0 | 5,958.7 | 0.0 | 9,971.7 | 0.0
 | Reg to Output | 24,574.4 | 24,629.4 | 24,486.1 | 24,543.5 | 24,317.8 | 24,330.5 | 24,371.2 | 24,431.2
 | Reg to Reg | 11,616.5 | 0.0 | 8,427.6 | 0.0 | 3,394.7 | 0.0 | 7,859.8 | 0.0
 | Input to Output | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A
Synthesis time |  | 28:00 |  | 28:00 |  | 35:20 |  | 27:49 |