## Slide 1: Radiation Integrals in MADX
Tobias Persson and Leon van Riesen-Haupt
Thanks to: Helmut Burkhardt, John Jowett

## Slide 2: Goals and Motivation
Check if radiation integrals are correct
  Users had reported issues with
  Explore momentum dependence
General discussion on requirements for integrals and radiation in MADX
Very relevant for MADX as a tool to design FCC

## Slide 3: Reliability of Integrals
Checked integrals for well studied lattices (on momentum)
  LEP: MADX vs python from twiss
  FCC-ee: MADX vs python vs SAD
All showed good agreement
Closer study of script from users
  Could not reproduce problem they were experiencing
  After consulting with users, they were using version 5.02.00
    Integrals last updated in 5.02.03 (2014)
“Standard” radiation integrals reliable in MADX

## Slide 4: Off Momentum
  part only non-zero in combined function magnets and or when non-zero orbit through quadrupole causes dipole kick
    Dipolar field:
    MADX does NOT take this into account (only evaluates when )
Off momentum: dipolar kick from offset in quadrupoles
  Offset:
In large machine is very small so term dominates off momentum behaviour
Smaller impact on other integrals as

## Slide 5: Off Momentum MADX vs SAD

## Slide 6: Integral
Introduce integral = [1]
  Describes momentum dependence of partition function
Roughly(!):
  in quadrupoles with yields
Explicitly, modified partition function[1]:
Extend python code to evaluate
Also plot
[1] J. Jowett SLAC-PUB-4033

## Slide 7: Including

## Slide 8: Discussion
Radiation integrals useful for first estimate of machine properties
  “Ideal” on-momentum machine
Can define large number of additional integrals to describe other effects
  These effects can also (more accurately) be studied using EMIT module or tracking
  Most additional integrals not needed
Identified two additional integrals that should be useful
  - energy loss in quadrupoles
    Not captured by - important in colliders
  - variation of damping partition with momentum
    Could experience variation of RF/length of machine
  Working on implementation in MADX
    To be checked vs. python and MAD-8 on LEP
Need to update MADX documentation to clarify radiation integrals scope and limitations