## Slide 1
Beam spot at EAR1
Laurent Tassan-Got
with capture collimator

## Slide 2
PPAC chamber in PRT experiment
2 x 235U samples
Localisation of emitting point on sample from line joining the crossing points on detectors on each side of the sample (coincidence method)

## Slide 3
Localisation
Localisation of each fission fragment in PPAC by delay line
Emitting point on sample reconstructed from the line joining the crossing points on PPACs
Accuracy ~1.5mm. At high energy (>10 MeV) the linear momentum transfer slightly blurs the reconstruction

## Slide 4
Circular spot well observed + neutron background covering the sample disk size (8cm diameter)
All energies
300 MeV < E < 1 GeV
Mapping of the beam spot

## Slide 5
Mean position
Standard deviation
Transition between 1 and 3 MeV visible in 1st and 2nd moments
Horizontal shift by 0.75 mm in the transition
1st and 2nd moments of beam spot

## Slide 6
Intensity radial distribution
Low energy
High energy
Distribution is not gaussian
Fitted by :
p1=0.007333
p2=3.25 10-5
Flat plateau at the center
Fitted by :
p1=4.7574 10-7
p2=0.01373
(1)
(2)

## Slide 7
Radial distribution in transition range
0.3-1 Mev (1) p1=0.007558, p2=3.51 10-5
1-3 MeV (1) p1=0.00900, p2=3.817 10-5
3-10 MeV (2) p1=3.614 10-7, p2=0.01281

## Slide 8
Comparison to simulations
simulation=Fluka+geometrical transport
Low and high energy
Transition range
Good agreement for the shape of radial distribution
Flat central plateau at high energy satisfactorily reproduced
Good agreement for the energy dependence

## Slide 9
Conclusion
Accurate measurement of the beam profile at EAR1 with the capture collimator
The profile is not gaussian and a flat central plateau shows up above 3 MeV
Fits are provided so that the beam interception factor can be accurately at any energy
Simulations well reproduce the shapes of the distributions and their energy dependence

## Slide 10
Backup

## Slide 11
Trajectory reconstruction with boost
The reconstructed point (green dot) deviates from the emitting point (black dot) due to the linear momentum transfer
The effect is limited due to limited angle (no effect at 0°)
The linear momentum transfer levels off at high energy beyond 30 MeV

## Slide 12
Mapping of α activity